## Slide 1: Stable and radioactive beam development at GANIL Recent progress and ongoing work
Pierre Chauveau for the Target & Ion-source group

## Slide 2: Introduction/Outline
Cyclotron facility
N+ sources
ECR4, ECR4M
LINAC facility
SILHI (ECR 1+)
PHOENIX V3 (ECR N+)
SPIRAL1 facility
1+ and N+ sources
TISS, PHEONIX V2
S3 facility
1+ laser source
S3-LEB
Stable beams: ECR ion sources
  Progress on stable beams
  Source monitoring
Radioactive beams: focus on SPIRAL1
  Types of TISS
  Recent progress and on-going work
Conclusion

## Slide 3: Stable beams: improving the rates (1/2)
High Voltage : 20.6kV
Drain current : 1.96mA
RF power : 342W
O2 support gas : 2.95V
Oven : 0.710A
Bias : 0V
High Voltage : 20.6kV
Drain current : 2.21mA
RF power : 294W
O2 support gas : 2.75V
Oven : 0.930A
Bias : -100V
Coax + oven at HV ground
Coax + oven at HV + bias
Slide credit: M. Dubois
Now used for every stable beam requiring an oven.
March 2025
experiment
 | 2007 | 2025
Average intensity of 206Pb31+ (µAe) | 0.6 | 1.1
Transport up to FC | 28% | 45%
Consumption (µg/h) | 65 | 27

## Slide 4: Stable beams: improving the rates (2/2)
Acceleration column (80kV)
Ion source
(25kV)
Solenoid
Mass
separator
Faraday cup
(FC0)
Collimator
Magnet
Faraday Cup
(FC11)
Before
After
Transport Evaluation on Injector 1 | 
Source to FC0 | 75%
FC0 to FC11 | 55 to 60%
2024 tests
+30% to 60% increased rate in FC11
Qpole permanently installed in I1
Installation of a Qpole
Slide credit: M. Dubois

## Slide 5: Stable beams: improving the stability
Slide credit: M. Dubois
Gaz valve regulated at 40°C
15 parameters modifications in 2 days to stabilize the output
Intensity variation : 40%
(2022)
<5% output variation over 4 days
(2024)
From 2-3 source retuning/day to once every few days
Less rate variation in between source retuning (typically <10%)
Now used for every beam
No source tuning during operation

## Slide 6: Stable beams: new beams
Images credit: M. Dubois
232Th30+ at 6.1 MeV/u, E849_21 (D. Ramos)
186W24+ at 5.1 MeV/u, E900_24 (C. Schmitt)

## Slide 7: Stable beams: monitoring the source
Images credit: A. Ribet
17/03/26 16h50
Temps d’intégration = 2 s Temps d’intervalle = 2 s
PHF=222 W, O=5.44 V, Pfour=12,64 W
Monitoring the source plasma through the viewport on the first dipole of I1: camera CCD + spectrometer
Optical electron spectroscopy
  Non intrusive
  Identification of contaminants, outgassing
  Time evolution of several species/charge states (observing instabilities)
  Plasma diagnostics (ne, Te)
Program developped by A. Ribet for operation.

## Slide 8: Radioactive beams: types of TISSs
58 primary beams from 12C to 238U
Thick targets: C, Nb (in development)
Thin targets: C, Ni
3 ion sources: ECR, SIS, FEBIAD
Target/stopper
Primary beam
Ion source
Separator
TISS
The ISOL technique
To user/
acceleration
 | ECR | SIS | FEBIAD
Thick target |  |  | 
Thin target (TULIP) |  |  | 
Nanogan
For gaz
N+
FEBIAD
For condensable
1+
MonoNaKe
For alkali
1+
TULIP
For alkaline
TULIP(-FEBIAD)
For neutron-deficient isotopes
1+
1+
Advantages
Intensity (directly N+ beam)
Purity (gases only)
Disadvantages
Lower charge states (and energy)
Gases only
Advantages
Broadband
Disadvantages
Non selective
Advantages
Intensity (high efficiency for most alkali)
Purity (low ionisation energies only)
Disadvantages
Only alkali
Advantages
Intensity (high efficiency for most alkali)
Purity (low ionisation energies only)
Fast release
Disadvantages
Only alkali
Low in-target production
Advantages
Broadband
Fast release
Disadvantages
Non selective
Low in-target production

## Slide 9: Radioactive beams: the TULIP TISSs
TULIP FEBIAD
Fully tested offline
Efficiency measurement with tracers (Ar, Ag, Sn, In, Eff≈9-15%)
First online test in 04/2026 aiming to produce Sn isotopes: Ag/Pd isotopes seen but no Sn
Rotating target (increased beam power)
Simple and radiation hard
Water wheel/magnetic coupling
Works but rotation speed limited by eddy currents
TULIP SIS
Proof of principle with Rb isotopes
Several experiments (2022,2023,2024)
Improved rate for 74Rb (T1/2 = 65ms)
20Ne Primary beam
Mo-Ni-Mo target
(fusion-evaporation)
graphite window
Graphite catcher
Radioactive ion beam
60 mm
TULIP cavity
Beam OFF
Beam ON
11,2 µs
74Rb+ (T1/2=64,5 ms)
Beam chopper 50 ms ON/10 ms OFF
I20Ne = 0,9 p.µA, Tcavity ~ 1500°C
Chart: Rb mass (a.u)
| 74 | 75 | 76 | 77 | 78
Calculated in the catcher 20Ne@117MeV | 72000 | 42050 | 245000 | 62500 | 67000
Expected in the identification 20Ne@117MeV | 14271.0375 | 2128.8275 | 30213.3972 | 24198.6393 | 22473.8347
Measured 20Ne@117MeV | 400 | 17591.5385
Measured 20Ne@90MeV | 17
x ~20
x ~25 ?
Slide credit: P. Jardin

## Slide 10: Radioactive beams: The FEBIAD TISS
Objective: production of radioactive metallic ions
April 2023 (50Cr)
July 2024 (58Ni)
September 2024 (129Xe)
Before 2023
Since 2021
Irradiated with 48Ca (2021), 36Ar, 84Kr (2022), 50Cr (2023), 58Ni (2024),129Xe (2024)
100+ radioactive isotopes/isomers seen, including around 60 at post-accelerable intensities (>1E5pps).
48,49Cr produced for the first time in 2023
Fe/Co/Ni beams produced for the first time in 07/2024
« Heavy » ions produced in 09/2024
Ongoing work
Investigation into the Ti contamination for the 48Cr beam
Investigation into the production of a 44Ti beam in batch mode
Online experiment (09/25, 07/26, XX/27?): post-acceleration and purification of 56Ni
58Ni @ 74.5AMeV ≈600W |  | 
Isotope | HL | measured rate (pps)
59Cu | 82 s | 5.03E+05
58Cu | 3.205 s | 1.60E+05
57Ni | 35.6 h | 2.52E+07
56Ni | 6.081 d | 1.99E+06
58Co | 70.883 d | 9.40E+07
57Co | 271.8 d | 2.21E+08
56Co | 77.236 d | 1.11E+08
55Co | 17.53 h | 2.33E+07
54mCo | 1.48 min | 2.39E+05
53Fe | 8.51 min | 7.80E+06
53mFe | 2.54 min | 2.39E+06
52Fe | 8.273 h | 4.80E+06
52mFe | 45.9 s | 6.47E+04
57Mn | 85.4 s | 4.10E+04
56Mn | 2.5788 h | 1.09E+06
52Mn | 5.591 d | 1.19E+08
52mMn | 21.4 min | 3.10E+07
51Mn | 45.84 min | 3.90E+07
50mMn | 1.75 min | 1.80E+06
129Xe @ 50AMeV ≈200W |  | 
Isotope | HL | measured rate (pps)
117Xe | 61 s | 8.72E+03
117I | 2.22 min | 3.41E+05
117Te | 62 min | 1.64E+05
117Sb | 2.8 h | 7.42E+05
109Sn | 18.1 min | 4.30E+04
117In | 43.2 min | 1.05E+04
109In | 4.159 h | 7.00E+05
109mIn | 1.34 min | 3.33E+04
109mPd | 4.694 min | 8.86E+02
50Cr @ 72AMeV ≈25W |  | 
Isotope | HL | measured rate (pps)
49Cr | 42.3 min | 5E+05
48Cr | 21.56 h | 3E+05
56(Fe,Co,Ni)15+
at ≈ 16AMeV
56Fe≤26+
56Co≤27+
56Ni≤28+
56Ni28+
56X27+
56X26+
Stripper foil

## Slide 11: Radioactive beams: Towards a new target cavity
New target design to optimize the release of Fe-Co-Ni isotopes (and others)
Gathering material data ✅
Building a parametric model for simulations ✅
Optimizing the geometry for high and homogeneous temperature ✅
Mechanical design 🔄
Building and testing ❌
Images credit: E. Le Villain

## Slide 12: Radioactive beams: Towards a new target material
New target material to improve the production rate of many isotopes
Production calculations : GANIL beams → graphite VS Carbon beam → new material (<Nb) ✅
Investigating and chosing materials (Nb, ZrO2) ✅
Testing material properties ✅
Designing and simulating a target 🔄
Building and testing ❌
Images credit: S. Hurier

## Slide 13: Radioactive beams: 39Ca for the MORA project
Images credit: C. Pfeffer
New TISS for intense 39Ca beams
Preliminary investigation
  production method (fragmentation) ✅
  Target/catcher materials (several choices) ✅
  Diffusion/effusion 🔄
  Ionization 🔄
Offline Ca ionisation tests (MonoNake + Re ionizer/FEBIAD) 🔄
Cavity design and thermal simulations ❌
Mechanical design, assembly and test ❌
Chart: Diffusion efficiency in Tantalum
| 1 | 2 | 3.0000000000000004 | 4 | 5 | 6.0000000000000009 | 7.0000000000000009 | 8.0000000000000018 | 9.0000000000000018 | 10.000000000000002
37K | 14.1204 | 7.0602 | 4.7068 | 3.5301 | 2.8241 | 2.3534 | 2.0172 | 1.7651 | 1.5689 | 1.412
40Ca | 79.3247 | 52.2412 | 36.4079 | 27.5038 | 22.029 | 18.361 | 15.7385 | 13.7712 | 12.2411 | 11.017
46Ti | 50.7526 | 26.5554 | 17.7223 | 13.2921 | 10.6337 | 8.8614 | 7.5955 | 6.646 | 5.9076 | 5.3168

## Slide 14: Takeway messages
Stable beams
Improved rate and stability on most beams
New tool for source monitoring
Radioactive beams
Many beams produced in the recent years … but wether they are expoitable or not depends on the experiment
Many ongoing developments: new beams with existing TISSs & new TISSs
Beam requests
Estimating the feasibility requires the minimum rate, the energy and the maximum contamination
Crucial for radioactive beams
Contact us
pierre.chauveau@ganil.fr
pascal.jardin@ganil.fr
mickael.dubois@ganil.fr
pierre.delahaye@ganil.fr
chartbeams-spiral1@ganil.fr

## Slide 15: Thank you for your attention