## Slide 1: AGATA/GANIL Mechanical design
Guillaume BRUNET
AGATA WEEK
Warsaw (Poland) - 11 September 2026

## Slide 2: GLOBAL OVERVIEW
Beam
Mechanical integration in the G1 hall:
Mechanical installation
Detectors position update
Movements : AGATA rotation
Movements : GRIT & VAMOS
Movements : AGATA honeycomb
New diagnostic box
Beam pipe VAMOS
Beam pipe GRIT
Mechanical interface : GRIT / VAMOS
Racks disposition
Cables management
Detectors handling
LN2 Distribution
Where we at ?
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026

## Slide 3: Mechanical installation
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026
Beam
Standard AGATA 2Pi setup
New diagnostics vacuum chamber
Rotating structure (curve rails) on the ground (0 to +28°)
New Rotating (0° to +28°) and Linear (0 mm to 150 mm) systems with 2 Hand Wheels
Original Vamos/G1 setup ( beam tube modifcation)
Moving back chassis ( - 500 mm)
New Vamos platform (GRIT / AGATA access)

## Slide 4: Detectors position update
GRIT needed some space on the top of the honeycomb for the targets loaders (the vacuum external part).
Change of 2 detectors position (from green position to red).
=> Mechanical integrity of the honeycomb simulations was carried out by Richard Smith and validated!
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026
Richard Smith : Report #/version: 1098-ph5-meng-fea-0001 v3.0

## Slide 5: Movements : AGATA rotation (0 to 28°)
AGATA : EXPERIMENTAL POSITION
0° 0mm
GRIT :
max rear position, target access limited
AGATA :
28° 0mm Vacuum pipe installation possible
GRIT :
max rear position, Target access
AGATA :
28° -500mm Vacuum pipe installation possible
GRIT :
=> Full access
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026

## Slide 6
Movements : GRIT & VAMOS linear translations
LN2 manifold & cable tray rotate with the shaft if we want to remove a detector (± 90°)
Note: Cable management is not included in the pictures!
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026
Honeycomb : 0° (Home position)
Homeycomb : + 90°
Homeycomb : - 90°
AGATA 0° to 28° : 
AGATA 0° :  AGATA ≠ 0°: 
Movements : AGATA honeycomb (±90°)

## Slide 7: Movements : GRIT & VAMOS (Linear translations)
AGATA : 0°, 0mm
GRIT : 0mm
VAMOS : 0°, 650mm
(bellow interface VAMOS / GRIT not included)
AGATA : 0°, 0mm
GRIT : 0mm
VAMOS : 1100mm (max rear position,
detector not in the picture !)
AGATA : 0°, 0mm =
GRIT : 450mm (max rear position, target access limited, ..)
VAMOS : 1100mm (max rear position)
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026
GRIT access :
Specialized
step ladder ??
EXPERIMENTAL SETUP

## Slide 8: New Diagnostic box
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026
Newly designed diagnostic box,
fitting within the tight geometric constraint (~375 mm)
All equipments on the same side to give room for the cables
  RED : Profiler (new design) GREEN : Faraday Cup YELLOW : Turbo pump DN160
  BLUE : Mechanical support PINK : Free Flange (DN160 for a detector ?)
Valve AGATA beam line side DN100

## Slide 9: Beam pipe VAMOS (lenght : 2 m) Connection without a clamp inside the AGATA honeycomb
The blue bellows is mounted on the valve diagnostic box.
The red spherical flange and pipe slide along the bellows and are pressed against the GRIT vacuum chamber.
(no clamp => no access).
To press it onto the GRIT pipe, we use the three screws around the bellows, which compress the three springs.
(Difficult access between DB and AGATA : 3 cm !!!!)
Internal dimensions validated by GANIL’s optical engineer (Bertrand Jacquot)
A prototype is currently being manufactured (expected completion: end of 2026).
Next steps: Mounting validation, spring force testing, and vacuum leak checks.
Centering cone
O-ring
Ball end
Springs (x3)
Brass bolds
2 mm Clearance with shaft
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026
GRIT beam
pipe
New
Diagnostic
Box

## Slide 10: Beam pipe GRIT (lenght : 300mm)
Major contraint for mounting GRIT on setup position:
The five AGATA detectors around the beam pipe must be retracted to insert or remove the spherical flange of GRIT ( ~ 15 mm)
Centering cone of
GRIT beam line
Ø52
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026
Machining directly with the GRIT reaction chamber => See GRIT presentation
Central
Pentagon AGATA
GRIT beam pipe

## Slide 11: Mechanical interface: between GRIT and VAMOS
GRIT / VAMOS Interface (~ 150mm) : bellows DN320 with dimensions dictated by the detector size.
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026

## Slide 12: Racks disposition
Cable management challenges:
  Strict localization of the platform : Due to the 2 rotations (Honeycomb and AGATA) and the length of the MDR cables => high difficulties in managing the cables in this constrained area
New fixed platform in stainless steel (unpainted):
  2 rows:
  4 racks for LVPS, Autofill, and other devices.
  3 racks for digitizers.
  Various cables routed on the top and underneath (30 cm available above ground).
EMC:
  Copper links between the electronics platform and VAMOS, GRIT.
  Copper surface under AGATA rails and the electronics platform.
  EMC : conductive shielding gaskets already planned
  Awaiting a full system analysis by Nabil KARKOUR.
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026
LVPS
DIGITIZERS
Autofil
HV, …

## Slide 13: Cables management challenges
Looped cables to absorb rotation along beam axis (±90°) and target axis (0° to +28°)
Volume under the grid racks is available for cables.
The cables are clamped :
  On the grid and with the support for bending (above the AGATA shaft).
  On the racks (at the far ends).
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026

## Slide 14: Detectors handling
100mm
Current Handling fixture
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026
Two most complicated detectors to handle are the top central ones in front of the grid cable
Mandatory to remove 6 cables for the left one, 9 to 12 for the right one
Removing the cable spacer (yellow) and U shaped terminal (for fixation)

## Slide 15: LN2 Distribution
Outlet (gas) with T°, no-return valve
On one side: Tied to the AGATA shaft.
On the end shaft side (enter beam): Fixed with screws.
Angled liquid nitrogen (LN2) delivery (limited headroom in G1 and also under the pillar jib crane, 80mm with the hook)
Like Legnaro: Patch box for (C&C) mounted on this distribution
Inlet and Oulet are insulated with vacuum and MLI
The detectors must only be filled when the honeycomb is at 0°
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026
Inlet (with Cryo valve)
700mm
2000mm

## Slide 16: Where we at ?
78% of the 78 mechanical drawings are done
All mechanical drawing have to be done before the end of august 2026
All part have to go to manufacturing before the end of 2026
A prototype of the beam pipe is in manufacturing and is meant to be used with GRIT
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026

## Slide 17: Thank you for your attention

## Slide 18: Some distances on beam line
30mm
400mm
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026
3330mm
900mm
2600mm
pillar jib crane (with hook)
80mm
600mm
2070mm
4000mm

## Slide 19: Beam pipe : connection without clamp inside AGATA honeycomb
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026

## Slide 20: Cables removal
Mandatory to remove :
6 cables for the left one,
9 to 12 for the right one
Removing the cable spacer (yellow) and U-shaped terminal (for fixation)
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026

## Slide 21: LN2 Distribution insulation
Inlet Outlet
Vacuum insulation
Inlet and outlet are insulated with Multi-Layer Insulation (MLI) and vacuum.
Same components as the current distribution are used (cryogenic valves, sensors, etc.)
Guillaume BRUNET, AGATA WEEK, Varsaw, 11 September 2026
700mm
2000mm