## Slide 1
GATE Activity @ DeSIs-IPHC
L. V. Garcia Garcia (lucia-victoria.garcia-garcia@iphc.cnrs.fr)
GATE Scientific Meeting 2026
Strasbourg – 1st April 2026

## Slide 2
GATE @ DeSIs-IPHC
DeSIs = Dosimetry Simulation and Instrumentation
Members : 4 lecturers, 4 engineers-technicians, 1 Post-Doc, 2 PhD
Applied nuclear physics:
  Radiation protection - Secondary neutron dosimetry
  MC software benchmarking/intercomparison
  Nuclear measurements

## Slide 3
Active Neutron Detection
Neutrons are the main secondary particle radiation in particle accelerators and space dosimetry
Most current neutron detectors are based on passive methods
AlphaBeast project:
  We aim to develop a CMOS sensor capable to detect Thermal and Fast neutrons on real-time  Obtain an electronic version of SSNTDs
  4D monitoring
sensor network (3D - space)
real-time monitoring (1D - time)

## Slide 4
Active Neutron Detection
Oxide layer
Epitaxial layer
Bulk
Thermal Neutron Detection
Oxide layer
Epitaxial layer
Bulk
nth
10B layer

## Slide 5
Active Neutron Detection
Oxide layer
Epitaxial layer
Bulk
Fast Neutron Detection
Oxide layer
Epitaxial layer
Bulk
nfast
PE
P+

## Slide 6
6
AlphaBeast Detectors
MonoBeast
Single detecting area
Extraction of both counters and analog signal [deposited energy]
TriBeast
Three detecting areas (simultaneous acquisition with Fast and thermal neutrons converter and background)
Extraction only of counter

## Slide 7
GATE in AlphaBeast Development
AlphaBeast Characterization
Calibration curve: relationship between deposited energy and ADC signal on MonoBeast
Calibration curve
AIFIRA Microbeam
241Am source (Ealpha ≈ 5.48 MeV)
Oxide layer
Apertures
Epitaxial layer
Bulk
CYRCE Proton Beam

## Slide 8
GATE in AlphaBeast Development
AlphaBeast Characterization
MC estimation of detection efficiency (hits per fluence)
  Calculations of the deposited energy distribution in the epitaxial layer
  Applied rejection low energy threshold (E_dep < 0.2 MeV) for electron and gamma.
Notes: Same slides

## Slide 9
AlphaBeast Experimental Methodology
Main Goal : Test the AlphaBeast response in various accelerator facilities to evaluate neutron detection in different type of mixed fields
Data acquisition with MonoBeast
Data acquisition with TriBeast
Data acquisition with SSNTD
MC simulation of Energy deposition in detector given the experimental condition
Check reliability between AlphaBeast technology,
state-of-the-art methods

## Slide 10
Radiation therapy room
Experimental Campaigns in Radiotherapy room
  Monitoring of secondary neutron production in radiotherapy
  Comparison between MC energy deposited and AlphaBeast experimental signal
33.5 cm
15 MV run with 10B converter
15 MV run with PE converter

## Slide 11
Hadrontherapy room
As part of the EURADOS WG9 members, AlphaBeast was tested in HIT alongside with other 8 neutron monitoring systems
  Use of MC simulation to determine expected number counts
  Comparison between FLUKA and GATE MC simulations
MonoBeast
TriBeast
SSNTDs

## Slide 12
Secondary Neutron Production in Hadrontherapy
As part of the EURADOS WG9 members, AlphaBeast was tested in HIT alongside with other 8 neutron monitoring systems
  Use of MC simulation to determine expected number counts
  Comparison between FLUKA and GATE MC simulations

## Slide 13
Cyclotron facility
  Neutron production monitoring during CYRCE cyclotron production of 18F  activation calculations
    Continuation of Simβ-AD project  neutron activation in particle accelerators
    Thermal neutron online monitoring during cyclotron operation
    Intercomparison between MC simulation, SSNTDs and AlphaBeast Technology

## Slide 14
Next steps in AlphaBeast Development
Short-term goal
Continue the evaluation of the reliability of AlphaBeast technology against state-of-the-art neutron detection systems
  Approach: Dedicated experimental campaign with three systems at the AmBe neutron calibration facility (IPHC) and comparison with GATE MC simulations
Ultimate Goal
Deploy a network of AlphaBeast sensors to enable real-time, 3D neutron fluence monitoring around particle accelerators (hadrontherapy, cyclotron, ...)
AmBe Neutron Calibration Facility (IPHC)
AmBe Neutron Spectrum

## Slide 15
Thank you!
Any Questions?
Lucia V. Garcia
Contact: lucia-victoria.garcia-garcia@iphc.cnrs.fr

## Slide 16
GATE in AlphaBeast Development
AlphaBeast Characterization
Determination of detection efficiency
  Analysis of detection efficiency of other particle such as protons
  Test the ability of AlphaBeast to detect neutron in mix fields

## Slide 17
Hadrontherapy room
As part of the EURADOS WG9 members, AlphaBeast was tested in HIT alongside with other 8 neutron monitoring systems
  Use of MC simulation to determine expected number counts
  Comparison between FLUKA and GATE MC simulations
Add results