## Slide 1
Stéphanie Grabielle, Mourad Merzougui, Walid Chaibi, Margherita Turconi
High Power Lasers and Parametric Instability Mitigation

## Slide 2
Plan
ET Laser baseline design
  Besoins en R&D
R&D laser à Artemis pour ET
Instabilités Paramétriques: un frein à l’augmentation de la puissance intracavité
Techniques d’atténuation des instabilités
Programme à Artemis: atténuation active par pression de radiation
Projet en cours et plans pour le futur
Conclusion

## Slide 3
ET Lasers Baseline Design
1064 nm, 700 W
Laser seed ultralow noise + solid state preamplifiers + fiber amplifiers + coherent beam combination
ET-HF
200 W
40 W
R&D:
Démontrer la combinaison cohérente de 4 faisceaux à 200W, couplage dans PMC et prestabilization de fréquence et puissance au niveau des spécification de ET (en cours d’évaluation).
Robustesse et fiabilité des amplis fibrés à améliorer.

## Slide 4
ET Lasers Baseline Design
DOI: 10.1103/PhysRevD.105.122004 (2022)
1550 nm, 5 W
All commercial components:
External cavity diode laser (ECDL) + fiber amplifiers
ET-LF
R&D
- Stabilization du laser au niveau des spécifications ET, surtout à basses fréquences <10Hz

## Slide 5
R&D laser à Artemis pour ET
https://doi.org/10.1364/OE.18.022781 (2010)
RIO system
Diode laser à cavité externe, un exemple:
Activité à Artemis :
Test de différent éléments sélectifs en fréquence: réseau, cavité Fabry-Perot.
Objectif: réduire la largeur de raie d’émission pour l’utilisation comme laser seed

## Slide 6
R&D laser à Artemis pour ET
Etude couplage bruit de phase et amplitude dans les amplis fibrés
Objectifs:
tester un autre type de technologie prometteuse par rapport à celle proposée par LZH, Hanovre (https://doi.org/10.1364/AO.401048)
Etudier la physique des amplis fibrés pour en améliorer les performances
Test d’amplificateurs fibrés Tapered avec pompe injectée à l’air libre
https://doi.org/10.1117/12.2290424 (2018)
Free space counter-propagating pumping
200 W

## Slide 7
R&D laser à Artemis pour ET
Etude couplage bruit de phase et amplitude dans les amplis fibrés
Objectifs:
tester un autre type de technologie prometteuse par rapport à celle proposée par LZH, Hanovre (https://doi.org/10.1364/AO.401048)
Etudier la physique des amplis fibrés pour en améliorer les performances
Test d’amplificateurs fibrés Tapered avec pompe injectée à l’air libre
https://doi.org/10.1117/12.2290424 (2018)
Free space counter-propagating pumping
200 W
Etat R&D à ARTEMIS: Financements préliminaire locaux, pas encore de résultats.

## Slide 8
  PI is a three-mode optomechanical instability
Evans et al, Phys. Lett. A, 374(4), 665-671 (2010)
Cavity
fundamental mode w0
w1=w0 -
Parametric Instability (PI)

## Slide 9
  PI is a three-mode optomechanical instability
Evans et al, Phys. Lett. A, 374(4), 665-671 (2010)
Cavity
fundamental mode w0
w1=w0 -
Parametric Instability (PI)
Stokes process

## Slide 10
  PI is a three-mode optomechanical instability
Evans et al, Phys. Lett. A, 374(4), 665-671 (2010)
Cavity
fundamental mode w0
w1=w0 -
Parametric Instability (PI)
Stokes process
More intracavity power  more instabilities

## Slide 11: LIGO solution since O3 Passive dampers to lower the Qm factor decrease of the parametric gain
[S. Biscans PHYS. REV. D 100, 122003 (2019)]
Impact: increase of thermal noise in detection BW
Mitigation strategies: Acoustic Mode Dampers

## Slide 12
Other Mitigation strategies
Thermal tuning of the optical mode resonance [Evans et al. PRL 114,161102 (2015)]
Active damping by Electrostatic drivers. [PRL 118, 151102 (2017)]
PI suppression through optical feedback. [DOI: https://doi.org/10.1103/PhysRevD.109.102006 (2024)]

## Slide 13
dz
Time
dz
Force
PI active mitigation by radiation pressure
        An auxiliary beam is reflected on the mirror
        The beam amplitude is modulated at the mechanical mode frequency
        A 2 D deflection system allow to apply the damping force optimizing the spatial overlap
2D deflection system based on
Acousto-Optic devices

## Slide 14
dz
Time
dz
Force
PI active mitigation by radiation pressure
        An auxiliary beam is reflected on the mirror
        The beam amplitude is modulated at the mechanical mode frequency
        A 2 D deflection system allow to apply the damping force optimizing the spatial overlap
        Expected mechanical mode frequencies 10 kHz-200 kHz  fast deflection
        Need to damp different modes  random access deflection
2D deflection system based on
Acousto-Optic devices
T. Harder et al. Optics Express Vol. 31, Issue 2, pp. 1486-1500 (2023).

## Slide 15
PI: ongoing projects in Artemis
ANR JCJC SPINA 2022-2027
Develop a table–top cavity able to host PI to validate our mitigation strategy
Monitor the mirror modes  to be able to detect the onset of PI

## Slide 16
PI: ongoing projects in Artemis
Setup of a Michelson interferometer with balanced detection at half-fringe.
Results: sensitivity down to 2 x m/ above 30 kHz, enough to detect thermally excited modes with Q-factor
ANR JCJC SPINA 2022-2027
Develop a table–top cavity able to host PI to validate our mitigation strategy
Monitor the mirror modes  to be able to detect the onset of PI

## Slide 17
PI: ongoing projects in Artemis
Setup of a Michelson interferometer with balanced detection at half-fringe.
Results: sensitivity down to 2 x m/ above 30 kHz, enough to detect thermally excited modes with Q-factor
ANR JCJC SPINA 2022-2027
Develop a table–top cavity able to host PI to validate our mitigation strategy
Monitor the mirror modes  to be able to detect the onset of PI +
measurement of mechanical Q
Goal: understand and measure the losses introduced by coating layers interface.
Collaboration with LMA (mirror samples with different number of coating layers) et LAUM (simulations) Commun internship in summer 2025.

## Slide 18
PI: future plans
Mirror’s axisymmetric mode measurement
Measurements of more complex modes with the 2D deflection system
In collaboration with LAUM and LMA : PI passive mitigation by dissipative coatings applied on the rear surface of the mirrors to reduce Q factor of the mechanical modes which potentially can trigger a parametric instability  Application ANR 2026

## Slide 19
Conclusions
Les instabilités parametriques doivent être contrôlées dans ET, une combinaison de technique d’atténuation peut être utilisée.
Notre équipe à Artemis travaille à un système d’atténuation actif par pression de radiation.
Collaboration LMA/LAUM/Artemis veut explorer l’idée d’une technique passive par dépôt de coatings dissipatifs sur la face arrière des miroirs.
Le baseline design des lasers pour ET prévoit l’utilisation d’amplificateurs fibrés, les prototypes à AEI (Hanovre) doivent encore atteindre les performances requises par ET.
Notre équipe a commencé des activités R&D sur des sources diodes à cavité externe et sur les amplis fibrés.

## Slide 20
Spare slides

## Slide 21
Table-top cavity hosting PI
Movable mirror: a suspended macroscopic mirror
In meter-scale stable cavities, the typical frequency difference between optical high-order modes is high (10-200 MHz) compared to the GW detectors
 the frequency matching between optical and mechanical mode frequencies will occur for high order mechanical modes.
 The spatial overlap might be difficult
Mirror Mass
Mirror Quality Factor
Mechanical
frequency
Intracavity power
Geometrical Overlap coefficient
With the nth optical Mode
Sum over all optical modes
,N
N
m
m
m
cav
Gain
R
m
M Ω2m
Choice: cavity closed to semiconfocal configuration

## Slide 22
How to monitor the mirror’s modes?
Goal: measuring the thermally excited displacement of a test mirror, we start by looking for the axisymmetric (drum) modes
Test mirror: diameter: 50.8 mm, thickness: 12.7 mm, quality factor: substrate fused silica, Rmax
ANSYS simualtions eigenfrequencies first drum mode: 35.67 kHz
Estimation of the mirror surface displacement due to thermal excitation
Amplitude Spectral Density of the displacement noise:
With: the eigenmode angular frequency
Q the quality factor of the mechanical mode
the mirror mass that contributes to the mode
the Boltzmann constant
T the temperature
Required Sensitivity of the detection: at least for frequencies > 30 kHz
First drum mode
m/

## Slide 23
How to monitor the mirror’s modes?
Michelson interferometer with balanced detection at half-fringe

## Slide 24
How to monitor the mirror’s modes?
Fast piezo: specially designed mechanical mount to reduce piezo resonances
Michelson interferometer with balanced detection at half-fringe

## Slide 25
Results
Shot noise limited detection
Noise floor: for , level consistent with characterization of the first three drum modes

## Slide 26
Results
Shot noise limited detection
Parasitic peaks
Parasitic peaks

## Slide 27
Results
Shot noise limited detection
Parasitic peaks
Parasitic peaks
Fast piezo first resonances
Recent work on reduction of the parasitic peaks and PZT resonances:
Optimized grounding
Isolation of key components
Optimized detection filters
Added electronic notch filters to the PZT correction signal

## Slide 28
Results
Reduction of the parasitic peaks:
Optimized grounding
Isolation of key components
Optimized detection filters
Reduction of the PZT resonance:
Added electronic notch filters to the PZT correction signal

## Slide 29
Perspectives towards implementation on a GW detector
T. Harder et al. Optics Express Vol. 31, Issue 2, pp. 1486-1500 (2023)

## Slide 30
PIs observation and mitigation
USRP
RF-AMP
RF-AMP
vacuum
L
L
Servo-control
Electrostatic actuator
cavity