## Slide 1
Collaborative study on Compton Polarimetry for future colliders
Zhe Duan and Aurélien Martens
on behalf of IHEP-IJCLab team
29 June-3 July, 2026, 17th FCPPN/L Workshop, Lyon, France, email: duanz@ihep.ac.cn

## Slide 2: Polarized beams @ CEPC: transverse polarization
Precision beam energy calibration based on Resonant Depolarization (~1e-6 accuracy)
  Precision measurements of Z&W mass (FCC EPOL, arXiv:1909.12245, CDFII: Science 376, 6589)
  Fiducial for Higgs & ttbar mass measurements (LEP2 CM energy evaluation above 80 GeV, arXiv:9901002,)
Requirements:
  Transverse Compton polarimeter: statistical uncertainty ~1%/second
  RF depolarizer: specs similar to bunch-by-bunch feedback kicker
  RD measurements every ~ 10 mins
  At least 5%~10% vertical polarization for e+/e-
LEP: Z. Phys. C 66, 45-62 (1995).
CEPC Z&W mass, CDR 2019
CEPC W mass: EJPC 80, 66 (2020)
CEPC ttbar, arXiv:2207.12177
polarimeter
IP/detector
IP/detector
depolarizer

## Slide 3: Polarized beams @ CEPC: longitudinal polarization
Measuring weak mixing angle from AFB, ALR @ Z-pole in the same experiment
G. Moortgat-Pick’s talk on CEPC Workshop EU @ Marseille, 2024 April
Solenoid spin rotators around each IP (~400 Tm per IP per ring)
(Xia et al, RDTM 6, 490, 2022)

## Slide 4: Injecting polarized beams from the source
Polarized source
  Polarized e- source (>85% polarization)
  e+ damping/polarizing ring (>20% polarization)
Booster
  free from intrinsic spin resonances
  polarization can be well maintained for Z & W
T. Chen, Z. Duan, D. H. Ji, D. Wang, Phys. Rev. Accel. Beams, 26, 051003 (2023).
Consistent results in recent FCC-ee studies (J. Wenninger, Polarization transport to the collider ring, FCC Week 2026)
Injecting polarized beams is under study for FCC-ee in the Reference Design Phase (M. Benedikt, FCC Status and Plans for Reference Design Phase,FCC Week 2026)

## Slide 5: R&D items
The operating e+e- double-ring collider BEPCII is an ideal test bed of beam polarization R&D for future colliders

## Slide 6: Introduction to Compton polarimeter
Eb=45.6 GeV, λlaser=515 nm
Muchnoi, FCC-ee polarimeter, arXiv:1803.09595
Left-right (Counting rate) asymmetry
Up-down (Spatial distribution) asymmetry
linear
polarization
circular polarization (helicity adjustable)
+ =1
scattered γ energy/Compton edge

## Slide 7: Compton polarimetry requirements for future colliders
3D Compton polarimeter
  vertical polarimeter for pilot bunches (RD): ~1%/~10s
  longitudinal/radial polarimeter for colliding bunches: ~0.1%
  coverage of Z, W and even Higgs energies
  7 * 24 robust operation
Experiments in operating machines would help address key systematic uncertainty sources
  advanced pixel detector
  laser polarization control and measurements
  helicity correlated asymmetries

## Slide 8: BEPCII and beam polarization
2024.7
2025.5
2026.5
Start tunnel installation
SR commissioning @ 1.84 GeV
1.11033cm-2s-1 @ 2.35 GeV
BEPCII is in a high-luminosity upgrade phase
e+/e- beams naturally develops sizable vertical polarization during operation, making it a realistic test environment
Simulated vertical polarization 1 hour after injection

## Slide 9: Collaboration on Compton polarimetry
FCPPN/L grant in 2024 and 2025: Future Collider Compton Polarimeter
Team member
  IJCLab: A. Martens (Leader), F. Zomer, D. Nutarelli, F. Mawas, J. Tamazirt etc
    Laser technology, performance simulations & data analysis etc
  IHEP: Z. Duan (Leader), Zhijun Liang, Guangyi Tang, Dechong Zhu, Mengyu Su etc
    Machine implementation, detector technology and beam commissioning etc
Research goal
  demonstrate a Compton polarimeter at BEPCII
  design & analysis of Compton polarimeters for FCC-ee/CEPC
Bi-weekly Zoom meeting, joint training of graduate students.

## Slide 10: More on collaboration
Personnel exchanges
  April 2024: visit of Zhe Duan to IJCLab
  December 2024: visit of Aurelien Martens to IHEP
  April 2026: 1-month visit of a student to IHEP, supported by “CAS International Visiting Student Program”
Joint funding acquisition
  2025 “PHC Cai Yuanpei -- Project”, approved
    IHEP: 6-month visit of a PhD student, 3-month visit of a staff to IJCLab
    IJCLab: awaiting official budget notification

## Slide 11: Compton polarimeter @ BEPCII
11
prototype of CEPC vertex detector
Location | beamline and experimental hall of 4W2 wiggler
Laser | 532nm, 4.5 kHz, 2 mJ, 1 ns
Observable | Vertical asymmetry of backscattered γ (up to 180 MeV)
Detector | Pb converter + silicon pixel detector
Signal | backscattered γ ~ 20kHz/mA/W
Background | bremsstrahlung γ ~ 1kHz/mA
11
Expected performance: ~1% statistical uncertainty in ~ 20 sec
Time step: 50 ns

## Slide 12: Overall progress
plastic scintillator + PMT
Causality between laser & signal
Correlation between signal intensity and laser power
M. Su et al., Status report toward implementation of a Compton polarimeter at BEPCII arXiv:2605.09001
Signature of polarization build-up observed

## Slide 13: Experiment setup

## Slide 14: Laser tagging with dual TaichuPix detectors
signal
background
The pulsed nature of gamma signal essential to improve signal-noise ratio
  TaichuPix detector in triggerless mode
  Synchronized dual TaichuPix detectors to facilitate laser tagging in offline analysis

## Slide 15: Mitigate the influence of electron beam orbit drift
  Gamma distribution perturbed by e- beam motion
  Laser helicity flipped at 10 Hz, tagged by the laser spot location on the detector
Chip A - Laser
Chip B - Gamma

## Slide 16: Data analysis chain
Denoising, triggering and grouping
Left helicity
Raw hit map
Right helicity
Chip A - Laser
Chip B - Gamma
=| Y，
Y ～ 82um～3.3 pixel

## Slide 17: How to verify the beam polarization measurement?
Different behavior in the beam polarization evolution:
Normal bunches in collision, refilled every 70 min, polarization “saw-tooth”
Non-colliding pilot bunches, free decay, polarization exponential build-up

## Slide 18: Signature of beam polarization build-up
Alternative measurements of the pilot bunch and normal bunches
Increase of asymmetry over time for pilot bunch, compared to the reference of normal bunches

## Slide 19: Signature of beam polarization build-up
Measured signal behavior differs from the background

## Slide 20: Measured asymmetry
Pilot bunch
Signal
Pilot bunch Background
Just after injection
~3 hours after injection
Theoretical asymmetry for 100% electron & laser polarization
Measured asymmetry for different conditions
=
Larger asymmetry for pilot bunch signal 3 hours after injection
Measured shape not yet match theoretical shape
Need to better understand potential sources of helicity-correlated asymmetry

## Slide 21: Summary
Direct synergy on beam polarization studies between CEPC and FCC-ee
BEPCII provides an operating collider test bed
Compton polarimeter has observed signature of beam polarization build-up
More refined error analysis and improvement of the instruments are planned
  Calibration of the analyzing power
  Sources of helicity correlated asymmetry
  External trigger to detector
  Real-time beam polarization measurement
International collaboration is highly beneficial!

## Slide 22: New solution to the laser-vacuum insertion
Driven by the need to improve laser focusing
  Replace the in-vacuum mirror with diamond window & in-air reflector
  Easier maintenance, less material in gamma pathway
Employ a single crystal diamond window with water cooling to seal the vacuum
borrowed from BEMS (BINP & IHEP)
measured