## Slide 1: China Jinping Underground Laboratory (CJPL)
Yue Qian Tsinghua University(THU)
Charling Tao
THU and CPPM
Long term FCPPL collaboration with LSM Modane.
Now partner of Nexus cf (talk of Feyrouz Malek)

## Slide 2
Jinping-I
Hydroelectric
Power Plant
Jinping-II
Hydroelectric
Power Plant
JinPing traffic tunnel
~18km length, overburden 2400m
CJPL
Yalong
River
CJPL, located in Xichang City of Sichuan, has advantages with a rock overburden of 2400m, ultra-low muon flux and environmental radiation background. Construction started in 2009
CJPL-I Total space: ~4000 m3, and CJPL-II total space 300000 m3.
Dark matter experiments (CDEX, PandaX) First world class results obtained less than 5 years after start of construction!
nuclear astrophysics(JUNA) , gravitational wave experiment, and others are running in CJPL
China Jinping Underground Laboratory (CJPL)

## Slide 3
China Jinping Underground Laboratory (CJPL)
CJPL-I
(4000 m3)
CJPL-II
（330,000 m3）
Rock overburden 2400 m
Muon flux 3.03×10−10 cm−2s−1
Experimental space >330,000 m3
Astro. Phys. 172 , 103147, (2025)

## Slide 4
μ-flux at CJPL-II
  3.03±0.24(stat)±0.18(sys)×10−10 cm−2s−1
Astro. Phys. 172 , 103147, (2025)
Deepest (2400 m) and Largest (>330,000 m3) UG-Lab
with an extremely low μ-flux of ~96 m−2yr−1
Features of CJPL

## Slide 5
Low background Rock and Cement
Ideal Site
Rock in Jinping mountain has low U, Th containments
Rock sample measured by Ge det.
Control U, Th in cement
Selected raw material
Improved production process
Material screening
(Unit: Bq/kg) | U-238 | Th-232
Jinping Rock | 1.8±0.2 | <0.27
Ground (Beijing) | ~25 | ~50
Tunnel
Shaft
Sci Sin-Phys Mech Astron, 2025, 55: 111017
Features of CJPL

## Slide 6
Neutron Flux ~1000 times lower than ground level
Lab | Neutron Flux [n/cm2/s] | 
 | Fast Neutron | Thermal Neutron
Y2L | 8.0E×10-7 | (2.4±0.2)×10-5
Soudan | / | (0.7±0.08±0.08)×10-6
LCS | (0.66±0.01)×10-6 | (1.13±0.02)×10-6
Yemilab | (1.4±0.1)×10-6 | (1.9±0.1)×10-6
Kamioka | (11.5±1.2)×10-6 | (8.25±0.58)×10-6
Boulby | 1.7×10-6 (E>0.5 MeV) | /
LNGS | 0.86×10-6 (E>1 keV) | 2.9×10-6 (E<1 keV)
SURF | / | (1.7±0.1±0.1)×10-6
LSM | (4.0±1.0)×10-6 | (1.6±0.1)×10-6
Baksan | 5.3×10-7 (E>700 keV) | /
SNO | 4.6×10-6 | 4.7×10-6
CJPL | (3.6±2.8)×10-6 (>1MeV) | (7.0±1.8)×10-6 (<0.5 eV)
 | PE-Room：(4.9±0.9±0.5)×10-9 (1-10 MeV) | 
Neutron spectrum at hall of CJPL-I
NIMA 859 (2017) 37–40
Expacs: simulated surface neutron spectrum
https://phits.jaea.go.jp/expacs/
AAPPS Bull. 34, 25, 2024. NIMA. 626-627, S64–S68, 2011. NIMA. 812:1–6, 2016, Eur. Phys. J. Plus. 127: 108, 2012. Eur. Phys. J. Plus, 127: 109, 2012. Eur. Phys. J. Plus. 127: 111, 2012
Features of CJPL

## Slide 7
Low Radon in large experimental space (~20 Bq/m3)
Radon Control
45,000 m3/h ventilation via pressurized pipes
All experiment area in positive pressure
Dedicated Radon-proof layer cover all surfaces of the Lab
Tunnel
Shaft
Sci Sin-Phys Mech Astron, 2025, 55(11): 111018
Boulby (7,200m3)
Rn～2.4 Bq/m3
Features of CJPL

## Slide 8
Water-Resistant and Radon Suppression (WRRS) layer
  A dedicated multi-layer protection against underground water and radon
Features of the WRRS layer
Preventing water and radon permeating from the rock simultaneously
Covering the full-space of each experiment hall (walls and floor)
Using low-background materials in WRRS
7 layers, 9 processing, dozens of materials
Water-resistant and radon suppression layer
Radon Control in CJPL-II

## Slide 9
Monitoring Rn-222 Before/After building WRRS
  Rn-222 in ventilation air ~ 20 Bq/m3 (Typical outdoor level)
  WRRS and ventilation reduce Radon from ~200 Bq/m3 to 20 Bq/m3
No WRRS (2017)
WRRS (2024)
Average~ 20.3 Bq/m3
Radon Control in CJPL-II
Ref：Sci Sin-Phys Mech Astron, 2025, 55(11): 111018

## Slide 10
Underground Lab
ARGUS
~10.0 μBq/kg
GeTHU:
3 sets in CJPL-I
15 sets in CJPL-II
2 sets,
XIA UltraLo-1800
2 sets,
Element-XR ICPMS
2 sets
low-Background LS
Ground lab in Xichang city
Low background facilities in CJPL

## Slide 11
Shielding Facilities at CJPL-II
Large Water Shielding in B2-Hall
PandaX LXe-TPC DM & 0𝛎𝛃𝛃 experiment
Large LN2 Shielding in C1-Hall
For CDEX HPGe DM & 0𝛎𝛃𝛃 experiment
Large PE Shielding Room in C2-Hall
Total 16 low-BG HPGe γ spectrometers
1745 m3 LN2 Tank
LN filling completed
5500 m3 Water
1 m thick PE wall
GeTHU（MDA～1mBq/kg）
15 low-BG HPGe detectors
ARGUS（MDA ～10 μBq/kg）
Ultralow-BG γ HPGe Array
GeTHU
ARGUS
Providing low γ/n environment
Pit
Top view of the Tank
Look at the PandaX det.

## Slide 12
ARGUS（ARray of GermaniUm gamma ray Spectrometer）in CJPL-II
  Five HPGe detectors assembled by Canberra.
  The MDA ~49.50 μBq/kg for a Copper sample in 609keV ROI by ARGUS.
ARGUS
ARray of GermaniUm gamma ray Spectrometer
Background spectrum by ARGUS in 60 days
unpublished result!
unpublished result!
Ref：TAUP2025 POSTER，Ultra-Low Background Germanium Spectrometers at the CJPL，2025.08，XiChang

## Slide 13
Research Activities at CJPL-II
CDEX (C1)
DM&0𝛎𝛃𝛃 via Natural Ge and Enriched Ge array
JUNA (A1) Jinping Underground Nuclear Astrophysics experiment
JNE (D2)
Jinping Neutrino Program
GeoDEX (D1)
Deep underground geologic time variation in-situ detector experiment
And more:
ICSER
Integrated Circuit Soft Error Research
JPDUQIE
Underground Quantum
Qubit experiment
…
PandaX (B2)
DM&0𝛎𝛃𝛃 via LXe-TPC
CJPL welcomes researchers worldwide to submit proposals!
CUPID-CJPL
Mo-100 0𝛎𝛃𝛃 via LMO scintillation bolometer

## Slide 14: CDEX
Founded in 2009, 11 institutions, more than 100 people now
Focused on Dark Matter detection and Ge-76 0νββ search using HPGe technology
(China Dark Matter Experiment)
CDEX (China Dark Matter Experiment)

## Slide 15
Main features
  Uses p-type point-contact germanium (pPCGe) detectors
  Extremely low energy threshold (around 160 eV)
  Excellent energy resolution
  Liquid nitrogen cooling
  Optimized for very small nuclear recoil signals
  CDEX specializes in the low-mass WIMP region.
Latest scientific results
  No statistically significant dark matter signal.
  World-leading limits on light WIMPs in the sub-10 GeV region.
  New constraints on sub-GeV dark matter using the Migdal effect.
  Improved background suppression demonstrating the feasibility of scaling toward a ton-scale experiment.
CDEX (China Dark Matter Experiment)

## Slide 16
Started in 2009, consists of dozens of universities and research Institutions
Goals: Increase LXe detector mass for DM and neutrino studies
PandaX
Phase-I
120 kg
Phase-II
580 kg
PandaX-4T
3.7 ton
2020-
2009
2010-2014
2015-2019
PandaX (Particle and Astrophysical Xenon Detector)

## Slide 17
Scientific objectives multipurpose experiment searching for:
  WIMP dark matter
  neutrinoless double beta decay
  exotic rare interactions
  neutrino physics
Main features
  Multi-ton xenon target
  Dual-phase liquid Xenon Time Projection Chamber (TPC)
  Simultaneous measurement of scintillation (S1) and ionization (S2)
  Full 3D event reconstruction
  Water shielding
Planned PandaX- 20T
Latest results: Dark Matter Search Results from 1.54 Tonne·Year Exposure of PandaX-4T , Phys Rev Lett 2025 Jan 10;134(1):011805.
Among the world's strongest limits
on spin-independent WIMP–nucleon scattering over a broad mass range.
PandaX (cf talk by Wang Wei)

## Slide 18
Scientific objective
The Jinping Neutrino Experiment aims to become one of the world's most precise detectors for low-energy neutrinos. Primary targets include:
  solar neutrinos
  geo-neutrinos
  supernova neutrinos
  neutrino oscillation physics
Why Jinping?
  CJPL is unusually far from nuclear reactors, giving it the lowest reactor-neutrino background of any major underground laboratory.
  This is a major advantage for measuring natural neutrino sources.
Planned detector:
  approximately 4-kiloton ultra-pure liquid scintillator
  extremely low radioactive background
  high light yield
  precision energy calibration
Current status
  A 1-ton prototype has been successfully operated.
  Engineering and detector R&D continue for the full-scale experiment.
Jinping Neutrino Program (Solar-ν，Geo-ν)

## Slide 19
Pit for 500-ton Neutrino Observatory at Hall D2
Neutrino detector design
1-ton prototype at CJPL-I
Hall D2
Jinping Neutrino Program (Solar-ν，Geo-ν)

## Slide 20
0νββ experiment based on Mo-100 isotope and LMO crystal calorimeter array.
10 kg experiment
- low enrichment
- demonstrate key technologies
250 kg+ experiment
- high enrichment
- probe mbb below 10meV
20
Possible CUPID-1T configuration
Crystal Testing
(2023-2028)
CUPID-CJPL-200/1T
(2028+)
> 250 kg enriched crystals
CUPID-CJPL Demo
(2026-2028)
10 kg enriched crystals
Develop CUPID-reach/1T Technology
Build CUPID-reach or CUPID-1T at CJPL
CUPID-CJPL

## Slide 21
0νββ experiment based on Se-82 isotope and High pressure TPC.
Topmetal technique to readout the ion signal.
High pressure 82SeF6 gas as the source and target.
200kg per module * 5
NvDEx

## Slide 22
Scientific objective JUNA studies the nuclear reactions that power stars. Instead of detecting particles from space, it reproduces stellar fusion reactions in the laboratory.
Main features
  Underground electrostatic accelerator  Very low cosmic-ray background
  Direct measurements at stellar energies previously inaccessible
  Focus on reactions important for:
    hydrogen burning
    helium burning
    carbon–nitrogen–oxygen (CNO) cycle
    stellar nucleosynthesis
Major reactions studied:
  13C(α,n)16O
  25Mg(p,γ)26Al
  19F(p,α)16O
  other key stellar fusion reactions
JUNA (Jinping Underground Nuclear Astrophysics)
Reduced uncertainties in stellar evolution and nucleosynthesis models.
Improved constraints on the origin of elements and stellar burning processes.
These measurements are considered internationally significant because the underground environment allows background levels impossible to achieve in surface laboratories.

## Slide 23
Proposed satellite-based gravitational wave observatory
Triangle of three spacecraft orbiting the Sun linked by laser interferometers
Two alternative plans for Taiji:
  take a 20 percent share of the European Space Agency’s LISA project
  launch China's own satellites by 2033 to authenticate the ASE project.
Test their instruments inside CJPL
Plan a new ~ 100m short-arm experiment.
Taiji (太极)

## Slide 24
For details on the MIMAC detector and its potential,
cf talk in this meeting by Olivier Guillaudin and Tao Yi
- Measurement of neutron background (cf talk by Fayrouz Malek)
- Directional Dark Matter detection (cf talk by Illias Ourahou)
MIMAC in CJPL ?

## Slide 25: Development of µTPC Micromegas for Directional Detection of Rare Events : D2S2 (MIMAC)
D2S2 : Directional Detection of dark matter and neutrons for Science and Society
LPSC (Grenoble) : D. Santos, F. Malek
- M. Marton, N. Sauzet, O. Guillaudin (G. Bosson, J. Bouvier), O. Bourrion, E. Lagorio, C. Houaro, Ilias Ourahou (PhD LPSC)
CPPM (Marseilles) : C. Tao , J. Busto
USTC (Hefei) : Z. Zhang,
CERN / GDD : Rui de Oliveira

## Slide 26
Summary
CJPL is a world-level underground low-background platform for multipurpose scientific and technological research with rock overburden of 2400m and internal capacity of 300000 m³;
Several collaborations including CDEX、PandaX、JUNA have run their facilities in CJPL and achieved a number of cutting-edge research results;
CJPL welcomes more collaborations in the world to establish their experiments therein;