## Slide 1
FEE 2026 · PARIS
Verification of Complex ASICs
Adithya Pulli
EP-ESE-ME, CERN
Front-End Electronics Workshop · May 2026

## Slide 2
Verification is a key enabler for first time silicon success
CONTEXT
Why Verification Matters?
Recent High Energy Physics (HEP) ASICs have far more digital complexity
  Highly optimized readout architectures
  On-chip processing, RISC-V, AI/ML
  e.g. RD53, FastRICH, PicoPix
Cost of engineering runs increase as we move to smaller technology nodes
  65nm → 28nm: engineering runs >2× more expensive
  A re-spin that was manageable at 130nm or 65nm can become financially prohibitive at 28nm
Source: CERN ASIC support
Chart: Full mask-set NRE costs
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
28nm | 1420 | 1430
65nm | 845 | 811 | 786 | 763 | 748 | 683.2 | 670.4 | 580.8 | 568 | 592 | 625.6 | 650 | 680 | 670
130nm | 322.62 | 318.06 | 312.36 | 305.52 | 301 | 292 | 286 | 292 | 225 | 215 | 260 | 250 | 266 | 270
250nm | 91 | 91 | 91 | 91 | 91 | 91 | 91

## Slide 3
CONTEXT
The Chips We'll Use as Examples
FASTRICH
MOSAIX
What | 16-channel front-end readout ASIC for timing detectors
Technology | TSMC 65 nm CMOS
Scale | 5 × 5.25 mm, 16 channels
Features | 25 ps ToA, 4× 1.28 Gbps Aurora, SEE-tolerant
Challenge | High precision TDC, readout optimized for wide range of detector occupancies
What | Monolithic stitched pixel sensor for tracking
Technology | TPSCo 65 nm CMOS imaging process
Scale | 265 × 19.6 mm, ~10M pixels
Features | Sync-based readout, 8× 10.24 Gbps, SEE-tolerant
Challenge | Massive scale — hierarchy & reuse from day one

## Slide 4
SECTION 1
The Verification Process
Illustrated with FastRICH and MOSAIX ASICs
Strategize
→
Plan
→
Implement
→
Sign-off

## Slide 5
STRATEGIZE
Defining the Verification Strategy
Aligns goals, methods, resources, and sign-off criteria

## Slide 6
STRATEGIZE
Defining the Verification Strategy
Aligns goals, methods, resources, and sign-off criteria
Identify requirements & goals — functional, performance, SEE robustness
FASTRICH — VERIFICATION GOALS
Control Interface
● I2C compliance
● 100 kHz – 1 MHz operation
● All RW registers verified
Command Interface
● Lock to fast-command frame
● All command combinations
● Constant command latency
Readout Interface
● Aurora compliance
● 1, 2, 4 links @ 320/640/1280 Mbps
● Recovery after link saturation
Data Integrity
● ToA accuracy <25 ps – TDC linearity
● No hit losses / ghost hits
● Test pulse covers all timing bins
SEE Robustness
● Configuration is not corrupted
● Commands are always responded to
● Command latency is always constant
● Automatic link recovery

## Slide 7
STRATEGIZE
Defining the Verification Strategy
Aligns goals, methods, resources, and sign-off criteria
Identify requirements & goals — functional, performance, SEE robustness
Pick methodologies — simulation vs. formal, RTL vs. netlist, mixed-signal, power-aware
FASTRICH — VERIFICATION METHODOLOGIES
Formal
● Model checking for critical controllers
● Auto formal checks: connectivity, linting, CDC
● Triple Modular Redundancy (TMR) correctness
Simulation — Coverage Driven Constrained Random Verification (CDCRV)
● RTL: protocol compliance, functional correctness, performance analysis
● Netlist: Clock domain crossings, asynchronous paths in TDC
Mixed-signal
● PLL simulations
● AFE + TDC co-simulation

## Slide 8
STRATEGIZE
Defining the Verification Strategy
Aligns goals, methods, resources, and sign-off criteria
Identify requirements & goals — functional, performance, SEE robustness
Pick methodologies — simulation vs. formal, RTL vs. netlist, mixed-signal, power-aware
Conceptualise application — languages and libraries (SV, UVM, Python, cocotb), testbench hierarchies, content reuse
MOSAIX VERIFICATION HIERARCHIES

## Slide 9
STRATEGIZE
Defining the Verification Strategy
Aligns goals, methods, resources, and sign-off criteria
Identify requirements & goals — functional, performance, SEE robustness
Pick methodologies — simulation vs. formal, RTL vs. netlist, mixed-signal, power-aware
Conceptualise application — languages and libraries (SV, UVM, Python, cocotb), testbench hierarchies, content reuse
Identify bottlenecks — compute, licenses, time, people

## Slide 10
STRATEGIZE
Defining the Verification Strategy
Aligns goals, methods, resources, and sign-off criteria
Identify requirements & goals — functional, performance, SEE robustness
Pick methodologies — simulation vs. formal, RTL vs. netlist, mixed-signal, power-aware
Conceptualise application — languages and libraries (SV, UVM, Python, cocotb), testbench hierarchies, content reuse
Identify bottlenecks — compute, licenses, time, people
Define sign-off strategy — checklist of tasks and metrics to declare the chip verified
MOSAIX SIGN-OFF CHECKLIST — 41 TASKS
Category | Hierarchies | Metric
RTL regression | All testbench hierarchies | vPlan score (coverage + pass-rate)
TMR regressions | All testbench hierarchies | vPlan score (coverage + pass-rate)
Netlist regressions (min/typ/max) | All testbench hierarchies | vPlan score (functional coverage + pass-rate)
Power-aware regressions (typ) | All testbench hierarchies | Pass-rate
Performance analysis | Sensor Tile | Efficiency plots
Quality checks | All testbench hierarchies | Warning counts, SDF annotation percentage, waiver review
Formal analysis | Sensor Tile, Left End Cap | Super lint and connectivity checks pass without errors

## Slide 11
SECTION 1
The Verification Process
Illustrated with FastRICH and MOSAIX ASICs
Strategize
→
Plan
→
Implement
→
Sign-off

## Slide 12
PLAN
Verification Plan & Project Plan
Verification Plan
● Test cases — what to verify
● Coverage — how to measure completeness
● Tracked in Cadence vManager or spreadsheet
Project Plan
● Implementation of verification environment
● Implementation of test cases and coverage
● Timeline for various regressions and coverage closure
● Tracked on GitLab — issues and milestones
Cadence vManager — vPlan
GitLab Milestone Progress Tracking

## Slide 13
SECTION 1
The Verification Process
Illustrated with FastRICH and MOSAIX ASICs
Strategize
→
Plan
→
Implement
→
Sign-off

## Slide 14
IMPLEMENT
Testbench Architecture — Reuse First, Build What's Unique
Reuse what is already available — don't rebuild testbench components
  Using a standardized methodology, such as UVM enables content reuse across projects through UVM Verification Components (UVCs)
  Several commonly used UVCs are available through CHIPS gitlab project
Focus effort on what is unique to the ASIC — checker, readout protocol decoders, coverage model
FASTRICH TESTBENCH ARCHITECTURE
FastRICHDUT
RTL / TMR / Netlist
clk_gen_uvc
pin_uvc
hits_uvc
i2c_cfg_uvc
control_uvc
checker
aurora_uvc
frame decoder
RAL
see_uvc
tests
Reference: Reusable verification components for High-Energy Physics readout ASICs, M. Lupi et al 2025 JINST 20 C02002

## Slide 15
IMPLEMENT
Verification Activities
Constrained Random Tests
● Random hit timing, occupancy, ToT
● Random commands and command sequences
● Random register access tests
Semi-directed Tests
● ToA scan across full timing range
● Test-pulse & TDC dead-time scan
● Readout efficiency vs. occupancy
Tests are rerun several times with different seeds until a coverage goal is achieved. Hundreds of jobs in parallel on the batch farm.
Continuous Integration
● Smoke regressions on every commit
● Ensures no bugs introduced
● Critical with >2 engineers on a project
Regressions
● RTL regressions
● Netlist regressions
● Sign-off regression suites
Bug Tracking
● GitLab issues for every bug
● Steps to reproduce + debug notes
● Reproducibility is essential

## Slide 16
SECTION 1
The Verification Process
Illustrated with FastRICH and MOSAIX ASICs
Strategize
→
Plan
→
Implement
→
Sign-off

## Slide 17
SIGN-OFF
Sign-off: A Rubber Stamp on a Clean Process
Run all sign-off checks (defined early in the project) on sign-off database
A sign-off report:
  Typically documented in a Gitlab issue
  Steps to reproduce the results
  Waivers and their justification
If the process is followed well, sign-off is the easiest part of the project
Project | Tape-out | Bugs found | Bugs escaped
lpGBT | Q1 2021 | 60 | 1
Altiroc | Q3 2022 | No data | 1
MOSS | Q4 2022 | 76 | 0
ECON-D | Q4 2022 | 373 | 0
ECON-T | Q4 2023 | 75 | 0
RD53 | Q3 2023 | 169 | 1
FastRICH | Q1 2025 | 247 | 0
MOSAIX | Q2 2025 | 592 | 1
PicoPix |  | 434 | 

## Slide 18
SECTION 2
Challenges & Path Forward

## Slide 19
CHALLENGE 1
The Process and Methodology Scales — Human Resources Don't
Coverage Driven Constrained Random Verification (CDCRV) and the other verification practices discussed here scale well for complex HEP ASICs
Challenges:
  Verification expertise is not immediately available
  Onboarding to full productivity takes ~12-18 months (one project cycle)
  Personnel often leave before this investment fully pays off (as observed at CERN)
  Knowledge continuity is fragile, with expertise effectively resetting between personnel generations
CERN's strategy:
  Treat verification as an independent discipline – significant investment in verification personnel and tools over the past 5 years
  Development of a robust verification methodology and process to ensure long-term continuity
Chart: Design (RTL+implementation) and Verification FTE normalized per project
| Q1 2021 | Q3 2022 | Q4 2022 | Q4 2022 | Q4 2023 | Q3 2023 | Q1 2025 | Q2 2025 | Q3 2026 | lpGBT | Altiroc | MOSS | ECON-D | ECON-T | RD53 | FastRICH | MOSAIX | PicoPix
Design | 7.8 | 2.7 | 5 | 7.5 | 11.2 | 31.4 | 3 | 16.7 | 8
Verification | 2.5 | 1.45 | 1 | 4.1 | 5.3 | 16 | 1.5 | 2.5 | 3

## Slide 20
CHALLENGE 2
The EDA Licensing Bottleneck — and a Path Around It
OUVERT — Open-source Universal VERification Technologies
Current verification throughput is gated by EDA license availability, not compute
As GenAI raises engineer throughput, license availability becomes the binding constraint even faster
Capability | Open-source alternative
Simulator | Verilator + Icarus Verilog
Testbench framework | cocotb + AVL (Python)
Regression management | pytest + pytest-xdist
Functional coverage | cocotb-coverage (from AVL)
Fault list generation | Based on yosys
Exploratory project to develop, validate, and document a fully open-source digital verification methodology as a credible alternative to the current methodology
Goal is not to replace the current commercial stack, but to merely explore alternatives which can scale well for most of the verification process
Python lowers the barrier to entry — new contributors reach productive output faster than with UVM SystemVerilog

## Slide 21
THE HONEST BLIND SPOT
Analog and Mixed Signal Verification
Verification process discussed today mainly applies to digital logic
HEP ASICs have complex analog and mixed signal IP blocks – AFEs, PLLs, ADCs, DACs etc.
Many recent bugs found in silicon are in analog blocks
Methodical AMS verification is largely unsolved in HEP
  Calls for another round of strategic investment into this topic to ensure first time silicon success
We have not cracked this!

## Slide 22
SUMMARY
Verification Techniques for Complex ASICs
The Process Works
Strategize → Plan → Execute → Sign-off
Reuse concentrates effort
Well established process assures continuity in verification effort
Challenges
Proficiency takes 12–18 months
EDA licensing wall
AMS verification — unsolved
Path Forward
OUVERT: open-source stack
GenAI improves verification throughput
Promote common verification practices
Invest in AMS verification expertise

## Slide 23
Thank you
Questions?
Adithya Pulli
EP-ESE-ME, CERN
adithya.pulli@cern.ch
ACKNOWLEDGEMENTS
Matteo Lupi · Simone Scarfi
Co-verification engineers on FastRICH, MOSAIX & PicoPix — EP-ESE-ME, CERN

## Slide 24
SECTION 3
Backup

## Slide 25
IMPLEMENT
The FastRICH Checker
CANONICAL CHECKER ARCHITECTURE
FASTRICH CHECKER — APPROXIMATE SCOREBOARD
Stimulus drives both DUT and reference model
Scoreboard compares outputs exactly
Works when output is fully deterministic
Exact prediction infeasible: clock phase uncertainty, metastability, ±1 bin ambiguity
Classify each hit: matched / mismatched / ghost / lost
Handles edge cases: bunch-crossing veto, gate filtering, ToT mismatch
Hits UVC
DUT
Readout UVC
Scoreboard
Reference model
Hits UVC
DUT
Readout UVC
Readout to hits
Hit Classifier (match/mismatch/lost/ghost)
Reference: Challenges and strategies in verification of FastRICH ASIC for the LHCb RICH detector, M. Lupi et al 2026 JINST 21 C03008

## Slide 26
IMPLEMENT
SEE Verification: Simulation & Formal
SIMULATION TRACK
FORMAL TRACK
TMR campaign: two parallel simulations with same seed - compare all DUT output strobes. Mismatch = incorrect triplication
Non-TMR campaign: inject faults in unprotected nodes, check fault-tolerance goals are preserved
Random fault + recovery: random SEE injection across full test; verify chip recovers via soft reset
SVA assertions auto-generated from netlist - one per TMR triplet
Proves exhaustively that voter always outputs majority - no simulation seeds
Catches triplication errors which takes much longer in simulation
Proof times: 90 sec → 36 hrs depending on block complexity
Design
Reference Simulation
Fault Simulation
Strobe comparison
strobe.vcd
strobe.vcd
References:
A simulation methodology for verification of transient fault tolerance of ASICs designed for high-energy physics experiments, A. Pulli and M. Lupi 2023 JINST 18 C01038
SEU injection framework for radiation-tolerant ASICs, a formal veriﬁcation approach, M. Lupi and A. Pulli 2023 JINST 18 C02023