## Slide 1: Smartpixels: In-pixel AI for on-sensor data filtering
Benjamin Parpillon
FEE2026
May 20th 2026

## Slide 2: Agenda
Physics Motivation
Filtering Machine Learning
Front-End Implementation
Test Result
Status And Next Steps

## Slide 3: Physics Motivation
01

## Slide 4: Silicon Pixel Detectors
Experiments at colliders typically have a silicon pixel detector at the center
  Concentric rings tiled with sensors
Silicon sensors are depleted of charge carriers by high voltage
When a charged particle from a collision passes through, it creates e/h pairs
Charge is read out and transferred off-detector
  Charge cluster information is used for physics analysis offline
Silicon Pixel Detector at CMS (LHC, CERN)

## Slide 5: Case Study
> 90% of detector data originates from silicon pixels
Pixel detector data rates continue to scale aggressively
In 2018, CMS saw ~40 simultaneous pp collisions
  The High Luminosity LHC will increase this to ~200
  5 times improved luminosity (radiation)
  7 times higher interaction rate (~3Ghit/cm2)
Technology | 65nm | 28nm
Pixel size | 100x25 | 50x12.5 𝛍m2
Pixels # | 157.6k | 0.63M
Trigger rate | 750KHz | 40MHz
Readout data rate | 1-4 links @ 1.28Gbps | Photonic link @ 30-100 Gbps
Radiation tolerance | 500Mrad | 1Grad
Power density | 1 W /cm2 | 1 W /cm2
CMS Phase-2
Exploratory R&D

## Slide 6: High Level Proposed System
1. Collision
2. Sensor
3. Cluster
4. ML model
5. Decision
AI on chip
No physics value
Physics
value

## Slide 7: Filtering Machine Learning
02

## Slide 8: Clusters Properties
Lorenz drift
https://iopscience.iop.org/article/10.1088/2632-2153/ad6a00
Cluster information across the y-direction can be used to infer the momentum of the track
Predicting pT from cluster morphology is not easily reducible to LUT logic
Global Y-coordinate [mm] *y-direction - along the bending plane of magnetic field
Incident charge particle  deposits cluster of charge in pixel array
B=(3.8,0,0)T
High pT
low pT
-ve charge
low pT
+ve charge

## Slide 9: Filtering Neural Network
+ve charge, pT < 0.2 GeV
-ve charge, pT < 0.2 GeV
pT > 0.2 GeV
∑
16 X-projected cluster values
Sample event display at 4 ns
Quantity of interest: Cluster profile along Y (sum of charge values over pixel rows after 4 ns) Correlated with:
y-position
incident particle’s pT
16 input values
∑
*The cluster shapes are dependent on global y-position of pixel sensors. Separate weights and biases are trained for different y-local regions
Training hyper-parameter
3 output classes
B=(3.8,0,0)T
High pT
low pT
-ve charge
low pT
+ve charge

## Slide 10: First Step: pT Filter at Full Precision
Train fully-connected, feed-forward network
Test selection of input features
  Cluster size (in bending direction) only
  Projected cluster shape, integrated over 4 ns
  Eight temporal “snapshots” of cluster shape in 200 ps intervals, showing evolution of cluster
Key metrics:
  Efficiency (tracks with true pT > 2 GeV correctly identified as high pT)
  Background rejection (tracks with true pT < 2 GeV correctly identified as low pT)
  Data reduction (all tracks classified as low pT)
Model 2 selected as benchmark for compromise between performance and simplicity
*
*
* Produced in 2024 with preliminary dataset

## Slide 11: Digitization And Simulated Performance
Untracked data reduction (single-pixel hits (noise), loopers) estimated between 61to 100%
Bkg. reduction > 20%
Total data reduction estimated between 54 to 75%
  Charge digitalization: 2-bit “flash” ADC
  Weight/activation quantized to 4-bit and 8-bit respectively
https://iopscience.iop.org/article/10.1088/2632-2153/ad6a00

## Slide 12: Training Data: Simulation
Datasets now made available publicly on zenodo! https://zenodo.org/records/17180303
https://zenodo.org/records/18472791
image credits: Danush Shekar
50 x 12.5 mm2 pitch pixels (100 mm thickness)
Dataset extracted for 16x16 pixel array.
Electric field maps of pixel sensor are generated using TCAD simulation.
Field maps are imported into PixelAV
Provide realistic detector response
200ps time slice
Public dataset !
A detailed simulation tool for silicon detectors
Charge deposited in pixel array for an incident particle

## Slide 13: Front-End Implementation
03

## Slide 14: Front-End Pixel Architecture: Synchronous ADC
25µm × 25µm pixel sizes
<1W/cm2 Power density
CSA architecture inspired by FCP130 (not Krummenacher)
AC coupled 40MSPS in-pixel 2-bit flash ADC
  Auto-Zero (AZ) in every pixel for threshold correction
  Insensitive to pile-up
  2 architectures tested
Global charge injection site with programmable capacitive array
No sensor bonded to this prototype
Comparison study here
Detail design here

## Slide 15: Implementable Network
Key Take-Away:
Reprogrammable Network
  Region specific training
  Improve resilience against faulty pixels
  Retrain after radiation damage
Classifier fully combinatorial
  Power proportional to hit density

## Slide 16: First Smartpixels Tapeout With Network

## Slide 17: Test Result
04

## Slide 18: First Prototype
1.5mm2 die – tsmc28
Pixel Analog Front End Prototype v1 with digital ML Filter
two16x16 (sensor side) superpixel variants
Mixed signal implementation but still analog on top

## Slide 19: ASIC Test Stand
Lightweight test stand duplicated at 3 universities
Pixel interface with DAQ and FPGA validated
Three comparators implement 2-bit flash ADC
Per-pixel S-curves extracted across matrix
Threshold and ENC characterization
Scurve on 3 bit
https://arxiv.org/abs/2510.07485

## Slide 20: Threshold Dispersion Characterization
Threshold Dispersion
Measured charge dispersion and ENC larger than expected from simulation
Total charge dispersion
Observed significantly larger spatial variation than expected from intrinsic front-end mismatch alone
QTH = 77.5 e-
ENC = ~55 e-
Threshold heat map
768 bits
Room Temp

## Slide 21: Characterization Non-Idealities Identified
Threshold dispersion QTH across pixels
Threshold Dispersion
Global injection network effect
  Distributed RC degradation on global injection grid
  Spatially varying injected charge amplitude
  Artificial shift in extracted thresholds
Threshold heat map
Global Injection connected to 512 pixels
QTH = 77.5 e-
ENC = ~55 e-

## Slide 22: Characterization Non-Idealities Identified
Threshold dispersion QTH across pixels
Threshold Dispersion
Global injection network effect
  Distributed RC degradation on global injection grid
  Spatially varying injected charge amplitude
  Artificial shift in extracted thresholds
Threshold-bias sensitivity
  Shared VTH bias grid affected by high leakage (>uA)
  Leakage creates systematic offsets across both matrices
Spatial pattern likely reflects combined injection + bias-grid effects
Effect dominated by characterization infrastructure
Fix implemented in future ASIC iteration
QTH = 77.5 e-
ENC = ~55 e-
Threshold heat map
Key question:
How much do these front-end non-idealities affect ML inference?

## Slide 23: Measured Classification Performance
Comparison of software, quantized, and measured ASIC inference
On-chip classifier evaluated using measured front-end response
Region-specific weights trained for y-local range [0.0, 1.35) mm
 | Sig. efficiency | Bkg rejection
Full precision model | ~92 | 42
Quantized model | ~92 | 40
160K event
Key metrics:
  Signal Efficiency (tracks with true pT > 2 GeV correctly identified as high pT)
  Bkg rejection (tracks with true pT < 2 GeV correctly identified as low pT)

## Slide 24: Measured Classification Performance
Comparison of software, quantized, and measured ASIC inference
On-chip classifier evaluated using measured front-end response
Region-specific weights trained for y-local range [0.0, 1.35) mm
2% loss of performance with threshold set at 10
 | Sig. efficiency | Bkg rejection
Full precision model | ~92 | 43
Quantized model | ~92 | 38
ASIC @1000e- | ~90 | 36
160K event

## Slide 25: Measured Classification Performance
Comparison of software, quantized, and measured ASIC inference
On-chip classifier evaluated using measured front-end response
Region-specific weights trained for y-local range [0.0, 1.35) mm
10% loss of performance with threshold set at 7
23% loss of performance with threshold set at 7
Noise level directly impact the signal efficiency
 | Sig. efficiency | Bkg rejection
Full precision model | ~94 | 42
Quantized model | ~94 | 40
ASIC @ 700e- | ~84 | 44
ASIC @ 400e- | ~71 | 33
160K event

## Slide 26: Promises On Noise Retraining
The model was re-trained with noise-injected simulation data
Retraining with realistic noise recovers substantial efficiency
Same Hardware, updated weights and biases
Flow is complex and mostly manual pipeline is a work in progress
Training Model In ASIC @1000e- | Sig. efficiency | bkg rejection
signal | 78.91 % | 45.42 %
signal & noise | 87.64 % | 45.33 %
smartpixel CPAD 2025

## Slide 27: Performance at Room Temperature
Specification | Target | Measured | Units
Analog power | < 5 | 3.1 | uW/pixel
Digital power | 300 | 243 | uW
Power density | <1 | 0.65 | W/cm2
ENC rms (no sensor) | 40 | 55 2 30 to 70 | e-
Threshold dispersion QTH | < 40 | 70 1,2 | e-
Total Charge Dispersion | <60 | 95 1,2 | e-
Signal efficiency | > 90 | 71 to 90 | %
Background rejection Low pT from tracked dataset | >20 | 39 | %
Data reduction All low pT event | > 50 |  | %
Specification | Target | Measured | Units
Analog power | < 5 | 3.1 | uW/pixel
Digital power | 300 | 243 | uW
Power density | <1 | 0.65 | W/cm2
ENC rms (no sensor) | 40 | 55 2 30 to 70 | e-
Threshold dispersion QTH | < 40 | 70 1,2 | e-
 | <60 | 95 1,2 | e-
Signal efficiency | > 90 | 71 to 90 | %
Background rejection Low pT from tracked dataset | >20 | 39 | %
Data reduction All low pT event | > 50 |  | %
Leakage on bias grid
Global Charge injection

## Slide 28: Incoming Test: Radiation Damage Correction
HL-LHC will reach unprecedented radiation levels, highest in barrel pixel layer 1, 3 cm from collisions
Generate datasets with simulated radiation damage (models from PixelAV)
  3.3 x 1015 neq/cm2 (370 fb-1 (Run 3) at Layer 1)
  1.0 x 1016 neq/cm2 (1100 fb-1 (half of HL-LHC) at Layer 1)
Retraining (new weights, same structure) recovers most performance for both benchmark and HL-LHC sensor geometry, and will be possible for an eventual detector
Next step: leverage leakage current injection to mimic effect of radiation and retrain the ASIC to recover performance
https://arxiv.org/abs/2510.06588
Under review NIM-A

## Slide 29: Status And Next Steps
05

## Slide 30: Future Dataset Productions
30
Current filtering network is mostly time-agnostic
Regression and neuromorphic ML need accurate timing modeling
We are upgrading our dataset flow
  CSA model ready and predicts rise time and saturation behavior correctly
  ADC and spike generation timing modeling is a work in progress
  ENC noise injection is next to train our ML with realistic ASIC conditions
New
In progress
Envisioned dataset production flow

## Slide 31: VIZARD 2026
Overview
Two 30mm2 chips
VIZARD_v0a - backside sensor connection (TSVs)
VIZARD_v0b – frontside sensor connection (Bump bond)
Improved and novel AFE architecture
Zero suppress readout on three 192x48 pixel matrices quadrant
Implementation of 36 digital filter ML (NW quadrant)
SPI interface for configuration and slow readout
High Speed RX/TX interface (1.28Gbps)
    Status
    Tapeout: End 2026
    Engineer run with CERN
    Chip delivery: Early 2027

## Slide 32: 3D chip tapeout
3D integration planned in January 2027
8 chiplets design dedicated for smartpixels
    Improved and novel AFE architecture
    Smarter digital auto zero cycle control
    Explore novel Filter ML architectures (race logic, SNN)
    Regression algorithms for real-time physics feature extraction
    Fabrication and test planned for 2027-2028
3D detector product
https://arxiv.org/abs/2602.15946

## Slide 33: Codesign Flow
Dataset production accelerated dramatically
Silicon Realistic Dataset including AFE timing and noise modeling
ML-to-ASIC flow improved Reduced HLS4M
  Tight integration of HLS4ML with siemens catapult
  We produced with siemens a more automatized flow that works for ASIC
Hardware iteration remains the bottleneck
1 week
weeks
A chip result is worth a thousand simulations

## Slide 34: The Smartpixels Team
Fermi National Accelerator Laboratory: Abhijith Gandrakota, Benjamin Parpillon, Chinar Syal, Douglas Berry, Farah Fahim, Gauri Pradhan, Giuseppe Di Guglielmo, James Hirschauer, Jennet Dickinson, Lindsey Gray, Nhan Tran, Ron Lipton
Cornell University: Jennet Dickinson, Ben Weiss
Johns Hopkins University: Dahai Wen, Morris Swartz, Petar Maksimovic
Northeastern University: Nick Manganelli
Northwestern University: Manuel Blanco Valentin
Oak Ridge National Laboratory: Aaron Young, Shruti R. Kulkarni
Purdue University: Mia Liu, Arghya Das
University of Chicago: Karri DiPetrillo, Anthony Badea, Carissa Kumar, Emily Pan, Rachel Kovach-Fuentes, Aidan Nicholas, Eliza Howard, Eric You
University of Colorado Boulder: Jannicke Pearkes, Ricardo Silvestre
University of Illinois Chicago: Corrinne Mills, Danush Shekar, Jieun Yoo, Mohammad Abrar Wadud
University of Illinois Urbana-Champaign: Mark S. Neubauer, David Jiang
University of Kansas: Alice Bean

## Slide 35: Backup
06

## Slide 36: Smartpixel In The Trigger

## Slide 37: Filtering neural network: performance metrics

## Slide 38: Data reduction
Dataset breakdown seen in the detector
https://arxiv.org/abs/2310.02474

## Slide 39: CSA schematic
ENC + MC
Csensor = 30fF
ENC simulation with 30fF sensor capacitor

## Slide 40: Comparator Schematic and AZ Modes
ENC + MC
Csensor = 30fF

## Slide 41: Future Dataset productions
41
Cadence plot
CSA model
pixelAV dataset
Ideal integration (used in Filter ML)

## Slide 42: CNN approach - Feature Regression Network
Treat the charge deposited in the pixel array as 2D image
Convolutional layers are powerful for image processing
  Each 200 ps time slice is treated as a channel
Predict and read out the traversing particle’s hit position (x, y) and incidence angle (cot ɑ)
https://arxiv.org/abs/2602.15946

## Slide 43: Test Setup Flow