## Slide 1: MightyPix: A HV-CMOS Pixel Chip for LHCb’s Mighty Tracker
Nicolas Striebig, Richard Leys, Lucas Dittmann, Toko Hirono
Ivan Peric*

## Slide 2: LHCb Experiment
LHCb Experiment
Forward-arm spectrometer at the LHC
Precision flavour physics:
  CP violation
  beauty and charm decays
  hadron spectroscopy
  rare decays
~9 fb⁻¹ recorded in Run 1 and Run 2
IP
Tracking Stations
Schematic side view of the Upgrade II LHCb detector. [1]
Notes: The LHCb experiment is a forward-arm spectrometer at CERN designed for precision flavour physics.
Its physics program includes studies of CP violation, beauty and charm decays, hadron spectroscopy, and rare decays that are sensitive to physics beyond the Standard Model.
During Run 1 and Run 2, LHCb recorded approximately 9 inverse femtobarns of data.
Yes, the inverse femtobarn (\(fb^{-1}\)) is a standard unit used in particle physics to measure integrated luminosity. [1, 2]
Here is a breakdown of what that means:
What it Measures: It represents the total amount of data collected by a particle accelerator (like the LHC) over a specific period, essentially measuring the potential number of collisions.
The "Barn": A "barn" (\(b\)) is a unit of area, used in nuclear and particle physics to express the cross-section (the likelihood) of a particle interaction. It is equal to \(10^{-28}\) square meters or 100 square femtometers (\(\text{fm}^{2}\)).
Femtobarn (\(fb\)): A femtobarn is \(10^{-15}\) barns.
Inverse Femtobarn (\(fb^{-1}\)): Because luminosity is defined as collisions per unit area per unit time, integrating this over time creates a unit of "inverse area." One inverse femtobarn (\(1\text{ fb}^{-1}\)) corresponds to roughly 100 million million (\(10^{14}\)) proton-proton collisions. [1, 2, 3, 4, 5]
Why it matters: If a specific particle process (like Higgs boson production) has a cross-section of \(1\text{ fb}\), then a detector that has accumulated an integrated luminosity of \(100\text{ fb}^{-1}\) would expect to record roughly 100 of those events

## Slide 3: Upgrade
LHCb Upgrade II
Higher luminosity operation
Increased:
  radiation dose
  particle multiplicities
  hit rates
Upgrade of downstream tracker:
  Mighty Tracker
Schematic of one layer of the Mighty Tracker. [1]
SciFi
MT
IT
~ 4 m
1 m
Notes: The main challenges of Upgrade II are significantly higher radiation levels, increased particle multiplicities, and much higher hit rates.
To cope with the operating conditions of Upgrade II, the LHCb detector requires substantial upgrades.
The upgrade of the downstream tracking detector is called the Mighty Tracker.

## Slide 4: Mighty Tracker Concept
Mighty Tracker
Hybrid tracking detector:
SciFi Tracker
Inner Tracker
Middle Tracker
Technology:
Scintillating fibres + HV-MAPS
Advantages:
High granularity
Fast timing
Radiation hardness
Schematic of one layer of the Mighty Tracker. [1]
SciFi
MT
IT
~ 4 m
1 m
Notes: The Mighty Tracker is a hybrid detector concept combining scintillating fibre technology with HV-MAPS pixel sensors.
The detector consists of the SciFi tracker together with the Inner and Middle Tracker regions instrumented with pixel sensors.
This hybrid solution provides a good balance between cost and detector performance, while delivering high granularity, excellent timing resolution, and strong radiation hardness.

## Slide 5: MightyPix Detector Scale
MightyPix Detector Scale
Baseline technology:
  HV-CMOS pixel chip MightyPix
46,000 silicon sensors
Total silicon area:
  ~18 m²
Schematic of one layer of the Mighty Tracker. [1]
SciFi
MT
IT
~ 4 m
1 m
Notes: The baseline for the pixel region is the HV-CMOS chip called MightyPix.
In total, more than 46 thousand silicon sensors are required to instrument an active area of approximately 18 square meters.

## Slide 6: Module Structure
Module structure:
28 modules/layer, 6 layers
Module size: 20 cm × 54 cm
Mighty Tracker Module
HV-MAPS mounted on both sides
Cooling pipes integrated into support structure
Continuous active coverage
Notes: Each of 6 tracking layer is divided into 28 modules, where each module covers an area of 20 by 54 centimeters. (252 chips)
This slide shows the top view and cross section of one detector module.
The blue regions correspond to the silicon sensors.
The HV-MAPS chips are mounted on both sides of the mechanical support structure, while cooling pipes are integrated inside the module.
This arrangement provides continuous active coverage over the entire module area.

## Slide 7: MightyPix Requirements
MightyPix Requirements
Pixel size:
  < 100 µm × 300 µm
Hit-rate capability:
  30 MHz/cm²
In-time efficiency:
  99% in 25 ns
Radiation hardness:
  6 × 10¹⁴ neq/cm²
Power:
  < 150 mW/cm²
4 × 1.28 Gbps data links
Notes: The requirements for MightyPix are quite demanding.
The chip must support hit rates above 30 megahits per square centimeter while maintaining an in-time efficiency above 99 percent within the 25 nanosecond bunch crossing interval.
In addition, the detector must tolerate high radiation levels and remain power efficient.
The chip also needs to integrate fully into the LHCb readout system and provide four high-speed data links operating at 1.28 gigabits per second.

## Slide 8: Development
MightyPix Development
MightyPix1
  first prototype
MightyPix2
  near-full functionality
MightyPix3
  final prototype
Parallel development:
LF-MightyPix
  150 nm CMOS backup technology
MightyPix1
MightyPix2
LFMightyPix
Notes: Our development follows a stepwise prototype strategy.
We started with MightyPix1 as the first prototype, followed by MightyPix2, which integrates almost the complete functionality planned for the final chip.
MightyPix3 will serve as the final pre-production prototype.
In parallel, we developed LF-MightyPix in a 150 nanometer CMOS technology as a backup option and to reduce long-term technology risks.

## Slide 9: MightyPix Chip Architecture
Config. register
MightyPix Chip Architecture
122 double columns
2 × 194 pixels per double column
Chip periphery includes:
Hit buffers
End-of-Column (EoC) circuits
Readout Control Unit (RCU)
DACs
I/O pads
pads
regulator
RCU
DAC
VDAC
EOC
EOC
EOC
EOC
EOC
Notes: MightyPix consists of 122 double columns, where each double column contains two rows of 194 pixels.
The central part of the chip is occupied by the pixel matrix, while the chip periphery contains the supporting readout and control circuitry.
This includes the hit buffers, the End-of-Column circuits, the Readout Control Unit, DACs for bias and threshold generation, as well as the interface and I/O pads.

## Slide 10: MightyPix: Analogue Part
Working principle:
1. Charge collected by pixel n-well
2. Converted to voltage signal by Charge Sensitive Amplifier
3. Analog voltage pulse shaped and converted to digital signal by comparator
4. Hit information stored in hit buffer
Source: Ivan Perić
Amplifier
Sensor
Comparator
Th
BL
TDAC
Injection
EnInjection_row_i
RAM
Q(0:2)
3
RAM in
WrRAM(0:2)_row_i
Cinj
Bias resistance
Tout
Data transfer line
column control(in pixel control reg)
-HV
1.8V
Hit buffer
Pixel
Offset
AnalogOut
row control (in pixel control reg)
VMinus
Injection
AmpOut
Notes: Each pixel integrates the complete front-end chain, including the sensor diode,

## Slide 11: MightyPix: Analogue Part
Working principle:
1. Charge collected by pixel n-well
2. Converted to voltage signal by Charge Sensitive Amplifier
3. Analog voltage pulse shaped and converted to digital signal by comparator
4. Hit information stored in hit buffer
Source: Ivan Perić
Amplifier
Sensor
Comparator
Th
BL
TDAC
Injection
EnInjection_row_i
RAM
Q(0:2)
3
RAM in
WrRAM(0:2)_row_i
Cinj
Bias resistance
Tout
Data transfer line
column control(in pixel control reg)
-HV
1.8V
Hit buffer
Pixel
Offset
AnalogOut
row control (in pixel control reg)
VMinus
Injection
AmpOut
Notes: a charge sensitive amplifier,

## Slide 12: MightyPix: Analogue Part
Working principle:
1. Charge collected by pixel n-well
2. Converted to voltage signal by Charge Sensitive Amplifier
3. Analog voltage pulse shaped and converted to digital signal by comparator
4. Hit information stored in hit buffer
Source: Ivan Perić
Amplifier
Sensor
Comparator
Th
BL
TDAC
Injection
EnInjection_row_i
RAM
Q(0:2)
3
RAM in
WrRAM(0:2)_row_i
Cinj
Bias resistance
Tout
Data transfer line
column control(in pixel control reg)
-HV
1.8V
Hit buffer
Pixel
Offset
AnalogOut
row control (in pixel control reg)
VMinus
Injection
AmpOut
Notes: a comparator, a threshold tuning DAC, and local RAM used for storing the tuning bits

## Slide 13: MightyPix: Analogue Part
Working principle:
1. Charge collected by pixel n-well
2. Converted to voltage signal by Charge Sensitive Amplifier
3. Analog voltage pulse shaped and converted to digital signal by comparator
4. Hit information stored in hit buffer
Source: Ivan Perić
Amplifier
Sensor
Comparator
Th
BL
TDAC
Injection
EnInjection_row_i
RAM
Q(0:2)
3
RAM in
WrRAM(0:2)_row_i
Cinj
Bias resistance
Tout
Data transfer line
column control(in pixel control reg)
-HV
1.8V
Hit buffer
Pixel
Offset
AnalogOut
row control (in pixel control reg)
VMinus
Injection
AmpOut

## Slide 14: Sensor
Deep n-well in high-resistivity substrate
Reverse bias up to ~260 V
Depletion depth:
  ~90 µm
Charge collection by drift
p-type substrate
Deep n-well
n-well
p-well
n-well
p-well
Vbias
260V
Notes: The sensing element is a pn diode formed by a deep n-well implanted in a high-resistivity substrate.
The diode is reverse biased up to approximately 260 volts, creating a depletion region of about 90 micrometers.
Charge generated by incident particles is collected by drift toward the deep n-well.

## Slide 15: Sensor Biasing
Sensor Biasing
Deep n-well biased through high-ohmic device
Maintains correct DC potential
Avoids low-impedance path for signal charge
p-type substrate
Deep n-well
n-well
p-well
n-well
p-well
n-well
p-well
PMOS transistor
NMOS transistor
Deep n-well
Vbias
260V
Notes: To avoid signal loss, we bias the deep n-well through a high-ohmic device.
This resistor keeps the deep n-well at the correct DC potential while avoiding a low-impedance path that could drain away the collected signal charge.
1. Electronics Placement in the N-Well
In our HVCMOS sensors, the readout electronics are integrated within the n-well, a shallow n-doped region implanted in a p-type substrate that forms the signal-collecting diode. This design choice has significant implications for the sensor’s operation and electrical isolation.
Potential Requirements: To prevent forward-biased junctions, the potential of the n-well must be maintained higher or at lease not lower than the potential of any p+ diffusion – 100mV (e.g., p-type regions forming transistor source/drain). Forward-biased junctions would lead to unwanted current flow, degrading sensor performance.
  Our Structure: The n-well potential is set to approximately 1.7-1.8 V, ensuring isolation from p+ diffusions
Isolation: Placing electronics in the n-well isolates them from the p-type substrate, allowing high bias voltages without damaging the circuitry. Signal Collection: The n-well serves as both the sensor diode and the housing for electronics, enabling monolithic integration and fast charge collection. Design Constraint: Careful potential management is required to maintain the n-well at a higher voltage than surrounding p+ regions, necessitating precise biasing circuits.
Our HVCMOS sensor employs an AC-coupled connection between the sensor diode and the charge-sensitive amplifier (CSA), which amplifies the current pulse induced by particle interactions.
Purpose: AC coupling isolates the high DC bias voltage of the n-well (~1.8 V plus the high bias voltage) from the amplifier’s input, protecting the CSA and allowing independent biasing of the sensor and electronics.
The CSA in our HVCMOS sensor uses a folded cascode topology, a common choice for high-performance analog circuits.
Description: The folded cascode is a single-stage amplifier with a cascode transistor configuration that “folds” the current path to improve gain and bandwidth.
Key Features:
  High Gain: The topology provides high open-loop gain (A), essential for achieving a closed-loop gain close to 1/(𝑠𝐶_𝑓 ) (as discussed in prior CSA lectures).
  Compact Design: Suitable for in-pixel integration within the n-well, balancing performance with area constraints.
he CSA’s feedback network is critical for signal integration and noise performance. In our design, both the feedback capacitance and feedback resistance are implemented with specific techniques to optimize performance.
Feedback Capacitance (Cf):
  Implementation: Cf is realized using the parasitic drain diffusion capacitance of a MOSFET. This leverages the inherent capacitance of the transistor’s drain region, reducing the need for additional components and saving area.
Implications: Compact design suitable for in-pixel integration.
The capacitance value is process-dependent, requiring careful calibration to ensure consistent gain
  𝑉_"out" =𝑄/𝐶_𝑓
Implementation: Rf
Rf​ is implemented as a MOSFET operating in the active-biased region, as detailed in the IEEE JSSC paper
Advantages: Tunable resistance via bias adjustment, allowing optimization of the feedback time constant
𝑇_𝑓=𝑅_𝑓⋅𝐶_𝑓,
Compact integration within the pixel, avoiding large physical resistors.
The bias resistance for the n-well sensor diode is also implemented with a specific technique to ensure proper operation.
Implementation: The bias resistance is realized as a MOSFET in the active-biased region, as described in the IEEE JSSC paper. Operation: The MOSFET provides a high-impedance path to set the n-well’s DC bias voltage (~1.8 V plus high voltage), while allowing the AC signal to be coupled to the CSA.

## Slide 16: Sensor Biasing
Bias device implementation:
Operation:
T2 provides bias resistance
T1 carries leakage current
Notes: The bias device is realized by a MOSFET.
Circuit maintains a nearly constant small-signal AC resistance even in the presence of sensor leakage current.
In this implementation, transistor T2 provides the effective bias resistance, while transistor T1 carries the leakage current component.
1. Electronics Placement in the N-Well
In our HVCMOS sensors, the readout electronics are integrated within the n-well, a shallow n-doped region implanted in a p-type substrate that forms the signal-collecting diode. This design choice has significant implications for the sensor’s operation and electrical isolation.
Potential Requirements: To prevent forward-biased junctions, the potential of the n-well must be maintained higher or at lease not lower than the potential of any p+ diffusion – 100mV (e.g., p-type regions forming transistor source/drain). Forward-biased junctions would lead to unwanted current flow, degrading sensor performance.
  Our Structure: The n-well potential is set to approximately 1.7-1.8 V, ensuring isolation from p+ diffusions
Isolation: Placing electronics in the n-well isolates them from the p-type substrate, allowing high bias voltages without damaging the circuitry. Signal Collection: The n-well serves as both the sensor diode and the housing for electronics, enabling monolithic integration and fast charge collection. Design Constraint: Careful potential management is required to maintain the n-well at a higher voltage than surrounding p+ regions, necessitating precise biasing circuits.
Our HVCMOS sensor employs an AC-coupled connection between the sensor diode and the charge-sensitive amplifier (CSA), which amplifies the current pulse induced by particle interactions.
Purpose: AC coupling isolates the high DC bias voltage of the n-well (~1.8 V plus the high bias voltage) from the amplifier’s input, protecting the CSA and allowing independent biasing of the sensor and electronics.
The CSA in our HVCMOS sensor uses a folded cascode topology, a common choice for high-performance analog circuits.
Description: The folded cascode is a single-stage amplifier with a cascode transistor configuration that “folds” the current path to improve gain and bandwidth.
Key Features:
  High Gain: The topology provides high open-loop gain (A), essential for achieving a closed-loop gain close to 1/(𝑠𝐶_𝑓 ) (as discussed in prior CSA lectures).
  Compact Design: Suitable for in-pixel integration within the n-well, balancing performance with area constraints.
he CSA’s feedback network is critical for signal integration and noise performance. In our design, both the feedback capacitance and feedback resistance are implemented with specific techniques to optimize performance.
Feedback Capacitance (Cf):
  Implementation: Cf is realized using the parasitic drain diffusion capacitance of a MOSFET. This leverages the inherent capacitance of the transistor’s drain region, reducing the need for additional components and saving area.
Implications: Compact design suitable for in-pixel integration.
The capacitance value is process-dependent, requiring careful calibration to ensure consistent gain
  𝑉_"out" =𝑄/𝐶_𝑓
Implementation: Rf
Rf​ is implemented as a MOSFET operating in the active-biased region, as detailed in the IEEE JSSC paper
Advantages: Tunable resistance via bias adjustment, allowing optimization of the feedback time constant
𝑇_𝑓=𝑅_𝑓⋅𝐶_𝑓,
Compact integration within the pixel, avoiding large physical resistors.
The bias resistance for the n-well sensor diode is also implemented with a specific technique to ensure proper operation.
Implementation: The bias resistance is realized as a MOSFET in the active-biased region, as described in the IEEE JSSC paper. Operation: The MOSFET provides a high-impedance path to set the n-well’s DC bias voltage (~1.8 V plus high voltage), while allowing the AC signal to be coupled to the CSA.

## Slide 17: Charge Sensitive Amplifier
Charge Sensitive Amplifier
Cascode amplifier architecture
Combined:
  NFET input
  PFET input
Enhanced transconductance:
  gm = gm,NMOS + gm,PMOS
outamp
Tload
VDD
VSS
Vpload
Tcasc
Tinn
Tinp
in
Vcasc
Vp
Vsf
Tscsf
Tscp
Tsf
outampsf
Notes: The CSA uses a cascode architecture with both NFET and PFET input transistors in order to increase the effective transconductance.
Effectively, the transconductances of both devices are added, improving speed and timing performance.

## Slide 18: Charge Sensitive Amplifier
CSA Operating Principle
NMOS gate controlled by DC feedback
Current source defines bias current
PMOS and NMOS share same current
VSS node:
  large capacitance
  AC ground behavior
AC currents add constructively
Increased effective gm
outamp
Tload
VDD
VSS
Vpload
Tcasc
Tinn
Tinp
in
Vcasc
Vp
Vsf
Tscsf
Tscp
Tsf
outampsf
Other pixel amplifiers
Notes: The gate-source voltage of the NMOS transistor is controlled by the DC feedback loop, while the current source defines the bias current.
The PMOS input transistor is connected in series with the NMOS device, meaning that both transistors share the same bias current.
The source of PMOS is common to all pixels and has a large capacitance. Therefore, for AC signals, this node behaves approximately as an AC ground.
As a result, the AC currents of the NMOS and PMOS transistors add, so the amplifier behaves like two parallel transistors with combined transconductance.
To improve bandwidth and reduce the amplifier time constant, we use a source follower stage.
The entire analog front-end is optimized for low timing jitter at the discriminator threshold crossing.

## Slide 19: Feedback Capacitance (Cf)
Feedback Capacitance (Cf) Realized using parasitic drain diffusion capacitance of a MOSFET
n-well
Tin
Deep n-well
VDD
VDD
Tload
outamp
in
nwell
Cf
nwell
outamp
Tload
VDD
VSS
Vpload
Tcasc
Tinn
Tinp
in
Cf
Rf
nwell
Vcasc
Vp
Vsf
Tscsf
Tscp
Tsf
outampsf
Notes: Feedback Capacitance (Cf):
  Cf is realized using the parasitic drain diffusion capacitance of a MOSFET.
1. Electronics Placement in the N-Well
In our HVCMOS sensors, the readout electronics are integrated within the n-well, a shallow n-doped region implanted in a p-type substrate that forms the signal-collecting diode. This design choice has significant implications for the sensor’s operation and electrical isolation.
Potential Requirements: To prevent forward-biased junctions, the potential of the n-well must be maintained higher or at lease not lower than the potential of any p+ diffusion – 100mV (e.g., p-type regions forming transistor source/drain). Forward-biased junctions would lead to unwanted current flow, degrading sensor performance.
  Our Structure: The n-well potential is set to approximately 1.7-1.8 V, ensuring isolation from p+ diffusions
Isolation: Placing electronics in the n-well isolates them from the p-type substrate, allowing high bias voltages without damaging the circuitry. Signal Collection: The n-well serves as both the sensor diode and the housing for electronics, enabling monolithic integration and fast charge collection. Design Constraint: Careful potential management is required to maintain the n-well at a higher voltage than surrounding p+ regions, necessitating precise biasing circuits.
Our HVCMOS sensor employs an AC-coupled connection between the sensor diode and the charge-sensitive amplifier (CSA), which amplifies the current pulse induced by particle interactions.
Purpose: AC coupling isolates the high DC bias voltage of the n-well (~1.8 V plus the high bias voltage) from the amplifier’s input, protecting the CSA and allowing independent biasing of the sensor and electronics.
The CSA in our HVCMOS sensor uses a folded cascode topology, a common choice for high-performance analog circuits.
Description: The folded cascode is a single-stage amplifier with a cascode transistor configuration that “folds” the current path to improve gain and bandwidth.
Key Features:
  High Gain: The topology provides high open-loop gain (A), essential for achieving a closed-loop gain close to 1/(𝑠𝐶_𝑓 ) (as discussed in prior CSA lectures).
  Compact Design: Suitable for in-pixel integration within the n-well, balancing performance with area constraints.
he CSA’s feedback network is critical for signal integration and noise performance. In our design, both the feedback capacitance and feedback resistance are implemented with specific techniques to optimize performance.
Feedback Capacitance (Cf):
  Implementation: Cf is realized using the parasitic drain diffusion capacitance of a MOSFET. This leverages the inherent capacitance of the transistor’s drain region, reducing the need for additional components and saving area.
Implications: Compact design suitable for in-pixel integration.
The capacitance value is process-dependent, requiring careful calibration to ensure consistent gain
  𝑉_"out" =𝑄/𝐶_𝑓
Implementation: Rf
Rf​ is implemented as a MOSFET operating in the active-biased region, as detailed in the IEEE JSSC paper
Advantages: Tunable resistance via bias adjustment, allowing optimization of the feedback time constant
𝑇_𝑓=𝑅_𝑓⋅𝐶_𝑓,
Compact integration within the pixel, avoiding large physical resistors.
The bias resistance for the n-well sensor diode is also implemented with a specific technique to ensure proper operation.
Implementation: The bias resistance is realized as a MOSFET in the active-biased region, as described in the IEEE JSSC paper. Operation: The MOSFET provides a high-impedance path to set the n-well’s DC bias voltage (~1.8 V plus high voltage), while allowing the AC signal to be coupled to the CSA.

## Slide 20: Feedback Resistor Implementation
Feedback Resistor Implementation
Feedback resistor Rf implemented using MOSFET
Simple implementation:
Common gate bias generated off-matrix
Tfb
Cf
nwell
outamp
Tload
VDD
VSS
Vpload
Tcasc
Tinn
Tinp
in
nwell
Vcasc
Vp
Vsf
Tscsf
Tscp
Tsf
outampsf
Notes: The feedback resistor Rf​ is implemented using a MOSFET
In the simplest implementation, the gate voltage controlling the feedback transistor, labeled Tfb, is generated outside the pixel matrix and distributed globally to all pixels.
However, in this configuration the conductivity of the feedback transistor depends strongly on the local VDD value.
Since the power rails carry substantial current, the local VDD voltage can vary significantly across the matrix.
These voltage variations can therefore affect the effective feedback resistance and influence the analog front-end behavior.
1. Electronics Placement in the N-Well
In our HVCMOS sensors, the readout electronics are integrated within the n-well, a shallow n-doped region implanted in a p-type substrate that forms the signal-collecting diode. This design choice has significant implications for the sensor’s operation and electrical isolation.
Potential Requirements: To prevent forward-biased junctions, the potential of the n-well must be maintained higher or at lease not lower than the potential of any p+ diffusion – 100mV (e.g., p-type regions forming transistor source/drain). Forward-biased junctions would lead to unwanted current flow, degrading sensor performance.
  Our Structure: The n-well potential is set to approximately 1.7-1.8 V, ensuring isolation from p+ diffusions
Isolation: Placing electronics in the n-well isolates them from the p-type substrate, allowing high bias voltages without damaging the circuitry. Signal Collection: The n-well serves as both the sensor diode and the housing for electronics, enabling monolithic integration and fast charge collection. Design Constraint: Careful potential management is required to maintain the n-well at a higher voltage than surrounding p+ regions, necessitating precise biasing circuits.
Our HVCMOS sensor employs an AC-coupled connection between the sensor diode and the charge-sensitive amplifier (CSA), which amplifies the current pulse induced by particle interactions.
Purpose: AC coupling isolates the high DC bias voltage of the n-well (~1.8 V plus the high bias voltage) from the amplifier’s input, protecting the CSA and allowing independent biasing of the sensor and electronics.
The CSA in our HVCMOS sensor uses a folded cascode topology, a common choice for high-performance analog circuits.
Description: The folded cascode is a single-stage amplifier with a cascode transistor configuration that “folds” the current path to improve gain and bandwidth.
Key Features:
  High Gain: The topology provides high open-loop gain (A), essential for achieving a closed-loop gain close to 1/(𝑠𝐶_𝑓 ) (as discussed in prior CSA lectures).
  Compact Design: Suitable for in-pixel integration within the n-well, balancing performance with area constraints.
he CSA’s feedback network is critical for signal integration and noise performance. In our design, both the feedback capacitance and feedback resistance are implemented with specific techniques to optimize performance.
Feedback Capacitance (Cf):
  Implementation: Cf is realized using the parasitic drain diffusion capacitance of a MOSFET. This leverages the inherent capacitance of the transistor’s drain region, reducing the need for additional components and saving area.
Implications: Compact design suitable for in-pixel integration.
The capacitance value is process-dependent, requiring careful calibration to ensure consistent gain
  𝑉_"out" =𝑄/𝐶_𝑓
Implementation: Rf
Rf​ is implemented as a MOSFET operating in the active-biased region, as detailed in the IEEE JSSC paper
Advantages: Tunable resistance via bias adjustment, allowing optimization of the feedback time constant
𝑇_𝑓=𝑅_𝑓⋅𝐶_𝑓,
Compact integration within the pixel, avoiding large physical resistors.
The bias resistance for the n-well sensor diode is also implemented with a specific technique to ensure proper operation.
Implementation: The bias resistance is realized as a MOSFET in the active-biased region, as described in the IEEE JSSC paper. Operation: The MOSFET provides a high-impedance path to set the n-well’s DC bias voltage (~1.8 V plus high voltage), while allowing the AC signal to be coupled to the CSA.

## Slide 21: Feedback Resistor Implementation
Improved Feedback Biasing
Local bias-current generation using Tbias
Tbias generates small current:
  ~100 pA
Current generates gate voltage for Tfb
PFB generated off-matrix by bias DAC
VDDFB
PFB
Tfb
Tbias
Cf
nwell
outamp
Tload
VDD
VSS
Vpload
Tcasc
Tinn
Tinp
in
nwell
Vcasc
Vp
Vsf
Tscsf
Tscp
Tsf
outampsf
Notes: The solution shown here avoids the dependence of the feedback resistance on local VDD variations.
A dedicated transistor, labeled Tbias, generates a very small bias current, typically around 100 picoamperes.
This current produces the gate voltage for the feedback transistor Tfb locally inside the pixel.
As a result, the operating point of the feedback transistor becomes significantly less sensitive to variations of the supply voltage across the matrix.
The global control voltage PFB is generated off-matrix using a bias DAC, allowing programmable adjustment of the feedback operating point
1. Electronics Placement in the N-Well
In our HVCMOS sensors, the readout electronics are integrated within the n-well, a shallow n-doped region implanted in a p-type substrate that forms the signal-collecting diode. This design choice has significant implications for the sensor’s operation and electrical isolation.
Potential Requirements: To prevent forward-biased junctions, the potential of the n-well must be maintained higher or at lease not lower than the potential of any p+ diffusion – 100mV (e.g., p-type regions forming transistor source/drain). Forward-biased junctions would lead to unwanted current flow, degrading sensor performance.
  Our Structure: The n-well potential is set to approximately 1.7-1.8 V, ensuring isolation from p+ diffusions
Isolation: Placing electronics in the n-well isolates them from the p-type substrate, allowing high bias voltages without damaging the circuitry. Signal Collection: The n-well serves as both the sensor diode and the housing for electronics, enabling monolithic integration and fast charge collection. Design Constraint: Careful potential management is required to maintain the n-well at a higher voltage than surrounding p+ regions, necessitating precise biasing circuits.
Our HVCMOS sensor employs an AC-coupled connection between the sensor diode and the charge-sensitive amplifier (CSA), which amplifies the current pulse induced by particle interactions.
Purpose: AC coupling isolates the high DC bias voltage of the n-well (~1.8 V plus the high bias voltage) from the amplifier’s input, protecting the CSA and allowing independent biasing of the sensor and electronics.
The CSA in our HVCMOS sensor uses a folded cascode topology, a common choice for high-performance analog circuits.
Description: The folded cascode is a single-stage amplifier with a cascode transistor configuration that “folds” the current path to improve gain and bandwidth.
Key Features:
  High Gain: The topology provides high open-loop gain (A), essential for achieving a closed-loop gain close to 1/(𝑠𝐶_𝑓 ) (as discussed in prior CSA lectures).
  Compact Design: Suitable for in-pixel integration within the n-well, balancing performance with area constraints.
he CSA’s feedback network is critical for signal integration and noise performance. In our design, both the feedback capacitance and feedback resistance are implemented with specific techniques to optimize performance.
Feedback Capacitance (Cf):
  Implementation: Cf is realized using the parasitic drain diffusion capacitance of a MOSFET. This leverages the inherent capacitance of the transistor’s drain region, reducing the need for additional components and saving area.
Implications: Compact design suitable for in-pixel integration.
The capacitance value is process-dependent, requiring careful calibration to ensure consistent gain
  𝑉_"out" =𝑄/𝐶_𝑓
Implementation: Rf
Rf​ is implemented as a MOSFET operating in the active-biased region, as detailed in the IEEE JSSC paper
Advantages: Tunable resistance via bias adjustment, allowing optimization of the feedback time constant
𝑇_𝑓=𝑅_𝑓⋅𝐶_𝑓,
Compact integration within the pixel, avoiding large physical resistors.
The bias resistance for the n-well sensor diode is also implemented with a specific technique to ensure proper operation.
Implementation: The bias resistance is realized as a MOSFET in the active-biased region, as described in the IEEE JSSC paper. Operation: The MOSFET provides a high-impedance path to set the n-well’s DC bias voltage (~1.8 V plus high voltage), while allowing the AC signal to be coupled to the CSA.

## Slide 22: Optimizing Amplifier Rise Time for Minimum Time Jitter
Time Jitter Formula:
Noise dependence:
where
Threshold dependence:
=
Combined Expression:
Time jitter depends nonlinearly on Tr.
Small Tr → higher noise. Large Tr → slower signal.
Optimal Tr minimizes TJ: trade-off between noise and signal timing.
Notes: We start from the formula for time jitter
Here, Tr is the rise time of the amplifier, N is the noise, Vsig is the signal amplitude, and VTH is the threshold voltage. Both the noise N and the threshold voltage VTH depend on Tr.
We write simplified formula for noise in a charge-sensitive amplifier (we take into account only thermal noise of the input transistor):
Where A is a constant that includes detector and feedback capacitances, temperature, and transistor parameters. Specifically:
Next, we assume that the threshold voltage VTH is set proportionally to the noise level. That is:
with m being some empirical constant, typically around 10.
Now we substitute these expressions into our formula for time jitter:
This gives us an expression that explicitly shows how time jitter depends on the amplifier rise time Tr, and on the detector and electronics parameters embedded in A.
This equation helps us search for an optimal Tr that minimizes time jitter. If Tr is too small, noise increases. If Tr is too large, the signal becomes slow, worsening jitter. So, there is a trade-off.
Let us now return to the formula for time jitter, which we’ve seen earlier:
"TJ"≈T_r⋅N/(V_sig−V_TH )
Here, Tr is the rise time of the amplifier, N is the noise, Vsig is the signal amplitude, and VTH is the threshold voltage.
But notice something important: Both the noise N and the threshold voltage VTH actually depend on Tr. This gives us a great opportunity to think about optimization — particularly how to choose an optimal Tr that minimizes time jitter.
So let's dig into this dependency.
First, based on the formula for noise in a charge-sensitive amplifier — and here we’re simplifying by assuming that thermal noise of the input transistor dominates — we can write:
𝑁=𝐴/√(𝑇_𝑟 )
Where A is a constant that includes detector and feedback capacitances, temperature, and transistor parameters. Specifically:
𝐴=1/2⋅𝐶_𝑑𝑒𝑡/𝐶_𝑓 √(4𝑘𝑇𝛾𝑛/𝑔_𝑚 )
Next, we assume that the threshold voltage VTH is set proportionally to the noise level. That is:
𝑉_"TH" =𝑚 𝑁
with m being some empirical constant, typically around 10.
Now we substitute these expressions into our formula for time jitter:
"TJ"≈𝑇_𝑟⋅𝑁/(𝑉_"sig" −𝑚 𝑁)=𝑇_𝑟⋅(𝐴/√(𝑇_𝑟 ))/(𝑉_"sig" −(𝑚 𝐴)/√(𝑇_𝑟 ))
This gives us an expression that explicitly shows how time jitter depends on the amplifier rise time Tr, and on the detector and electronics parameters embedded in A.
This equation is important because it helps us search for an optimal Tr that minimizes time jitter. If Tr is too small, noise increases. If Tr is too large, the signal becomes slow, worsening jitter. So, there is a trade-off.

## Slide 23: Optimizing Amplifier Rise Time for Minimum Time Jitter
Optimal Rise Time:
;
At optimum:
Notes: By taking the derivative with respect to Tr​ and setting it to zero, we find the optimal rise time:
At this optimum, the noise voltage becomes:
which means the signal-to-noise ratio, SNR, is:
Finally, the timing jitter at this minimum simplifies to:
Now, to evaluate A more explicitly, let's assume the transistor operates in the weak inversion region, where the transconductance is:
Here, Ibias​ is the bias current, n is the subthreshold slope factor, and UT​ is the thermal voltage, approximately 25 millivolts at room temperature.
Substituting this into the expression for A, we get:
Putting all these together, the timing jitter can be approximated as:
To see what this means in practice, consider these realistic values:
m = 10, Cdet = 100fF, Cf = 2.5fF, Vsig = 0.1V (Qsig = Cf Vsig ~ 1500e), Ibias = 10µA, n = 1.25, = 2/3
Substituting these into the formula, the timing jitter is approximately:
TJ∼66.75 ps
This small timing jitter highlights how effective the design can be when these parameters are carefully optimized.
By taking the derivative with respect to Tr​ and setting it to zero, we find the optimal rise time:
𝑇_𝑟=((2 𝑚 𝐴)/𝑉_"sig" )^2
At this optimum, the noise voltage becomes:
𝑁=𝑉_"sig" /(2 𝑚)
which means the signal-to-noise ratio, SNR, is:
𝑆𝑁𝑅=𝑉_"sig" /𝑁=2𝑚
Finally, the timing jitter at this minimum simplifies to:
"TJ"≈𝑇_𝑟/𝑚
Now, to evaluate A more explicitly, let's assume the transistor operates in the weak inversion region, where the transconductance is:
𝑔_𝑚=𝐼_𝑏𝑖𝑎𝑠/(𝑛𝑈_𝑇 )
Here, Ibias​ is the bias current, n is the subthreshold slope factor, and UT​ is the thermal voltage, approximately 25 millivolts at room temperature.
Substituting this into the expression for A, we get:
𝐴=1/2⋅𝐶_𝑑𝑒𝑡/𝐶_𝑓 √(4𝑘𝑇𝛾𝑛/(𝐼_𝑏𝑖𝑎𝑠/(𝑛𝑈_𝑇 )))=𝑛𝑈_𝑇 𝐶_𝑑𝑒𝑡/𝐶_𝑓 √(𝑒𝛾/𝐼_𝑏𝑖𝑎𝑠 )
Putting all these together, the timing jitter can be approximated as:
"TJ"≈𝑇_𝑟/𝑚=1/𝑚 ((2𝑚 𝑛 𝑈_𝑇)/𝑉_𝑠𝑖𝑔 𝐶_𝑑𝑒𝑡/𝐶_𝑓 )^2 𝑒𝛾/𝐼_𝑏𝑖𝑎𝑠
To see what this means in practice, consider these realistic values:
m = 10, Cdet = 100fF, Cf = 2.5fF, Vsig = 0.1V (Qsig = Cf Vsig ~ 1500e), Ibias = 10µA, n = 1.25, 𝛾 = 2/3
Substituting these into the formula, the timing jitter is approximately:
TJ∼66.75 ps
This small timing jitter highlights how effective the design can be when these parameters are carefully optimized.

## Slide 24: Optimizing Amplifier Rise Time for Minimum Time Jitter
Step 1: First, we scale down Cf until the Rf - noise contribution becomes small enough.
Step 2: Adjust rise time Tr​ (via output capacitance Co) to achieve SNR = 2m
Step 3: Multiply transistors to increase bias current Ibias​
  Keeps SNR optimal
  Decreases Tr ​ → reduces timing jitter
Trade-off: Increasing Ibias​ raises power consumption → balance time resolution vs. power efficiency
Assumption: Charge collection time ≪ Tr​
2
3
Reduces jitter
Achieves SNR
1
smaller RF noise
Notes: How to optimize timing performance in HVCMOS sensors?
We assume that we reduced the detector capacitance as much as possible.
Let us start with the "minimum size" Cf (e.g. 10 fF) and with a small transistor and small transistor current (e.g. 10 µA).
First, we scale down Cf until the Rf - noise contribution becomes small enough.
First, we adjust the rise time, Tr ​, by varying the output capacitance Co ​ so that we achieve a target signal-to-noise ratio—specifically, an SNR of 2m, where m is our empirical factor, often around 10.
Once this optimal SNR is achieved, the next step involves transistor multiplication—that is, increasing the number of parallel transistors to raise the bias current Ibias​. This increase in Ibias​ allows us to reduce Tr​, since higher current improves the speed of the amplifier.
By doing this, we keep the SNR optimal while pushing the timing jitter down. However, this comes at a cost: multiplying transistors and raising Ibias​ increases power consumption.

## Slide 25: Comparator Design
Comparator Architecture
Challenge:
Large signals on PMOS diffusion contacts can cause parasitic charge injection into sensing deep n-well
Solution: Isolated n-well
Isolated n-well available in:
AMS aH18
TSI 180 nm HV-CMOS
LFoundry 150 nm
(isolated) n-well
PMOS transistor
Deep n-well
VDD
Deep p-well
Notes: The comparator converts the small analog signal from the front-end amplifier into a digital signal suitable for the readout logic.
One challenge is that large fast signals appearing on PMOS diffusion contacts can produce parasitic charge injection into the sensing deep n-well.
For this reason, the comparator architecture strongly depends on the availability of isolated PMOS transistors.
An isolated n-well means that the PMOS n-well is electrically isolated from the sensing deep n-well.
This option was available in older AMS aH18 technologies, in the TSI 180 nanometer HV-CMOS process, and also in the LFoundry 150 nanometer process.

## Slide 26: Comparator Design
MightyPix2:
no isolated PMOS option available
PMOS transistor
Deep n-well
VDD
Deep p-well
Notes: Unfortunately, the production version of the AMS technology used for MightyPix2 does not provide isolated PMOS devices.

## Slide 27: Comparator Design
MightyPix2:
fully NMOS-based comparator
Three-stage cascade
NFET differential amplifiers, NFET loads
No PFET loads:
avoid parasitic charge injection
1.0V
2.1V
1.8V
1.8V
inp
inn
CP
PMOS transistor
Deep n-well
VDD
Deep p-well
Notes: The comparator consists of a cascade of three NFET differential amplifier stages with NFET loads.
The cascade structure is necessary because the gain of a single stage is relatively small, approximately given by the ratio of the transconductance of the input transistor to the load transconductance.
PFET load transistors are avoided in order to suppress parasitic charge injection and signal coupling into the sensing deep n-well caused by fast digital transitions.

## Slide 28: Readout
pixel
0
RCU
pixel
pixel
Hit buffers
EOCs
N. Striebig et al 2026 JINST 21 C04059
Notes: Let me now move to the digital part located at the chip periphery.
The digital architecture consists of three main blocks.
First, we have the matrix of hit buffers located below the pixel matrix, with one hit buffer assigned to each pixel. Two columns of hit buffers share one End-of-Column, or EoC, block. The hit buffers and EoCs are implemented as full custom designs, while the Readout Control Unit, or RCU, is synthesized from RTL code.

## Slide 29: …
pixel
3
3
TS
HitFlag1
RdPix
LdPix
PrioOut
RdCol
Data bus
LdCol
PrioIn
CompIn
HitFlag2
Prio. Logic
TSRam
LdPix
TS
PrioOut
Data
RdPix
PrioOut
PrioIn
&
HitFlag and prio. logic
Data latch
Data bus
Hit buffer
EOC buffer
Notes: The output of each comparator is connected directly to a hit buffer. The hit buffer contains hit flags, synchronization logic, and priority selection circuitry.
At the leading edge of the discriminator pulse, a 12-bit time-of-arrival timestamp is stored in DRAM cells. In LF-MightyPix, a 13-bit timestamp is used.

## Slide 30: …
State
Machine
3
5
5
RCU
Notes: At the trailing edge, an additional 4-bit timestamp is captured in order to determine the time-over-threshold, which is later used for time-walk compensation.

## Slide 31: …
3
5
B
9
8
B
A
State
Machine
RCU
Notes: next hits entering the hit buffer.

## Slide 32: …
State
Machine
3
5
B
9
8
B
A
State
Machine
RCU
Notes: The hit buffer is loaded asynchronously by the hit signal, while the readout itself is synchronized.
Ldpix signal is important for synchronizing the hit acquisition and readout process.

## Slide 33: …
State
Machine
3
5
B
9
8
B
A
State
Machine
RCU
Notes: HitFlag2 is set.

## Slide 34: …
State
Machine
3
5
B
9
8
B
A
State
Machine
RCU

## Slide 35: …
3
5
9
8
B
A
State
Machine
B
State
Machine
RCU
Notes: Priority logic is used to select the highest-priority full buffer within the column.

## Slide 36: …
3
5
9
8
B
A
State
Machine
B
State
Machine
RCU
Notes: Priority logic is used to select the highest-priority full buffer within the column.

## Slide 37: …
9
8
B
A
State
Machine
B
3
5
State
Machine
RCU
Notes: Priority logic is used to select the highest-priority full buffer within the column.

## Slide 38: …
9
8
B
A
State
Machine
B
3
5
State
Machine
RCU
Notes: Outputs of all hit buffers in one column are connected to a shared data bus, or bitline.

## Slide 39: …
3
5
9
8
B
A
B
TS
HitFlag1
RdPix
LdPix
PrioOut
RdCol
Data bus
LdCol
PrioIn
CompIn
HitFlag2
Prio. Logic
TSRam
LdPix
TS
PrioOut
Data
RdPix
PrioOut
PrioIn
&
HitFlag and prio. logic
Data bus
Hit buffer
EOC buffer
Notes: In the lower part of the slide we see the End-of-Column buffer.
Its structure is similar to the hit buffer, but it operates at the column level and temporarily stores the selected hit data before readout by the FSM.

## Slide 40: …
3
5
9
8
B
A
State
Machine
B
State
Machine
RCU
Notes: An AND function between PrioOut and LdCol generates the signal RdPixel.
The data are then stored in the first EoC (preload) latch. Preloading flag is set.

## Slide 41: …
A,B,row1,col2
5,3,row0,col0
3
5
9
8
B
A
State
Machine
B
State
Machine
RCU

## Slide 42: …
A,B,row1,col2
5,3,row0,col0
3
5
9
8
B
A
State
Machine
B
State
Machine
RCU
Notes: At the same time, the read operation clears HitFlag1 and HitFlag2 inside the hit buffer.
However, an internal latch, not shown here, keeps the Select signal active until RdPixel returns to zero.

## Slide 43: …
5,3,row0,col0
3
5
9
8
B
A
State
Machine
B
A,B,row1,col2
State
Machine
RCU

## Slide 44: …
5,3,row0,col0
5,3,row0,col0
A,B,row1,col2
A,B,row1,col2
3
5
9
8
B
A
State
Machine
B
State
Machine
RCU
Notes: Ldpix signal transfers the data from the preload latch into the main latch and sets the corresponding main hit flag.
The preloaded hit becomes available for the normal End-of-Column readout process.

## Slide 45: …
5,3,row0,col0
5,3,row0,col0
A,B,row1,col2
A,B,row1,col2
3
5
9
8
B
A
State
Machine
B
State
Machine
RCU

## Slide 46: …
5,3,row0,col0
5,3,row0,col0
A,B,row1,col2
A,B,row1,col2
9
8
3
5
B
A
State
Machine
B
State
Machine
RCU
Notes: The state machine receives this PrioOut signal, which indicates that valid hit data are now stored in the End-of-Column buffer.

## Slide 47: …
5,3,row0,col0
5,3,row0,col0
A,B,row1,col2
A,B,row1,col2
9
8
3
5
B
A
State
Machine
B
State
Machine
RCU
Notes: The state machine then generates the signal RdCol to read out the data stored in the End-of-Column buffer.

## Slide 48: …
5,3,row0,col0
5,3,row0,col0
A,B,row1,col2
A,B,row1,col2
9
8
3
5
B
A
State
Machine
B
State
Machine
RCU
N. Striebig et al 2026 JINST 21 C04059

## Slide 49: …
9,8,row1,col0
5,3,row0,col0
A,B,row1,col2
A,B,row1,col2
9
8
3
5
B
A
State
Machine
B
State
Machine
RCU
N. Striebig et al 2026 JINST 21 C04059
Notes: Now we come to the preloading operation.
At the same time that the current EoC data are being read out, a new RdPix signal is already generated for the next hit.
As a result, the next hit data are transferred from the hit buffer and stored into the preload latch of the first EoC stage.
In this way, the next readout cycle is prepared in parallel with the current one, which significantly improves the readout efficiency.

## Slide 50: …
9,8,row1,col0
5,3,row0,col0
A,B,row1,col2
A,B,row1,col2
9
8
3
5
B
A
State
Machine
B
State
Machine
RCU

## Slide 51: …
9,8,row1,col0
5,3,row0,col0
A,B,row1,col2
A,B,row1,col2
9
8
3
5
B
A
State
Machine
B
State
Machine
RCU

## Slide 52: …
9,8,row1,col0
5,3,row0,col0
A,B,row1,col2
A,B,row1,col2
9
8
3
5
B
A
State
Machine
B
State
Machine
RCU

## Slide 53: …
9,8,row1,col0
5,3,row0,col0
A,B,row1,col2
A,B,row1,col2
3
5
B
A
State
Machine
B
9
8
State
Machine
RCU

## Slide 54: …
9,8,row1,col0
5,3,row0,col0
A,B,row1,col2
A,B,row1,col2
3
5
B
A
State
Machine
B
9
8

## Slide 55: …
9,8,row1,col0
5,3,row0,col0
A,B,row1,col2
A,B,row1,col2
3
5
B
A
State
Machine
B
9
8

## Slide 56: …
9,8,row1,col0
9,8,row1,col0
A,B,row1,col2
A,B,row1,col2
3
5
B
A
State
Machine
B
9
8
Notes: Now the signal LdPix is generated again.
This signal LdPix transfers the data from the first, or preload, latch into the second main latch and sets the corresponding main hit flag.
As a result, the preloaded hit becomes fully available for the standard End-of-Column readout process.

## Slide 57: …
9,8,row1,col0
9,8,row1,col0
A,B,row1,col2
A,B,row1,col2
3
5
B
A
State
Machine
B
9
8

## Slide 58: …
9,8,row1,col0
9,8,row1,col0
A,B,row1,col2
A,B,row1,col2
3
5
B
A
State
Machine
B
9
8

## Slide 59: …
9,8,row1,col0
9,8,row1,col0
A,B,row1,col2
A,B,row1,col2
3
5
B
A
State
Machine
B
9
8
Notes: The last data word is transferred to the readout bus.

## Slide 60: …
9,8,row1,col0
9,8,row1,col0
A,B,row1,col2
A,B,row1,col2
3
5
B
A
State
Machine
B
9
8

## Slide 61: …
9,8,row1,col0
9,8,row1,col0
A,B,row1,col2
A,B,row1,col2
3
5
B
A
State
Machine
B
9
8

## Slide 62: Readout Control Unit (RCU)
Readout Control Unit (RCU)
Main digital readout block
Contains:
Readout FSMs
Asynchronous FIFOs
Readout multiplexer
Round-robin arbiter
Gearbox
Scrambler
Serializer
DDR output stage
Slow Control Interfaces
Used for:
Chip configuration
Monitoring
Status register readback
On-chip ADC readout
Main interface:
ECS downlink
10 Mbps serial link
8b/10b encoded
N. Striebig et al 2026 JINST 21 C04059
Notes: The Readout Control Unit, or RCU, is a relatively complex digital block responsible for controlling the complete chip readout.
It contains the readout finite state machines, asynchronous FIFOs, multiplexers, arbitration logic, gearbox circuits, scramblers, serializers, and the final DDR output stage.
The chip also incorporates several slow-control interfaces that are primarily used for device configuration, monitoring, status register readback, and access to on-chip ADC data.
The main control interface is the ECS downlink operating at 10 megabits per second.

## Slide 63: Test Results
Test Results
Measured prototypes:
MightyPix1
LF-MightyPix
Focus:
Radiation hardness
Hit efficiency
Timing performance
Notes: Finally, I would like to show some measurement results.
So far, we have tested both MightyPix1 and LF-MightyPix.
In the following slides, I will highlight several important results related to radiation hardness, hit efficiency, and timing performance.

## Slide 64: DESY Test Beam
DESY Test Beam
Measurements performed after irradiation
Scans:
Threshold scans
Bias voltage scans
Conditions:
Up to 3 × 10¹⁵ neq/cm²
High-voltage operation up to 480 V
Notes: These are preliminary results from our recent DESY test beam campaign investigating the radiation hardness of LF-MightyPix.
We performed threshold scans at 190 volts = the full unirradiated depletion voltage, and the maximum safe operating voltage, for each irradiation fluence.
For fluences of 5 x 1014 and 1015 neq /cm2, additional scans of the bias voltage were performed at constant threshold.

## Slide 65: Radiation Hardness
Radiation Hardness
LF-MightyPix achieves:
99% hit efficiency
up to 3 × 10¹⁵ neq/cm²
Operation voltage:
up to 480 V
Measurements: Lucas Dittmann (U. Heidelberg)
Notes: LF-MightyPix achieves hit efficiencies above 99 % up to fluences of 3 x 1015 neq /cm2.
This was achieved at bias voltages up to 480 volts.
These results demonstrate radiation hardness and significantly exceed the original detector requirements.

## Slide 66: Timing Resolution
Timing Resolution
Without timewalk correction:
~2.5 ns
  up to 1 × 10¹⁵ neq/cm²
~4.5 ns
  at 3 × 10¹⁵ neq/cm²
In-Time Efficiency
LHCb requirement:
99% within 25 ns
Measured:
fulfilled up to 1 × 10¹⁵ neq/cm²
98.6% at 3 × 10¹⁵ neq/cm²
Measurements: Lucas Dittmann (U. Heidelberg)
Notes: At high bias voltages, the measured time resolution is approximately 2.5 nanoseconds up to fluences of 1015 neq /cm2, even without applying timewalk correction.
At the highest tested fluence of 3 x 1015 neq /cm2, the timing resolution degrades to approximately 4.5 nanoseconds.
We also evaluated the in-time efficiency within the 25 nanosecond bunch-crossing interval.
The LHCb requirement of 99 % efficiency within 25 nanoseconds is fulfilled up to fluences of 1015 neq /cm2.
Even at the highest fluence, we still measure 98.6 % in-time efficiency.

## Slide 67: Conclusion
Conclusion
MightyPix demonstrates:
  high-rate capability
  fast timing
  strong radiation hardness
HV-CMOS is a strong candidate for:
  LHCb Mighty Tracker
Next steps:
MightyPix2 measurements
MightyPix3 development
Notes: In conclusion, MightyPix demonstrates that HV-CMOS technology is a strong candidate for the LHCb Mighty Tracker.
The prototypes achieve high-rate capability, fast timing performance, and excellent radiation hardness.
The next steps are the measurement campaign for MightyPix2 and the further optimization towards MightyPix3.
Thank you for your attention.