## Slide 1
XIII FEE Workshop 2026 - Paris
A Low-Power Fully Depleted Monolithic CMOS Pixel Detector with Time and Charge Measurement
for Space-Based Compton Imaging
Matteo Barbagiovanni(1,2) on behalf of the Space it Up! collaboration
Politecnico di Torino(1) / INFN Sezione di Torino(2)

## Slide 2
MOTIVATION & CONTEXT
Space Compton Telescope
Science Driver
MeV Gap
Target the MeV gap (100 keV – 1 GeV) currently invisible to Fermi-LAT (20 MeV – 300 GeV) → AMEGO-X
Needed for studying extreme accelerators and multimessenger sources, including supermassive black hole jets (blazars), binary neutron star mergers (gravitational wave counterparts), and Galactic supernovae
Detection Principle
Characterize gamma-rays:
Single-site (< 100 keV)
  Increases sensitivity for low-energy transients, just triggers one pixel (Photo-electric effect)
Compton Scattering (< 10 MeV)
  Measures the energy and position of the interaction to determine the initial scatter angle (ϑ)
Pairs Production (> 10 MeV)
  Tracks the electron-positron pair to reconstruct the incident photon's direction
Calorimeter
Single-Site event
Untracked Compton
event
Tracked Compton
event
Pair event
Tracking Planes
1

## Slide 3
MOTIVATION & CONTEXT
Space Compton Telescope
Science Driver
MeV Gap
Target the MeV gap (100 keV – 1 GeV) currently invisible to Fermi-LAT (20 MeV – 300 GeV)) → AMEGO-X
Needed for studying extreme accelerators and multimessenger sources, including supermassive black hole jets (blazars), binary neutron star mergers (gravitational wave counterparts), and Galactic supernovae
Requirements:
Low power consumption < 10 mW/cm2
  6.25 μW/channel @ pitch 250 μm
High input energy dynamic range [101, 109] keV
Low rate 10 Hz/cm2
Low noise SNR > 10 & ENC < 200 e-
Timing Resolution 200 ns rms
Energy Resolution 10% @ 60 keV
Space graded working range [-35, 50]°C
Calorimeter
Tracking Planes
Single-Site event
Untracked Compton
event
Tracked Compton
event
Pair event
2

## Slide 4
MOTIVATION & CONTEXT
Why a MAPS for space-borne γ-ray detection?
ARCADIA FD-MAPS
Monolithic integration
Sensor + Readout on same wafer
Electronics buried in deep p-wells
ARCADIA heritage
110 nm CMOS custom process (LFoundry)
N-type high resistivity active region
Backside reverse biased juction
  Fully Depleted (FD)
  Depletion grows up to the top
N-type epitaxial layer to limit punch-through current
Proven up to 400 µm FD substrates
>500 µm - thick FD-MAPS
Increase the interaction probability (stopping power)
Maintain low power consumption
Pixel Matrix
Chip Tiling
Multi-plane HICs
MIP
Pixel
3

## Slide 5
MOTIVATION & CONTEXT
ARCADIA Collaboration
Advanced Readout CMOS Architectures with Depleted Integrated sensor Arrays · INFN CSN5
Technology Platform
R&D in semiconductor sensor technology IP-core design,
mixed-signal ASICs, and advanced DAQ systems
all on the INFN-LFoundry 110 nm CIS process
Applications
High-energy particle physics (vertex & tracking), astroparticle physics in space, medical instruments, nuclear imaging & dosimetry
Key Achievements
High-granularity MAPS down to 5 µm spatial resolution
System-ready MD3 demonstrator
  512×512 pixels, 1.64 cm²,
  17 mW/cm² in low-rate mode
CMOS LGAD targeting timing performances better than 20 ps rms
Monolithic strip sensors with embedded electronics for space-borne applications
Detection Efficiency
Cluster Size
Resolution
Vth
Vth
Vth
Test beam at FNAL with 120 GeV protons
Single-point resolution ~ 4.7 μm
average efficiency 99.23%
MD3
4

## Slide 6
MOTIVATION & CONTEXT
ARCADIA Collaboration
Advanced Readout CMOS Architectures with Depleted Integrated sensor Arrays · INFN CSN5
Molybdenum Kα1 and Kα2 X-rays (17 keV)
X-ray microfocus (up to 140 keV) for radiography and CT setups
MD3
Technology Platform
R&D in semiconductor sensor technology IP-core design,
mixed-signal ASICs, and advanced DAQ systems
all on the INFN-LFoundry 110 nm CIS process
Applications
High-energy particle physics (vertex & tracking), astroparticle physics in space, medical instruments, nuclear imaging & dosimetry
Key Achievements
High-granularity MAPS down to 5 µm spatial resolution
System-ready MD3 demonstrator
  512×512 pixels, 1.64 cm²,
  17 mW/cm² in low-rate mode
CMOS LGAD targeting timing performances better than 20 ps rms
Monolithic strip sensors with embedded electronics for space-borne applications
5

## Slide 7
System Architecture

## Slide 8
SYSTEM ARCHITECTURE
Top-level block diagram
Pixel
Data flow →
← Configuration (token ring)
250×250 µm²
CSA
PDH
Discriminator
MacroPixel
2×2 pixels
Shared ADC
FE Logic
*Serializer
Serializer
24-bit words
DDR - 12 CLK
16 ser./chip
EOC
Time reconstruction
Sparse readout
Configuration
▶
▶
▶
▶
▶
▶
▶
Pixel
ADC
MacroPixel
Serializer
Addr
Energy
TimeFlag
▶
▶
Addr+Energy
Addr+Time
Config
▶
EOC
16×16
Grouping
Macropixels composed of 2x2 pixels
  Low Hit occupancy
  Cluster size
Resource sharing
  Wilkinson ADC
  Common Logic
EOC
Sparse Readout
Timestamping
  Global coarse timestamp
  Local fine-time
Final data 24 bit words
  Address
  Fine Time
  Energy Value
32x32
6

## Slide 9
DIGITAL WORKING PRINCIPLES
Macropixel Event Handling
Word Transmission
24-bit words in DDR, same line for charge and time
Async trigger storage
Event fires → pixel stores arrival word position (0-11) and word counter at arrival (0-5), pixel is immediately blocked
Round Robin scan
Two indipendent pointers scan all 4 pixel registers looking for valid events
Priority TIme > Charge
Pixel release
After both time and charge are transmitted the pixel is unblocked and ready for the next hit
Pixel | Arr. word pos. | Word Ctr. | Time | Charge
00 | bbbb | bbb | 1 | 1
01 | bbbb | bbb | 1 | 1
10 | bbbb | bbb | 1 | 1
11 | bbbb | bbb | 1 | 1
Pixel Register State
Time Path
12 clk cycles per word
Transmit counter (0-11) encodes sub-word phase
Word counter (0-5) encodes inter word delay
Charge Path
ADC digitizes pixel analog memory
Up to 256 cycles ADC conversion
Time and charge information
are processed in parallel if present
↓
Round Robin Processing
Charge
Time
ADC
Serializer
12 clk cycles
Up to 256 clk cycles
7

## Slide 10
DIGITAL WORKING PRINCIPLES
Timing Reconstruction in EOC
EOC timing reconstruction
T_event = T_global − (N_words_waited + 1) × T_word − (12 − transmit_counter)
Word arrives with fixed delay (calibration routine at startup) on a dedicated wire (Macropixel to EOC)
Global timestamp is latched at EOC on time word arrival
Transmit count track position within the current word
Word counter counts how many words elapsed since event
IDLE
OTHER
OTHER
TIME WORD
IDLE
Event Arrival
EOC receives event time word
Time to subtract
8

## Slide 11
Sensor Design

## Slide 12
SENSOR DESIGN
Fully depleted n-on-n sensor structure
Synopsys TCAD Sentaurus simulations — 110 nm LFoundry process
Cross-section schematic
Design choices
Pitch → 250 μm → 6.25 μW/channel
Limit the number of channels for power constraints
No sacrifice on reconstruction capabilities
Thickness → 715 μm
Electrical Characterization
On going tests on new substrates
Capacitance → < 250 fF
gap optimization
p-well/n+ ratio
Pixel Layout
Single pad
Subpixels
9

## Slide 13
SENSOR DESIGN
Sensor Layout Optimization
Key figure of merit: lateral n⁺/p-well junction capacitance
Electrical Characterization
PT shifts with thickness but remains accessible across 300-700 μm.
C(V) identified FD as capacitance plateau; well-defined working range also for 700 μm.
Key findings
Segmented pixels increase perimeter capacitance until 6×6 sub-pixel layouts improve scaling — but routing complexity grows
Single-pad selected: superior field uniformity, simpler routing, space for MIM decoupling capacitor
C(V) sweep identifies full depletion as capacitance plateau; working range well-defined for all thicknesses up to 700 µm
Punch-through sets upper bias limit — shifts with thickness but remains accessible across 300–700 µm range
Predictive Capacitance Modeling
Developed geometry-based models to accelerate layout optimization
Main capacitance contribution is the lateral one for the
n+/p-well junction
Gap optimization leads to half of the capacitance wrt default value
Segmented pixels increase perimeter capacitance until 6×6 sub-pixel layouts improve scaling — but routing complexity and parasitic capacitance grows
Thickness [μm] | VFull Depletion [V] | VPunch-Through [V]
300 | 30 | 70
500 | 80 | 140
700 | 125 | 210
10

## Slide 14
SENSOR DESIGN
Sensor MC Testing
99th percentile of Energy released in one pixel
TCAD
Device layout and simulation → export following maps
Doping Concentration
Electrostatic Potential → Weigthing Potential
Electric Field
Monte Carlo Framework
Particle transport and interactions simulations
Energy deposition and ionization modeling
Charge carrier drift and signal induciton computations
Key findings
Signal Integrity
Unipolar signals ensure full charge collection without cancellation effects from bipolar induction — critical for accurate energy and timing measurements
Weighting Potential Uniformity
More uniform weighting potential across the pixel area means the induced signal is less dependent on the track hit position, giving consistent response over the full 250 µm pitch
Charge Collection Equivalence
Since integrated collected charge is identical between the two layouts, the capacitance penalty (200 fF vs 50 fF) is the only real drawback of the single pad — and it is a known, manageable trade-off
Simpler Signal Processing
Unipolar pulses are easier to threshold, integrate, and time-stamp; bipolar signals require more careful shaping and can cause baseline shifts or undershoot at high rates
Reduced Risk of Partial Signal Loss
In bipolar signals, if the negative lobe is clipped or the shaping time is poorly matched, net collected charge is underestimated; the single pad avoids this risk entirely
Design Simplicity & Yield
A single large pad has no inter-subpad routing, fewer lithographic constraints, and is more robust against process variation in a thick fully-depleted substrate
Thickness [μm] | VFull Depletion [V] | VPunch-Through [V]
300 | 30 | 70
500 | 80 | 140
700 | 125 | 210
200 fF
50 fF
Eγ [keV] | 99th percentile [keV]
1e1 | 10 → 3k e-
1e3 | 400 → 110k e-
1e4 | 450 → 125k e-
1e5 | 570 → 160k e-
Allpix signals for 30 ke- released at 100 μm
Depth at the center of one pixel
11

## Slide 15
Front-End Implementation

## Slide 16
FONRT-END IMPLEMENTATION
Pixel Architecture Overview
Pixel
250×250 µm²
CSA
PDH
Discriminator
MacroPixel
2×2 pixels
Shared ADC
FE Logic
*Serializer
Serializer
24-bit words
DDR - 12 CLK
32 ser./chip
EOC
Time reconstruction
Sparse readout
Configuration
▶
▶
▶
▶
CSA
DAC
Cf
Rf
Discriminator
ADC
PDH
MacroPixel
Pixel
Sensor Capacitance
Single pad layout → 200 fF
Dynamic Range
3k - 160k electrons in sensor
Focus on 3k - 100k electrons
Temperature Range
Space grading → [-35,50] °C
PreAmplifier
CSA
TP injection
Energy Branch
Peak Detector and Hold circuit
Shared Wilkinson ADC
Time Branch
Timing Discriminator
Data flow →
← Configuration (token ring)
Energy
Time Flag
12

## Slide 17
Charge Sensitive Amplifier
CSA Features
Telescopic cascode with split bias current branch and PMOS input transistor
  CDetector = 200 fF
  CFeedback= 45 fF → expected gain 22 mV/fC
  [3, 160] kelectrons input → [10, 570] mV output swing
Sensor cathode needs at least 0.7 V bias
  Active feedback network to give enough room for the output
    τRC = 3.5 μs
    Peaking Time = 150 ns
1.2 μW
CSA Simulations
DC Levels:
Vin > 0.8 V
Vout ~ 450 mV
Vout ~ 40 mV change
Need for baseline holder
Linearity:
21.8 mV/fC measured gain
INL ± 0.2% @ [3-100] ke-
FRONT-END IMPLEMENTATION
13

## Slide 18
Peak Detector and Hold
PDH Features
Class AB OTA
Adaptive Biasing via Positive Feedback
  Boost current during pulse edges
Enhanced Slew-Rate/Power Ratio
Weak-Inversion Quiescent Operation
Cascoded rectifing current mirror
Prevent voltage drop and leakage
Limit baseline pedestal
1.8 μW
FRONT-END IMPLEMENTATION
[1] Ah-Reum Kim et al. "Low-power class-AB CMOS OTA with high slew-rate," 2009 International SoC Design Conference (ISOCC), Busan, 2009, pp. 313-316, doi: 10.1109/SOCDC.2009.5423790
14

## Slide 19
Peak Detector and Hold
PDH Features
Class AB OTA
Adaptive Biasing via Positive Feedback
  Boost current during pulse edges
Enhanced Slew-Rate/Power Ratio
Weak-Inversion Quiescent Operation
Cascoded rectifing current mirror
Prevent voltage drop and leakage
Limit baseline pedestal
1.8 μW
PDH Simulations
Itail = 40 nA
Ch = 300 fF
Pedestal < 2 mV
Settling time ~ 0.5 μs
Linearity
PDH/CSA ± 3% @ [3, 100] ke-
Strong dependence on temperature for more energetic events
FRONT-END IMPLEMENTATION
[1] Ah-Reum Kim et al. "Low-power class-AB CMOS OTA with high slew-rate," 2009 International SoC Design Conference (ISOCC), Busan, 2009, pp. 313-316, doi: 10.1109/SOCDC.2009.5423790
15

## Slide 20
Peak Detector and Hold
PDH Features
Class AB OTA
Adaptive Biasing via Positive Feedback
  Boost current during pulse edges
Enhanced Slew-Rate/Power Ratio
Weak-Inversion Quiescent Operation
Cascoded rectifing current mirror
Prevent voltage drop and leakage
Limit baseline pedestal
1.8 μW
PDH Simulations
Itail = 40 nA
Ch = 300 fF
Pedestal < 2 mV
Settling time ~ 0.5 μs
Linearity
PDH/CSA ± 3% @ [3, 100] ke-
Strong dependence on temperature for more energetic events
FRONT-END IMPLEMENTATION
[1] Ah-Reum Kim et al. "Low-power class-AB CMOS OTA with high slew-rate," 2009 International SoC Design Conference (ISOCC), Busan, 2009, pp. 313-316, doi: 10.1109/SOCDC.2009.5423790
16

## Slide 21
Timing Discriminator
DiscirminatorFeatures
Dual stage cascoded leading-edge discriminator
Cells connected with active biasing network
  Minimal quiescent current
  Boost tail current of the second stage
Fast recovery limiting voltage swing
1.5 μW
Discriminator Simulations
Jitter < 10 ns
Timewalk < 45 ns
FRONT-END IMPLEMENTATION
[2] Menouni, Mohsine. “Low Power Discriminator for ATLAS Pixel Chip,” 2009. doi:10.5170/CERN-2009-006.606.
17

## Slide 22
Front-end simulated results
Front end response to Allpix² signals
Power Consumption:
10 mW/cm2
250 μm pitch
→ 6.25 μW/channel
Temperature Range
Space Application
→ [-35, 50]°C
Timing Resolution:
200 ns r.m.s.
Dynamic Range
Main focus on 3k - 100k electrons
Technology | LFoundry 110 nm CIS
Power Supply | 1.2 V
NChannels | 32 x 32 Pixels / 16 x 16 MP
Input Polarity | Negative
CSensor | 200 fF
ENC | < 200 e-
SNR @ 3 ke- | 17
FE Power Consumption | 4.5 μW/channel
FRONT-END IMPLEMENTATION
18

## Slide 23
Substrates Characterisation

## Slide 24
SUBSTRATES CHARACTERISATION
First test results
IV Characterisation at the MicroProbing station (passive structures)
    500 μm – thick substrates
    700 μm – thick substrates
  Testing of ARCADIA MD3 on thicker substrates
Substrate Characterisation
  Uranium cup used as source
  Hitmaps: number of hits showed relatively to the 512x512 pixels MD3 matrix
500 μm
700 μm
PRELIMINARY
19

## Slide 25
Status and Outlook

## Slide 26
STATUS AND OUTLOOK
A Low-Power FD-MAPS for Space Compton Imaging
Sensor
700 µm n-on-n TCAD pixel optimised at 250 µm pitch
single-pad layout selected for field uniformity
200 fF capacitance achieved
full depletion at ~80 V on real 700 µm substrates
Digital
MacroPixel async event storage
time-priority round-robin arbitration
EOC sub-word timestamp reconstruction validated in simulation
24-bit DDR serialisation implemented
Front-End
CSA
  150 ns peaking
  Output swing 10 - 600 mV
  ±0.2% INL
PDH
  0.5 us settling time
  2 mV pedestal
Time Discriminator
  timewalk < 45 ns
  Jitter < 10 ns
Ongoing work
Wilkinson ADC design: ramp linearity and power optimisation in progress
Full analog–digital integration: floor-planning and mixed-signal verification upcoming
Complete thick substrate qualification on 700 µm samples under way
Module integration with multiple HIC options under study (PCB, FPC, FLEX)
4.5 μW
-35 to 50 °C

## Slide 27
Thank you for your time!
Design, Simulation and Test Group
M. Barbagiovanni, L. Baldini, M. Da Rocha Rolo, A. Di Salvo,
E. Posteraro, A. Frassà, L. Latronico, M. Mandurrino,
U. Savino, C. Sgrò, E. Trossarello

## Slide 28
Backup Slides

## Slide 29
BACKUP
GEANT Simulations
Tracker simulation details
Detector
  simulated with worst case single block of all metallization on top of sensor
  32x32 pixels
  EOC
Hybrid Integrated Circuit
Multiplane tracker
  1 m2 chip planes
Monocromatic source
  100 keV - 1 GeV
Courtesy of A. Frassà

## Slide 30
BACKUP
GEANT - Eγ = 100 keV, Ethr = 5 keV
Courtesy of A. Frassà

## Slide 31
BACKUP
GEANT - Eγ = 100 MeV, Ethr = 5 keV
Courtesy of A. Frassà

## Slide 32
BACKUP
Module assembly options
PCB
Printed circuit board
Thermal Performances
Steady-state thermal simulation
32 chips (16 per side)
  Dissipated power/chip 13mW
ideal thermal contact and a wall temperature fixed at 15°C
Maximum global variations:
PCB → 4.5°C
FPC → 2.5°C
Higher thermal drain for FPC
2x2 chips layout
Hybrid Integrated Circuit
HICs on Al Frame
FPC
Al flexible printed circuit
PRELIMINARY
Courtesy of U. Savino
PCB
FPC
Flex embed
Al Chip embedded in flex printed circuit
FBK flex demonstator
spTab bonded to ALPIDE chip