## Slide 1: EICROC : AC-LGAD readout chip for EIC FEE workshop 21 may 2026
F. Bouyjou, H. Chanal, F. Dulucq, M. El Berni, S. Extier, M. Firlej, T. Fiutowski, K. Guillossou, F. Guilloux, M. Idzik, N. Kachkachi, B.-Y. Ki, C. de La Taille, J. Moron, D. Marchand, L. Royer, N. Seguin-Moreau, L. Serin, A. Shama, A. Soulier, K. Swientek, D. Thienpont, A. Verplancke

## Slide 2: ePIC experiment far-forward region
Roman Pots for ePIC experiment
          Used in the far forward tracking of particle collisions, mandatory for exclusive reactions
2 stations ~2m apart
  2-3 layers of sensors per station
  Square pixels of (500µm)²
Stringent requirements
  AC-LGAD sensors will be used because of their capability to provide excellent resolution in timing and spatial resolution.
EIC Conceptual Design Report, 2021

## Slide 3: ePIC AC-LGAD detectors

## Slide 4: DC LGAD and AC LGAD
MIP timing detectors (HGTD, ETL) use DC LGAD sensors
  ~10 fC/MIP
  Area : (1.3 mm)²
  Good timing resolution : 30-50 ps
  Poor position resolution : ~400 µm
  « dead zone » between pixels
AC LGADs for EIC
  Resistive layer to get signal sharing
  Area (500 µm)²
  Good position resolution : < 50 µm
  No dead area
  Good timing resolution (as DC LGAD)
From S. Nanda : https://indico.cern.ch/event/1232761/contributions/5321425/

## Slide 5: AC LGAD performance [FNAL]
Here for strips : 500 µm x 5 mm
  ~30-35 ps timing resolution
  ~10 µm position resolution
  Oscilloscope readout
  Still preliminary results and improvements underway on gain uniformity
  Chosen as baseline for several EIC detectors
New and promising detector
  Need readout chip
  Strips (see next talk by A. Apresyan)
  Pixels 500 µm x 500 µm : EICROC
From S. Nanda : https://indico.cern.ch/event/1232761/contributions/5321425/

## Slide 6: ALTIROC : DC-LGAD readout chip
1 GHz preamplifier and discriminator
2 vernier TDCs for ToA and ToT
Hit buffer: SRAM 1536 x 19 bit (38 µs latenccy)
One pixel : 1.3x1.3mm²
15 x 15 pixels
2 x 2 cm2

## Slide 7: EICROC0
Analog frontend similar to ATLAS ALTIROC
  Cd = 1 pF (max 3 pF)
Need ADC instead of ToT for charge measurement : 8bit 40 MHz from AGH Krakow
TDC taken from HGCROC by CEA Saclay
Simple digital readout but SEE-proof I²C slow control
~2 mW/pixel
Fabricated in spring 2022 in TSMC 130nm

## Slide 8: EICROC0 measurements : S-Curves
6-bit DAC for channel-wise threshold alignement
Correction of channels for a charge of 5 fC (ASIC alond)

## Slide 9: EICROC0 measurements : ADC linearity
8 bit 40 MHz SAR ADC [Krakow]
  Noise ~1 UADC but large common mode noise (here substracted)
  Signal 50 UADC ~500 um => 1 UADC ~10 um
ADC mean & residuals – no sensor
ADC mean & residuals – BNL Flipchip sensor

## Slide 10: EICROC0 measurements : TDC ToA
Time walk measurement :~400 ps
TDC ToA – no sensor
TDC ToA – BNL Flipchip sensor
500 ps

## Slide 11: EICROC0 measurements : TDC jitter
TDC jitter – no sensor
TDC jitter – BNL Flipchip sensor
Charge range degraded with sensor, still need to properly calibrate the TDC for each channel and remove correlated noise

## Slide 12
ADC pedestal subtraction computed from “far” pixel
More charge sharing (~23%) for adjacent neighbors
Time walk correction applied successfully to TDC data
A. Sharma, B.-Y. Ky, D. Marchand, L. Serin
Pixelated AC-LGAD read-out characterization
Measurements with 90Sr 𝛃 source at IJCLab PSI platform (July ‘25)
EICROC0 (4 x 4 channels) CMOS 130 nm
From ADC data
1) digital data stored when the PreAmp signal amplitude of at least 1 channel among the 16 is passing the discriminator threshold

## Slide 13
A. Sharma & D. Marchand
Pixelated AC-LGAD read-out characterization
Preliminary results with Infrared Laser (1/2)
ADC waveforms (8 time samples = 8 points/event): BEFORE & AFTER pedestal subtraction (based on « far » pixel evt by evt)

## Slide 14
A. Sharma, D. Marchand & L. Serin
Pixelated AC-LGAD read-out characterization
Preliminary results with Infrared Laser
Barycenter calculation from ADC data
Considering pixels #01, #05 & #09
Amplitude Ratio = (A9-A1)/(A1+A5+A9)
Horizontally the laser is shooting the center of pixel #05
Mean = 0.0022
RMS = 0.065 = 33 µm

## Slide 15
TDC values difference [DACu] between hit pixels w.r.t. pixel #05
𝜎 [pix05 – pix06]DACu = 1.623 ➜ TDC jitter for individual pixel [= 𝜎 / √2]: 28.7 ps
𝜎 [pix05 – pix10]DACu = 1.059 ➜ TDC jitter for individual pixel [= 𝜎 / √2]: 18.7 ps
𝜎 [pix05 – pix09]DACu = 1.387 ➜ TDC jitter for individual pixel [= 𝜎 / √2]: 24.5 ps
Pixelated AC-LGAD read-out characterization
With Infrared Laser
TDC differences between 2 hit neighboring pixels
Individual Pixel jitter from 19 ps up to 29 ps
BNL sensor biased at HV = -190V

## Slide 16: EICROC prototypes
EICROC0 : 4x4 pixels with simple readout (2022)
EICROC OA/0B 1/1B fabricated in 2025 « ATLAS/ EIC » engineering run TSMC 130n
  EICROC0A/B : 4x4 with improved blocks and testability
  EICROC1/1A : 32x32 and 4x32
EICROC2 will be fabricated Q1 2027
  Should be the final chip…

## Slide 17: First measurements of EICROC0A
Only partial configuration is possible : look at ADC data and s-curves
  Improved ADC baseline, similar minimum threshold (3 fC)

## Slide 18: EICROC0 Coupling investigation
Large coupling seen on the ADC data which was completely hiding the signal up to 20 fC
Large coupling capacitance between local (pixel) digital block and preamp / shaper bias lines
Layout improved by adding exclusion zones and a shield between bias lines and digital
Bias / digital block layout in new EICROC ASICs

## Slide 19: EICROC1
32x32 chip : final dimensions
Goal :
  test full-scale chip analog performance (IR drops)
  Allow final sensor characterization
  Test interface with DAQ : fast commands and 320 Mb/s data output
  Progress on module/front-end boards
Caveats :
  Not (yet) zero-suppressed data
  Still 2mW/ch
  Still analog-on-top

## Slide 20: EICROC1 description
Designed as 8 blocks of 4x32
  Read out sequentially, like EICROC0
  Pixel similar to EICROC0A
  8 CLPS outputs at 40 MHz
  Clock tree for isochronous calib_pulse distribution
Common balcony (End of column)
  Biases and slow control
  New : fast command decoder (clock, calib_pulse, enable_acquisition, start_readout)
  Backup clock and cmd_pulse inputs available
  New : 320 MHz serializer for 1 CLPS output

## Slide 21: First measurements of EICROC1 ADC&TDC

## Slide 22: next EICROC2 (2027)
What is missing in EICROC1 ?
  Larger rate compatibility ?
  Derandomizer for successive events (how many ?)
  Digital on Top (DoT) design for digital power reduction and timing verification on large area : more powerful tools available (UVM)
  Auto-trigger and zero_suppressed data
  Power reduction if possible below 2 mW/ch
Clermont Ferrand lab has joined to take responsibility for the DoT
  Already participated in ATLAS ALTIROC
  The design and verification should take ~9 months from now
Technology choice
  Seems to converge to 130n provided rate remains low enough

## Slide 23
Goals
  Less digital logic possible inside pixel/matrix
  Less signals possible between matrix and periphery
  Triplication of sensitive circuits (configuration registers for example)
    No triplication on data path
  Complexity on periphery side, simple logic inside pixel
Proposal : Based on clusters of 4 pixels, controlled by the periphery
  Some logic shared at cluster level
  Shared data bus between 2 columns
First iteration of this architecture is ready at RTL level, some debug in progress
 Physical implementation can reveal new constraints, architecture may change
Triggered Pixel (TP)
Neighbor pixel (TL1)
Busy cluster
Cluster waiting for hit
Architecture proposal [A. Soulier et al.]

## Slide 24
First physical implementation done in 130nm
  Check if we manage to fit digital readout inside pixel
Preliminary layout of the cluster of 4 pixels and the column
Triplication of cluster (probably need some refinement)
Using a pixel_analog_dummy macro, not the real analog front-end
Need more time to validate that this architecture can fit using 130nm technology
Double column
Cluster of 4 pixels
Physical implementation

## Slide 25: Path towards production and QC
For roman pots ~500 chips would be needed (500 k ch) = 6 wafers
For FToF 10k chips ~100 wafers
EICROC2 should be a final version (all features implemented)
  Schedule accomodates a possible EICROC3 to fix bugs in EICROC2
  ~1 year after EICROC2 tests and system tests complete
Wafer probing station and test setup will be needed
  Can be inspired from ALTIROC setup

## Slide 26: summary
EICROC now reached full scale 32x32 with EICROC1
  Important for analog performance and sensor test
  Also allows to progress on system design
Small scale EICROC0s 4x4 still under test to improve performance and reduce power
  Tests to start soon with sensors
EICROC2 now needs its digital design DoT : ~6 months design time from now
  Responsibility of Clermont Ferrand lab
  Main driving specification is power minimization and low hit rate (< 100 Hz/pixel)
  Submission in Engineering run in TSMC130n Q1 2027
System tests will be (as always) an important input for chip(s) finalization

## Slide 27: backup

## Slide 28: EICROC0 : discriminator jitter measured on probe
Measurements done with the oscilloscope

## Slide 29
ePIC Detectors & Far-Forward Region
electron beam
p/A beam
Luminosity
System
Low-Q2 Taggers
Zero Degree Calorimeter
B0 Magnet
Spectrometer
Off-Momentum Detectors (OMDs)
Far-Forward Region
Roman Pots (RPs)
Off-Momentum Detectors (OMD)
  Detect small angle particles with a different rigidity than the beam
    Access angles down to 0 for rigidity < 0.65
  Necessary for all tagged measurements
    Study of nuclear effects
    Effective neutron target
  Far-Forward detectors are essential to measure exclusive processes, as Deep Virtual Compton Scattering (DVCS) ➜ Generalized Parton Distributions (GPDs)
Roman pots (RP)
  Detect particles scattered at very small angle (< 5 mrad)
  Required to measure exlusive processes on proton targets
    DVCS, DVMP…
    All the channels relevant to GPDs of quarks and gluons