## Slide 1: Cryogenic CMOS Design for Scalable Qubit Control and Readout
2026-05-21 |Dennis Nielinger, Jonas Bühler, Phanish Chava, Carsten Degenhardt, Andre Kruth, Sabitha Kusuma, Daniel Liebau, Jonas Mair, Lea Schreckenberg, Patrick Vliex, Stefan van Waasen

## Slide 2: CONTENT
Designs in 65nm bulk and 22 nm FD-SOI
    Cryogenic measurement results
    Lessons learned (what to watch out for)
Co-integration experiment with qubits at mK
    Thermal management
Other activities at ICA for QC:
    Cryogenic device measurement and modelling
    Cryogenic photonic link (for superconducting qubits and cryo. electronics)

## Slide 3: Cryogenic CMOS Design
Move (parts) of classical control & readout electronics closer to the qubit
Consequence  operate at cryogenic temperature
Cryogenic CMOS enables high-integration
    Comply to ultra strict cooling power budget
Qubits are evolving quickly  modular IC framework

## Slide 4: DC Bias
Specification
Several uncorrelated bias voltage per qubit to form potential wells
Voltage range up to approx. 1.7V
A step size in the hundreds of
Si/SiGe Architecture[3]
Specification for DC Bias via DAC
[3] I. Seidler, T. Struck, R. Xue et al., ”Conveyor-mode single-electron shuttling in Si/SiGe for a scalable quantum computing architecture,” npj Quantum Inf 8, 100, 2022.

## Slide 5: DC Bias
Charge-redistribution topology
  Negligible static power
Digital
DAC
S&H & OPA
QUOCCA
JTAG Interface
RISC-V Processor
DAC FSM
Individual refreshable
Testing amplifier
Digital[4]:
Bias DAC:
Sample & Hold Output Channel:

## Slide 6: DC Bias
Characteristics | Specification
Output Channels | 12
Voltage Range | 0V to 1.8V
Resolution | 12 Bit
Step Size | ~ 439 V
Characteristics | Specification
Output Channels | 12
Voltage Range | 0V to 1.8V
Resolution | 12 Bit
Step Size | 
Digital
JTAG
DAC
Voltage Outputs
1.25 mm
1.25 mm
No output buffer needed due to low leakage
  Reduce power and noise
Defined control of the DAC refresh
  Internal or external trigger signal
CMOS Bias DAC

## Slide 7: DC Bias
506 skipped input words  11.81 Bit
DAC Output

## Slide 8: Measurements
Defined hold trigger for qubit operation between refresh
[5]
Defined hold trigger for qubit operation between refresh
Periodical refresh due to leakage in S&H channels
Refresh increases noise at qubit gates
Low temperature makes long hold time possible
Voltage drift: 746

## Slide 9: DC Bias
Power Consumption And Noise
Component | Power Consumption @ 5 MHz Clock
Analog DAC | 0.96
Analog DAC reference | 0.86
Analog DAC total | 1.8 (152 per channel)
Digital IO | 24.9
Digital Core | 26.4
Total | 53.1
Component | Power Consumption @ 5 MHz Clock
Analog DAC | 
Analog DAC reference | 
Analog DAC total | 
Digital IO | 
Digital Core | 
Total | 
12 Channel running at 24 kHz channel refresh rate at 5 MHz Clock
Integrated noise added by DAC @ 1MHz Clock
Notes: 10 Hz to 300kHz noise bandwidth

## Slide 10: Power draw in padframe
Padframe IP is not made for cryo. temperature
Analog pads are good
    Typically less leakage in ESD structures
Digital pads:
    Functionality (mostly fine)
      even with complex internal circuitry
    Power (every µW counts at mK)
      Consider internal power OK generation
      May generate internal bias voltages (e.g. for IO ↔ core voltage levelshifter)
Padframe IP Considerations

## Slide 11: OPAMP
Clipping of Opamp output at cryo temp.
    Subthreshold operation problemetic
    Due to steep SS
Increase supply for extra headroom
    Use low supply circuit topologies
Pay extra attention to stay in strong inversion
    Compensate or be aware of VTH shift
Steep SS
VTH↑

## Slide 12: Voltage references
Voltage Reference and Regulator Circuit in 22nm FD-SOI
[2] A. R. Cabrera-Galicia, et.al, "Voltage Reference and Voltage Regulator for the Cryogenic Performance Evaluation of the 22nm FDSOI Technology," in IEEE Open Journal of Circuits and Systems, vol. 5, pp. 377-386, 2024, doi: 10.1109/OJCAS.2024.3466395

## Slide 13: NOISE
Cryostat and Voltage Reference & Regulator
Ground loop noise is coupled to regulator output via cold plate.
Ground loop noise is removed by electrically detaching the regulator from the cold plate.
Higher temp. due to thermal pad and imperfect thermalization of cables; improvement on progress.
Avoid GND loops in the cryostat
    Counteracting the wish to thermal couple
Increased 1/f noise; decreased thermal noise
Voltage reference noise
Voltage regulator noise
[2] A. R. Cabrera-Galicia, et.al, "Voltage Reference and Voltage Regulator for the Cryogenic Performance Evaluation of the 22nm FDSOI Technology," in IEEE Open Journal of Circuits and Systems, vol. 5, pp. 377-386, 2024, doi: 10.1109/OJCAS.2024.3466395
Notes: Triboelectric effect (vibration induced)
Gap Pad 500S35 (for space applications)
Shorter connections (through shroud)
Break GND loops (also USB isolators)
RLC low-pass filters
EMC electro magnetic compatibility

## Slide 14: Qubit Readout
Qubit Readout - QUOCCA.SET: A Scalable Readout IC for Semiconductor Quantum Dots
Target: Current readout of quantum dots
Pauli spin blockade to convert spin to charge
Single electron transistor (SET) to convert charge to current (signal ca. 250 pA)
[3] J.Buehler et al., "QUOCCA.SET: A Scalable Readout IC for Semiconductor Quantum Dots", Global Physics Summit 2025, MAR-G19/4
[[10] Kammerloher, E. (2022) Improving the output signal of charge readout for quantum computing in electrostatically defined quantum dots with a new sensing dot concept.
1,25 mm

## Slide 15: Qubit Readout
Qubit Readout - QUOCCA.SET: A Scalable Readout IC for Semiconductor Quantum Dots
Correlated Double Sampling (CDS)
    1st sample after qubit initialization
    2nd sample after qubit operation
    Cancellation of low frequency noise
Signal
OUT
IN
S/H1
S/H2
Signal
SET-Signals Singlet
Triplet
Real Ideal
SET drain current for
SET drain current for
Signal (a.u.)
Signal (a.u.)
Time (a.u.)
[3] J.Buehler et al., "QUOCCA.SET: A Scalable Readout IC for Semiconductor Quantum Dots", Global Physics Summit 2025, MAR-G19/4

## Slide 16: Qubit Readout
Qubit Readout - QUOCCA.SET: A Scalable Readout IC for Semiconductor Quantum Dots
223 pA RMS @ 1 µs, max. BW
111 pA RMS @ 1 µs, 1 kHz BW
Digital Power: 41 µW
Analog Power: 33.6 µW/SET
[3] J.Buehler et al., "QUOCCA.SET: A Scalable Readout IC for Semiconductor Quantum Dots", Global Physics Summit 2025, MAR-G19/4

## Slide 17: Qubit Readout
Qubit Readout - QUOCCA.SET: A Scalable Readout IC for Semiconductor Quantum Dots
Target: Voltage readout of quantum dots
Pauli spin blockade to convert spin to charge
Single electron transistor to convert charge to voltage
Signal: ≈ 3 mV [5]
[4] J.Buehler et al., "Scalable integrated readout of semiconductor quantum dots using current biasinG", Global Physics Summit 2026
https://summit.aps.org/smt/2026/events/MAR-Z17/15
10] Kammerloher, E. (2022) Improving the output signal of charge readout for quantum computing in electrostatically defined quantum dots with a new sensing dot concept.
S/H with variable Capacitances
Dynamic Comperator
7 bit SAR ADC
Digital
Triggerd FSM
JTAG and UART
Current-mirror bank
Front-End
Biasing
Back-End
1 mm

## Slide 18: Qubit Readout
Amplifier Measurements at 8 K
Power: 57 µW
Gain: 8 - 45 dB
Bandwidth: 1.5 - 5.5 MHz
Active area: 1500 µm²
[4] J.Buehler et al., "Scalable integrated readout of semiconductor quantum dots using current biasinG", Global Physics Summit 2026
https://summit.aps.org/smt/2026/events/MAR-Z17/15

## Slide 19: Qubit Readout
Performance of 1-Bit readout
500 ns Sampling Time
  138 µV RMS @ 20 pF
  318 µV RMS @ 0,2 pF
43] J.Buehler et al., "Scalable integrated readout of semiconductor quantum dots using current biasinG", Global Physics Summit 2026
https://summit.aps.org/smt/2026/events/MAR-Z17/15
Power:
  Digital Power: 8.5 µW
  Analog Power: 115 µW

## Slide 20: Integrated RISC-V
Rapid Prototyping Platform for Integrated Circuits for Quantum Computing
[5] J. Mair et al., "Rapid Prototyping Platform for Integrated Circuits for Quantum Computing," 2024 20th International Conference on Synthesis, Modeling, Analysis and Simulation Methods and Applications to Circuit Design (SMACD), Volos, Greece, 2024, pp. 1-4, doi: 10.1109/SMACD61181.2024.10745395.
RISC-V with SRAM and APB
Enables flexibility in control (algorithms)
Leakage negligible at cryo
Notes: 32-Bit RISCV with 3 Pipeline Stages
2x32kB SRAM (Data and Instructions)
Single Clock Access Over (modified) APB
Area:
700 µm x 300 µm
Gate Count:
19628
Dynamic Power @25°C:
0.13 mW (5MHz, 0.8V)
Leakage Power @25°C:
0.70 mW (0.8V)

## Slide 21: Digital Interface
Write & read IC config regs
Configuration of IC blocks
Comparison of Industry Standard Protocols
Protocol | Pro  | Cons 
UART | 2-wire interface (RX TX) No pull-up/down | Requires sync.
I²C | 2-wire interface (SDA SCL) | Pull-ups
SPI | No pull-up/down | 3[4]-wire interface (SCLK MOSI MISO [CE])
JTAG | No pull-up/down | 4-wire interface (TCK TMS TDI TDO) Complex state-machine
cJTAG | 2-wire interface (TCKC TMSC) | Complex state-machine Less established Optional Pull-ups/downs

## Slide 22: Cryogenic co-integration
Multiple Approaches
Electron Temperature Qubit: ca. 2-3K
Divided Interposer
Electron Temperature Qubit: ca. 0.5-1K
Electron Temperature Qubit: < 0.4K
Copper
PCB Material
Interposer
IC
Qubit
Copper
Interposer
IC
Qubit
Interposer
Copper
IC
Qubit
[6] L. Schreckenberg et al., "SiGe Qubit Biasing with a Cryogenic CMOS DAC at mK Temperature," ESSCIRC 2023
IC and Qubit:
Direct Copper
IC and Qubit:
Same Interposer
IC and Qubit:
Two Interposer

## Slide 23: Cryogenic co-integration
Ultra-low Leakage Currents
Bias DAC cycling through 7 metal electrodes
    SET used as measurement amplifier
    Visible cross-talk depending on location
Leakage rates on metal electrodes meas.
    2 pF on-chip cap.; ca. 300 fF off-chip cap.
    Ultra-low voltage drift of <1 µV/s
Cryo Bias-DAC
RT DAC
[6] L. Schreckenberg et al., "SiGe Qubit Biasing with a Cryogenic CMOS DAC at mK Temperature," ESSCIRC 2023

## Slide 24: Cryogenic co-integration
Qubit DC Biasing
[3]
Cryo setup
at mK stage
Charge sensing of single and double quantum dot
[6]
[5]
[7] P. Vliex et al., "Bias Voltage DAC Operating at Cryogenic Temperatures for Solid-State Qubit Applications," IEEE Solid-State Circuits Letters, 2020
[6] L. Schreckenberg et al., "SiGe Qubit Biasing with a Cryogenic CMOS DAC at mK Temperature," ESSCIRC 2023
Co-integration bias DAC with Si / SiGe qubit

## Slide 25: Cryogenic Measurements
Inputs for a Cryo-PDK for 22 nm CMOS
Analyzer
Transistor Arrays
60 K Stage
300 K Stage
ID [a.u.]
7 K
7 K
Input Data for BSIM-IMG Based Modeling
done by AdMOS GmbH
Cryogenic Model Library
Short-Channel I-V-Curves [8]
DUT
[8] Chava, Phanish, et al. "Evaluation of cryogenic models for FDSOI CMOS transistors." 16th IEEE Workshop on Low Temperature electronics. No. FZJ-2024-05369. Zentralinstitut für Elektronik, 2024.
The QSolid project acknowledges the support of the Federal Ministry of Education and Research (BMBF) within the framework programme “Quantum technologies – from basic research to market” (Grant No. 13N16149).
Setup @ ICA | FZJ: Tmin ~ 7 K

## Slide 26: Qsolid – Photonic link
Optical Data and Power Link to Cryo
Passive optical photodiode link as alternative approach
  Significantly improved bandwidth & dark currents at cryo
  Purely passive operation, no bias needed
  Power and data communication envisioned
Measurement with SC Qubit in Munich ongoing
[9] S.Mutum, et. Al, "A Photonic Link at 4.7K with >1 GHz bandwidth towards an Optical Quantum Computing Interface", IEEE MTT-S International Microwave Symposium (IMS) 15-20 June 2025, Moscone Center, San Francisco, CA
The QSolid project acknowledges the support of the Federal Ministry of Education and Research (BMBF) within the framework programme “Quantum technologies – from basic research to market” (Grant No. 13N16149).

## Slide 27: Summary
Cryo-CMOS readout shown with current and voltage biasing.
DC qubit biasing demonstrated in 22 nm and 65 nm, at cryo and with qubits
System Modeling
Cryo Measurement
Cryogenic IC Design
System Engineering
Cryogenic Pitfalls:
  Hidden IP power
  Cryo model shifts
  Ground loops in the cryostat
  Steep subthreshold slope
  Thermal anchoring

## Slide 28: Follow Us!
Jobs & Social Media Accounts @ ICA
www.threads.com/@fzj_ica
www.ica.fz-juelich.de
www.linkedin.com/showcase/ica-pgi4
https://social.fz-juelich.de/@fzj_ica
Threads:
Current Vacancies:
LinkedIn:
Mastodon:

## Slide 29: References
[1] H. Banba et al. “A CMOS bandgap reference circuit with sub-1-V operation”. In: IEEE Journal of Solid-State Circuits 34.5 (May 1999), pp. 670–674. doi: 10.1109/4.760378.
[2] A. R. Cabrera-Galicia, et.al, "Voltage Reference and Voltage Regulator for the Cryogenic Performance Evaluation of the 22nm FDSOI Technology," in IEEE Open Journal of Circuits and Systems, vol. 5, pp. 377-386, 2024, doi: 10.1109/OJCAS.2024.3466395
[3] J.Buehler et al., "QUOCCA.SET: A Scalable Readout IC for Semiconductor Quantum Dots", Global Physics Summit 2025, MAR-G19/4
[4] J.Buehler et al., "Scalable integrated readout of semiconductor quantum dots using current biasinG", Global Physics Summit 2026 https://summit.aps.org/smt/2026/events/MAR-Z17/15
[5] J. Mair et al., "Rapid Prototyping Platform for Integrated Circuits for Quantum Computing," 2024 20th International Conference on Synthesis, Modeling, Analysis and Simulation Methods and Applications to Circuit Design (SMACD), Volos, Greece, 2024, pp. 1-4, doi: 10.1109/SMACD61181.2024.10745395.
[6] L. Schreckenberg et al., "SiGe Qubit Biasing with a Cryogenic CMOS DAC at mK Temperature," ESSCIRC 2023
[7] P. Vliex et al., "Bias Voltage DAC Operating at Cryogenic Temperatures for Solid-State Qubit Applications," IEEE Solid-State Circuits Letters, 2020
[8] Chava, Phanish, et al. "Evaluation of cryogenic models for FDSOI CMOS transistors." 16th IEEE Workshop on Low Temperature electronics. No. FZJ-2024-05369. Zentralinstitut für Elektronik, 2024.
[9] S.Mutum, et. Al, "A Photonic Link at 4.7K with >1 GHz bandwidth towards an Optical Quantum Computing Interface", IEEE MTT-S International Microwave Symposium (IMS) 15-20 June 2025, Moscone Center, San Francisco, CA
[10] Kammerloher, E. (2022) Improving the output signal of charge readout for quantum computing in electrostatically defined quantum dots with a new sensing dot concept. Dissertation/PhD thesis. Aachen: RWTH Aachen University. DOI: 10.18154/RWTH-2022-01567.

## Slide 30: New Spin-Off:
IceCirc is a spin-off of the Institute for Integrated Computing Architectures at Research Center Jülich which:
Has 10 years of experience in cryogenic IC design
Employs state of the art semiconductor technology
Has demonstrated integration of cryogenic electronics with qubits
Provides electronic design service for cryogenic integrated electronics
Visit us at icecirc.com