## Slide 1: LArPix & LightPix Scalable, cryogenic-compatible pixelated readout for noble liquid detectors
Brooke Russell on behalf of the LArPix and LightPix Teams
XIII Front-End Electronics Workshop
May 22, 2026

## Slide 2: Outline
LArPix
  DUNE NDLAr Implementation
  Prospective DUNE Far Detector
LightPix
  Scale-able cryo-compatible SiPM readout

## Slide 3: Outline
LArPix
  DUNE NDLAr Implementation
  Prospective DUNE Far Detector
LightPix
  Scale-able cryo-compatible SiPM readout

## Slide 4: Deep Underground Neutrino Experiment (DUNE)
1.2 MW (upgradeable to 2.4 MW) LBNF (anti-)neutrino beam
LArTPC charge signal:
inherently slow & sparse
millimeter-scale charged particle tracking
O(100) keV charge signal threshold

## Slide 5: DUNE Far Detectors 1 & 2
Wire and strip continuous readout with in-situ cryogenic readout electronics
LArASIC front-end amplifier
==> See next talk on CHARMS by P. Mukim
ColdADC digitization
COLDATA manage data & fast commands-
DUNE FD will collect ~30 neutrino interactions per week
Time
Channel

## Slide 6: DUNE LAr Near Detector
Anticipate O(100) interactions per 10µs beam spill
70 optically-segmented LArTPCs with pixelated readout charge sensing in NDLAr
200 m2 active anode area
224k LArPix ASICs
  14.3M channels at 3.7 mm pixel pitch
DUNE ND will collect ~1.5 million neutrino interactions per week

## Slide 7: LArPix Evolution
LArPix-v1, 2016-2018
LArPix-v2, 2019-2024
LArPix-v3, 2025-
32 channel inputs
275 e- ENC @ 87K
O(103) channel readout via 2 wires demonstrated technical feasibility
O(105) channel prototypes demonstrated industry-produced, scalable system architecture
64 channel inputs
>10k digital multiplexing
800 e- ENC @ 87K
Improved data integrity (v3c)
350 e- ENC @ 87K
Differential buffer (v3c)
Differential, asynchronous 10-bit ADC (v3a)

## Slide 8: LArPix-v3 ASIC Overview
Specification | Value
Analog Inputs | 64
Gain | 3.4 µV/e-
Noise | 350 ENC
Power | <170 µW/channel
Dynamic Range | 340 ke-
AFE Settling Time | <200 ns
Minimum Resampling Time | 1.4 µs
Timestamp Precision | 100 ns
Linearity | 0.9%
ADC Resolution | 10 bits
Operating Temperature | 77 K to 300 K
Cryo-compatible, low-power mixed-signal ASIC (TSMC 130 nm) designed for pixelated, true 3D readout of LArTPC detectors
Continuous self-triggered pixelated free streaming readout, ~100% uptime
Principal component of the end-to-end LArPix readout system: $0.10/channel ($10k/m2)

## Slide 9: LArPix Analog Front-End
5.4mm
64-channel SoC, in 130nm
Front-end Amplifier
SAR Digitizer
Self-triggering Discriminator
Charge sensing: per-pixel integrating amplifier with self-triggered digitization and readout

## Slide 10: Asynchronous 10-bit SAR ADC
  Differential design with bi-directional switching, reduces area and power
  Asynchronous logic: internally-generated clock speeds ADC conversion
DNL <1 LSB
INL <1.6 LSB
(512 is a missing code attributed to a layout artifact)
Design and implementation by Panos Zarkos (LBNL)

## Slide 11: Triggering Schemes
Self-trigger reset (nominal operating mode): digitize and drain charge after threshold crossed
Cross-trigger reset: digitize and drain sub-threshold charge based on self-trigger of another pixel
External-trigger reset: digitize and drain sub-threshold charge based on external signal
Periodic-trigger reset: periodically digitize and drain sub-threshold charge at fixed cadence on a channel rolling or chip-synchronous basis
Optional burst modes
  Fixed burst: process N hit cycles for each self-trigger
  ADC threshold: continue to process hit cycle until an ADC dataword ceiling (or floor) is exceeded
  ADC settle: continue to process hit cycles until change in ADC value is below set value
ADC settle triggering scheme
MIP track ~parallel to anode

## Slide 12: Reset Schemes
Front-end periodic reset at a configurable cadence on a channel rolling or chip-synchronous basis
  Highly effective in mitigating detector environment noise
    Microphonics
    Cryocooler power cycling
  Long-range induction mitigation
100 ns AFE deadtime incurred with each reset
Reset at 2.4 Hz
Reset at 2.4 kHz
Pixel pedestal RMS (50k channels)

## Slide 13: Operating Thresholds
Channel thresholds are highly configurable
  Ability to dynamically set/change thresholds during operation
Investigating channel reset-induced pickup
  Results in spurious triggers at ~3000 e- threshold level
Digital reset signal
AFE monitor output
PRELIMINARY

## Slide 14: Analog Front-End
Known bug in management of memory buffer causes few percent data loss
Key design changes:
Super source follower front-end buffer
Asynchronous 10-bit SAR ADC
Correlated-double sampling
Performance benchmarked in small-scale LArTPC

## Slide 15: LArPix Digital Back-End
5.4mm
64-channel SoC, in 130nm
Digital control: data aggregation, amplifier configuration, inter-chip communication
Data transmitted on every rising clock edge (10 Mbit at 10 MHz CLK)

## Slide 16: Digital I/O
Custom tunable low-voltage digital transmitter and receiver
Similar to LVDS in concept, but much lower power: O(10 µW) per transmitter & receiver
Highly-tunable loop current and termination resistance supports multiple modes of operation (chip-to-chip, chip-to-controller)
Optional mode for automatic transmitter power-down when no data
off-tile I/O

## Slide 17: Hydra I/O
Example failed chip
Example 5x5 pixel tile network
Each ASIC capable of configurable I/O in any cardinal direction
I/O can occur between any neighboring chips on pixel tile
ASIC network constructed by explicit configurable connection between neighboring ASICs in a determined fashion

## Slide 18: Power
Power dissipation is reduced with:
Low voltage supplies (VDDA 2.2 V, VDDD 1.2 V)
Low data rates
  Channel power is lowered by avoiding digitization and readout of mostly quiescent data
Minimizing the number of active components in the cryogenic environment
Use a standard TQFP128-EP package
==> ground pad serves as a heat sink to aid thermalization and mitigate localized heat density

## Slide 19
Robotic chip testing @ Caltech
6457 LArPix-v3 ASICs screening:
94.7% good
2.6% fail due to high noise/leakage
2.7% fail due to I/O fail (includes DOA)
<<1% fail due to bit flips
900 chips/day testing throughput with 1 robot
ASIC Yield

## Slide 20
To reach O(108) pixel system scale, need to reduce the number of cables/feedthroughs
  Aggregate data I/O from multiple pixels to reach O(105) pixels per data channel
MADCAP (multiplexer ASIC for data and clock aggregation) in development as a cryo-compatible digital multiplexer
  130 nm TSCM MPW tapeout next month
Prospective DUNE Far Detector

## Slide 21: Outline
LArPix
  DUNE NDLAr Implementation
  Prospective DUNE Far Detector
LightPix
  Scale-able cryo-compatible SiPM readout
LightPix-v1 readout system for GHe applications at UC Berkeley: 50x 3 mm by 3 mm VUV SiPMs with single cable power, I/O

## Slide 22: Motivation
Traditional tradeoff for SiPM-based applications requiring high photocoverage: sacrifice spatial resolution for collection efficiency
Design considerations driving multiplexing requirements:
Cost
Power dissipation
Technical need for scalabe (high collection efficiency, high channel count), low-power SiPM readout without ganging signals and operating 77 K to 300 K
Example of direct SiPM detector format from DarkSide-20k prototype
Example of large area light trap with X-ARAPUCA

## Slide 23: SiPM Dark Counts on LArPix-v2 AFE
23
1 PE
2 PE
3PE

## Slide 24: LightPix-v1
Unique channel input for each SiPM
A single photoelectron discriminator with a TDC for fine-timing
Designed for very-high-channel-count systems with low occupancy, where the typical number of photons per channel is less than one
  Calorimetry and pulse-shape discrimination achieved through the aggregate distribution of photon arrival times across many SiPMs
"LightPix-mode": tuneable multi-channel coincidence triggering mode to suppress excess data from dark noise
  1-64 channels over threshold in 100 ns to 13 µs window
LightPix-v1 produced in
180 nm TSCM

## Slide 25: LightPix-v1 Performance
TDC evaluation for O(1) PE inputs:
  TDC linear to <10% within 10 ns of ramp generator start
  < 1 ns jitter
  < 2 ns time-walk bias
  <1 ns RMS global timing accuracy
Dark count suppression logic validated

## Slide 26
Proof of concept for joint charge/light readout with direct VUV light detection in LArTPC
SiPM PCB attaches directly to LArPix anode tile
Single PACMAN controller, two shared data/power cables
16 HPK Direct VUV 3mm x 3 mm SiPMs
LArPix-LightPix Dual TPC Readout

## Slide 27: LightPix TPC Performance
Issue: significant cross-talk from LArPix-v2a single-ended I/O
Per-event timing correlations slewed by pickup from single-ended clock & digital I/O

## Slide 28: LightPix-v3
Design changes relative to version 1:
Replaced CSA with TIA optimized for larger SiPM capacitance (6 mm x 6 mm or larger)
Added ADC in parallel with TDC for use in higher-occupancy detectors
Fully differential, low-swing clock and digital I/O
32 "super channels" with sub-ns timing +multi-PE calorimetry
LightPix-v3 produced in
180 nm TSCM

## Slide 29: LightPix-v3 TDC
TDC resolution and linearity < 1 ns

## Slide 30
Demonstrated multi-PE discrimination and single-PE self-trigger efficiency
Flexible application:
Channel threshold tunability for single-channel dark count rejection
Chip-level dark count rejection
Initial studies (without optimization) demonstrate ~20 PE dynamic range
Adjusted channel trigger threshold
LightPix-v3 ADC
Triggers (area normalized)
ADC word

## Slide 31: Summary & Outlook
LArPix has demonstrated continuous self-triggered pixelated free streaming readout at the O(105) channel scale
  Targeted improvements to be incorporated into the next ASIC tapeout (v3c in Summer '26)
    Fully-differential front-end buffer
    Remediate data loss from FIFO event contention
    Remediate reset correlated front-end pickup
  Further system channel scaling requires implementation and system integration of a digital multiplexer (MADCAP)
LightPix is a low-power, cryo-compatible, scale-able readout ASIC for targeting a general multipurpose, high-channel-count SiPM systems
  Multiple development threads in progress:
    LightPix+SiPM timing-energy correlation evaluation in progress
    LightPix-specific system controller architecture
    In-situ detector format implementation