## Slide 1: Microelectronics at IRFU Saclay
Olivier Gevin

## Slide 2
Microelectronics Lab at Saclay
  Fields of application, technical and human resources
Domain of expertise
  Muti-channel for particle detectors, radiation hard, low noise…
Families of ASICs
  Preamp-shaper, TDC, CRASICs, MAPS…

## Slide 3
Technical divisions
Biology, Chemistery, Energy, health, physics, nano sciences, Instruments and technology, climate and environment. (6000)
Fundamental research
IRFU
DIS
DACM
DEDIP
DPhP
DPhN
DAp
9 other labs
STREAM
Detectors, Computing, Electronics
J. Bobin(~150)
Real time and Mircroelectronics
Lab, O. Gevin (18)
All the skills to think, build, and operate a complete instrument
  Centre de Saclay
  25 km from Paris
  7000 people.
Physics divisions
Astrophysics, High Energy Physics, Nuclear Physics and associated instrumentations Institute
F Sabatié(675)
GANIL
French Alternative and Atomic Energy Commision (CEA)
Defense and security, low carbon energies, technological research for industry, fundamental research in the physical sciences and life sciences. (17000 permanent people)
Mechanical engineering
Heavy ion accelerator at CAEN
Accelerators and cryogeny and magnetism
Particle Physics
Nuclear Physics
Astrophysics
and Instrumentation

## Slide 4: Design Lab
Microelectronics Lab was created in the 90’s for LHC
First designs in the radhard DMILL 0.8 µm homemade technology. Initially for CERN: the HAMAC analog memory sampler chip in 1998. But rapidly also for Space Applications
Today: team of 12 designers
  6 analog and mixed-signal designers
  4 digital & verif designers (DoT, UVM)
  2 analog designers for CRASICs (cryo ASICs down to 50 mK)
Talk on chip for Space
Talk on Chip for EIC

## Slide 5
Wire bonding Machines (wedge)
Bonding machine for ATLAS ITK
Microscope with chip/wafer probing
Climatic chamber
2 Mass production test facilities (here for Coluta ADC validation)
MATIS: Multi-ASIC test setup
Multi domain power supply
domain Latchup analyser
COCASE: low dose rate 60CO source irradiation facility
PAGURE: medium dose rate 60CO source irradiation facility
Cryostat: 50 mK stage
Microelectronics lab as part of SACLAY site benefits from several local platforms and testing facilities for :
Packaging : semi-automatic wire bonding machine for prototyping and production packaging
Testing: Multi-ASIC Testing setup (MATIS), automatic testing machines for mass production characterization
Cooling: Climatic chamber and cryostat
Irradiadiation : 60Co at COCASE(1.5=>1500 rad/h for space qualification) and at PAGURE (3k=>50krad/h)

## Slide 6
Microelectronics: domain of expertise
Scaled Charge Sensitive Amplifiers
      Patented architecture
      Optimized for detectors from 300 fF to 1nF
      Dynamic range from 1 fC to 50 pC, both polarities
Trans Impedance Amplifier
Very low input impedance
Dynamic range of few mA.
Tunable shapers
      Peaking time from 25 ns to 15 µs
      Versatile: lots of programmable values
Analog memories/digitizers
      Ultra fast low depth (200ps, 64 cells)
      Fast-high depth (0.5-10ns, 512-1024 cells)
TDC
25ps online,
      5ps offline (DLL + pulse replicator or sampling)
ADC
      // Boosted-Wilkinson: 1 MHz, 12 bits, 32 channel
      Pipeline: 20 MHz, 12 bits
      SAR-TDC hybrid, 50MHz, 12 bits
Radiation hard Services
      Low jitter PLL, TMR-I2C, DACs, T°@TID probes, Fast Drivers...
Multi-channel (2-72)
Radiation hard (TID, SEU, Latchup)
CATIA for CMS
IDeF-X for Solar Orbiter
MONACAL for CMS
DREAM for CLAS12 (Jlab)
NECTAR for CTA
SAMPIC
OWB1
DRD7
IDeF-X for SVOM (ESA)
We design ASICs for Particle Physics, Nuclear Physics and Astrophysics and for some exotic applications (medical, beam diagnostic, homeland security…).
99% of our ASICs are multi-channel ASICs to read particle detectors
Almost all of our ASIC architectures consist of a set of modules and can be represented by this generic diagram:
In HGCROC for CMS

## Slide 7
Monolithic Active Pixel Sensor (MAPS)
      HV, Hres, gain layer
      Tracker, timing
CRASICs (Cryogenic ASICs)
Very low power
FE for bolometers, amplifiers, MUX circuits
Digital
Serializer, SPI, I2C ...
CACTUS for timing
ECLIPSE for SPICA (ESA)
We design ASICs for Particle Physics, Nuclear Physics and Astrophysics and for some exotic applications (medical, beam diagnostic…).
99% of our ASICs are multi-channel ASICs to read particle detectors
Almost all of our ASIC architectures consist of a set of modules and can be represented by this generic diagram:
Multi-channel (2-72)
Radiation hard (TID, SEU, Latchup)
Microelectronics: domain of expertise

## Slide 8
CHIPNAME(collaboration) (Experiment)
Collaboration
Under test
Prod
Technologies
DMILL 800
AMS 350 SiGe
AMS 350
AMS 180
X-FAB 180
Tower Jazz 180
Lfoundry 150
TSMC 130
TSMC 65nm
Roadmap: too many technologies, more and more collaborations
Still used

## Slide 9
Some of our ASIC families
  Low noise front-ends for low capacitor detectors for space
  Multichannel space-proof ASICs made of Charge Sensitive Amplifier + Shapers
  Typical architecture: IDeF-X HD
  Different flavors
    Analog output readout: Mux or //
    Geometry: 1D or 2D
    Anode, cathode or both electrodes readout optimized
    Technology: all CMOS (AMS 0.35, AMS 0.18, XFAB 0.18)
  Typical applications
  Readout of Cd(Zn)Te and Si detectors for space applications
IDeF-X ECLAIRs with CdTe from ACRORAD. ECLAIRs, SVOM mission. Launched in 2024
IDeF-X HD in CALISTE spectro-imager Solar Orbiter mission launched in 2020

## Slide 10
Some of our ASIC families
  Low noise front-ends for low capacitor detectors for space
  Multichannel space-proof ASICs made of Charge Sensitive Amplifier + Shapers
  Typical architecture: IDeF-X HD
  Different flavors:
    Analog output readout: Mux or //
    Geometry: 1D or 2D
    Anode, cathode or both electrodes readout optimized
    Technology: all CMOS (AMS 0.35, AMS 0.18, XFAB 0.18)
  Typical applications:
  Readout of Cd(Zn)Te and Si detectors for space applications:
IDeF-X ECLAIRs with CdTe from ACRORAD. ECLAIRs, SVOM mission. Launched in 2024
IDeF-X HD in CALISTE spectro-imager Solar Orbiter mission launched in 2020

## Slide 11
Some of our ASIC families
  Fast analog memories (high speed photodetectors)
  Single or Multi-channel analog memories with or without ADC.
  Based on the patented circular analog memories made of sampling capacitor array (SCA):
  Different flavors
    Output format: analog or digital (ADC included)
    Depth of the memory (64 to 1024)
    Sampling frequency (400M-10GHz)
    Readout frequency: 100 MHz/sample max
    Dead time free
    Technology: all CMOS (DMILL, AMS 0.8, AMS 0.35, AMS 0.18)
  Typical applications
  Readout of fast detectors, generic sampler
NECTAR for the CTA telescope
SAMPIC, Picosecond multi-channel
TDC (collaboration IN2P3)
MATACQ (heart
of the Caen V1729)

## Slide 12
Some of our ASIC families
  FE-SCA type ASIC: designed for gaseous detectors and semi-conductor detector for high dynamic range.
Typical architecture
  Multi-channel architecture with, for each channel:
  CSA (multi-gain) + Filter (multi peaking time) + Sampling Capacitor Array (analog memory)
  This architecture memorizes for each event (validated by internal or external trigger) the waveform of the output of the filter:
  Different flavors
    Dynamic range (10 pC max)
    Peaking time range (50ns-8µs)
    Scaling for detectors
    External/internal trigger
    Dead time
    Technology: all CMOS (AMS 350, TSMC 65)
  Typical applications
  Readout of gaseous detectors and silicon detectors for trackers or TPCs
AFTER ASIC for T2K
DREAM ASIC for CLAS12 at JLAB

## Slide 13
Some of our ASIC families
  FE-SCA type ASIC: designed for gaseous detectors and semi-conductor detector for high dynamic range.
Typical architecture
  Multi-channel architecture with, for each channel:
  CSA (multi-gain) + Filter (multi peaking time) + Sampling Capacitor Array (analog memory)
  This architecture memorizes for each event (validated by internal or external trigger) the waveform of the output of the filter.
  Now replaced by :
  CSA (multi-gain) + Filter (multi peaking time) + Sampling Capacitor Array (analog memory) ADC + DSP and streaming readout
  Different flavors
    Dynamic range (10 pC max)
    Peaking time range (50ns-8µs)
    Scaling for detectors
    External/internal trigger
    Dead time
    Technology: all CMOS (AMS 350, TSMC 65)
  Typical applications
  Readout of gaseous detectors and silicon detectors for trackers or TPCs
AFTER ASIC for T2K
DREAM ASIC for CLAS12 at JLAB
SALSA for EIC

## Slide 14
Some of our ASIC families
  FE-SCA type ASIC: designed for gaseous detectors and semi-conductor detector for high dynamic range.
Typical architecture
  Multi-channel architecture with, for each channel:
  CSA (multi-gain) + Filter (multi peaking time) + Sampling Capacitor Array (analog memory)
  This architecture memorizes for each event (validated by internal or external trigger) the waveform of the output of the filter.
  Now replaced by :
  CSA (multi-gain) + Filter (multi peaking time) + Sampling Capacitor Array (analog memory) ADC + DSP and streaming readout
  Different flavors
    Dynamic range (10 pC max)
    Peaking time range (50ns-8µs)
    Scaling for detectors
    External/internal trigger
    Dead time
    Technology: all CMOS (AMS 350, TSMC 65)
  Typical applications
  Readout of gaseous detectors and silicon detectors for trackers or TPCs
AFTER ASIC for T2K
DREAM ASIC for CLAS12 at JLAB
SALSA for EIC

## Slide 15
Some of our ASIC families
  Monolithic Active Pixel Sensors
Typical architecture
  The ASIC is the detector and the readout. Based on (almost) the same technologies as for visible imaging but readout optimized for particle tracking.
  High scale matrix (Mpixel) with single conversion stages and digital output
  Source follower or Charge (filtering) preamplifier + Discriminator
Participation to ALPIDE chip with CERN for the Muon Forward Tracker in ALICE experiment
  Different flavors
    Size of the pixel from 30 x 30 µm2 to 1 mm2
    Technology node (AMS350, TJ180, LF150)
    Technology option: Hres, HV, gain layer
    Event buffers
    In-pixel or column discrimination
    Technology: all CMOS (AMS 350, TSMC 65)
  Typical applications
  Trackers, timing. Us today: LHCB and Cactus
  CACTUS, HV MAPS for timing LF 150nm, 50 ps rms (FEE 2018, Degerli)
IRFU Designs
Analog DAC
Readout Management
Power On Reset
Monitoring ADC

## Slide 16
Some of our ASIC families
  And many other chips
  CATIA for CMS BCAL
  TSMC 130nm, 80K produced and almost tested for HLLHC (FEE 2023, Guilloux)
  SAMPIC 16-channel TDC
  AMS 180nm, 5ps waveform tdc (FEE 2014, Gevin)
  TOA and ToT of HGCROC
  TSMC 130nm, 100K produced and almost tested for HLLHC (FEE 2023, Bouyjou)
  LF-MONOPIX proto for ATLAS, MAPS for tracking LF150nm, (FEE 2018, Hemperek)

## Slide 17
Today at Saclay
  Design of the SALSA2 chip for ePiC MPGD detectors for the Electron Ion Collider (TSMC65) : talk on Tuesday
  Design of the RADPIX maps for LHCB tracker (LF150)
  Design of the CESAR ASIC for spectro imaging modules with CdTe detectors (XFAB180) : talk on Friday
  Design of the tdc of EICROC for AC-LGAD detectors for ePIC (TSMC130)
  Design of CRASICs (AMS350) for space applications