## Slide 1: Analysis of 3He neutron proportional counter spectrum taken in potential PAUL site
Gaël Poussot-Pelaez

## Slide 2: Overview
Analyse Helium-3 neutron proportional counter spectrum determine neutron spectrum in the underground site
  Particular interest in fast neutrons.
Use PHITS (Particle and Heavy Ion Transport code System) to model the detector response for monoenergetic neutrons.
Fit a linear combination of these spectra to approximate the neutron spectrum incident on the detector.
Compare to literature on underground neutron spectra.

## Slide 3: Literature review
V. Chazal et al. (1999) , “Neutron background measurements in the underground laboratory of Modane”
Lithium-6 doped liquid scintillator

## Slide 4: Literature review
Joong Hyun Kim et al. (2026) – “Neutron spectrum measurement in the Yemi underground laboratory”
10 He-3 proportional counters with different levels of shielding

## Slide 5: Detector
2 dominant reactions between neutrons and 3He:
  Capture: 3He + n 3H + p + 764 keV
    191 keV taken by 3H, 573 keV taken by p
  Elastic scattering

## Slide 6
_
_
Elastic scattering cross section
Neutron capture cross section
Overlap ~ 100 keV

## Slide 7: Detector
Stainless steel tube containing Helium-3 + an unknown percentage of a gas at 4 bar.
  likely to be CH4 + Ar, higher proportion of CH4 than Ar
  Total unknown gas < 10% of total
Neutron captured by 3He, proton and tritium ionise gas.
Electrons drift to anode, avalanche of electrons where number of electrons proportional to energy of proton+tritium
45cm
2.5cm

## Slide 8: Measured spectrum – taken over ~1 month
Peak > 764 keV
Saturation
Electric noise + gamma background
Partial energy deposition of fragments
Elastic scattering + some high energy captures

## Slide 9: PHITS simulations
Goal: deduce the neutron spectrum incident on the detector from the measured spectrum
Method:
  Simulate the response of the detector using PHITS for many monoenergetic sources
  Fit a linear combination of these monoenergetic spectra to the measured spectrum
  Estimate the incident neutron spectrum based on the coefficients of the linear combination

## Slide 10: PHITS simulations
Isotropic source of neutrons – cylindrical / cuboidal
10e8 neutrons simulated for each spectrum
Collection of charges is not simulated
Simulations of 3 different gases:
  3He + 7% CH4 + 3% Ar
  3He + 8% CH4 + 2% Ar
  3He + 9% CH4 + 1% Ar
Steel tube
Gas mixture

## Slide 11: PHITS simulations
For energies between 10 meV - 0.1 MeV, simulations run for 10 meV, 100 meV, 1eV, 10 eV…, 0.1 MeV
For energies between 0.2-10 MeV: one simulation every 200 keV.
Compromise between time of simulation and statistical fluctuation in spectra.

## Slide 12: PHITS Simulations
Spectrum from simulation of 10 meV neutrons
~100% of contributions are neutron captures
Detector resolution simulated in PHITS
764 keV
573 keV, tritium no deposition
191 keV, proton no deposition

## Slide 13: PHITS Simulations
Spectrum from simulation of 100 keV neutrons
Capture and elastic scattering cross sections are approximately equal
864 keV
Elastic scattering

## Slide 14: PHITS Simulations
Spectrum from simulation of 1 MeV neutrons
Elastic scattering cross section > neutron capture
Maximum energy deposited by an elastic scattering event:
= for A = 3
750 keV
1764 keV

## Slide 15: Fitting spectra
Aim is to determine the coefficients defined by:
which minimises the difference of squares: , and where:
is the measured spectrum,
is a matrix of the simulated spectra.
= number of energies = 63
= number of channels = 543

## Slide 16: Fitting spectra
As well as the unknown coefficients, we also don’t know the calibration of channels energies.
To find the correct calibration, first use approximate calibration – guess peak is at 764 keV (only true in the case of 100% thermal neutrons).
Use minimisation algorithm to find the combination of calibration and coefficients which fits best.

## Slide 17: Preliminary results
The best result we have obtained up to now is using 9% CH4 + 1% Ar and a cuboid neutron source
Good fit at low energies and up to channel 400
Problem of energy deposition at high energies
Peak estimated at 782 keV using best calibration

## Slide 18: Preliminary results

## Slide 19: Preliminary results
Spectrum for this fit is reasonable
Shows contribution of thermal and epithermal neutrons
Main fast neutron peak around 3 MeV, similar to Chazal et al. paper.
Approximated incident neutron spectrum

## Slide 20: Next steps
Missing information in saturation – attempt to use the number of neutrons above saturation to add information to fit.
Simulation of 4 tubes together.
Increase bin widths in measured spectrum to remove statistical noise.
Continue exploring different gas mixtures, as this is a significant unknown.
Validate our method of analysis by measuring known spectrum e.g. using Americium-Beryllium source