## Slide 1
Target manufacturing activities at INFN-LNL
J. Esposito, on behalf of INFN- Legnaro National labs (LNL) targets group- juan.esposito@lnl.infn.it
A quick review of techniques focused on different topics
“Target production” for nuclear physics (NP) experiments
“Target production” for applied NP (radioisotopes production)
“Quality Control techniques: nuclear targets characterization ”
Second Meeting on "Targets for Nuclear Physics" within EURO-LABS​
18–19 May 2026 GSI lab, Darmstadt (Germany)

## Slide 2: Target production at LNL Nuclear Physics (NP) studies

## Slide 3: Target production at LNL NP studies
Target production at LNL – Nuclear physics studies
Text
Targets for nuclear physics experiments typically are thin films of isotope-enriched materials obtained by various techniques:
- lamination (few mg/cm2)
- vacuum evaporation (few tens - few hundred µg/cm2)
- Ion beam sputtering
There are different types of fabrication:
• self supporting
• with backing
• strip-targets
sandwich-target
• plunger – target

## Slide 4: Some examples
Text
Self supporting target of C2D4 produced by thermal evaporation (2mg/cm2)
Target of 130Te, thickness 500 µg/cm2, on Au backing of 500 µg/cm2 obtained by thermal evaporation (Thermal-based PVD) in vacuum.
Target production at LNL – Nuclear physics studies
Target of 124Sn, thickness 300 µg /cm2, on C backing of 20 µg/cm2 and C shield of 15 µg/cm2.
Very fragile film; difficult to peel away from the glass substrate
Adhesion improved by special heat treatment on the Au backing
(Sandwich target – Strip target)

## Slide 5
Text
Target Plunger of 40Ca (800 µg/cm2), on Au 4 mg/cm2 and Au shield of 150 µg cm2. Chemical reduction and simultaneous evaporation of calcium metal in vacuum.
Target of 10B, thickness 500 µg/cm2, on Au backing of 4mg/cm2. The Au backing was previously prepared by rolling.
Target production at LNL – Nuclear physics studies
Extremely slow evaporation of Boron using an electron-beam

## Slide 6
Solid target development by PVD magnetron sputtering technology
Target production at LNL – Nuclear physics studies
LUNA 400 kV (LNGS)
Bellotti IBF (LNGS)
HZDR Felsenkeller Laboratory
Solid targets for nuclear physics experiments
High Purity
Enriched compound
Alkali compound

## Slide 7: LNL Sputtering chamber and design
Characteristics:
3 sputtering source (50mm x 140mm)
2 sputtering source (150mm x 230mm)
Active gettering system (porous Ti /Ba/Al)
Optical emission plasma diagnostics for reactive processes (deposition of compound layers
Different power supply technologies: High-power Impulse Magnetron Sputtering (HiPIMS, DC, pulsed-DC, or RF)
2 different sample holder
Target production at LNL – Nuclear physics studies

## Slide 8
TaN 2.8*1018 atoms/cm2 deposited on 7.8*1017 atoms/cm2 of high purity Ta interlayer Tantalum substrate
LUNA solid target development by PVD magnetron sputtering technology
Ta
TiN 2.7*1018 atoms/cm2 deposited Tantalum substrate and Silicon substrate (for EBS analysis)
429 keV 15N resonance scan
of TaN and TiN
278 keV 14N resonance
scan of TaN
After an irradiation of 15 C
Analysis A. Compagnucci
Ti
Production and EBS characterization performed @ LNL (AN2000)
Low energy resonance scan and endurance test performed @ LNGS (LUNA400)
Target production at LNL – Nuclear physics studies
Targets preparation for LUNA experiments (INFN Gran Sasso Laboratory): Nitrides (TanatN, ZrnatN, TinatN)
High-Z metals nitrides for reduction of neutrons production for LUNA-MV
TaN target produced by PVD techniques using 14N enriched gas
EBS analyses

## Slide 9
GM (Sumitomo) cryogenic source (2W @ 4K) – free orientation
4 mm gas cell
Aluminum body to reduce 𝛾-ray absorption and scattering
As modular as possible for portability
Temperature kept constant by a temperature controller feedback
Havar windows 3.8 or 2.5 𝜇m thickness
At 1 bar, 10 K, 4He 3･1020 at/cm2
In seal
Havar
Al-steel
transition
Cut view of the central flange
Y. Peinnaud, P. Rosier, C. Soulet
Target production at LNL – Nuclear physics studies
CTADIR: design, construction and commissioning of the prototype of a 3,4He cryogenic target for direct reactions in inverse kinematics.
Next RIB’s @ SPES have opened the opportunity to perform direct reactions with unstable beams in inverse kinematics.

## Slide 10
CTADIR in-beam commissioning (I)
Commissioning at CN accelerator with 5 MeV protons
Manual filling 4He gas system
Micron S1 detectors in front and back of the target
Cryocooler
Temperature controller
Scattering chamber
Sauron electronics
4He tank
M. Sedlak
Target production at LNL – Nuclear physics studies

## Slide 11: CTADIR in-beam commissioning (II)
5 MeV proton scattering on Havar
3.8 𝜇m windows
Test at different He gas pressures
Temperature kept at 12 K to limit density
Proton energy spread behavior on 4He gas target compatible with thickness of few 1020 at/cm2
The peak at higher energy represents the protons scattered on the Havar® foil window at the exit of the target. The peak with lower energy is due to protons scattered on the 4He gas filling the target.
Experimental data
Scattering on He
Scattering on Havar
M. Sedlak
Target production at LNL – Nuclear physics studies
GEANT 4 calcs

## Slide 12: CTADIR performances
Cool down in about 80 minutes
Significant de-icing already at 40 K:
de-icing procedure feasible in 2 hours
(including gas removal/refilling)
Gamma-ray transparency greatly enhanced compared to Hector, thanks to lower material budget and Al body
M. Sedlak
Target production at LNL – Nuclear physics studies
Exploiting the intense radioactive beams from existing and upcoming ISOL facilities (for instance ISOLDE, TRIUMF, SPES, RAON) the CTADIR target will allow one to perform proton adding (3He,d) and neutron stripping (3He, 4He) reactions around the key doubly-magic nuclei 78Ni and 132Sn combining the AGATA energy resolution with the granularity of GRIT.

## Slide 13: Target production at LNL Applied NP studies (emerging radioisotopes production for thenanostics radiopharmaceuticals)

## Slide 14: Study and production of novel/emerging medical radionuclides feasible at SPES facility
Target production at LNL – Nuclear physics applications
RIFAC
RILAB
ISOL technology
Possible collaboration with multinationals to supply the market needs of RIs
https://web.infn.it/LARAMED/
DIRECT technology
https://isolpharm.pd.infn.it/web/

## Slide 15
Target production at LNL – Nuclear physics applications
Radioisotope of Interest
Dissolution
Extraction/
separation
Purification
Pure radioisotope
Radio-
pharmaceutical
preparation
Target activation
Target recovery
Target
preparation
Radiochemistry
process
Quality Control
Cyclotron irradiation
Nuclear physics studies
Contaminants
Cyclotron production cycle
Fore more details, follow Sara Cisternino’s presentation right after this one.

## Slide 16: Target production at LNL Quality Control (QC) techniques: nuclear targets characterization

## Slide 17
IBA facilities for nuclear target characterization @ LNL
-15° beam line at CN facility [a), b)]
EBS analysis
PIXE analysis
PIGE analysis
0° beam line (m-beam) at AN2000 facility [c)]
EBS analysis
PIXE analysis
60° beam line at AN2000 facility [d)]
EBS analysis
ERDA analysis
quantitative determination of composition
thickness measurements in terms of dose (at/cm2)
depth profiles analysis
non-destructive
High accuracy and resolution
c)
d)
b)
a)
Target characterization at LNL

## Slide 18
IBA facilities for nuclear target characterization @ LNL
Dedicated experiments in nuclear target analysis:
Deposition of Elements on Substrates (DES) involved in NUMEN project
Elastic backscattering spectrometry (EBS)
Characterization of HIVIPP targets for REMIX project (HIX) involved in LARAMED project
Elastic backscattering spectrometry (EBS)
Advances Nuclear Target (ANT)
involved in SALVIA project, LUNA collaboration (target development) and LNL target service (target characterization)
Elastic backscattering spectrometry (EBS)
Nuclear Reaction Analysis (NRA)
particle induced X-ray emission (PIXE)
particle induced -ray emission (PIGE)
Target characterization at LNL

## Slide 19
IBA characterization of nuclear target @ LNL
Target characterization at LNL
Boron contamination reduction using High Purity PVD Tantalum deposited on tantalum backing
Beam induced background reduction
PVD Ta thickness > 2.5mm (Epmax=400keV)
Ta(PVD-LNL)
Ta(acid etched LNL)
Ta(after laser cut)
Ep=680keV, ~13µm Mylar
ΘNRA=150° ; sample tilt=70°
11B(p,α)8Be[2 α]
18O(p,α)15N
=Blue color
SAMPLE TILTED 70°

## Slide 20
Target characterization at LNL
IBA characterization of nuclear target @ LNL
Targets preparation for : 23Na(p,)20Ne experiment (LNGS) Alkali targets produced by PVD technics and contaminants reduction
7Li content (ppm) in different deposition process setup
Sodium Niobate Nuclear Target
Irradiated Target

## Slide 21
TaN 0.8-1.2-2.4*1018 atoms/cm2 deposited on 1.1*1018 atoms/cm2 of high purity Ta interlayer Tantalum substrate
IBA characterization of nuclear target @ LNL
Target characterization at LNL
Targets for : 15N(,g)19F experiment (Felsenkeller Laboratories) TaN target produced by PVD technics using 15N enriched gas
Felsenkeller experimental setup
Irradiated target Ta15N @ HZDR
RBS spectrum a beam 1.6MeV(AN2000)
witness samples
Target degradation under intense He+ beam
Thanks E. Masha

## Slide 22
IBA characterization of nuclear target @ LNL
Target characterization at LNL
Target degradation induced by blistering (intense He+ beam)
-RBS analysis and 2-D maps using AN2000 -beam probe
Thickness evaluation using -RBS 2-D maps

## Slide 23
Massimo Loriggiola
Lorenzo Loriggiola
Matteo Campostrini
Valentino Rigato
Andrea Gottardo
Sara Cisternino
Alisa Kotliarenko
Gaja Piteo (PhD UNIPD)
Stefano Corradetti
me
EURO-LABS WP2.5.2 Collaboration meeting May 18th, 2026 GSI lab, Darmstadt (Germany)
Thank you from target makers group @LNL