## Slide 1: R2D2: a xenon TPC for neutrinoless double beta decay search
F. Piquemal (LP2i Bordeaux - CNRS/IN2P3)
On Behalf of R2D2

## Slide 2: Introduction: physics case
The search of neutrinoless double beta decay (bb0n) is related to the determination of the nature of neutrino.
The determination of the neutrino nature has huge implications in particle physics (generation of neutrino masses) and cosmology (leptogenesis model).

## Slide 3: Introduction: physics case
The observation of bb0n decay requires to have very low background (mostly from natural radioactivity)
Observation of the 2 electrons is mandatory to confirm any signal
Double beta decay
Domain of energy of natural radioactivity
Qbb
Transition energy
Sum of the electron energies (MeV)
Experimental signatures
The emission of the 2 electrons
bb(2n)
bb(0n)
bb(0n)
Sum of electron energies E1 + E2 (MeV)
35 isotopes emitter bb including 136Xe
136Xe  136Ba +
bb (2n)
136Xe  136Ba +
Not yet discovered
Neutrinoless double beta decay bb (0n)

## Slide 4: Next generation requirements
(eV)
Inverted hierarchy
Normal hierarchy
light neutrino exchange process
Limitations:
Background from natural radioactivity in detector materials or surroundings
No identification of 2e-
KamLAND-Zen (800 kg 136Xe)
R2D2 project
Next generation challenges
Ton-scale
Zero background
Next generation objective
      Suppression residual natural radioactivity
      Excellent energy resolution
      Identification of the 2 emitted electrons
Inverted hierarchy
Normal hierarchy

## Slide 5: R2D2 : Radial Detector for rare Decay
Objectives:
Large mass of isotopes
Two electron identification
Excellent energy resolution
Low background
To optimize number of readout channels
High pressure TPC with a single anode
Two possible configurations
Spherical TPC
Cylindrical TPC

## Slide 6: CTPC prototype
The HV was applied to the cathode up to values of 5 kV
Different anodes were tested from wires of 50 mm diameter, to rods of 1.2 and 12 mm diameter.
Operation in ionisation mode.

## Slide 7: Gas purity
Gas purity is a key issue for the operation of the CTPC.
A system based on cold and hot getter was set up granting purities up to few ppb in terms of electronegative impurities such as Oxygen.
However, the purification system limits the operation of the detector at 10 bar.
Development new purification system
Ti spark discharge

## Slide 8: Signal
The reconstructed waveforms are used to extract observables such as the total charge of the event, its duration and the width at half height.
Each observable is associated to a specific feature of the original signal.

## Slide 9: Data analysis
The Qt of selected events (cuts on Dt and Dh) were fitted to establish the energy resolution.
Data for xenon at 3 bar, anode of 1.2 mm diameter, and -3000 V applied to the cathode

## Slide 10: Resolution results
The same procedure was applied filling the detector with different gases (Ar and Xe) at various pressures and with different anode sizes.

## Slide 11: Data selection
The observables were used to select the events, namely the Po or the Rn issued alphas.
Data for xenon at 3 bar, anode of 1.2 mm diameter, and -3000 V applied to the cathode

## Slide 12: Data selection
The observables were used to select the events, namely the Po or the Rn issued alphas.
Data for xenon at 3 bar, anode of 1.2 mm diameter, and -3000 V applied to the cathode

## Slide 13: Data analysis
Measurement of the BiPo decay
Data for argon at 16 bars, anode of 1.2 mm diameter, and -4000 V applied to the cathode

## Slide 14: Simulation of 500 kg prototype
Bragg peak
electron 1
Bragg peak
electron 2
bb Simulated event (Xenon, 40 bars)
Objectives : to demonstrate 2 e- identification by measuring bb(2n) of 136Xe
to demonstrate zero backgound in bb(0n) energy region
Use of 500 kg of natXe (44 kg of 136Xe)
Background simulations
Eur.Phys.J.C 85 (2025) 7, 732

## Slide 15: Simulation of 500 kg prototype

## Slide 16: NEXT STEPS
Readout of the longitudinal position along the anode :
Current pre-amplifier ASIC (Subatech) produced
Electronic card (LP2i Bordeaux) in production
Resistive anode design in progress
Experimental identification of the 2 electrons at high pressure :
Use of e+e- pair creation from 2.6 MeV gamma-rays
Coïncidence with 511 keV anihilation gamma-rays
Purification of gas by Ti spark discharge :
    Setup is in commissioning
    Efficiency to be measured
Low radioactive composite vessel development (pressure and vacuum)
Work with IRT Jules Venre (Nantes), ICMCB and LCTO (Bordeaux)
Choice of the fiber (carbon, Si carbure,…)
Choice of Epoxy
Low radioactive measurements in progress

## Slide 17: Conclusions
The R&D to achieve a composite low radioactivity thin vessel is ongoing with industrial partners.
A “full scale” demonstrator (commercial composite tank, no low radioactivity) to validate the drift over 42 cm is under commissioning.
The simplicity of the detector results on low electric consumption.
The R2D2 R&D demonstated the simple CTPC detector can be used for neutrinoless double beta decay search.
All possible technical issues (gas purification, recirculation etc.) can be solved based on the know-how developed by R2D2 and the existing one in the xenon community.
R2D2 collaboration
France: LP2iB, Subatech, CPPM, IPHC
CZ : IEAP Prague
SK: U. Bratislava
PL: Astrocent
Option for PANDA-X gas detector