## Slide 1: Evolution of underground science in LSM
Laboratoire Souterrain de Modane
From digging to modern experiments

## Slide 2: Laboratoire Souterrain de Modane
Located in Modane,France
Middle of Fréjus tunnel
Part of LPSC; Lab in Grenoble
National facility for underground science
1000 visitors days per year
Wide range of interdisciplinary topics
Astroparticles, nuclear physic, environment, electronics, radioactivity measurement, biology

## Slide 3: Laboratoire Souterrain de Modane
Merger with Laboratoire de Physique Subatomique & Cosmologie (LPSC-IN2P3) in Grenoble
  70 researchers, 90 Engineers & technicians
  Covering fields in particle & nuclear physics, astroparticle and cosmology
LSM now becomes a « national facility » as labelled by the CNRS
  National facility for IN2P3 / CNRS
LSM as a national experimental facility for :
  Fundamental Physics
    Neutrino property determination
    Direct Dark matter search
  Gamma spectrometry measurement
    14 detectors measuring continuously
    Open to geosciences, materials, biology and medecine
      Actually 1000 samples measured per year
    PARTAGe project to automatize measurments
      Increase significantly the scope of the LSM

## Slide 4: Location and access
4 fire-proof doors
Footmen entrance
Tunnel Routier du Fréjus
LSM

## Slide 5: History of LSM
2.10-6 n/cm2.S
4 µ/m2.d
3500m3
400m2
1979 - 1981
1982- 1990
1990- 2000
2000 - ….
Proton decay
Prototypes Experiments
Digging
15Bq/m3 Rn in air
Radonless air 125m3/h 15mBq/m3

## Slide 6: Double beta decay
Double beta decay
DL = 2
n = n Majorana’s neutrino
mn  0
Full electron energy
Measure
< mn >  mass hierarchy
( )-1 = C ( ) M2 <mn>2
C : phase space factor
M : nuclear matrix element
< mn > : effective neutrino mass
bb0n : (A,Z)  (A,Z+2)+2e-
(Qbb ~ MeV)
Q5
bb


## Slide 7: Dark matter search
Theoretical
Measured
Speed
CMB anisotropy
Major physics goal
Direct detection would answer to a lot of question
WIMP candidate is a target for underground detection

## Slide 8: SHIN
Super heavy element with half life >238U
Z=108 targeted with self fission producing >5n
TGV II
Nuclear physics
Super Heavy Element In nature
SHIN (osmium ore surrounded by 3He neutron detectors)

## Slide 9: Low radioactivity constraints
Requirement on material below mBq
Strong pressure on analytical capabilities
Increased number of pieces and longer time
Main measurement performed by gamma ray spectrometry
Constant effort took place in LSM to develop ultra low background germanium
Hosting 22 HPGe by 2020
16 effectively in shield

## Slide 10: High purity germanium
Semi conductor crystal cooled down to 77 K
Sample at room temperature
Sensitive to gammas from 20keV up to 3MeV
Non destructive measurement
Sensitive to muons and cosmic activation
Different detectors adapted to samples shape
Coax
Well
Planar
endcap
sample
crystal
cold finger
Notes: Quick reminder of the basis of a Germanium detector

## Slide 11: Future of measurement at LSM
PARTAGe project
  Combining shields in common walls
Robotisation
Optimisation of measurement time based on the radiopurity objectives

## Slide 12: Shielding in progress

## Slide 13: Germanium facility
Example of detection limits
Mafalda : (our swiss army knife)
Size 150 cc – 43,1%
  Φ 80mm h 31,7mm
Resolution
  122 keV 920 eV
  1,33MeV 1,97keV
  Background
    Integral 1153,5 count/day
    133 c/kg
    Peaks
    46,5 keV 1,49  0,37 c/d [210Pb]
    75 keV 3,6  0,62c/d [Pb]
Nucleide |  | Bq/kg
210Pb | < | 1,58E-02
226Ra | < | 1,27E-03
238U | < | 6,27E-03
228Ra | < | 3,82E-03
228Th | < | 8,66E-04
Silicon wafer measurement
700 000s 650g
Std
Std
536
Shielding
ARCH
limit (Bq)

## Slide 14: Germanium facility
Improving detection limit :
  Imply choices :
Obélix :
Size
  600cc-160%
Background
  95 counts/kg.d
Resolution
  122 keV 1,1 keV
  1,33MeV 2keV
250 mm
200 mm
Nucleide |  | Bq/kg
210Pb |  | NA
226Ra | < | 4,96E-4
238U |  | NA
228Ra | < | 1,78E-03
228Th | < | 4,37E-04
Theoretical sample of 1kg for 500000s
Sample Chamber
This detector can welcome much bigger sample but the low energy gamma are stopped by the dead layer around the detector.

## Slide 15: Nickel measurement
Decay mode | Final state or Decay transition | T1/2, (90% CL) | Previous limits, T1/2
β+EC | g.s. | 1.7×1022 y | 7.0×1020 y (68%CL)*
β+EC | 811 keV | 2.3×1022 y | 4.0×1020 y (68%CL)*
EC/EC | 811 keV | 3.3×1022 y | 4.0×1019 y (90%CL)**
EC/EC | 1675 keV | 3.4×1022 y | 4.0×1019 y (90%CL)**
0νEC/EC resonant | Radiative 1918 keV | 4.1×1022 y | 2.1×1021 y (90%CL)***
*S.I. Vasil'ev et al., JETP Lett. 57 (1993) 631.
**E. Bellotti et al., Lett. Nuovo Cim. 33 (1982) 273.
***B. Lehnert et al., J. Phys. G: Nucl. Part. Phys. 43 (2016) 065201
N.I.Rukhadze (JINR, Dubna)

## Slide 16: Germanium detector
Example of detection limits
Mafalda : (our swiss army knife)
Size 150 cc – 43,1%
  Φ 80mm h 31,7mm
Resolution
  122 keV 920 eV
  1,33MeV 1,97keV
  Background
    Integral 1153,5 count/day
    133 c/kg
    Peaks
    46,5 keV 1,49  0,37 c/d [210Pb]
    75 keV 3,6  0,62c/d [Pb]
Nucleide |  | Bq/kg
210Pb | < | 1,58E-02
226Ra | < | 1,27E-03
238U | < | 6,27E-03
228Ra | < | 3,82E-03
228Th | < | 8,66E-04
Silicon wafer measurement
700 000s 650g
Std
Std
536
Shielding
ARCH
limit (Bq)

## Slide 17: IRSN
Modane
Orsay
anti-cosmic devices
 | 52E | XXL | PPT
Pb (cm) | 20 | 25 | 15
Archeologiocal Pb (cm) | 5,4 | 4 | 6
Background coute rate 30-1600 keV (d-1.kgGe-1) | 245 | 120 | 116

## Slide 18: Analitycal power for interdiciplinarity
Possibility to measure a wide range of nucleides
Used in many environmental datation
137Cs only
1986
137Cs + 241Am
1963
Relative datation
Absolute datation

## Slide 19: Lake survey
210Pb gives the sedimentation rate
Confirmed by artificials nucleides
Allowing to reconstruct the history of a lake without archives
Sabatier et al., 2014, PNAS

## Slide 20: Ice survey
Datation of ice core in antartica
Calibration of radar
Temporal marker for climate change
2 days measure needed in underground lab

## Slide 21: Erosion survey
Sources of sediment in mining catchments of New Caledonia
137Cs
Ø 137Cs
Two main sources of sediment to the main river
Mining tributaries
Non-mining tributaries
Discrimination of contributions of both types of tributaries based on their activities in natural/artificial radionuclides
Quantification using mixing models
Analysis of sediment cores collected in the delta to reconstruct changes in source contributions with time

## Slide 22: Millesime identification
1 Bq/l
Nuclear fallout
Tchernobyl
year /
Margaux 1900 ?

## Slide 23: Biology at LSM
Evolution driven by radiation
Comparison between surface and underground bacteria culture 800 generations harvested

## Slide 24: Stem cell storage
LSM-pasteur institute collaboration
Funded by interdisciplanary mission from CNRS
Allowed to test a stem cell storage shielded from natural radioactivity and terrestrial cosmic rays
Patented solution
Publication in progress
P. ROCHETEAU, G. WAROT, M. CHAPELLIER, M. ZAMPAOLO, F. CHRETIEN et F. PIQUEMAL – Cryopreserved Stem Cells Incur Damages Due to Terrestrial Cosmic Rays Impairing their Integrity Upon Long-Term Storage, Cell Transplantation, 2022.

## Slide 25: Conclusion
Underground labs are designed for large scale fundamental physics
Unique environment find always a use sometimes unforeseen at digging
Leaves room for interdisciplinary program at moderate cost
New fields and discoveries made possible by the access to low level radiation environment