## Slide 1: ALFA
Advanced, Lightweight and Fine-grained Apparatus
for e+e− physics

## Slide 2: History and status
A young project: started from scratch less than one year ago
High-level goal: develop a detector design that will become a proposal for one of the four FCC-ee detectors
  The four detectors should be sufficiently different from each other
Problem-driven approach: optimize performance
Adopt state-of-the-art (… but not futuristic) detector technologies, and technical solutions for system design
Make sure the detector is realistic and affordable
Minimize complexity and M&O cost
  Minimal number of different detector technologies
  Robust detector design, requiring minimal/no maintenance to the extent possible

## Slide 3: The ALFA detector
High-performance all-MAPS Tracker
ARC (Array of RICH Cells)
  Good particle ID over large momentum range
ECAL based on GRAiNITA
  Excellent energy (and position) resolution with a cost-effective technology
Coil for 3T field
  3T not guaranteed for the Z run
  Coil dimensions are reasonable
Dual Readout HCAL in iron
  Best option for hadronic energy resolution
  Iron absorber keeps the overall detector dimension relatively compact
Muon tag
  No need of muon tracking beyond the Tracker
  Simple and cost-effective
N.B. The Luminosity Calorimeter is not shown in this sketch

## Slide 4: The ALFA detector
High-performance all-MAPS Tracker
ARC (Array of RICH Cells)
  Good particle ID over large momentum range
ECAL based on GRAiNITA
  Excellent energy (and position) resolution with a cost-effective technology
Coil for 3T field
  3T not guaranteed for the Z run
  Coil dimensions are reasonable
Dual Readout HCAL in iron
  Best option for hadronic energy resolution
  Iron absorber keeps the overall detector dimension relatively compact
Muon tag
  No need of muon tracking beyond the Tracker
  Simple and cost-effective
N.B. The Luminosity Calorimeter is not shown in this sketch
Work in progress

## Slide 5: The all-MAPS Tracker for the ALFA detector
Is a silicon tracker a meaningful choice for FCC-ee?

## Slide 6: Why MAPS?
Curved MAPS are the compelling choice for the Vertex Detector
  Silicon sensors are needed to cope with the rates
  MAPS enable the smallest pixels, highest precision points
  Rates and radiation levels are not prohibitive (OK for MAPS)
  Curved MAPS with air cooling provide the lowest possible material budget
    Single sensor up to 26 cm long, with stitching
    Thinned down to 50 𝜇m (or even 30 𝜇m)
Under development for the ALICE ITS3

## Slide 7: A full-MAPS Tracker
High-precision points and low mass sensors are good for the whole Tracker
Rates (and radiation levels) are lower in the Outer Tracker
A full-silicon Tracker can be made very robust
  Aim at an Outer Tracker that can work without maintenance
Can it be made sufficiently light?
  Competitive in performance with a gas detector?
Can it be made of reasonable size and cost?
  N.B. Needs to be complemented with a PID detector

## Slide 8: A full-MAPS Tracker
High-precision points and low mass sensors are good for the whole Tracker
Rates (and radiation levels) are lower in the Outer Tracker
A full-silicon Tracker can be made very robust
  Aim at an Outer Tracker that can work without maintenance
Can it be made sufficiently light?
  Competitive in performance with a gas detector?
Can it be made of reasonable size and cost?
  N.B. Needs to be complemented with a PID detector
Need a sufficiently detailed design to answer these questions

## Slide 9: A full-MAPS Tracker
High-precision points and low mass sensors are good for the whole Tracker
Rates (and radiation levels) are lower in the Outer Tracker
A full-silicon Tracker can be made very robust
  Aim at an Outer Tracker that can work without maintenance
Can it be made sufficiently light?
  Competitive in performance with a gas detector?
Can it be made of reasonable size and cost?
  N.B. Needs to be complemented with a PID detector
N.B. There are different flavours of MAPS
The design with small collection electrode
⟶ minimal capacitance
⟶ minimal power density
(and minimal pixel size)
is the flavour needed for an all-MAPS Tracker

## Slide 10: Key ingredients: MAPS
Tentative MAPS specs (inspired by the ALICE developments)
We must have 10 μm pixels everywhere – key ingredient of the ALFA detector concept
How to exploit the low rate in the outer layers?
  Slower front-end
Time resolution of ≲ 1 μs for the VTX layers, with ≲ 40 mW/cm2 of power density
  Target air cooling
Time resolution of ~ 5 μs for the OT layers, with < 20 mW/cm2 of power density
  Lower power density ⟶ lower mass
  A pileup of a few Z decays cannot be a problem with the granularity of ALFA
Continuous triggerless readout ⟶ real-time event reconstruction and filtering
Defining the MAPS specs is a main objective for the next 2-3 years

## Slide 11: Stitched MAPS for VTX layers (conservative geometry)
100 mrad
cos𝜗 = 0.99 (141.5 mrad)
Wafer-size sensor
Two wafer-size sensors for L4
L4 R=32.8 mm
L3 R=26.2 mm
L2 R=19.6 mm
L1 R=13.0 mm
Each sensor covers ½ layer in r𝜑
Beam pipe
R=11.7 mm
231 mm

## Slide 12: Stitched MAPS for VTX layers (“aggressive” geometry – not realistic with current beam pipe)
Wafer-size sensor
Two wafer-size sensors for L5
L5 R=36.2 mm
L4 R=30.1 mm
L3 R=24.0 mm
L2 R=18.0 mm
L1 R=11.9 mm
Each sensor covers ½ layer in r𝜑
Beam pipe
R=11.7 mm
254 mm

## Slide 13: Mechanics for VTX layers
Starting point is the mechanics of the ALICE ITS3
To be adapted for a geometry with conical boundaries
  Non trivial
Some design work started
No doubt that curved MAPS are the option to aim for
  And air cooling is a must

## Slide 14: Outer Tracker (silicon, or not silicon?)
Reticle-size MAPS, bump-bonded onto a High-Density Interconnect circuit
25×32 mm2 MAPS ⟶ 50×128 mm2 module
Building block of the barrel staves
Industrial flip-chip process for module construction
Cope with MAPS process yield
Chip peripheries are located side by side in the center of the module
50.05 mm
128.15 mm

## Slide 15: Mechanics for the Outer Tracker
glue
heater (chip)
Polyimide cooling pipes
Starting point is the “cold plate” invented for the ALICE ITS2
    [Corrado Gargiulo & Massimo Angeletti]
  Extremely light and efficient thermal interface
Deploy with larger size, remove space frame and couple two plates with thick foam structures in between
  Lightweight ultra-stiff mechanical structure
Use to support two active layers
  Lightweight ⟶ lightweight / 2
  The detector layout is optimized for physics and mechanics
Self-supporting structures, joined by flanges at the end (barrel)

## Slide 16
HDI
MODULE
(2 x 4 chips)
Chip
On a cold plate are glued (2 x 21) = 42 modules
Cold plate + modules ⟶ Module string
Two module strings + the foam structures ⟶ Stave
Two active layers
21 modules
2 modules
The Outer Tracker Stave
Giada Bonini
~ 10 cm (width) x 5 cm (height) x 268.8 cm (length)
~ 0.170 kg (mass)

## Slide 17
Each cold plate embeds 2 cooling pipes (straight – no bends)
The flow direction is opposite in the two pipes of a cold plate (single-phase cooling)
Cooling pipes are located under the chips periphery
Staves are supported by flanges at the two ends
The Outer Tracker Stave
Giada Bonini
Full block
at stave ends
15 mm

## Slide 18
Outer Tracker layout (barrel)
MID1
MID2
MID3
OUT1
OUT2
Middle layers
Outer layers
 | Lower cold plate | Upper cold plate
MID1 | 712.1 | 762.1
MID2 | 839.4 | 889.4
MID3 | 966.8 | 1016.8
OUT1 | 1603.1 | 1653.1
OUT2 | 1730.3 | 1780.3
Average radius (mm):
Front view
Giada Bonini

## Slide 19
Outer Tracker layout (barrel)
MID1
MID2
MID3
OUT1
OUT2
Middle layers
Outer layers
 | N. of staves | N. of modules | Silicon active surface (m2) | Power (kW)
MID1 | 48 | 4032 | 25.80 | 5.16
MID2 | 56 | 4704 | 30.11 | 6.02
MID3 | 64 | 5376 | 34.41 | 6.88
OUT1 | 104 | 8736 | 55.91 | 11.18
OUT2 | 112 | 9408 | 60.21 | 12.04
Giada Bonini

## Slide 20
Outer Tracker cooling: fluids
Key properties:
Eco-friendly
Suitable for electronics immersion cooling
 no damage to the sensors in case of leaks
OpteonTM SF10 identified as a plausible choice, taking into account all relevant thermo-physics properties
Giada Bonini
3MTM Novec 774 will no longer be produced
Low boiling points  not optimal

## Slide 21
Outer Tracker cooling: sizing
(ΔT=5°C)
(ID=1.6mm)
Next step: thermal simulation
Pixel Power dissipation: 20 mW/cm2
Periphery Power dissipation: 50 mW/cm2
MAPS operational temperature: < 30°C
Power dissipated per chip: 0.161 W
Power dissipated per module: 1.29 W
Power dissipated per cold plate: 54.15 W
Nominal values chosen:
Pipe internal diameter: ID = 1.6 mm
Fluid in-out difference temperature: ΔT = 5°C
Pressure drop: 0.95 bar
Graphics based on fluid parameters at 15°C
Chip power density is not uniform
Giada Bonini

## Slide 22
Structural analysis
Objective: evaluate stave sag under (modules + electronics + pipes + cooling fluid) weight  Total mass: ~ 0.175 Kg
Applied a distributed mass on the two cold plate surfaces to model electronic components
Applied a distributed mass on specific locations to model pipes with fluid
sag = 1.02 mm
sag = 0.69 mm
Simple support
Simple support
Clamped
Clamped
Giada Bonini

## Slide 23
Outer Tracker mechanics: next steps
Thermal simulations
Construction of a 1.5 m long stave demonstrator, in collaboration with Purdue
  Material being procured
Design of the flange
…

## Slide 24: Outer Tracker Stave: electronics system
    Key technologies:
Serial powering for delivering the required power to the modules
Aluminium interconnets (rather than copper) for power and readout
Data merging and command sharing across multiple chips
Silicon photonics readout (tbc)
Stella Orfanelli

## Slide 25: Serial powering concept
Modules powered in constant current chain
Demonstrated in CMS & ATLAS (5–14 modules)
Insensitive to voltage drops
Reduces cable mass & losses
Uses on-chip Shunt-LDO regulators
Failure tolerant → current redistributed
CMS barrel SP chain of 8 modules
ATLAS barrel system test
Stella Orfanelli

## Slide 26: Implementing serial powering over a stave
Two chains of 20+22 modules
Two serial powering nodes per module
  4 MAPS per node
  Cooling pipes below the SLDO location to avoid hotspots
  Charge pump integrated on the periphery to bias the sensor (no extra bias line required)
Z=0
Iin1
Iout1
Iin2
Iout2
Stella Orfanelli

## Slide 27: High Density Interconnect (HDI)
Iin1
Iout1=Iin2
Iout2
< 5% losses on the HDI
8-MAPS module flip-chipped on HDI
1 µm Al
1 µm Al
40-50 um dielectric (PI or prepreg)
Small power connector
with 2 pins (0.3 A/pin)
Power pigtail to pass the current to the next module in series
Stella Orfanelli
Rest of the two layers used for readout lines

## Slide 28: Data merging & Command sharing
Each node of the SP chain must have independent AC-coupled readout/command lines
Data merging and command stream (CMD) shared to reduce the number of links
2 readout diff. lines and 2 command diff. lines per 8-MAPS module → 8 pins connector
Assuming max bit rate of 1 Gbps/20 modules
  50 Mbps per module → 6 Mbps per MAPS over 5-10 cm of 1 µm Alu
  Need to keep paths short (resistive losses in 1µm are significant) - needs to be demonstrated
Command lines could potentially be slower
Stella Orfanelli

## Slide 29: 1 µm Alu – is it even possible?
There is no Al sheet with 1 µm thickness.
  Physical Vapour Deposition (PVD) sputtering process
  Adhesion layer: Ti/Cr (~30 nm)
  Proven in industry (nm-scale films)
ALICE is using it for a two-layer flex with 25 µm Aluminium thickness and 50 µm Kapton.
Next steps: kick-off R&D with CERN workshop on the optimisation of the HDI stack
Stella Orfanelli

## Slide 30: Readout flex
Each module needs 4 differential pairs. For a chain of 20 modules:
  80 pairs in a flex for lines of 50 Mbps over < 1.5m
~3.2 cm flex width with 20-30% fill factor (part of the layer used for traces)
Effective metal thickness ~2.4 µm
No reference plane (to validate)
5 cm
12.8 cm
128 cm
Stella Orfanelli

## Slide 31: End of stave services
One layer Alu flex on the flange to connect to two Copper-Cladded Alu (CCA) wires AWG26 for each Serial Power Chain of 0.6A
Silicon photonics integrated circuits (PIC) that convert electrical to optical signal (and vice versa)
  PIC pigtailed with 3 single-mode glass fibres with 125 µm diameter
  Implemented on a mezzanine wire-bonded to the readout flex
Three fibres inserted into a loose tube with an outer diameter of approximately 1 mm​
Example Alu flex for the flange of the
CMS Phase-2 Inner Tracker barrel (TBPX)
Stella Orfanelli
SiPh sketch from EP-ESE

## Slide 32: Summary …
First broadbrush plan of services laid out
  Based on demonstrated concepts
  Using cutting edge technologies for very low mass services
Serial powering is fundamental to the system architecture
  Will dictate readout grouping and specs for the chip
… and next steps
Demonstrate with CERN PCB workshop and test boards:
  PVD process with 1 𝜇m Al is reliable – optimise thickness of Al and dielectric
  HDI data transmission over 1 𝜇m Al for short paths
  Long flex transmission without reference plane
Collaborate with EP-ESE towards the integration of SiPh
Stella Orfanelli

## Slide 33: All together
cos𝜗 = 0.99 (141.5 mrad)
100 mrad
1.8
1.6
1.4
1.2
1.0
0.8
0.6
0.4
0.2
0.2 0.4 0.6 0.8 1.0 1.2 1.4 1.6 1.8 2.0
N of modules | 56825 |  | 
Silicon active surface (m2) | 364 |  | 
Power (kW) | 72.74 |  | 
N of wafers | 9471 | 28.41 | MCHF
LumiCal

## Slide 34: Nomenclature
1.8
1.6
1.4
1.2
1.0
0.8
0.6
0.4
0.2
0.2 0.4 0.6 0.8 1.0 1.2 1.4 1.6 1.8 2.0
Tracker

## Slide 35: Nomenclature
1.8
1.6
1.4
1.2
1.0
0.8
0.6
0.4
0.2
0.2 0.4 0.6 0.8 1.0 1.2 1.4 1.6 1.8 2.0
Outer Tracker (OT)
Vertex Detector (VTX)

## Slide 36: Nomenclature
1.8
1.6
1.4
1.2
1.0
0.8
0.6
0.4
0.2
0.2 0.4 0.6 0.8 1.0 1.2 1.4 1.6 1.8 2.0
Barrel
Endcap
Outer Layers
Middle Layers

## Slide 37: But…. what about the endcaps?

## Slide 38: The endcaps: from a stave to a Dee
Endcaps are always a headache
Extend the concept adopted for the barrel
Minimize added complexity (… and, obviously, mass )
Take advantage of square pixels
No design work done, yet
Just a concept - to be developed

## Slide 39
Use the same module string construction
Install on large foam structures covering a “Dee” (half disk)
Same ~ 5 cm foam thickness
One support structure carrying two active layers (many strings of different length)
Disk 1

## Slide 40
Use the same module string construction
Install on large foam structures covering a “Dee” (half disk)
Varying background rates across a string
Central region will probably be “relatively hot”
Might require faster MAPS
... in worst case (yet another) slightly different flavour
Disk 1

## Slide 41
Use the same module string construction
Install on large foam structures covering a “Dee” (half disk)
Too big to be glued
Probably needs elements (rails) on the foam structures
Features on the back of the cold plates to slide in the rails
Insert from the two sides and block in place
For now in the material model:
×4 density in the structures wrt barrel
Disk 1

## Slide 42: One more subdetector: the luminometer

## Slide 43: One more subdetector: the luminometer
One existing concept made of W and Si-strip layers
  Inspired by the OPAL luminosity calorimeter
Attempt to position silicon strips according to the desired acceptance
  Centred around the outgoing beam direction
Cannot work in practice with the required precision
  …and it’s not the desired acceptance anyway
Acceptance needs to be defined a posteriori using physics constraints
  Like the alignment for the Tracker

## Slide 44: One more MAPS-based subdetector: the luminometer
Replace Si strips with MAPS positioned as close as possible around the beam pipe(s)
Define the acceptance contour a posteriori
Small pixels are the best possible option for a precise definition of the acceptance contour
MAPS will not be the limitation
  Stability of the mechanics is key
  Offline reconstruction

## Slide 45: MAPS: summary
  Aim at one single development, with some “variants”
Faster front-end for the VTX layers, designed for stitching
(b) Slower front-end for the OT barrel layers, reticle size, designed for flip-chip
(ab) Reticle size MAPS designed for flip-chip, with faster front-end for the OT endcaps
(ab’) MAPS designed for flip-chip, with faster front-end and fine-tuned size for the LumiCAL
N.B. Perhaps the speed of the front-end could be made “programmable”

## Slide 46: Material estimates

## Slide 47: Mass estimates (some highlights)
Silicon Module |  | Avg X/X0 (%)
MAPS | Si | 0.0534
 | Cu | 0.0139
Bumps | Sn95Ag5 | 0.0009
HDI | Coverlay | 0.0103
 | Al | 0.0022
 | HDI prepreg | 0.0281
 | Decoupling cap | 0.0071
Connector power | LCP | 0.0003
 | Cu | 0.0006
Connector data | LCP | 0.0006
 | Cu | 0.0015
Total |  | 0.1190
Stave |  | Avg X/X0 (%)
Cold plates | C paper | 0.0225
 | C fleece | 0.0112
 | K13D2U | 0.0577
Foam structures | ERG Duocel foam | 0.0577
Pipes | Kapton | 0.0092
Coolant | Opteon SF10 | 0.1302
FPC | Kapton | 0.0175
 | Coverlay | 0.1026
 | Al | 0.0539
 | Epoxy | 0.0118
Total |  | 0.4743

## Slide 48: Mass estimates (some highlights)
 | N of staves in phi | Avg X/X0 modules (%) | Avg X/X0 staves (%)
OUT2 | 112 | 0.12 | 0.48
 |  | 0.12 | 
OUT1 | 104 | 0.12 | 0.48
 |  | 0.12 | 
MID3 | 64 | 0.12 | 0.48
 |  | 0.13 | 
MID2 | 56 | 0.12 | 0.48
 |  | 0.13 | 
MID1 | 48 | 0.12 | 0.48
 |  | 0.13 | 

## Slide 49: Performance
From DELPHES

## Slide 50: Outline
Baseline ALFA vs CLD/IDEA: comparison of all track parameters
Baseline vs 5-layer VTX
  possible only with smaller beam pipe
Baseline vs 50 𝜇m OT pixels: pT resolution
Robustness: dead middle/outer layer
Ignore coordinates in VTX: d0/z0 resolution
  For outward ⟶ inward reconstruction and displaced topologies

## Slide 51: Baseline performance

## Slide 52
Michele Selvaggi
Based on available DELPHES cards

## Slide 53
Michele Selvaggi

## Slide 54
Michele Selvaggi

## Slide 55
Michele Selvaggi

## Slide 56
Michele Selvaggi

## Slide 57
Michele Selvaggi

## Slide 58
Michele Selvaggi

## Slide 59
Michele Selvaggi

## Slide 60
Michele Selvaggi
Based on available DELPHES cards

## Slide 61
Michele Selvaggi

## Slide 62
Michele Selvaggi

## Slide 63
Michele Selvaggi

## Slide 64
Michele Selvaggi

## Slide 65
Michele Selvaggi

## Slide 66
Michele Selvaggi

## Slide 67
Michele Selvaggi

## Slide 68: 5-layer VTX
Possible only with a smaller beam pipe

## Slide 69
5-layer VTX Baseline
Michele Selvaggi

## Slide 70
Michele Selvaggi

## Slide 71
Michele Selvaggi

## Slide 72: Outer Tracker with 50 𝜇m pixels

## Slide 73
Michele Selvaggi

## Slide 74: One dead layer in OT
Assess robustness

## Slide 75
Eduardo Ploerer

## Slide 76
Eduardo Ploerer

## Slide 77: Ignore coordinates in VTX
For outward ⟶ inward reconstruction and displaced topologies

## Slide 78: Resolution d0, z0
Michele Selvaggi

## Slide 79: What we have achieved
Sufficiently detailed conceptual design to demonstrate that an all-MAPS Tracker is a promising option for ALFA
  Feasible
  Affordable
  High-performance
  Robust
A lot of interesting work ahead

## Slide 80: Work ahead
OT barrel
  Thermal simulations
  Flanges
  Conceptual design of assembly tooling and sequence
  Services
  Construction of stave demonstrator
  Lab tests to assess thermo-mechanical properties and validate simulations
OT endcaps
  A lot of creative design work
Electronics
  Design, fabricate and test demonstrators for HDI and flex
  Discuss and define implementation of data links
Vertex layers
  Mechanical structures and assembly procedure to be adapted to our geometry (more creative design work)
  Should be then tested with dummy elements

## Slide 81: Last but not least: simulations (…and reconstruction)
Critical goal for the next 2-3 years: define and consolidate precise specs for the MAPS
  Needs accurate simulation of the MAPS response
  Implementation of the detector geometry
  Samples of beam-induced background
Possibility of characterization of MAPS in the lab
  Joint effort on serial powering with ALICE

## Slide 82: The ARC for the ALFA detector
Development started in 2021

## Slide 83: ARC (Array of RICH Cells)
Lightweight and compact solution for particle ID
  20 cm radial depth, 10% X0
Cellular design
Two radiators (gas + aerogel) to cover the full momentum range of interest
Silicon Photomultiplier array mounted on a cooling layer
The aerogel also acts as insulator between the SiPM and the gas

## Slide 84: Silicon PhotoMultipliers
High photo-detection efficiency in the relevant wavelength range
Good timing performance
Compact, robust and cost-effective
High granularity (0.5 × 0.5 mm2 pixels considered)
  Enables good resolution on the Cerenkov angle
High dark count rate – requires low-temperature operation

## Slide 85: Radiators
Dual-radiator system (gas + aerogel) to cover a wide momentum range
A widely used gas radiator in RICH detectors is C4F10 at atmospheric pressure
  High GWP – not a good option for FCC
  Pressurized Xenon under study as alternative
Silica aerogel is an excellent choice for the low-momentum radiator in ARC
  Very low thermal conductivity (0.015 W m−1 K−1) also provides thermal insulation in front of the cooled SiPM modules
  Drawback: emitted photons traverse the aerogel, leading to some scattering losses

## Slide 86: ARC mechanics: concept
Carbon-fibre composite vessel
  First design and FE analysis by Corrado Gargiulo (CERN EP-DT)
CF sandwich with foam core: stiff, light, suitable for a pressure vessel
12-fold rib structure for stiffness and stability (sectors)
Wall thickness ~20 mm, outer diameter 4.4 m, low material budget: 2.7% X0

## Slide 87: Performance from simulation
Excellent expected performance over a broad momentum range
Serena Pezzulo

## Slide 88: Next steps: from ARC to ARC for ALFA
Adapt geometry to the ALFA dimensions
  Already ongoing
Develop the xenon option (top priority )
Revisit the cooling and electronics concept in the context of a large detector assembly
  Exploit synergies with Tracker for thermal management and system design
Develop concept for services and barrel/endcap transition
  Keeping also ECAL in mind
Study mechanical integration with neighbouring subdetectors
  Can the pressure vessel also serve as Tracker Support Tube?
  How is the ARC supported?

## Slide 89: The ECAL for the ALFA detector
Based on the GRAiNITA development:
IJCLab: S. Barsuk, I. Boyarintseva, D. Breton, G. Hull, J. Lefrançois, J. Maalmi, MH.Schune
ISMA: A. Boyarintsev, I. Tupitsyna
LPClermont: H. Chanal, Y. Hou, M. Magne, S. Monteil, D. Picard, M. Yeresko
TSNUK: O. Bezshyyko, A. Dubovik, D. Klekots, A. Kotenko, N. Semkiv

## Slide 90: The GRAiNITA concept
Crystal grains (ZnWO4) immersed in a heavy transparent liquid (sodium tungstate water solution)
  Mass fraction 80% ZnWO4, 20% heavy liquid
Light emitted by the crystal grains is collected by WLS fibres, spaced by 7 mm
~1 mm scintillator grains (solid) in high-density transparent liquid
Incoming particle
Scintillator characteristic [1] | ZnWO4
Effective Z | 61
Density (g/cm3) | 7.87
Refractive index | 2.0-2.3
Light yield (photons/MeV) | ~9000
Peak emission wavelength (nm) | 480
Decay time (μs) | 25
Radiation length (cm) | 1.2
Moliere radius (cm) | 1.98

## Slide 91: The GRAiNITA concept: advantages
Excellent energy resolution, with high transverse granularity
  ⟶ also excellent position resolution
Grains are produced with the flux method
  ⟶ cost-effective compared to homogenous crystals
~1 mm scintillator grains (solid) in high-density transparent liquid
Incoming particle
Scintillator characteristic [1] | ZnWO4
Effective Z | 61
Density (g/cm3) | 7.87
Refractive index | 2.0-2.3
Light yield (photons/MeV) | ~9000
Peak emission wavelength (nm) | 480
Decay time (μs) | 25
Radiation length (cm) | 1.2
Moliere radius (cm) | 1.98

## Slide 92: GRAiNITA: the first prototype
28 x 28 x 55 mm3 active volume
~200 grams of ZnWO4 and heavy liquid
4 x 4 WLS fibres, spaced by 7 mm
Clear fibre at the center, for light injection
Prototype without grains
Prototype with grains

## Slide 93: GRAiNITA: some achievements (highlights)
Test on cosmic bench
  ~400 photo-electron for ~40 MeV deposited energy
  10k p.e. per GeV ⟶ 1% contribution to stochastic term
Test beam at SPS (muons and pions)
  1% stochastic term from p.e. statistics confirmed
  Scan of prototype surface in steps of 1mm, to check for intrinsic dis-uniformities
    The observed disuniformity translates to a constant term of ~0.6%
  Check for light confinement
    75% of the scintillation light is collected by the 4 closest WLS fibres (7 × 7 mm2)
Published in JINST
arXiv:2312.07365

## Slide 94: GRAiNITA: status and next steps
Based on results from the prototype, a stochastic term of < 2% and a constant term of < 1% seem realistic
A full-size EM calorimeter module demonstrator (17 × 17 × 40 cm3) is under construction
  25 X0 in depth to contain 25 GeV photons
  Lateral size adequate for extensive measurements of uniformity
  Quantitative assessment of all components of the resolution
45 kg of grains

## Slide 95: In parallel: studies to improve hadron energy measurement
Pulse shape discrimination
  Exploits the fact that light emission time is different for different particle types
  Requires precise reconstruction of the pulse shape
Measurement of Cerenkov light
  A small but detectable amount of Cerenkov light is produced by the grains
  Requires fast sampling in the beginning of the signal

## Slide 96: Towards ECAL
Several specific issues to be addressed to develop an ECAL concept based on GRAiNITA
  Implement longitudinal segmentation in (at least) two sections
    A few ideas to be explored
  Develop a design of “the box”, adequate for a full-scale hermetic detector
  Develop an overall geometry without dead regions that minimizes adverse effects of inactive material (box walls, fibres…)
  Resolve barrel-endcap transition and routing of inner detectors services
  Overall mechanical structure, support of inner detectors
Design work to start over the Summer
Consider results of PSD and Cerenkov light R&D and start reflecting on readout electronics

## Slide 97: What about HCAL?

## Slide 98: HCAL in ALFA
    Only some initial considerations:
  If PSD and/or Cerenkov detection in ECAL perform as intended, the HCAL will be the limiting factor for the jet energy resolution
  A dual-readout HCAL appears to be the only option to approach the performance level set by the tracker and the ECAL
  HCAL must be located outside the solenoid, otherwise the coil dimensions become unrealistic
  The absorber should be iron, combining calorimetric function with that of the magnetic return yoke, to limit the overall detector size
Dual readout HCAL in iron

## Slide 99: Dual readout HCAL
Ongoing R&D activities feature prototypes with fibres at a pitch of 1.5 mm
For the envisaged detector dimensions, this corresponds to ~75 million fibres embedded in iron, with positioning precision at the level of ~100 μm
It is not clear whether the construction of such a device is realistic
Initiate dedicated studies, starting from the engineering aspects

## Slide 100: Organisational
The e-group fcc-ped-detectorconcepts-alfa has been established, as part of the FCC PED organization
If you are interested in ALFA, please register via https://gms.web.cern.ch/
Plan to start regular meetings in June, after the FCC week
  Monthly or bi-weekly, depending on the speed of the progress
Some of the meetings may be “topical”

## Slide 101: Thank you!
… questions?

## Slide 102: Backup material

## Slide 103: Considerations on schedule

## Slide 104: FCC-ee official schedule

## Slide 105
CDR 2
Linac4 approval
3 MeV test place ready
SPL & PS2 approval
Start for Physics
2nd SLHC-PP annual meeting, CERN 26th February 2009
For high-lumi we have a delay of 13 years (… and counting…), on top of a timeline of 8 years
Schedules: the lesson we never learn!

## Slide 106: Example of a detector: the CMS Hi-Lumi Tracker
We started in 2009, with reasonably clear ideas, and a solid collaboration already in place
The detector will (?) be ready for installation in 2030

## Slide 107: Considerations on schedule
If the detectors were really to be ready for operation in 2045, we would already be late
If we want the FCC-ee timeline to slip by only a few years (rather than a few decades), it’s time to focus and start developing solid detector designs

## Slide 108
Foam bars: material
The bars are made of foam with a high strength-to-weight ratio  low density and high structural rigidity.
Reticulated Vitreous Carbon (RVC) foam was considered in the model  ultra-light, highly porous carbon material with up to 97% open porosity and very low density.
Giada Bonini

## Slide 109
Cold plate
High thermal conductivity carbon plate embedding ultralight polyimide cooling pipes.
The chips that need to be cooled down are glued on the cold plate and are in thermal contact with it.
The heat is transferred from the chips into the cooling pipes by the carbon substrate and is removed by the coolant flowing in the pipes.
Developed by ALICE Deployed in the ITS2
Giada Bonini

## Slide 110
Cold plate: lay-up
Polyimide pipes
Different carbon materials are laid-up in the plate thickness to enhance thermal performance and guarantee structure integrity.
Lay-up total thickness = 0.21 mm
Modules are glued on this side
Giada Bonini

## Slide 111
The "box beam" configuration provides high resistance to twisting and torque.
The flexural rigidity of the structure (EI) increases with the distance between cold plates  a value of 5 cm allows the stave to support the applied loads with an acceptable deflection
Foam bars provide continuous support to the cold plates in the longitudinal direction, preventing buckling phenomenon
Stave: "Box beam" configuration
50 mm
10 mm
9.5 mm
This offset is fixed by the position of the staves in the barrel  this value ensures a minimum distance between two adjacent staves of ~ 3 mm (in the OT innermost layer).
Stave front view
Carbon plate  high Young’s Modulus (E).
Foam bar  low density (ρ)
HIGH SPECIFIC STIFFNESS
Giada Bonini

## Slide 112
Cold plate: materials
Carbon K13D2U Unidirectional Prepreg
Made from ultra-high thermal conductivity K13D2U fibres.
It serves as the primary thermal structure to quickly transport heat generated from the chips to the tubes.
The carbon fibres are oriented transversally to the stave, enhancing the heat spreading towards the cooling channels from the sides of the stave.
Carbon fibre
Unidirectional prepreg
Filament diameter = 11μm
Density = 120 g/m2
Thickness = 120 μm

## Slide 113
Unidirectional prepreg is produced by aligning continuous carbon fibres in a single, uniform direction and surrounding them with a polymer matrix  This manufacturing process creates a ready-to-mold material in sheet form.
It is used EX-1515 Cyanate Ester Resin System  it is preferable to epoxy resin for its low humidity absorption and better dimensional stability in time.
Carbon K13D2U Unidirectional Prepreg: Resin System
Low curing temperature: 121°C
Cold plate: materials

## Slide 114
Cold plate: materials
Thermal Pyrolytic Graphite
High in-plane thermal conductivity and flexibility
A Graphite foil is laid over the cooling pipes to enhances the thermal contact between the top of the cooling pipes and the plate.
It transfers and spreads the heat from the carbon fibre plate to the embedded polyimide tubes.

## Slide 115
Carbon Fleece
Continuous-strand mat made of non-oriented carbon fibres, which are finished with a chemical binder to hold the fibres securely in place.
Two carbon fleece layers encapsulate the whole plate layout to protect it, providing resistance to abrasion and peeling, and to add mechanical stiffness.
A third layer is placed between the polyimide cooling tubing and the high-thermal conductivity plate, ensuring that the cooling channels remain firmly positioned and their section remains circular.
Cold plate: materials

## Slide 116
Polyimide pipes
Thermal stability: As a thermoset polymer, polyimide cannot be reshaped by heat at low temperatures (below 200°C) after it has been extruded.
Low deterioration rate: It is highly inert and compatible with most refrigerants, materials, weak acids, and solvents.
The pipes are embedded in the carbon structure  In this way their fragility and tendency to pinch and buckle under localized load does not aﬀect their use.
Cold plate: materials

## Slide 117
OTHER OPTION: PEEK pipes
Kapton tubes are available in various lengths, internal diameters and wall thicknesses.
In the model, the following assumptions were made:
Polyimide pipes
Internal diameter = 1.6 mm
Wall thickness = 32 μm
PEEK provides excellent mechanical properties, chemical stability and durability, at low material budget.
3 meters long pipes are commercially available.
Minimum wall thickness available: ~100 μm
Cold plate: materials

## Slide 118
Cold plate: production process
Prepare carbon paper, prepreg, fleece, pipes and resin.
Prepare the substrate:
Cover mould for substrate with vaseline/teflon tape 10 micron
Place plyes of fleece-prepreg-fleece inside the bottom mould
Close the mould with the top part
Cure at ~130°C 3h  extract the substrate for next use.
Prepare polyimide tubes with internal steel wire mandrel  this allows polyimide pipes to retain their shape during the process.
A specific jig is used to produce the substrate
Mandrel
Pipe

## Slide 119
Cold plate: production process
Cover the mould (plate side) with a vaseline/teflon film
Cover the mould (pipe side) with Penta 111(silicon oil) and teflon
Place the impregnated substrate (previously produced) in the mould (plate side)
Place fleece on bottom mould (pipe side) and put resin
Place carbon paper on bottom mould and put resin
To create the entire cold plate is used another jig  this is flat on one side and has pipes grooves on the other.

## Slide 120
Cold plate: production process
Place tubes with mandrels in the mould
Join top and bottom mould, screw together
Rise temperature up to 60°C and apply nominal value torque screw  This value regulates the exit of excess resin
Cure 24h at Room Temperature
Finishing cleaning  cut the cold plate to give it the final dimensions.
After curing:

## Slide 121
OpteonTM SF10
Zero Residue: evaporates completely without leaving films or deposits that could interfere with sensor performance (in case of leak).
Material Compatibility: compatible with most metals, plastics and elastomers, including Polyimide and Peek.
Dielectric Properties: has a low dielectric constant, making it safe even for direct immersion cooling.
Thermal Stability: with a boiling point of 110 °C and a wide operating range (from -80 °C to 60 °C), it ensures consistent heat dissipation.
Low environmental impact: OPD (Ozone Depletion Potential) = 0, GWP (Global Warming Potential) = 2.5 (100yr).
Non-flammable and low toxicity.
Does not oxidize nor degrade during storage.
Alternative fluid for replacing PFCs, PFPEs, HFEs, HFCs, and HCFCs in heat transfer applications.
Giada Bonini