## Slide 1: From PALLAS to DESY
Plasma targets for high-repetition-rate laser-plasma accelerators
Jana Serhal
22/10/2026

## Slide 2: Laser Plasma Acceleration: the concept & mechanism
2
Simulation: the laser pulse (orange) drives a plasma wave (blue) behind it
The pulse ionises the gas —> plasma
It then drives a wave in the plasma.
Electrons surf the wave and gain energy over few millimetres
An intense laser pulse (≅) is shot at a gas target
1
3
100 GV/m
accelerating gradient
X 1000
RF cavities

## Slide 3: Catching the electrons
Simulation: a bunch of trapped electrons rides at the back of the wave
ionisation injection
Only fast electrons are trapped
The challenge: injection
Put electrons in the right place, at the right moment.
Add dopant
1
2
3
A little bit of nitrogen N2 in Helium
Outer electrons leave early
Freed by the front of the pulse , helps to the formation of the wave
Inner shell electrons leave later
N⁵⁺ → N⁶⁺, N⁷⁺ only at peak intensity, inside the wave → trapped

## Slide 4: PALLAS : Laser-Plasma Injector at IJCLab
3 J . 45 fs
Laser pulse
1 —> 10 Hz
Repetition rate
12 µrad —> <1 µrad
Pointing stability
<5 m
Beamline
Focusing
quadrupoles

## Slide 5: Recent Beams from PALLAS
29.5 pC
Charge
187 MeV
Peak energy
Spectra averaged over groups of 10 shots, from a ~350-shot long run of the February campaign.

## Slide 6: Understanding the correlations
Laser & target conditions
Stable gas target
Pressure in both chambers held to 0.6 % over 300 shots.
Charge follows the vacuum.
Laser pointing matters:
Horizontal laser pointing correlates with charge.

## Slide 7
Through the injection process
How to counteract energy spread?

## Slide 8: DIANA : Two Chamber Gas Cell
1 cm
Injection Chamber
N₂ / He mixture → ionisation injection
Acceleration Chamber
Pure He → energy gain
Diagnostic
Probe beam for density · emission lines for dopant localisation
The injector

## Slide 9: What about Energy Spread?
Cause 1 : A long injection zone
Born earlier, accelerated longer
Short injection → narrow spectrum
2
1
Electrons are born where the dopant is:
A long dopant region injects over a long distance.
Injected at −1 mm vs 0: one extra millimetre in the wave, so more energy.

## Slide 10: What about Energy Spread?
Cause 2 : Beam Loading
The electron beam drives its own wakefield which superimposes that of the laser.

## Slide 11: After DIANA :
ROSA and SIMONE localise the dopant
Controlled injection
Lower energy spread

## Slide 12
Towards Higher Repetition Rates:

## Slide 13: Every Shot Leaves a Mark
Heating
Heat is absorbed to the walls
2
1
Ablation
The laser erodes the material
Contamination/Debris
Solid atoms enter the gas and vacuum chambers.
3
Change in geometry
—> Change in gas profile
—> Affect electron beam’s quality and stability

## Slide 14: What the laser does to a nozzle at 1 Hz
x 2
Hole diameter : 0.5 -> 1 mm
x 4
Open area : more gas escapes

## Slide 15: Going to Higher Repetition Rates:
Less time to cool down : stronger thermal load to manage

## Slide 16: Thank you, to both teams