2nd year CSI – juin 2026
Augustin Demagny
Backscattered light noise in the Virgo interferometer
PhD advisors : Michal Was & Romain Gouaty

---
Gravitational wave
- Space-time metric’s deformation
- 2 polarisations (+, ×)
A prop frac { 1 } { d }
v = c
Gravitational Wave Illustration
Credit : Swinburne Astronomy Productions

---
Detection principle
- Space-time deformation → change distance between free-falling masses
- Use electromagnetic wave to measure displacement
Test mass 1
Test mass 1
d
d+δd
Test mass 2
Test mass 2
`%delta d = { frac { h } { 2 } } d

---
Michelson ITF
phase difference between arms → amplitude on the anti-symmetric port
Dark fringe offset:
%delta { { P } _ { t } } prop %delta %DELTA L

---
Sensitivity curve
ASD of h(t)
Affected by various noises

---
Benches layout
Benches :
SNEB
SWEB
SDB1
SDB2
End-of-arms benches
Detection benches
In vacuum
Suspended

---
Transfer function
Constructive/Destructive interference :
→ change amplitude of the beam
→ change radiation pressure
⇒ Named
Quadratic interference :
→ add phase noise
→ directly change measurement
⇒ Named
{ { K } _ { frac { %delta P } { P } } }
{ { K } _ { { n } _ { %phi } } }

---
Computing backscattered factor
mirror transmission
sensitivity
bench movement
h_r(f) = sqrt {f_r} cdot {frac {P_out} {P_{ital "in"}}} cdot lbrace K_{n}(f) cdot fourier [ sin({frac {4 cdot %pi} {%lambda}}(x(t))) ] + K_{P}(f) fourier [ cos({frac {4 cdot %pi}{%lambda}}(x(t))) ] rbrace
fraction of backscattered light
Pin
bench
Pout
transfer function by radiation pressure (Kp) and phase (Kn)
x(t)

---
Simulation upgrade
- Simulating SR alignment
- HOMs added to the simulation
By DrBob at English Wikipedia, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=18064771

---
Impact on SDB1

---
New injection on benches
- 17 june 2025
  - SR aligned (LN2)
  - SR misaligned (LN3)
- Benches :
  - SDB1
  - SDB2
  - SWEB
18 μm
A×sin(2πf)
 0.1 Hz

---
Projected vs real impact on sensitivity

---
Evolution of fsc measurement
date	SR yaw	injection power	bench	fsc
2023-03-24	0	25.4 W	SDB1	7×10-10
2023-03-24	0	25.4 W	SDB2	3×10-12
2023-03-24	0	25.4 W	SNEB	1.1×10-8
2023-03-24	0	25.4 W	SWEB	3×10-9
2023-12-20	2 μrad	12.1 W	SWEB	4×10-9
2024-01-21	2 μrad	12.1 W	SNEB	8×10-9
2024-10-31	2 μrad	18 W	SDB1	5×10-9
2024-10-31	2 μrad	18 W	SDB2	5×10-12
2024-10-31	2 μrad	18 W	SNEB	1.2×10-8
2024-10-31	2 μrad	18 W	SWEB	6×10-9
2025-06-17	0	18 W	SDB1	2×10-9
2025-06-17	0	18 W	SWEB	2×10-9
2025-06-17	2 μrad	18 W	SDB1	7×10-9
2025-06-17	2 μrad	18 W	SDB2	1.5×10-12
2025-06-17	2 μrad	18 W	SWEB	4×10-9

---
SR alignment and fsc
- SR alignment change fsc measurement
- fsc is a characteristic of a bench
  → unmodel effect in current simulation ?

---
Adding defects to the simulation
- RoC change
- Add point absorber to mirrors

---
Defects impact on transfer function
No change at low frequencies (less than 20 Hz)
→ Do not explain fsc change

---
Backscattermeter
laser power
Sample
{ { P } _ { 1 } } ( t ) - { { P } _ { 2 } } ( t ) = frac { { P } _ { 0 } } { sqrt { 2 } } sqrt { { f } _ { sc } } cos (2 %pi frac { %DELTA L ( t ) } { %lambda })
Suspended bench
wavelength
P1
fraction of backscattered light
P2
bench movement
A ( t ) = frac { { { P } _ { 1 } } ( t ) - { { P } _ { 2 } } ( t ) } { { { P } _ { 1 } } ( t ) + { { P } _ { 2 } } ( t ) } = sqrt { 2 { { f } _ { sc } } } cos ( 2 %pi frac { %DELTA L ( t ) } { %lambda } )
Motorized mirror

---
Re-characterization : beam size and visibility

---
Re-characterization : motor steps
- What we want :
  - Change position of the beam on the sample
- Issue :
  - Also change incidence angle by 0.82°

---
Crystal measurement
- Multiples Faraday crystals :
  - Old TGG
  - New TGG
  - KTF (better thermal performance)
  → new TGG scatter less

---
Bench speed study
Requirement on fsc and relative bench speed.
→ need to study current bench movement
- Speed can be computed as the differential of the bench position (times its frequency)
- Divide every five consecutive minutes (an observation) in which the ITF is in SCIENCE mode
- Here, the bench speed is the relative motion between the bench and its associated mirror

---
Filtering bench position
- Higher than 2Hz → dominated by sensing noise
- FIR low-pass filter:
  - Pass-band frequency: 1Hz
  - Stop-band frequency: 2Hz
  - Attenuation: 100dB
- Applied on the position of the bench. Speed is computed after.
signal
noise
2 Hz

---
Bench speed evolution
Excess noise

---
Correlation between signals
Bench / Correlation	SDB1	SNEB	SWEB
wind speed	25%	10%	16%
Micro-seismic 600-1000 mHz	74%	11%	28%
Micro-seismic 300-500 mHz	81%	13%	27%
Micro-seismic 100-200 mHz	53%	17%	21%
Micro-seismic 10-100 mHz	24%	27%	23%
Impact of excess noise

---
Projection for different speed

---
Summary
- New work on simulations (HOMs/defects)
- New measurements on back-scattermeter (TGG crystals)
- Bench backscattered light study :
  - Evolution fraction of backscattered light
  - Correlation and impact of bench speed

---
Future work
- Back-scattermeter :
  - OMC
  - New Faraday components (crystals/half-waveplate, polarization splitter)
- Investigation of bench backscattered light variation :
  - New measurement on Virgo
  - Improve the model (more realistic defects)
  - analyze the impact of the calibration error on the Virgo detector data
- Check backscattered light with new configuration with detuned signal recycling cavity
- Simulation of O5 configuration
  → Validate the methodology