## Slide 1
cocotb to model a DCO inside an ADPLL
Thomas Lauber
Université de Strasbourg – IPHC
thomas.lauber@etu.unistra.fr

## Slide 2
Overview
05
04
03
Behavioral modeling
with cocotb
02
ADPLL
How does it work
01
Context
Me and my internship
Testbench, LUT, noise generation and validation
ADPLL testbench
Conclusion
Example of testbench and results

## Slide 3
Context – My profile & my work
MSc Electronic & MicroElectronic Systems (SEME)
Intern at C4PI from March to August (6 months)
Designing an All-Digital PLL in 65nm node
PLL
PAD
40MHz
1.28GHz
Clock Synthesis

## Slide 4
ADPLL – Bang-bang All Digital PLL
PAD
40MHz
1.28GHz
PLL
Digitally Controlled Oscillator
(ring oscillator)

## Slide 5
Behavioral DCO – Why ?
Digital blocks
Analog block
DCO is the only analog block
PLL transients with Spectre can take up to weeks of simulation time
Transistor level simulator (analog) or event driven simulator (digital) ?
RTL simulator is used

## Slide 6
Behavioral DCO – Phase noise and jitter concepts
Jitter is a time domain measure of the timing accuracy of the oscillator period
Phase noise is a frequency-domain view of the noise spectrum around the carrier
f
offset
Chart: 
Time domain
Frequency domain
jitter

## Slide 7
Behavioral DCO – How ?
Need of a behavioral model that reproduces these three regions
Use Spectre results as the reference and try to match it
DCO phase noise

## Slide 8
Behavioral DCO – How ?
Injection of timing deviations from the nominal period
One amplitude for each phase noise region

## Slide 9
Behavioral DCO – How ?
}
Inspired on [Waheed, K. and Staszewski, R.B.] paper
Noise_injection.py
noise

## Slide 10
Behavioral DCO – How ?
Spectre

## Slide 11
Behavioral DCO – How ?
Noise_injection.py
noise
Python wrapper
DUT.sv
Xcelium
Post-layout simulation
Spectre results (PSS + PN)
fout
Post_process.py
csv
pn_fc
pn_1f2
floor
fc
f_1f2
FFT
Match ?

## Slide 12
Behavioral DCO – Advantage of cocotb
Jitter and wander can be directly injected as normal distribution samples & (trivial)
Flicker however requires shape (non trivial)
Generate samples with numpy and pass it
through IIR filters and then scale it with
random.standard_normal()
Filtering is easy in python (numpy)

## Slide 13
Behavioral DCO – Advantage of cocotb
Generation of shape

## Slide 14
Behavioral DCO – model validation
Jitter injection –
vs

## Slide 15
Behavioral DCO – model validation
Wander injection –
vs

## Slide 16
Behavioral DCO – model validation
Flicker injection –
vs

## Slide 17
Behavioral DCO – model validation
All
vs

## Slide 18
ADPLL simulation – testbench

## Slide 19
ADPLL simulation – setup

## Slide 20
ADPLL simulation – testbench example
Closed loop phase noise testbench
Injection timing noise and ripple on supply
Accumulate N cycles
Compute phase noise

## Slide 21
ADPLL simulation – testbench example
Initialization of pll parameters (filter coefficients, lock detection, …)
Set reference jitter
Set ripple config : 0.2mV @1MHz
Set the number of simulation cycles : 2M -> ~1.56ms

## Slide 22
ADPLL simulation – testbench example
User set the Spectre measurements by calling the class

## Slide 23
ADPLL simulation – testbench example
Start both noise and ripple injection co-routines

## Slide 24
ADPLL simulation – testbench example
Record edges of PLL output
Make sure PLL stays locked during the entire simulation

## Slide 25
ADPLL simulation – testbench example
Collect timestamps
Compute phase noise
Save the data

## Slide 26
ADPLL simulation – results 2M cycles
~1hr for 1.56ms
Verisium

## Slide 27
ADPLL simulation – results 2M cycles
ripple

## Slide 28
Conclusion
Xcelium
Makefile
Bridging Python's scientific stack and Xcelium for mixed digital/behavioral simulation

## Slide 29
Thank you