Update on the crack study - muon events analysis
Jan Blaha
Micromegas Physics Meeting, 8 December 2010, LAPP

---
Objective and set-up
For PFA is useful if muons can be easily identified in a calorimeter and assigned to the ones measured in muon chambers
The aim is to estimate the fraction of muons that will be lost in a crack for the projective and non-projective geometry
20 kevents generated for all geometry configurations (NoFeP, 1cmFeP, 2cmFeP, and 2cmFeP_WE) for single muons of different energies (3, 10, 50, 100, 150, 200 GeV)
Data generated for a cone angle of 15° that corresponds to an impact area of about 40 cm on a front face
Comparison in this presentation is focused on standard configuration (2 cm thick supporting plate and a 1 cm of dead area in each module) and 50 GeV muons

---
Projective and non-projective geometry
Projective geometry
Non-projective (tilted) geometry
15°
15°
2°
2°
Particles directed as they coming from the vertex
Two data sets:
Small impact area: ~ 5 cm diameter around the boundary at front of the detector (a cone angle of 2°) → effects on cracks
Large impact area: ~ 40 cm diameter around the boundary at front of the detector (a cone angle of 15°) → effects on large phi

---
Pions versus muons
2 cm Fe plate between modules, 50 GeV pions
Projective
Non-projective
muons
pions
Pions: - For the large cone angle the projective and non-projective geometry show same	results
Mons: - Different distributions for the projective and non-projective geometry
   - about 5% of muons are lost in a crack in case of the projective geometry
    - all muons can be easily identified in the non-projective geometry (always more
than 25 hits in an event)

---
Pions versus muons
2 cm Fe plate between modules, 50 GeV pions
Number of hits versus distance of the impinging particle from the crack
muons
pions
Pions: - The projective geometry has 20% less hits around the crack in comparison with	non-projective geometry
   - For both geometries, the crack affects an area of around 20 cm
Mons: - Response in the projective geometry drops sharply to zero. Affected area is only	several cm around the crack
  - Response in the non-projective geometry decrease by 20% in a area of about
18 cm around the crack. No muon is lost in the crack.

---
Conclusions
Considering only muon events, the non-projective geometry is
a better choice because there are no muons lost in the crack
as it is in case of the projective geometry
N.B.: It is expected that the fraction of muons which are not
detected due to the crack in the projective geometry
will be smaller in a real detector due to the presents
of the magnetic field
N.N.B: An analysis note concerning the whole crack study is
ready now and will be distributed in next few days