## Slide 1: The LHCb 2010 Computing
Philippe Charpentier
CERN – LHCb
On behalf of the LHCb Computing Group

## Slide 2: Guidelines for the Computing Model
Small processing time, but high trigger rate
  24 kHS06 required for reconstruction
    Typically 2000 CPU slots
  Tier0 could not provide the necessary CPU power
  Use Tier1s as well for reconstruction (first pass)
Most problems for analysis jobs are related to Data Management
  SE accessibility, scalability, reliability…
  Restrict the number of sites with data access
  Use Tier1s for analysis
High requirements on simulated data
  Background identification, efficiency estimation for signal
  Typically 360 HS06.s per event
  Use all possible non-Tier1 resources for simulation

## Slide 3: The LHCb Computing Model

## Slide 4: LHCb real data in 2010
LHC started with very low luminosity
  Very few colliding bunches
  Not worth for rare b-physics decays
    Minimum bias trigger for 2 months
    Introduce tighter triggers when luminosity increases
LHC change of strategy for higher luminosity
  Large number of protons per bunch
  Small squeezing
  Still low number of bunches (16, 25, 48, increasing since September, up to 400 bunches)
  Consequence: larger number of collisions per crossing
    µ=1 to 2.3 !!!
    Much higher pile-up (1.6 to 2.3 collisions per trigger)
  Effects on Computing
    Larger events
    More complex events to reconstruct
    Larger pre-selection retention

## Slide 5: Adaptability of the Computing Model
Needs to be reactive to continuously changing conditions
First months: minimum bias data
  No preselection
    Reconstruction creating DSTs for all events
As of July: large µ data
  Event size
    50 to 60 kB
    Twice more than design
  Reconstruction time
    Quadratic with event size
    4 times more than design
  Stripping time and memory
    Large combinatorics for pre-selection
    Stripping time exponential with event size
    Algorithms tuned for µ=0.4 were taking up to 60 HS06.s
      Twice the reconstruction time!
      Memory consumption up to 3 GB (nominally 1.5 GB)

## Slide 6: New Computing Conditions
Both event size and CPU time rise with µ
Compatible with expectations at µ=0.4
Notes: Brighter colors
Put a reference

## Slide 7: Adaptability (2)
Reconstruction / stripping jobs
  Need to fit in Tier1 Grid queues
    Reduce file size (nominally 3 GB) to 1 GB
  Extensive work on reducing computing time
    Reconstruction: factor 2 reduction
    Stripping: factor 10 reduction in time, large increase in rejection
Nevertheless, this takes… time!
For optimisation, data is needed
  Run with existing applications
    High failure rate (CPU time limit, max memory exceeded)
  Use a lot of space for storing too many (too large) events
  Possible thanks to the available disk (foreseen for more data)
  Continuous data management operations
    Remove obsolete processings (keep only 2)
    Reduce number of replicas (from 7 to 3 or 4)
Notes: sAve tiem on that one

## Slide 8: Weaknesses of the Grid
Workload Management System
  Mitigated by usage of pilot jobs (DIRAC)
  Workload optimisation using generic pilot jobs
    Run multiple payloads (e.g. production + analysis)
Data Management System
  Data access by protocol unreliable for long jobs
    Errors when opening files (servers overloaded)
    Connections broken when job lasts hours
  Use as few files as possible, i.e. as large as possible
    Requires merging of output files (DSTs)
    Keep runs (1 hour data taking) as granularity of datasets
  Mitigated by local copy of input data
    Standard procedure for reconstruction-stripping jobs and merging
    Not possible for analysis jobs though…
Notes: Skip a bit

## Slide 9: Data collection
42.2 pb-1 delivered
37.7 pb-1 recorded
89.3% data taking efficiency
Most data collected after 15 September

## Slide 10: RAW data distribution
65.7 TB of physics RAW data collected
  Slightly more transferred to Castor
    Calibration and test data
    Not distributed to Tier1s
Distributed immediately to Tier1s
  A full run (1 hour) goes to a single Tier1
  RAW data share according to CPU pledges of Tier1s
    When a Tier1 is unavailable, share temporarily set to 0

## Slide 11: Global Grid usage
121 sites used
  22 countries
Since April 2010:
  Simulation: 72%
    Mainly since December
  Analysis: 17%
  Reconstruction: 11%
Notes: Put labels

## Slide 12: Reconstruction jobs
Continuous processing
  From time to time reprocess all existing data when changes are worth it
    Major one in August
Notes: Remove prodsand enlarge plot

## Slide 13: Analysis jobs
Over 250 users used the Grid for analysis
  Only 2% of analysis at Tier2s (toy MC, private small simulations)
No a-priori assignment of site: share by availability of resources and data
Notes: Enlarge plot, reduce text

## Slide 14: Job success
Overall 81% successful jobs
Main cause of failures (15%): job exceeding CPU time limit
  Infinite loop in Geant4 on 64-bit
  Large µ
    Jobs eventually all completed after several retries!
  Also few user jobs
4% data access problem in application
Notes: Simulation CPU limit as well

## Slide 15: Winter re-processing
Re-processing of all 2010 data
New calibration
New pre-selection (stripping) algorithms

## Slide 16: Winter Simulation Campaign
Large campaign of simulation for extracting physics from 2010 data
  Uses the beam and detector conditions of 2010
  Steady pace of 32,000 jobs per day (about 5 million events)
  Already half of the highest priority events have been simulated

## Slide 17: Conclusions
The LHCb Computing Model looks global sound
However the new LHC running conditions imply some changes to the offline reconstruction and analysis conditions
During 2010, several iterations were needed in order to adapt to these conditions
The full reprocessing of 2010 data will take place starting in November 2010
Increase in CPU requirements and disk space will have to be watched carefully in order to match the pledges
Usage or resources beyond Tier1s for reconstruction and analysis are being investigated