## Slide 1: The High Luminosity Large Hadron Collider
Reyes Alemany
CERN BE/OP
Engineer In Charge of LHC
Journée HL-LHC à Saclay (31.05.2011)

## Slide 2: Next Years
2012
MD will tell us about the real potential of LHC  beam beam, aperture, emittance, intensity (pile-up)  may be we can do better than foreseen!!
Following measurements of the copper stabilizers during the Christmas stop we will re-evaluate the maximum energy for 2012 (Chamonix 2012)
2013
Repair/upgrade the magnet interconnects for operation at 6.5-7 TeV/beam
2014- 2017
2018
Install new collimation system in Dispersion Suppression zone  needed to reach NOMINAL LHC
2019-2030
Hardware upgrades for High Luminosity LHC  next slides
High Luminosity LHC  PEAK LUMI: 5×1034 cm-2s-1 with levelling, 250 fb-1 per year, 3000 fb-1 twelve years after the upgrade
2031-XX
High Energy LHC
CMS
ALICE
LHCb
ATLAS
This luminosity is more than ten times the luminosity reach of the first 10 years of the LHC lifetime.
MD: Machine Development

## Slide 3: The goal  5x1034 cm-2s-1
5×1034 cm-2s-1
1×1034 cm-2s-1  Nominal LHC
Leveling
limit proton burning and consequent lumi fast decay rate (peak lumi)
less pile-up
less radiation to the detectors
less heat load in IRs
L integrated = 250 fb-1 per year
L integrated = 1 fb-1 per day

## Slide 4: How  There is no magic … but the golden formula
... increase number of protons per bunch
N1,N2 = 1.7*1011
... decrease the beam size at IP
βx= βy= 0.22 m
... reduce the geometric loss factor  F
crab cavities
Goal
Φ
F
β*↓↓
↑↑
↑↑
↑↑
↓↓
L
↓↓
*
*
F is a pure crossing angle (Φ) contribution:
Φ
ρ1(x,y,s,-s0)
ρ2(x,y,s,-s0)
s
x
FLHC = 0.836
Φ

## Slide 5: The Main Ingredients
stronger focusing / larger aperture at the mini beta triplet quadrupoles. Goal:  as small as 22 cm with a
           factor 2.5 in luminosity.
 High Gradient Quadruples, Nb3 Sn technology
combined with a mechanism to compensate the geometrical reduction  Crab Cavities
combined with higher single bunch currents
 new Pre-Accelerator

## Slide 6: Luminosity Upgrade: Stronger Focusing & Larger Aperture
IP1
TAS*
Q1 Q2 Q3
D1
(1.38 T)
TAN*
D2 Q4
(3.8 T)
Q5
Q6
Q7
4.5 K
1.9 K
Warm
Separation/ Recombination
Matching Quadrupoles
Inner Triplet
1.9 K
4.5 K
4.5 K
188 mm
Tertiary collimators

## Slide 7: Stronger Focusing & Larger Aperture
Stronger focusing  smaller beam size at the IP
  High Gradient/Large Aperture Insertion Quadupole Magnets
    possibly: l = 8 m, G= 175 T/m, Φ=120 mm
    β* ≤ 22 cm are possible with a factor ~ 2.5 in luminosity by itself
new sc. technology Nb3Sn
IR2
IR1
IR3
IR4
IR5
IR6
IR7
IR8
β* = 55 cm
β*=35cm
~11 km

## Slide 8: High Field Nb3 Sn Quad
Nb3Sn is becoming a reality (first LQ l = 3.6 m – Φ = 90 mm)
This year we expect a second LQ: l = 1 m long – Φ =120 mm
In 3 years: l = 4-6 m – Φ = 120 mm - G = 180-200 T/m
G= 200 T/m
160 T/m Gequiv LHC
reminder: LHC standard inner triplet NbTi: GLHC=215 T/m, ΦLHC=66 mm
G (for a given current) = f(1/ρ2) (ρ is the aperture radius)
So for 2xΦLHC  G = ¼ x GLHC if standard NbTi technology
Clearly NbTi technology cannot be used

## Slide 9: Crab Cavities
Elliptical 800 MHz not far from being designed.
400 MHz small cavity under conceptual study, they can (?) fit in 194 mm beam-beam. Required for final solution
Technical challenge: fast, precise, compact
court. F. Zimmermann, Ed Ciapala
ρ1(x,y,s,-s0)
ρ2(x,y,s,-s0)
s
x
ρ1(x,y,s,-s0)
ρ2(x,y,s,-s0)
s
x
1st proposed in 1988, in operation at KEKB since 2007

## Slide 10: Problem: Crab Cavities have to be fast Machine Protection & Safety
Machine Protection:
beam loss & possible
machine damage
Phase space deformation in case of failure of RQ4.LR7 (A. Gómez)
Short Summary of the studies:
- quench in sc. arc dipoles: τ loss =20 - 30 ms
BLM system reacts in time, QPS is not fast enough
- failure of nc. quadrupoles: τ det = 6 ms
τ damage = 6.4 ms
- failure of nc. dipole: τ damage = 2 ms
crab cavities: instantenous ( τ ≈ ns ) → a true technical challenge
→ FMCM installed

## Slide 11: Single bunch intensity
Luminosity depends directly upon beam brightness N/ε* (i.e. particle density)
Brightness is limited by space charge at low energy in the injectors
Need to increase the injection energy in the pre-accelerator chain
Tune shift

## Slide 12: Space Charge problem
court. L. Hein
t1
t2
t3
Defocusing force

## Slide 13: LINAC4
Np=1.15  1.7 * 1011 p+/bunch
RFQ: Radio Frequency Quadrupole
DTL: Drift Tube Linac
CCTL: Coupled Cells DTL
PIMS: πMode Linac
(Linac2 50 MeV)
New tech, never used before in linacs
H-
PSB
Stripoff foil
p+
p+

## Slide 14
L. Tavian,
2005
H. Maury Cuna,
2009
“ultimate”
nominal
spare cooling capacity
for 0.55 m b*
going above Nb=1.7x1011 & ultimate luminosity requires
dedicated IR cryo plants; limit then becomes Nb~2.3x1011
spare
cooling
capacity
at zero
luminosity
(=total-SR
-impedance)
e-cloud
heat
load for
SEY=1.3
Cooling & e- heat for 25 ns spacing
More Lumi  More cooling power

## Slide 15
(longer flat bunches)
L. Tavian,
2005
H. Maury Cuna,
2009
spare cooling capacity
for 0.25 m b*
Spare cooling
Capacity at zero
Luminosity (=total-SR-impedance)
e-cloud
heat
load for
SEY=1.5!
going above Nb=2.3x1011 & ultimate luminosity requires
dedicated IR cryo plants; limit then becomes Nb~5.0x1011
cooling & e- heat for 50 ns spacing

## Slide 16: Are there any other challenges ? ... sure there are
Intensity dependence of Electronics:
  e.g. BPM signals
One nominal bunch of 1×1011
slowly scraped away using a primary collimator
Intensity (p+/bunch)
time
1010
2
4
6
8
10
Low Sensitivity
High Sensitivity
Dead zone where neither setting works well
×1010
×1010
Average (position(t)-position(to)) (µm)
Average (position(t)-position(to)) (µm)
Intensity (p+/bunch)
Intensity (p+/bunch)

## Slide 17: Problem: Collimation Efficiency
  Collimation limits luminosity to 2*1033 cm-2s-1
   additional collimators needed in the cold section
Option: stronger and shorter dipole magnets
... again: Nb3 Sn technology
Nb3Sn 4.2 K
Nb3Sn 1.9 K
B coil
Jc (A/mm2)
Field (T)
2
4
6
8
10
12
14
16

## Slide 18: Problem: Radiation Background
Displacement of Power Converters & DFBs of Inner Triplets and other equipment on surface by means of SC links.
1.1 mm
MgB2 wire
MgB2 Tc=39K
or even Bi-2223 / Y-123

## Slide 19: How can we level?
F is a pure crossing angle (Φ) contribution:
Φ
ρ1(x,y,s,-s0)
ρ2(x,y,s,-s0)
s
x
FLHC = 0.836
Φ
1. Via crossing angle
2. Via the β*
Leveling by separation used today at LHCb
3. Via beam separation

## Slide 20: What happens to the pile-up?
µ_NOMINAL LHC= 1034 cm-2s-1 6x10-26 cm2 / (32 x106 s-1) ~ 20
inelastic cross section
bunch collision rate
#events per bunch crossing:
e.g. 10 times higher luminosity at same #bunches
→ ~200 events per crossing
Detector upgrade!

## Slide 21: thank you for your attention!
generated tracks per crossing,
pt > 1 GeV/c cut, i.e. all soft tracks removed!
5x1034 cm-2s-1
I. Osborne

## Slide 22: LHC Performance Estimates
22
Chamonix, January 2011 Oliver Brüning BE-ABP
Parameter | nominal | 25ns | 50ns | 50ns
N | 1.15E+11 | 1.2E+11 | 1.7E+11 | 1.7E+11
nb | 2808 | 2808 | 1404 | 1404
beam current [A] | 0.58 | 0.61 | 0.43 | 0.43
x-ing angle [mrad] | 300 | 320 | 320 | 270
beam separation [s] | 10 | 10 | 10 | 10
b* [m] | 0.55 | 0.5 | 0.5 | 0.5
en [mm] | 3.75 | 3.75 | 3.75 | 2.5
eL [eVs] | 2.51 | 2.5 | 2.5 | 2.5
energy spread | 1.00E-04 | 1.00E-04 | 1.00E-04 | 1.00E-04
bunch length [m] | 7.50E-02 | 7.50E-02 | 7.50E-02 | 7.50E-02
IBS horizontal [h] | 80 -> 106 | 101 | 71 | 29
IBS longitudinal [h] | 61 -> 60 | 58 | 41 | 25
Piwinski parameter | 0.68 | 0.76 | 0.76 | 0.78
geom. reduction | 0.83 | 0.80 | 0.80 | 0.79
beam-beam / IP | 3.10E-03 | 3.1E-03 | 4.4E-03 | 6.6E-03
Peak Luminosity | 1 1034 | 1.0 1034 | 1.2 1034 | 1.7 1034
nominal emittance
small emittance
Performance reach for existing machines @ 7 TeV:
Radiation
damping:
hor: 26h
ver: 13h
Notes: Smaller than nominal beam current for small emittance beam; aperture margin due to smaller required crossing angle; potential for smaller beta*, less e-cloud effect due to larger bunch spacing; Transverse damping time = 26 h and longitudinal damping time = 13 h; RF noise seems to be small

## Slide 23: LHC Performance Estimates
23
Performance reach for existing machines + LINAC4:
Chamonix, January 2011 Oliver Brüning BE-ABP
Parameter | nominal | 25ns | 50ns
N | 1.15E+11 | 1.4E+11 | 2.5E+11
nb | 2808 | 2808 | 1404
beam current [A] | 0.58 | 0.71 | 0.64
x-ing angle [mrad] | 300 | 320 | 320
beam separation [s] | 10 | 10 | 10
b* [m] | 0.55 | 0.5 | 0.5
en [mm] | 3.75 | 3.75 | 3.75
eL [eVs] | 2.51 | 2.2 | 2.5
energy spread | 1.00E-04 | 1.00E-04 | 1.00E-04
bunch length [m] | 7.50E-02 | 7.50E-02 | 7.50E-02
IBS horizontal [h] | 80 -> 106 | 80 | 45
IBS longitudinal [h] | 61 -> 60 | 41 | 23
Piwinski parameter | 0.68 | 0.76 | 0.76
geom. reduction | 0.83 | 0.80 | 0.80
beam-beam / IP | 3.10E-03 | 3.64E-03 | 6.5E-03
Peak Luminosity | 1 1034 | 1.6 1034 | 2.5 1034
nominal emittance
Notes: 50ns beam option provides possibility of more than twice the nominal performance at approximately nominal total beam current; reduced e-cloud due to larger bunch spacing

## Slide 24: LHC Performance Estimates
24
Chamonix, January 2011 Oliver Brüning BE-ABP
Parameter | nominal | 25ns | 50ns | 25ns | 50ns
N | 1.15E+11 | 2.0E+11 | 3.3E+11 | 2.0E+11 | 3.3 E+11
nb | 2808 | 2808 | 1404 | 2808 | 1404
beam current [A] | 0.58 | 1.02 | 0.84 | 1.02 | 0.84
x-ing angle [mrad] | 300 | 420 | 520 | 270 | 320
beam separation [s] | 10 | 10 | 10 | 10 | 10
b* [m] | 0.55 | 0.2 | 0.2 | 0.5 | 0.5
en [mm] | 3.75 | 2.5 | 3.75 | 2.5 | 3.75
eL [eVs] | 2.51 | 3.0 | 3.0 | 3.0 | 3.0
energy spread | 1.00E-04 | 1.00E-04 | 1.00E-04 | 1.00E-04 | 1.00E-04
bunch length [m] | 7.50E-02 | 0.1 | 0.1 | 0.1 | 0.1
IBS horizontal [h] | 80 -> 106 | >40 | 56 | >40 | 56
IBS longitudinal [h] | 61 -> 60 | >40 | 56 | >40 | 56
Piwinski parameter | 0.68 | 2.57 | 2.59 | 1.04 | 1.00
geom. reduction | 0.83 | 0.36 | 0.36 | 0.69 | 0.70
beam-beam / IP | 3.10E-03 | 3.6E-03 | 4.9E-03 | 6.8E-3 | 7.6E-3
Peak Luminosity | 1 1034 | 5.5 1034 | 4.9 1034 | 4.2 1034 | 3.9 1034
small b*
‘large’ b*
Performance reach for LINAC4 + LIU + HL triplet: long bunch
Beam current well beyond ultimate design is needed
Notes: Gain from lower beta* becomes smaller if bunch length is increased

## Slide 25: Beam parameters (nominal)
 |  | Injection | Collision
Proton energy | GeV | 450 | 7000
Particles/bunch |  | 1.15 x 1011 | 
Num. bunches |  | 2808 | 
Longitudinal emittance (4) | eVs | 1.0 | 2.5
Transverse normalized emittance | µm rad | 3.5 | 3.75
Beam current | A | 0.582 | 
Stored energy/beam | MJ | 23.3 | 362
Peak luminosity related data |  |  | 
RMS bunch length | cm | 11.24 | 7.55
RMS beam size @IP1 & IP5  x,y =  | µm | 375.2 | 16.7
RMS beam size @IP2 & IP8  x,y =  | µm | 279.6 | 70.9
Geometric luminosity reduction factor (F) |  |  | 0.836
Instantaneous lumi @IP1 & IP5 (IP2Pb-Pb, IP8) | cm-2s-1 |  | 1034(1027 , 1032)
Instantaneous lumi/bunch crossing @IP1 & IP5 | cm-2s-1 |  | 3.56 x 1030
= 0.55 m
 = 0.5 nm rad
= 10 m
 = 0.5 nm rad

## Slide 26: approaches to boost LHC luminosity
low b* & crab cavities (80 MV)
low b* & higher harmonic RF (7.5 MV @800 MHz) + LR compensation
large Piwinski angle (& “flat” bunch shape) + LR-BB compensation
always pushing intensity to “limit”
qc
qc
qc