## Slide 1
Pion test beam from KEK: momentum studies
Data provided by Toho group:
2512 beam tracks
D. Duchesneau April 27th 2011
Track qx
Track qy
Base track positions
Relative X (mm)
Relative Z (mm)
Relative Z (mm)
Relative Y (mm)
Base track positions

## Slide 2
For the momentum measurement the number of segments per track is chosen > 15
Number of segments/track
3 D angle
Angle (rad)
Assumption: the base tracks are already corrected for plate alignment.

## Slide 3
calculating BT resolution ...
P=3317 MeV/c (this momentum is lower than expected for a 4 GeV/c pion beam)
double base track resolution= 4.13 mrad
From the sigma of the previous distribution we usually fit the Ncell dependence with the MCS formula with the base track resolution and the global momentum as free parameters
Observation of a different resolution in XZ and YZ projection planes. Also some geometrical shifts of the plates=> very good and efficient discussion with Toho group ; it has been studied in deeper details.

## Slide 4
Using only the angle differences measured in XZ plane
Using only the first 400 tracks from the file
data
rad
XZ
Very similar to Toho measurement even the shape
Using the first 1000 tracks from the file
XZ
Control of the mean angle shifts to understand the difference
We have the same values if we use the full data set
rad

## Slide 5
Momentum obtained from p and 1/p distribution =3.81 GeV/c
Resolution D(1/p)/(1/p)=[39.6+-6.1] %
Applying track by track the PMCS algorithm with the double base track resolution= 4.13 mrad
This resolution is less than expected (30%) from this algorithm but this is due to the double base track resolution of 4.1 mrad instead of 2.1 mrad.
p
1/p
1- <p>/p
Data
Data
Data
Test beam data

## Slide 6
Monte Carlo Studies (double base track angular resolution of 2.4 mrad)
Use a sample of 4 GeV pion tracks simulated in a brick
XZ + YZ
MC
calculating BT resolution ...
P=3.8 GeV/c
double base track resolution= 2.5 mrad
Note the Y axis scale
Choose only portion of tracks to match the number of segments in the KEK data (about 20)
rad
rad

## Slide 7
Momentum obtained from p and 1/p distribution =4.09 GeV/c
Resolution D(1/p)/(1/p)=[29.2+-2.6] %
Applying track by track the PMCS algorithm with the double base track resolution= 2.4 mrad
p
1/p
1- <p>/p
MC
MC
MC
Monte Carle events (double base tracks angular resolution of 2.4 mrad)

## Slide 8
Monte Carlo Studies (double base track angular resolution of 4.1 mrad)
Use a sample of 4 GeV pion tracks simulated in a brick
XZ + YZ
MC
calculating BT resolution ...
P=3.8 GeV/c
double base track resolution= 4.06 mrad
Note the Y axis scale
Choose only portion of tracks to match the number of segments in the KEK data (about 20)
rad
rad

## Slide 9
Momentum obtained from p and 1/p distribution =3.96 GeV/c
Resolution D(1/p)/(1/p)=[34.6+-2.8] %
Applying track by track the PMCS algorithm with the double base track resolution= 4.06 mrad
p
1/p
1- <p>/p
MC
MC
MC
Monte Carle events (double base track angular resolution of 4.1 mrad)

## Slide 10
KEK data
P3D=3.81373[0.0347992] GeV - DP/P=39.6496[6.07086] %
PL=3.79157[0.0212307] GeV - DP/P=43.0014[5.00714] %
PT=3.85968[0.0366781] GeV - DP/P=43.6257[6.51717] %
MC
2.4 mrad in both projections
P3D=4.0879[0.00929236] GeV - DP/P=29.2465[2.65249] %
PL=4.08167[0.0168638] GeV - DP/P=34.1401[3.81461] %
PT=4.15084[0.0139606] GeV - DP/P=33.8707[3.4425] %
4.06 mrad in both projections
P3D=3.95652[0.00884724] GeV - DP/P=34.622[2.85425] %
PL=3.98682[0.036938] GeV - DP/P=42.0231[6.31024] %
PT=4.22465[0.000709772] GeV - DP/P=42.4319[1.29759] %
Data
Transverse coord.
MC
Transverse coord.
P (GeV/c)
P (GeV/c)
Summary in 3D and in transverse and longitudinal projections
Note: the sensitivity to BT resolution is very high with 4 mrad at 4 GeV

## Slide 11
Some examples of a few tracks;
the blue line corresponds to a 4 GeV/c beam track and the black line is the MCS fit result:
Pmcs=3.99 GeV/c
Pmcs=3.38 GeV/c
Track 1
Track 5
Test beam data

## Slide 12
Pmcs=5.44 GeV/c
Pmcs=3.99 GeV/c
Track 8
Track 7
Test beam data

## Slide 13
Conclusions:
The momentum measured with the test beam data provided by Toho is:
3.8 GeV/c with an uncertainty on the absolute scale of about 7%.
This uncertainty is mainly dominated by the angular resolution knowledge
The resolution is estimated to be 39% when using both projections and 43% in the transverse projection only
MC studies of 4 GeV/c pions gives (with the same algorithm) 4.1 GeV/c with a systematic uncertainty of about 5% which has been estimated by changing the fit range, varying the angular resolution, changing the track length etc…
We continue detailed comparison with Toho measurements and we track the differences in the momentum estimates knowing that the angular measurements are the same.

## Slide 14
Pmcs=3.99 GeV/c
Pmcs=3.78 GeV/c
Double BT resolution = 4.1 mrad
Double BT resolution = 3.9 mrad
Understanding of the difference in fit result between Toho an DD for the track 1
Going from 4.1 mrad to 3.9 mrad the momentum decreases by about 6%
=> 3.99 GeV/c becomes 3.78 GeV/c and the fitted line should now match Toho fit
The remaining difference in the P value comes from a different scaling factor used in the MCS formula. In our MCS study we are using 14.64 instead of the usual 13.6. This was estimated with MC data and test beam data with the OPERA brick structure composed of lead+emulsion. The net effect is to scale up the momentum by 7.6%.
=> 3.78 GeV/c becomes 3.51 GeV/c
Note that a resolution of the order of 4 mrad makes the momentum measurement sensitivity of 3 or 4 GeV particles more critical than the sensitivity one can get with a smaller resolution of 2 mrad where a 5% change would not make a 6% effect. It should be taken as a systematic probably.
D. Duchesneau, May 6th 2011

## Slide 15
The reason why it is not at 0 for the first emulsion plate is that the phi angle used to transform the reference frame to TL planes is not calculated using the first base track slopes.
The phi is obtained from the direction of an average track fitted to all the base tracks. This avoids some possible or too strong deviation of the first base tracks.
This can also explain the very little difference seen in the position of the data points shown on the plots of the previous slides.
Summary:
The difference of 13% on the momentum of track 1 can be explained by the different MCS formula factor and the different double base track resolution (4.1 vs 3.9 mrad)
Now if we apply 3.9 mrad instead of 4.1 mrad to the whole pion data set, the beam momentum measurement goes from 3.78 GeV/c to 3.58 GeV/c.
Concerning these plots:

## Slide 16
// correlation matrix (long tracks more than 50 plates)
{
1.0000000 , 0.7019440 , 0.6305600 , 0.5719876 , 0.5257840 , 0.4969909 , 0.4632392 , 0.4348128 , 0.4113047 , 0.3895742 , 0.3672101 , 0.3548928 , 0.3354470 ,
0.7019440 , 1.0000000 , 0.8324922 , 0.7697662 , 0.7219567 , 0.6786730 , 0.6373476 , 0.6047858 , 0.5727320 , 0.5476525 , 0.5177510 , 0.5037926 , 0.4806298 ,
0.6305600 , 0.8324922 , 1.0000000 , 0.8787227 , 0.8373768 , 0.8019863 , 0.7648694 , 0.7319199 , 0.6988111 , 0.6742211 , 0.6417400 , 0.6229187 , 0.5976337 ,
0.5719876 , 0.7697662 , 0.8787227 , 1.0000000 , 0.9139644 , 0.8816085 , 0.8511400 , 0.8181283 , 0.7891668 , 0.7613313 , 0.7320850 , 0.7089916 , 0.6870035 ,
0.5257840 , 0.7219567 , 0.8373768 , 0.9139644 , 1.0000000 , 0.9336929 , 0.9063070 , 0.8758149 , 0.8474949 , 0.8213611 , 0.7904972 , 0.7679949 , 0.7429309 ,
0.4969909 , 0.6786730 , 0.8019863 , 0.8816085 , 0.9336929 , 1.0000000 , 0.9484023 , 0.9238797 , 0.8982391 , 0.8724679 , 0.8444602 , 0.8190991 , 0.7949968 ,
0.4632392 , 0.6373476 , 0.7648694 , 0.8511400 , 0.9063070 , 0.9484023 , 1.0000000 , 0.9588344 , 0.9382656 , 0.9170466 , 0.8911247 , 0.8704507 , 0.8463998 ,
0.4348128 , 0.6047858 , 0.7319199 , 0.8181283 , 0.8758149 , 0.9238797 , 0.9588344 , 1.0000000 , 0.9644410 , 0.9475883 , 0.9269939 , 0.9063236 , 0.8852876 ,
0.4113047 , 0.5727320 , 0.6988111 , 0.7891668 , 0.8474949 , 0.8982391 , 0.9382656 , 0.9644410 , 1.0000000 , 0.9683985 , 0.9525011 , 0.9346613 , 0.9158600 ,
0.3895742 , 0.5476525 , 0.6742211 , 0.7613313 , 0.8213611 , 0.8724679 , 0.9170466 , 0.9475883 , 0.9683985 , 1.0000000 , 0.9728346 , 0.9600545 , 0.9437444 ,
0.3672101 , 0.5177510 , 0.6417400 , 0.7320850 , 0.7904972 , 0.8444602 , 0.8911247 , 0.9269939 , 0.9525011 , 0.9728346 , 1.0000000 , 0.9763121 , 0.9641387 ,
0.3548928 , 0.5037926 , 0.6229187 , 0.7089916 , 0.7679949 , 0.8190991 , 0.8704507 , 0.9063236 , 0.9346613 , 0.9600545 , 0.9763121 , 1.0000000 , 0.9780779 ,
0.3354470 , 0.4806298 , 0.5976337 , 0.6870035 , 0.7429309 , 0.7949968 , 0.8463998 , 0.8852876 , 0.9158600 , 0.9437444 , 0.9641387 , 0.9780779 , 1.0000000
} ;
// covariance matrix (x 3249 tracks)
Double_t cc[169]=
{
0.0002831 , 0.0002555 , 0.0002742 , 0.0002952 , 0.0003151 , 0.0003400 , 0.0003537 , 0.0003689 , 0.0003801 , 0.0003929 , 0.0004017 , 0.0004237 , 0.0004286 ,
0.0002555 , 0.0004679 , 0.0004653 , 0.0005108 , 0.0005561 , 0.0005968 , 0.0006257 , 0.0006596 , 0.0006803 , 0.0007100 , 0.0007280 , 0.0007733 , 0.0007895 ,
0.0002742 , 0.0004653 , 0.0006678 , 0.0006966 , 0.0007706 , 0.0008425 , 0.0008970 , 0.0009536 , 0.0009917 , 0.0010443 , 0.0010780 , 0.0011422 , 0.0011728 ,
0.0002952 , 0.0005108 , 0.0006966 , 0.0009410 , 0.0009984 , 0.0010994 , 0.0011849 , 0.0012653 , 0.0013294 , 0.0013999 , 0.0014598 , 0.0015433 , 0.0016004 ,
0.0003151 , 0.0005561 , 0.0007706 , 0.0009984 , 0.0012682 , 0.0013517 , 0.0014647 , 0.0015725 , 0.0016574 , 0.0017532 , 0.0018299 , 0.0019407 , 0.0020092 ,
0.0003400 , 0.0005968 , 0.0008425 , 0.0010994 , 0.0013517 , 0.0016527 , 0.0017497 , 0.0018936 , 0.0020053 , 0.0021260 , 0.0022316 , 0.0023629 , 0.0024544 ,
0.0003537 , 0.0006257 , 0.0008970 , 0.0011849 , 0.0014647 , 0.0017497 , 0.0020596 , 0.0021939 , 0.0023384 , 0.0024946 , 0.0026289 , 0.0028032 , 0.0029171 ,
0.0003689 , 0.0006596 , 0.0009536 , 0.0012653 , 0.0015725 , 0.0018936 , 0.0021939 , 0.0025420 , 0.0026703 , 0.0028637 , 0.0030382 , 0.0032425 , 0.0033896 ,
0.0003801 , 0.0006803 , 0.0009917 , 0.0013294 , 0.0016574 , 0.0020053 , 0.0023384 , 0.0026703 , 0.0030157 , 0.0031876 , 0.0034002 , 0.0036422 , 0.0038195 ,
0.0003929 , 0.0007100 , 0.0010443 , 0.0013999 , 0.0017532 , 0.0021260 , 0.0024946 , 0.0028637 , 0.0031876 , 0.0035928 , 0.0037906 , 0.0040834 , 0.0042959 ,
0.0004017 , 0.0007280 , 0.0010780 , 0.0014598 , 0.0018299 , 0.0022316 , 0.0026289 , 0.0030382 , 0.0034002 , 0.0037906 , 0.0042257 , 0.0045035 , 0.0047596 ,
0.0004237 , 0.0007733 , 0.0011422 , 0.0015433 , 0.0019407 , 0.0023629 , 0.0028032 , 0.0032425 , 0.0036422 , 0.0040834 , 0.0045035 , 0.0050353 , 0.0052707 ,
0.0004286 , 0.0007895 , 0.0011728 , 0.0016004 , 0.0020092 , 0.0024544 , 0.0029171 , 0.0033896 , 0.0038195 , 0.0042959 , 0.0047596 , 0.0052707 , 0.0057672
};

## Slide 17
//______________________________________________________________________________
void GraphFitChisquareDD(Int_t &npar, Double_t * /*gin*/, Double_t &f,
Double_t *u, Int_t /*flag*/)
{
//*-*-*-*-*-*Minimization function for Graphs using a Chisquare method*-*-*-*-*
//*-* =========================================================
//
// In case of a TGraphErrors object, ex, the error along x, is projected
// along the y-direction by calculating the function at the points x-ex and
// x+ex.
//
// The chisquare is computed as the sum of the quantity below at each point:
//
// (y - f(x))**2
// -----------------------------------
// ey**2 + ((f(x+ex) - f(x-ex))/2)**2
//
// where x and y are the point coordinates
Put covariance Matrices etc…. here
TVirtualFitter *grFitter = TVirtualFitter::GetFitter();
TGraph *gr = (TGraph*)grFitter->GetObjectFit();
TF1 *f1 = (TF1*)grFitter->GetUserFunc();
Foption_t Foption = grFitter->GetFitOption();
Int_t n = gr->GetN();
Double_t *gx = gr->GetX();
Double_t *gy = gr->GetY();
Double_t fxmin = f1->GetXmin();
Double_t fxmax = f1->GetXmax();
npar = f1->GetNpar();
// printf(" we are in GraphFit of EdbMomentum \n");
f1->InitArgs(x,u);
f = 0;
for (bin=0;bin<n;bin++) {
x[0] = gx[bin];
if (!f1->IsInside(x)) continue;
cu = gy[bin];
TF1::RejectPoint(kFALSE);
fu = f1->EvalPar(x,u);
if (TF1::RejectedPoint()) continue;
fsum = (cu-fu);
npfits++;
if (Foption.W1) {
f += fsum*fsum;
continue;
}
ex = gr->GetErrorX(bin);
ey = gr->GetErrorY(bin);
if (ex < 0) ex = 0;
if (ey < 0) ey = 0;
if (ex > 0) {
xm = x[0] - ex; if (xm < fxmin) xm = fxmin;
xp = x[0] + ex; if (xp > fxmax) xp = fxmax;
xx[0] = xm; fm = f1->EvalPar(xx,u);
xx[0] = xp; fp = f1->EvalPar(xx,u);
eux = 0.5*(fp-fm);
} else
eux = 0.;
eu = ey*ey+eux*eux;
if (eu <= 0) eu = 1;
f += fsum*fsum/eu;
if (bin<13) v[bin] = fsum; // fill with residual
}
// perform residual^T COV^-1 residual vector matrix vector operation
v2 = v;
v *= hinv;
f = v*v2; minimise this value
f1->SetNumberFitPoints(npfits);
}
Modify the Minimization function for Graphs
eG=new TGraphErrors(vind3d,da,errvind3d,errda);
TVirtualFitter::Fitter(eG)->SetFCN(GraphFitChisquareDD);
eG->Fit("eF1","QRU");
Use the modified the Minimization function for Graphs

## Slide 18
MC 4 GeV pions:
No covariance matrix for the fit
Error from fit (GeV)
Error from parametrisation (GeV)
D. Duchesneau 16/05/2011

## Slide 19
MC 4 GeV pions:
With covariance matrix for the fit
Error from parametrisation (GeV)
Error from fit (GeV)
Conclusion: taking into account the correlations makes a 5% systematic effect
And the error from the fit matches well the parametrisation used,

## Slide 20
Momentum obtained from p and 1/p distribution =3.9 GeV/c
Resolution D(1/p)/(1/p)=[27.5+-2.3] %
Applying track by track the PMCS algorithm with the double base track resolution= 2.1 mrad
p
1/p
1- <p>/p
Data
Data
Data
Test beam data from Napoli

## Slide 21
Monte Carlo Studies (4 GeV pions)
calculating BT resolution ...
P(XZ)=3.8 GeV/c
double base track resolution= 2.5 mrad
calculating BT resolution ...
P(YZ)=3.8 GeV/c
double base track resolution= 2.5 mrad
XZ
YZ
XZ
YZ
MC
MC
MC
MC
In the MC all the values are in full agreement between (XZ+YZ) and XZ and YZ
rad
rad
rad
rad