## Slide 1: ATLAS T1/T2 Name Space Issue with Federated Storage
Hironori Ito
Brookhaven National Laboratory

## Slide 2: Global name space
Federated storage
  Universal access to all available storages
    Protocol
      Xrootd, http, etc…
    Name space
      File name itself should uniquely determine the location of the file in the storage system.

## Slide 3: GUID, physical file path in storage and logical file path in LFC
GUID of a file is the unique identifier.
  Unique key in LFC, eg. lcg-la guid:XYZ
  It maps to a particular path in LFC name space.
    /grid/atlas/dq2/mc10_7TeV/NTUP_TOP/e737_s933_s946_r2215_r2260_p542/mc10_7TeV.107670.AlpgenJimmyZtautauNp0_pt20.merge.NTUP_TOP.e737_s933_s946_r2215_r2260_p542_tid326436_00/NTUP_TOP.326436._000527.root.1
One guid/lfc path can have multiple physical files.
  In the different SEs
  In the same SE in different physical paths

## Slide 4: Physical file path
ATLAS physical file
  No Global name space of physical files
    Various space tokens in a single SRM end point
      Identical files could be located at various SURL paths
    Use of _sub by Panda system
    Use of DQ2_XYZ extensions
        Caused by the lack of “re-name” in SRM protocol.
          SRM should do this internally!
            Essential for the tape area since the external rename is a bit tricky
        Without its use, due to asynchronous nature of write and delete, legitimate files could be deleted after the successful transfers (particularly after a few failed transfers)
          Really painful to clean.

## Slide 5: Logical file path
ATLAS logical file
  Logical file path in LFC is generally universal
    No _DQ2_XZY extension unlike physical file
    No storage dependent prefix or suffix
      Does not depend on the space tokens.
      Does not depend on the storage service name
        srm/managerv2
        srm/v2/server
      Almost deterministic based on the dataset name.
  It is the closest thing to be the global name space
    Still has _sub directories at T1s
    Still has some site dependence on the site configuration
      Eg
        User datasets locations are defined in PANDA schedule configuration, which are different for each sites.

## Slide 6: Not quite unique LFC path
Example of dataset name and file
  DSN: mc10_7TeV.107670.AlpgenJimmyZtautauNp0_pt20.merge.NTUP_TOP.e737_s933_s946_r2215_r2260_p542_tid326436_00
  File name NTUP_TOP.326436._000527.root.1
  Should be located in LFC as /grid/atlas/dq2/mc10_7TeV/NTUP_TOP/e737_s933_s946_r2215_r2260_p542/ NTUP_TOP.326436._000527.root.1
  Could be located at one of many /grid/atlas/dq2/mc10_7TeV/NTUP_TOP/e737_s933_s946_r2215_r2260_p542/mc10_7TeV.107670.AlpgenJimmyZtautauNp0_pt20.merge.NTUP_TOP.e737_s933_s946_r2215_r2260_p542_tid326436_00_subXYZ/NTUP_TOP.326436._000527.root.1
    T1s only!!! For files produced at T2s, “_sub” are lost by DDM transfer.
  ATLAS convention is not quite concrete
    Forced by SE limitation
      Ext3 file system: 64K sub directories.
      HPSS file system: 64K sub directories.

## Slide 7: Name space convention changing
The convention has changed over the years.
  Force by the storage file system limitation
    64K subdirectories limit in ext3
    64K subdirectories limit HPSS tape systems
  Eg
    DSN/file: data11_7TeV.00180309.physics_Egamma.merge.NTUP_TOP.f369_m812_p530_p577_tid367204_00/ NTUP_TOP.367204._000043.root.1
      Current convention:
        /atlas/dq2/data11_7TeV/NTUP_TOP/f369_m812_p530_p577/data11_7TeV.00180309.physics_Egamma.merge.NTUP_TOP.f369_m812_p530_p577_tid367204_00/ NTUP_TOP.367204._000043.root.1
      Actual path
        /atlas/dq2/data11_7TeV/NTUP_TOP/data11_7TeV.00180309.physics_Egamma.merge.NTUP_TOP.f369_m812_p530_p577_tid367204_00_sub021131151/ NTUP_TOP.367204._000043.roo.1

## Slide 8: Different LFC path at different site
Caused by the difference in the site configuration
  Lfcpath=/grid/atlas/dq2
  Lfcpath=/grid/atlas/users/pathena
    Eg. File User.ABC.DDD.1 could be located at
      /grid/atlas/dq2/user/ABC/DDD/user.ABC.DDD.1
      /grid/atlas/users/pathena/user/ABC/DDD/user.ABC.DDD.1

## Slide 9: Name-to-name module
xRootd allows the use of external module to translate the externally requested path to the actual path in the storage
  Name-to-name module
External request
/a/b/c/d.1
Actual file
/V/W/X/Y/Z.1
Name-to-name

## Slide 10: Current name-to-name module
Current implementation of NtoN module by Charles
  Search files in LFC name space
  Leading /grid is removed from LFC path.
    /grid/atlas/A/B/C -> /atlas/A/B/C
    In US LFCs, there is a symlink in LFC. /atlas is a simlink for /grid/atlas
      So, it is equivalent.
  The request is expected to be correctly formatted in the current ATLAS convention.
    /atlas/dq2/proj/…./filename
  It can search parent _subXYZ directories (for T1s)
    Eg. /atlas/dq2/A/B/C.1 -> /atlas/dq2/A/B_subXYZ/C.1

## Slide 11: Deficiency of current NtoN
Not 100% of files can be found.
  Files are stored with the different conventions won’t be found.
  Search on _subXYZs might be problematic???
  Inherent problem of assuming that the file path in LFC is unique.
    Only GUID is unique.
      If guid was the filename in the flat filename structure, we won’t be having this discussion.
        Can’t be possible by the SE’s limitation

## Slide 12: Improving NtoN
Modify the possible search path to accommodate the changing conventions and/or configuration
Add correct symlink
Use GUID:
  DQ2 has 100% hit rate because it uses GUID to find a file.
    Eg. To find /A/B/C/D.1, NtoN might accept /A/B/C/D.1+guid=XYZ

## Slide 13: dCache xRootd door with NtoN
dCache has the own, native xRootd service.
  Can access files via xrootd protocol.
Name-to-name is not quite modular or flexible.
  Prefix can be changed with fixed path.
  ATLAS needs dynamic changes of path.
    Needs code change->doable.