## Slide 1: MPGDs for neutron detection applications
A. Delbart,
CEA/DSM-IRFU,
CE-Saclay, 91191 Gif-Yvette, France
2D-200 GEM CASCADE
n-TOF 2D X-Y neutron
micromegas beam profiler

## Slide 2: Outline
Neutron detection : applications, principles, commonly used detectors
The « 3He crisis » and the need for new & innovative high efficiency, large area 3He free neutron detectors
Some examples of neutron detectors using MPGDs :
  for neutron radiography
  for neutron beam profile & flux measurement
  for Time Of Flight neutron spectroscopy
  for nuclear reactor in-core neutron flux measurements
Conclusions & perspectives

## Slide 3: Neutron detection applications
Industrial applications
Fundamental research
Homeland security
Nuclear reactor instrumentation
The science which can be made with the use of neutron beams is, in many cases, unbeatable or even inaccessible to any other methods thanks to the neutron unique properties. Use to investigate structure & dynamics of mater.
Control (neutron flux) & safety
Nuclear safeguards
safeguards systems are installed at facilities that process, handle, use and store Pu, U, nuclear fuel, spent fuel or nuclear waste
oil and gas exploration : use in conjunction with a neutron source to locate hydrogenous materials, severe 320°C temperature and vibrations environment
neutron scattering experiments for material science, food and medical research
Detection of radioactive materials, explosives, chemical and biological warfare agents, narcotics for air and ground and sea transportations (cargo screening, airport security, …)
Out core (in measurement pits) : > 1010 n.cm-2.s-1, 103 à 104 Gy.h-1of g, 80 to 100°C.
In core (in guide tubes in the center of the fuel elements assembly) :
> 1014 n.cm-2.s-1, 107 Gy.h-1 of g, 320°C.
Neutron radiography : Non destructive survey of materials
Neutrons can penetrate high density materials, which are opaque to X-rays, thus allowing the inspection of objects obstructed by a dense material
For experiments on high intensity neutron sources (SNS, ESS, …), the high counting rate is one of the key issues for small-angle neutron scattering experiments and neutron reflectometry for instance.
Neutron radiography
X-ray radiography

## Slide 4: Detecting neutrons
Ref: A. Oed, NIM A 525 (2004) 62–68
Natural
abundance
=1.8 Å
5320
942
3842
255k
1,4 10-4 %
7,4%
19.8%
0,7%
16%
Commonly Used thermal Neutron Reactions
As charge-neutral particles, neutrons can only interact via strong interactions and ionize via secondary reactions
n(113Cd, Cd) e- Conversion electrons 0,558 20,7k
gas
solid
~ 1/v ~ E-1/2
+ gs
2 ways to detect fast neutrons
– Thermalize  only provide neutron flux (lose position)
– Elastic scattering from protons at high energy : proton detection & reconstruction of recoils for time-of-flight (ToF)
25,3 meV
Cross
Section (b)
1.8 Å

## Slide 5: Position sensitive detectors for thermal neutrons
Ref: A. Oed, NIM A 525 (2004) 62–68
3He

## Slide 6: Commonly and worldwide used thermal neutron detectors
Gas proportional counters
g lab. St Gobain (Fr)
3He gas counters
P=5-10 bar (!)
V >850V (2 bar)
1.75 kV (10 bar)
Gain~ >20
BF3 gas counters
Toxic & corrosive
P ~ 0.5 – 1 atm
reV~ 2000 – 3000 V
Gain ~ 100-500
Typical 25 mm diameter tube, 50 μm anode
BF3 or
C ~ 20 pF / Tcollection > 10 μs (!)
… and Boron-lined proportional counters (10B conversion layer, Ar+CO2 …)
centronics (UK)
Referenced to BF3
@0,68 bar
90% 10B enriched
10B layer for Boron-lined
proportional counters

## Slide 7: Optimum converter layer thickness and detection efficiency
Ref: C. Höglund, J. Birch, et al. “B4C thin films for neutron detection”, JVST, submitted (2011)
30 layers for 64% efficiency
≈ 1 mm 10B4C for max
73% escape efficiency
Other foil materials @1.8 Å
Ref: A. Oed, NIM A 525 (2004) 62–68

## Slide 8: Beam-line IN5@ILL: a time-of-flight spectrometer for quasi-elastic and inelastic scattering
http://www.ill.eu/fileadmin/users_files/multimedia/IN5/ill_in5.swf
Position sensitive proportional
Counter tubes
3m long position-sensitive proportional counters

## Slide 9
The 3He crisis
3He is a by product of Tritium production for use in nuclear weapons by Titium ß-decay into 3He with a half life of 12.3 years.
End of the Cold War the 3He : production from Tritium decay has been reduced and since September 2001 the demand of 3He has increased drastically due to security programs
severe depletion of the existing 3He stockpile and shortage.
Cost increase by a factor of 25 , from 80 €/l up to 2000 €/l.
The cost for the ILL/IN5 30 m2 3He detector (3000 l @ 4.5 bars) was 1.5 M€
(incl. 240 k€ for 3He). It would cost 7.2 M€ (incl. 6 M€ for 3He) today !!!
3He demand for neutron scattering in 2009 – 2015 is estimated to 125 kl and the projected demand for US security applications is 100 kl for a ≈20 kl/year available (US+Russia)
Needs for hundreds of m2 for ESS : 140 m2 in 2019 for 7 detectors (22 detectors in 2024)
Need for alternatives !! (with close performances to a 10 bar 1 inch 3He tube)
 The NMI3-II/JRA FP7 program started in february 2012 …
« Neutron Scattering and Muon Spectroscopy Integrated Initiative »
… and includes work packages to support R&D for 3He alternatives

## Slide 10
A grid is made of Boron-coated aluminum blades forming sections of square tubes
neutrons
Stacking of several grids to make Boron coated tubes
The grids are electrically insulated
Anode wires are mounted in the middle of each tube
Y
(grid readout)
X
(wire readout)
Proto #2, spring 2011
Ref: B. Guerard et al. ECNS-conference, July 2011, Prague
The ILL multi-grid area detector (ILL-Patent appl. #: 20110215251)

## Slide 11
The CACADE GEM detector
Each GEM has two 10B layers
Last GEM operated as amplifier
10 GEM foils for ~50% efficiency
Christian J. Schmidt et al (GSI, Darmstadt)
2D-200 CASCADE Detector (200x200 mm2)
INFM - Perugia
Forschungszentrum Jülich
Hahn Meitner Institut - Berlin
Ruprecht Karls Universität - Heidelberg
AGH University of Sci. and Tech. - Krakow
Other solutions based on Boron-coated straw tubes
 room for innovative ideas to maximize conversion efficiency
GEM-foils coated with 10B and 2D readout structure
Power supply and thermal management
FPGA based readout board
ASIC frontend-electronic
Detector entrance window (100 µm Al)

## Slide 12
old PC-Mouse
Ref:Christian J. Schmidt et al. (GSI Darmstadt)
2D-200 CACADE GEM detector performances
~ 1-3 mm spatial resolution
with 1.56 mm pixel size
10 MHz/cm2 counting rate capability
Old PC
Mouse
A radiography with the CACADE GEM detector
TOF Dynamics Achieved with CASCADE
Tesa-Tape
Dispenser
Water
Flow-Indicator

## Slide 13: Micromegas for neutron radiography
6Li converter : 50 µm
Conversion gap : 400 µm
Amplification gap : 50 µm
Self-supported 50 mm micromesh
Gassiplex cards readout
Gadolinium
object
Holes
Imaging Mask: Gadolinium foil (5x5 cm², 25 µm thin) holes from 75 to 500 µm
HV1
HV2
e-
Charged
particle
amplification (50 m)
Micromesh
E1 ~ 1kV/cm
E2 ~ 40kV/cm
100 µm
conversion
(400-700 mm)
neutron
CEA/DSM-IRFU + CEA/DRT-LIST-DETECS collab.
« classical » micromegas prototype
proof of principle (1D 2002, 2D 2004)
Li6 converter

## Slide 14: Imaging capabilities of the prototypes
3 108 thermal neutrons/cm2/s
Beam tests at the Orphee Nuclear plant
Image of the Gd mask
350 mm
Tomographic image of a multi-wires cable
(∅ 6 mm, 12 wires, ∅ 0.5 mm each)
Distorted tomograhy reconstruction with ~160 mm resolution because of the pillars supporting the “classical” micromegas mesh
Should be greatly improved today by use of the 2D micro-bulk
To be continued …
F. Jeanneau, IEEE TRANSACTIONS ON NUCLEAR SCIENCE, VOL. 53, NO. 2, APRIL 2006

## Slide 15: n-TOF transparent neutron beam flux monitor
Micro-bulk technology for very low budget material detector
Use of 2 converters : 10B(n,a)7Li for up to 100 eV neutrons and 235U(n,f) for 100 eV-1 MeV
Ar+2%iC4H10+10%CF4
35 mm diameter active area
1 plane Anode
1 channel : on-shelf fast current preamp. + 1GHz flash ADC
Specifications
Sputtering from B4C at CERN (0,6 mm)
on 1 mm copper coated 12,5 mm Kapton foil
~1 mm on a F 35 mm
10B Converter
Vaccuum Evaporation (1 mg 235U @ 99,94%) at JRC-IRMM (Geel)
on 1,5 mm aluminized mylar foil
1 mg on a F 20 mm
235U Converter
Ref: S. Andriamonge et.al., proceedings of ND2010, International Conference on Nuclear Data for Science and Technology
500 mm

## Slide 16: CERN/n-TOF 2D X-Y neutron beam profiler
128 mm Bulk-micromegas technology with 2D X-Y readout (CAST-like)
Use of 10B(n,a)7Li for up to 1 MeV neutron conversion
Ar+2%iC4H10+10%CF4
6x6 cm2 active area
F 60 mm, 24 nm 10B4C layer on a 1 mm copper coated 12,5 mm Kapton foil
212 channels : readout with 2 x 96 ch. Gassiplex cards
Specifications
Ref: S. Andriamonge et.al., proceedings of ND2010, International Conference on Nuclear Data for Science and Technology
X & Y strips
+ Y vias
Woven mesh (30 um)
Pyralux pillar (128 mm)
X readout
Y readout
50 mm kapton

## Slide 17: n-TOF beam profile and flux monitor
n-TOF beam flux monitoring (2008)
Ref: S. Andriamonge et.al., proceedings of ND2010, International Conference on Nuclear Data for Science and Technology
n-TOF beam profile (2009)
@ 185 m from spallation target

## Slide 18: DEMIN : Micromegas Detector for Neutron spectroscopy for MégaJoules Laser and ICF experiments
Up to 30 MeV neutron spectrum diagnostics for inertial confinment DD and DT fusion
Prototype specifications
80x80 mm2 « classical » micromegas with 40 x 1 mm width strips
500 m thick drift volume, filled with He+10%C4H10+10%CF4
CH2 converter
Front-end electronics
Fast current preamp + MATACQ readout (SEDI)
40 electronic channels
Ref: M. Houry et.al., NIM A 557 p648 (2006)

## Slide 19: DEMIN : performances @ OMEGA (Rochester, USA)
DEMIN group (CEA/DIF/DCRE and IRFU)
Ref: M. Houry et.al., NIM A 557 p648 (2006)
DT SHOT, 31769; 4.1013 n14MeV
Primary
neutrons
Scattered
Neutrons in
the target bay
g induced
by neutrons
Tertiary neutrons
time window
Time (ns)
Signal (mV)
T0
30 eV/mm stopping power of 1 MeV e- in gas
 the thinner drift gap, the better the g rejection

## Slide 20: The Piccolo micromegas
In-core Nuclear plant integrated neutron flux measurement
Piccolo collaboration (TRADE WG) : IRFU / CEA-DEN
Small sealed 10 cm3 micromegas (160 mm)
Standard design, with woven bulk type mesh
Non-flammable Ar+2%iC4H10
Wide neutron energy sensitivity with :
  235U et 10B, thermal to several MeV
  232Th , En > 1 MeV
  H recoils , thermal to several MeV
Designed for use in the extreme conditions of a reactor core (heated water 300°C, radiation)
Use of stainless steel & ceramic materials
4 individually polarized anode channels
2 readout modes :
  counting mode with fast current preamp. + 1GHz flash ADC + MATACQ (SEDI)
  current mode by mesh current reading for high reactor power
Specifications
Ref: J. Pancin et al., Nuclear Instruments and Methods in Physics Research A 592 (2008) 104–113

## Slide 21: Piccolo micromegas : performances
Ref: J. Pancin et al., Nuclear Instruments and Methods in Physics Research A 592 (2008) 104–113
Counting rate Vs Vmesh @ P=0 kW
Current Vs reactor P in center
Current Vs reactor P in edges
~1011 n (109 g ) /cm2/s @ P=10 kW
Piccolo inside a 1 MW TRIGA reactor (Gasaccia)
- Good linearity and n/g discrimination
- Space charge effects & ageing needs to be studied at high flux
good I=f(P[kW]) linearity

## Slide 22: Conclusions and perspectives
Novel transparent micro-bulk structure for X-Y 2D neutron beam profile and flux monitoring detector (new 2D readout thin micro-Bulk)
TPC for fission fragments, n-alpha reactions, or neutron elastic scattering….. (micro-Bulk, Bulk, GEMs)
High precision neutron radiography
(new 2D readout micro-Bulk with hidden pillars, GEMs )
Large detectors for spallation source (neutron diffraction….) and for alternative to 3He based detectors (Large, low cost, Bulk detectors, multi-stage CASCADE GEMs)
  Sub-mm spatial resolution for neutron thomography
  Sub-ms time resolution for TOF measurement (see DEMIN, CASCADE)
  High MHz (and more) counting rate intrinsic capability
  Radiation hardness and
MPGDs benefits for neutron detection
Prospectives
  More & more developments of neutron detectors using MPGDs for neutron beam flux and profile measurements, neutron spectroscopy (TOF measurements) and neutronography (Germany, Italy, France, Japan …)

## Slide 23: Backup slides

## Slide 24: Other limitations of gaseous proportional counters
Ref: A. Oed, NIM A 525 (2004) 62–68
Limited position resolution on the neutron interaction localisation
The so-called « wall effect »
Example of BF3
Same effect in BF3
The spectrum reflects detector response
rather than neutron energy ….

## Slide 25
B4C thin film deposition @ Thin Film Lab, Linköping Univ.
10B4C-Coatings Patent appl. #: PCT/SE2011/050891
Ref: J. Birch, Development of Thin-film 10B-based neutron detectors, Saclay 2011-11-30

## Slide 26: 2D readout Micro-bulk manufacturing process

## Slide 27: Comparison of bulk & micro-bulk technologies
- Large size
- Large scale production
- Low-budget material
- Excellent energy resolution
Ref: A. Delbart et.al., GLA2010, proceedings of 1st International Workshop towards the Giant Liquid Argon Charge Imaging Experiment
r.m.s

## Slide 28: The micro-bulk micromegas
“All-in one” structure mesh+anode
Excellent Energy resolution
11% FWHM @ 5,9 keV, 6 % @ 22 keV, 1,5 % @ 5 MeV)
Good uniformity
Low materiel budget detector
Flexible structure
Low intrinsic radioactivity
Fabrication process still improving
Fragile
Limited sizes (<100 cm2)
Micromesh
5 µm copper
25 or 50 µm
Kapton
Readout anode
Lower capacitance
Under development
Ref: S. Aune et al. NIM A 604, 15-19, 2009
S. Andriamonje et al. JINST 4, MPGD2009 conf. proceedings
11% FWHM at 5.9 keV
Ar + 5% Iso at 1 bar
Same manufacturing techniques as GEM :
Copper & Kapton etching of a copper cladded Kapton
1 mm
1
2
2
1
Better mesh transparency &
12 mm gap under development
CEA-CERN Patent 09 290 285.0 (2009)

## Slide 29: The bulk-micromegas
First prototypes in 2004. CERN-TS-DEM/Irfu collaboration
A woven micro-mesh is embeded between 2 layers of photo-imageable material. Amplification gap of 128 mm is standard, 104 mm should be ok, 64 mm is tricky
No farme, no mechanics  % level dead zones
Up to 40x40 cm2 is standard
Robust, Industrial process
Copper segmented anode
Lamination of Vacrel
Positioning of Mesh
Encapsulation
Development
FR4
Photo-imageable
polyamide film
Stainless steel
woven mesh
Border frame
Spacer
Contact to Mesh
Base Material
Ref: I. Giomataris et.al., NIM A560 (2006) 405
63 m pitch, 18 m wires
Top 500 mm pillar

## Slide 30: The T2K/TPC bulk-micromegas
Bulk-micromegas detector cost : ~10 k€ /m2 ( 80% of the cost in the 4 layers PCB ! )
MICROMEGAS
final cutting
NIM A574 (2007) 425-432
NIM A602 (2009) 415-420
  1 year production of 10 m2
  - bulk-MM produced @ CERN-TS-DEM
  - 115 PCBs produced
  - 86 modules produced (6 rejected)
  Finalement, 72 détecteurs + 8 spares
  - 10 faulty pads / 124000 !
Ref: A. Delbart et.al., TIPP2009 conference proceedings NIM A preprint doi:10.1016

## Slide 31: T2K/TPC Module calibration : a uniform production
55Fe spectra
1726 pads scan @ -350 V
1 FEC dead ch.
HV connection.
Gain vs HV curve
Gain=1500
@ -350 V
Gain
Uniformity
2.1%
Energy
Resol.
Uniformity
5.6%

FWHM
8% performance uniformity over the 86 modules