Strengths and Limitations of
Atmospheric Cherenkov Telescopes (ACTs)
- Present and Future -
for Transient VHE Sources
M. Punch - APC-CNRS/IN2P3

---
What is needed for Transient Sources?
The ideal AGN variability survey would have the following properties:
1. AVS-P1: broad sky coverage, W,
to maximize the number of AGN observed and to enable rare classes of variable objects, and low duty cycle events, to be found;
2. AVS-P2: long total survey duration, D,
of survey observations which each detect minimum source flux Smin on
time-scale t0 and with fractional uncertainty in flux dSt0 and enable variations on time-scales from a maximum tmax ~ D/2 down to a minimum (median)
tmin ~ 0.7D/N to be measured from N randomly sampled observations; and
3. AVS-P3: large total number of measurements, N,
to enable measures of source variability on time-scales tn ~ (n−1) tmin/2, where n = 2 ...N, and fractional variability sensitivity improves as
dStn ~ dSt0/n0.5
Grindlay, Proc Central Engine of AGN,
China, Oct 2006, arXiv.0704.3294v1

---
What is needed for Transient Sources?
The ideal AGN variability survey would have the following properties:
1. AVS-P1: broad sky coverage, W,
to maximize the number of AGN observed and to enable rare classes of variable objects, and low duty cycle events, to be found;
2. AVS-P2: long total survey duration, D,
of survey observations which each detect minimum source flux Smin on
time-scale t0 and with fractional uncertainty in flux dSt0 and enable variations on time-scales from a maximum tmax ~ D/2 down to a minimum (median)
tmin ~ 0.7D/N to be measured from N randomly sampled observations; and
3. AVS-P3: large total number of measurements, N,
to enable measures of source variability on time-scales tn ~ (n−1) tmin/2, where n = 2 ...N, and fractional variability sensitivity improves as
dStn ~ dSt0/n0.5
Grindlay, Proc Central Engine of AGN,
China, Oct 2006, arXiv.0704.3294v1

---
What is needed for Transient Sources?
Related considerations:
4. Avoidance of “periodically-gapped” data
caused by gaps due to satellite orbit (cf Jan Katoka's talk), daylight effects (diurnal, 24h ), moon effects (lunations, 29.53d )
5. Avoidance of instrumental changes during the observation
For ACT, caused by weather, Zenith angle dependence (short term), and instrument degradation, modification, upgrade (long term)
... It's not just a question of getting the record in fast-time variability,
but also essential to have long-term campaigns in order to characterize the variability.

---
Current/Past ACT strength/weakness
Limitations:
Narrow field-of-View, O(4° Ø)
Surveys, continuous monitoring not possible
Difficult background rejection of charged Cosmic Rays
Continuous O(Hz) background count level
Observations only possible in dark-time, in clear weather
10-15% duty cycle (~1200h/yr), periodic gaps
Instrument characteristics change with observation conditions
(atmosphere, Zenith angle)
Strengths:
Huge collection areas O(105 m2),
though needed for the low fluxes at the energies considered
Relatively low-cost technique (no launch vehicle needed), O(20M€)
so can build many installations for increased coverage

---
Past sensitive ACT detectors
Whipple
... i.e. those having discovered or
    made major contributions to AGNs !
HEGRA
7TA
CAT
Whipple
HEGRA
CAT
Durham Mk VI

---
Current VHE Gamma-ray World
VERITAS
VERITAS
MAGIC
CANGAROO III
HESS
CANGAROO-III
H.E.S.S.
(note... change of scale)
MAGIC
MAGIC II
HESS-II

---
Characteristics of Current ACTs
Sensitivity  by an order of magnitude
over previous generation
Threshold  by factor of a few
Access to shorter time-scales of variability

---
The H.E.S.S. Stereoscopic system
Key point: Stereoscopic
12 m diameter mirror
 107m2 surface x 4-telescopes
5 ° FoV camera, fast electronics
Trigger threshold of
E = 100 GeV
Sensitivity of
0.7 % Crab flux in 50h
© Philippe Plailly

---
Telescope Structure
Near-future upgrade to HESS-II
Parabolic Mirror
596 m2
f = 36 m
Large Cherenkov-photon collection area
2048 pixel camera,
  0.07° pixel size
  3.5° FoV
Fine-pixel imaging

---
Gain with HESS-II
Sensitivity
Sensitivity increase by factor 2 in core range, threshold decrease by factor  2
HESS I
low rate
low light
Energy
HESS II
mono
HESS II stereo

---
The MAGIC Telescope
The MAGIC Telescope
17 m diameter mirror
 236m2 surface
3.5 ° FoV camera
Trigger threshold of
E = 60 GeV
Sensitivity of
2.2 % Crab flux in 50h
(10-11ph/cm2/s)
Can operate under moonlight conditions

---
Near-future upgrade to MAGIC-II
Structure and mirror,
clone of MAGIC-I
Camera, initially
similar to MAGIC-I
Later, improved camera	foreseen
Sensitivity increase by factor 2, with increased angular resolution and background rejection

---
Gain with MAGIC-II
Sensitivity
MAGIC I
Energy
MAGIC II stereo

---
Current and near-future ACTs
The near-future ACTs (MAGIC-II, HESS-II) will provide a factor-two increase in sensitivity,
+ some decrease in threshold

---
Current & near-future ACT sensitivity

---
AGNs detected with ACTs
Grey  unpublished

---
Characteristics of the AGNs detected
Refer to W. Benbow's presentation for lots of details!
Redshift (z)
Photon Index (Gamma)
Grey  unpublished

---
Multi-ACT, MWL campaigns
Campaigns by one or several detectors on the brightest sources
Crucial for initial credibility of the field
Now, provide quite well sampled light-curves for MWL campaigns
... but hard to keep such campaigns going
Protheroe et al., 25th ICRC, Durban (1997)
1997-2000 Light Curve Compilation
Albert et al., ApJ, 669, 862, 2007

---
Short time-scale variability at VHE
Historically, first was Mkn 421,
4 years after 1st detection:
Variability of 15m measured in 1996 with Whipple,
when source at 10-Crab level
May 15, 1996
4.5 min. bins
Gaidos et al., Nature, 383 (1996)

---
Compare flares
Shortest time-scale variability at VHE
1st time with Hz count rate
tvar ~ 3 minutes
With current instruments,
are we down to the limit of the sensitivity?
For near-future upgrades, some progress will happen...
Crab Flux
HESS
PKS 2155-304
28th July 2006
MAGIC
Mrk 501
9th July 2005
RXTE-PCA
Mkn 421
Błażejowski et al., ApJ 630 (2005) 130
... any need to go finer for correlated variability (with X-ray)?

---
VHE showing similar capability to X-ray
Kataoka, ApJ 560 (2001) 659
E > 200 GeV
Mrk 421
Mrk 501
PKS2155
~f-2.5
~f-1
Aharonian et al. ApJ 664 (2007) L71
PKS2155

---
VHE showing similar capability to X-ray
cf. presentation of J. Kataoka
Mrk 421
Observed
artifacts?
cf. presentation of B. Degrange
PKS 2155-304
Data: MJD 53946
Effect of flux measurement errors
Current instruments, are powerful detectors to reveal the time-scales of the brightest sources,
... but missing well-sampled long time-scale

---
The Cherenkov Telescope Array facility
The Next step: CTA
Cherenkov Telescope Array
aims to explore the sky in the
few 10 GeV to 100 TeV energy range, with “core” regime from
~100 GeV to ~ 10 TeV
with milliCrab sensitivity
combines guaranteed science with significant discovery potential
builds on demonstrated and reliable technologies and provides guaranteed performance parameters
is an observatory that provides access and data to a wide community
provides full sky (N/S) coverage

---
The Next step: CTA
Cherenkov Telescope Array
aims to explore the sky in the
few 10 GeV to 100 TeV energy range, with “core” regime from
~100 GeV to ~ 10 TeV
with milliCrab sensitivity
combines guaranteed science with significant discovery potential
builds on demonstrated and reliable technologies and provides guaranteed performance parameters
is an observatory that provides access and data to a wide community
provides full sky (N/S) coverage
AGIS, similar US
project, with more
exploratory techniques
Towards a Thousand
VHE gamma-ray sources

---
Design Optimization An advanced Facility for ground-based gamma-ray Astronomy
Implementation & Operation of CTA
Modes of operation
Deep wide-band mode: all telescopes track the same source
Survey mode: staggered
fields of view survey sky
Search & monitoring mode: sub-clusters track different sources
Narrow-band mode:
halo telescopes accumulate
high-energy data,
core telescopes hunt pulsars
…
Possibly mix of telescopes:
    e.g (5m), 14m, 28m
Large FoV
 Factor of 10 in sensitivity
    with only factor of 10 in Euro ($, Yen, …)
Will need
  O(50 – (100) ) telescopes
  O(10000) m2 mirror area
  O(50) m2 photo sensitive area
  O(50000-100k) electronics channels

---
Advantage of Large Arrays of ACTs
More intersections of single-telescope
effective areas		More “golden events”
sweet
spot
300 m
Single telescope

---
CTA Simulations currently underway
Systematic studies how performance changes with single parameters
dish size
field of view
pixel size
spacing
height
Strawman arrays
(these simulations
  from K. Bernlöhr)

---
CTA, huge sensitivity improvement
“small” = 14m
“large” = 28m

---
Comparison with Current ACTs
Order of magnitude increase in sensitivity
Access to second-scale variability
in the brightest sources

---
CTA status & optimistic outlook
   Design Study
Prep. Phase ?
Component prototypes
Site exploration
Partial operation
Array construction
Array prototype
Telescope design
Array layout
13
12
11
10
09
08
07
06

---
What CTA provides for AGN
Through larger array area, improved shower imaging,
more Cherenkov photons per shower,
more “golden” multi-telescope events
“Survey mode” using sub-arrays
can follow several sources simultaneously
with sensitivity at same level as currently
Higher sensitivity at TeV energies (x 10)‏
using large sub-arrays or full array,
 finer variability measurements for known sources
Lower threshold (few 10s GeV)‏
with the large telescopes,
for distant AGN detection, source mechanisms
Higher detection rates
    - Much finer transient phenomena measurement

---
What can CTA do on Transient Sources?
Back to Grindlay's criteria
1. AVS-P1: broad sky coverage, W,
CTA telescopes can have a wide field of view, up to 6-8°.
Working in survey mode,
with 20 sub-groups of “cells” of 4-telescopes or more,
could cover up to O(0.2 str)
2. AVS-P2: long total survey duration, D,
A very large array would naturally have
a long time-scale for operations
3. AVS-P3: large total number of measurements, N,
CTA “cells” can take regular samples of the
few hundred Blazars which will be in the future catalogue

---
What else for Transient Sources @ VHE?
Related considerations (beyond CTA):
4. Avoidance of “periodically-gapped” data
Daylight effects (diurnal, 24h ) only avoidable with several sites worldwide
Moon effects (lunations, 29.53d ), some mitigation if running with reduced	sensitivity (lowered voltages, raised thresholds) in “thin moon” time.
5. Avoidance of instrumental changes during the observation
Weather effects, Zenith angle effects mitigatable only with several sites
Instrument degradation naturally corrected with large array,
constant maintenance

---
Conclusions
The current sensitive instruments (H.E.S.S., MAGIC, VERITAS) have made great strides beyond the previous generation, providing now coordinated campaigns of observation and short time-scale variability.
Hope for the future (CTA/AGIS), will make
another order of magnitude increase in sensitivity and
a decrease of a factor of a few in threshold
providing access to weaker or more distant Blazars
allowing the measurement of
shorter time-scales in the bright sources
and	similar time-scales to those currently seen, in the weaker
allowing the long-term, fairly dense coverage of Blazar variability
... and beyond, multi-site facilities...
To work in MWL correlation with the future detectors in
X-rays (EXIST, Simbol-X, Constellation-X, XEUS..),
Radio (SKA...), Optical (PanStarrs, LSST...)
and of course GLAST!

---
CTA as a user facility
CTA as a User facility, and Funding
Significant fraction of open time (~50%)
Guaranteed time for CTA consortium (~50%)
Probably local staff for basic operation,
plus experts when needed
Facilities to make data available to outside users
Data public after certain time (~1 y)
Significant fraction of operating funds / user support / data center support needs to come from external (EC?) sources
  - Project has high priority in ApPEC and ESFRI roadmaps
  - FP7 (European Framework Plan 7)
    design study applied for ... not currently accepted