## Slide 1: Introduction to Accelerators
Mika Masuzawa (KEK)

## Slide 2: Contents
Brief history & major inventions
  1930~1960
Introduction
DC: Cockcroft-Walton, Van de Graaff
AC: Drift tube, Cyclotron
  Betatron
  Betatron oscillation, weak focus
  A.G. Synchrotron
  phase stability, strong focus, synchrotron radiation, (Linear collider)
  1960~
    Collider
New era of large circular colliders
Energy frontier, Luminosity frontier
Virtual tour of KEKB
Challenges
  SuperKEKB as an example
  Future accelerators
Final thoughts

## Slide 3: Brief history & major inventions 1930~1960
  1930~1960
Introduction
DC: Cockcroft-Walton, Van de Graaff,
AC: Drift tube, Cyclotron
  Betatron
  Betatron oscillation, weak focus
  A.G. Synchrotron
  phase stability, Strong focus, synchrotron radiation (Linear collider)

## Slide 4: Introduction: units
V
U=eV
Unit for energy
[eV] electron volt
Energy unit charge [e] receives from potential difference of 1 [V].
Why not [J] ?
[J] Joule
Energy unit charge [C] receives from potential
difference of 1 [V]
“Joule” is too large
1 kV = 10 3 eV
1 MeV = 10 6 eV
1 GeV = 10 9 eV
1 TeV = 10 12 eV
e

## Slide 5: Introduction Livingston's curve : The beam energy of accelerators vs. time.
DC generators
Electrostatic
Cyclotron
Proton linac
Betatron
Electron linac
Electron synchrotron
Proton synchrotron
A.G. Synchrotron
From PARTICLE ACCELERATORS by Livingston and John P. Blewett, 1962, p. 6.
1930~1960
An order of magnitude
increase every 6 years!
10000
1000
100
10
1
[MeV]

## Slide 6: Introduction Dawn: The first nuclear reaction by Rutherford
He demonstrated in 1919, that alpha particles could knock protons out of nitrogen nuclei and merge with what was left behind.
Radioactive
material
Fluorescent
material
Nitrogen
gas
proton
This provoked strong demand for generating high energy beams to study nuclear disintegration phenomena in more detail.
A race to develop high energy accelerators started.

## Slide 7: Cockcroft-Walton: First disintegration of atomic nuclei with accelerator
750 keV Cockcroft-Walton
at KEK
High voltage is provided by charging capacitors and discharging them in series.
Cavendish Laboratory
1932, Cockcroft and Walton used their machine to accelerate protons, and directed the beam of protons at a sample of lithium. This resulted in changing lithium atoms into two helium atoms. They had disintegrated – “smashed” – the lithium atom by means of artificially accelerated protons.

## Slide 8: Cockcroft-Walton: First disintegration of atomic nuclei with accelerator
http://www.daviddarling.info/encyclopedia/C/Cockcroft.html
"Transmutation of atomic nuclei by artificially accelerated atomic particles"
On 14 April 1932 Walton set up the tube and bombarded lithium with high energy protons. He then crawled into the little observation cabin set up under the apparatus and immediately saw scintillations of the fluorescent screen. The reaction was giving off alpha-particles.
http://www-outreach.phy.cam.ac.uk/camphy/cockcroftwalton/cockcroftwalton9_1.htm

## Slide 9: Van de Graaff
The Van de Graaff generator was developed, starting in 1929, by physicist Robert J. Van de Graaff at Princeton University. ~10MV.
Van de Graaff generator (1931)
An electrostatic generator which uses a moving belt to accumulate very high voltages on a hollow metal globe on the top of the stand.

## Slide 10: Limits on Electrostatic Accelerators
DC acceleration is limited by high-voltage breakdown.
Ambience | Breakdown voltage
Air 1atm | ~30 kV
SF6 (Sulfur hexa-fluoride) 1atm | ~80 kV
SF6 7atm | ~360 kV
Transformer oil | ~150 kV
UHV | ~220 kV
Typical breakdown voltage for a 1cm gap of parallel metal plates
From K. Takata “Fundamental Concepts of Particle Accelerators”
http://research.kek.jp/people/takata/home.html

## Slide 11: Drift tube: From DC to AC, Radio-Frequency Accelerators
The principle of the acceleration with alternating fields was proposed by G.Ising in 1924.
R. Wideröe accelerated alkali ions (K+, Na+) up to 50 keV (25kV ×2) using the accelerator based on alternating fields (1 MHz) and drift tubes in 1928.
The particles must be synchronized with the rf fields in the accelerating sections.

## Slide 12: Drift tube: From DC to AC, Radio-Frequency Accelerators
Prototype of linear accelerator.
The idea of rf acceleration is also used by circular accelerators.
Need longer tubes and gaps as energy increases.
Concept of Wideröe accelerator

## Slide 13: Cyclotron: From DC to AC, Radio-Frequency Accelerators
(1) A cyclotron consists of two large dipole magnets (Ds) designed to produce a semi-circular region of uniform magnetic field.
(2) An oscillating voltage is applied to produce an electric field across the gap between two Ds.
(3) Particles injected into the magnetic field region of a D trace out a semicircular path until they reach the gap.
(4) The electric field in the gap then accelerates the particles as they pass across it.
Lorentz Force
F = q v × B

## Slide 14: Cyclotron: Frequency and orbit radius how it works.
Suppose a uniform magnetic induction B is applied perpendicular to the velocity v of a particle with mass m, charge q:
The Lorentz Force F = q v × B produces a circular track.
Force, relationship between momentum p and radius r:
F = qvB
p= qBr (since mv2/r=qvB )
and for non-relativistic case:
p=mv
We obtain cyclotron frequency and radius as:
frev=v/2pr=qB/2pm Frequency is independent of velocity
r = mv/qB and radius is proportional to velocity
The particles can be excited at a fixed rf frequency and the particles will remain in resonance throughout acceleration.
Centrifugal force

## Slide 15: Cyclotron: limits
When particles become relativistic
the mass of the particle increases as
which results in
→ decrease of ωrev
→ asynchronism with RF
Breakthrough in 1945
Phase stability principle
Vladimir Veksler (1944) and
Edwin M. McMillan (1945)
⇒Synchrotron
(some slides later)
Some methods to overcome this limit tried:
Magnetic field distribution
Changing rf frequency with particle energy…
But no drastic improvement beyond
20 MeV with protons.
Recall
frev=v/2pr=qB/2pm

## Slide 16: Betatron: non RF, accelerate electrons (beta particles)
http://physics.illinois.edu/history/Betatron.asp
The first successful betatron was built by Donald Kerst in 1940, accelerating electrons to 2.2 MeV.
Principle: Electromagnetic induction, not RF.
Maxell’s eq.
Stoke’s theorem
Eq. of motion
For r = const.
From (1) and (2) we obtain the condition for constant orbit for betatron.
“2:1 rule” (Wideröe, 1928)
Not dependent on mass.
Good for relativistic particles!

## Slide 17: Betatron: limits of accelerating particles by magnetic induction.
We can accelerate particles by increasing the magnetic field, keeping the orbit radius constant. This means, we still need to cover the entire region with a magnetic field (magnets). And this also means that the maximum energy we can obtain is limited by the magnetic field (saturation of the iron core).
Phys. Rev. 78, 297–297 (1950)
Constant orbit, good for relativistic particles but…
limits

## Slide 18: Betatron: Basis of today’s betatron oscillation theory
Side view
Magnetic field, not uniform but still cylindrically symmetric.
If the particle passage (orbit) is near the central orbit, r=r
Field index
Key word (1) Orbit stability

## Slide 19: Betatron: betatron oscillation
Z
r
recall
For the passage
near the central
orbit r=r0
From (1) and (3) and using v=r0w, we obtain eq. of motion for x as
and similarly (sort of) for z as
Equation of motion for betatron oscillation
in an axisymmetric field.
Betatron frequency
Betatron tune
Stable oscillation in horizontal plane: 1-n>0
in vertical plane: n>0
Key word (1) Orbit stability
Use cylindrical coordinate

## Slide 20: Betatron: “weak” focusing
If 0<n<1, stable oscillation in BOTH horizontal and vertical plane!
But n<1 …. This is why this scheme is called “Weak” focusing.
Motion in Betatron
Tune is less than 1, meaning betatron wave length is larger than the circumference.
If you achieve higher energy, will need large magnets as mentioned in the previous slide.
Stronger focus with more compact scheme is needed.
Discovery of strong focusing
1949 by N. Christofilos
1952 by E.D.Courant, M.S.Livingston and H.Snyder
Betatron
Progress in understanding particle orbits in a magnetic field was made.
Basis of today’s betatron oscillation theory was established.
Key word (1) Orbit stability

## Slide 21: Betatron: concept of emittance
Radius of the design orbit
Betatron tune
Horizontal position
Betatron amplitude
phase
y’
y
Ellipse indicates the phase space condition for stable circulation
Acceptance
emittance
w
nw/R
Key word (1) Orbit stability
Instead of t, use s, the distance along the path.
At s=0, y=y0 and y’=y’0 and y’=dy/ds
Larger n results in smaller a1

## Slide 22: Phase stability: the concept of “bunch” & the Synchrotron
Many particles in a bunch, circulating many turns (tens of thousands, for example.
Particles of different energies have differences in velocity and in orbit length;
Particles may be asynchronous with the RF frequency.
The RF field, however, may have a restoring force at a certain phase, around which asynchronous particles be captured, that is to say “bunched.”
This enables a stable, continuous acceleration of the whole particles in a bunch to high energies.
Circular accelerators based on this principle are called “synchrotrons.”
Key word (2) Phase stability

## Slide 23: Phase stability: a concept of “bunch”
Assume RF electric field V = V0 sin ωt
Va acceleration voltage
There are there are two φs which satisfy Va = V0 sin φ in one RF period
Only one of them can capture particles and make oscillations around the phase.
Which one?
Key word (2) Phase stability

## Slide 24
Which phase gives stable oscillations?
DC = 0
DC > 0
DC < 0
Depends on the characteristics of the orbit. (Particle momentum P and orbit C)
Example of a circular orbit
Case (1) Particles with DP >0 travel DC > 0
Particles arriving at the gap earlier (i.e. particles with DP < 0) receive more energy
⇒will travel DC > 0
⇒will arrive at the gap later.
Particles arriving at the gap later (i.e. particles with DP > 0) receive less energy
⇒will travel DC < 0
⇒will arrive at the gap earlier.
Oscillations around
Fs （Synchrotron phase）
Synchrotron oscillations
⇔
Key word (2) Phase stability
Phase stability: a concept of “bunch”

## Slide 25
Case (2) Particles with DP >0 travel DC < 0
Quiz: Which phase give stable oscillation?
Phase stability: a concept of “bunch”

## Slide 26
http://lhe.jinr.ru/english/img_01.htm
Phase stability: the concept of “bunch” & the Synchrotron

## Slide 27: Strong focus: Alternating Gradient synchrotron
For example, compare
B=2[Tesla] and 10kV/mm (10MV/m).
Both are reasonable numbers for today’s accelerators.
Use 2 [T] = 2 [Wb/m2]=2 [Vs/m2]
The magnetic term is 2 [Vs/m2]×3108[m/s]
=6108V/m=600MV/m>> 10 MV/m
For very high energy particles, magnetic force is much larger than electric.
Magnetic fields
Lorentz force
To bend (deflect) To focus & defocus
Key word (3) Strong focus
Why do we use
magnetic field to
deflect, focus,,
not electric?

## Slide 28: Strong focus: Alternating gradient synchrotron
Focusing in horizontal direction and defocusing in vertical direction -- let’s call it a Focusing or F-type quadrupole magnet.
If the polarity is reversed (N and S are reversed), it becomes defocusing in horizontal and focusing in vertical: a Defocusing or D-type quadrupole magnet.
A big difference from weak focusing case, where focusing is obtained in both directions simultaneously.
By alternating F- and D- , we can obtain a net focusing effect.
Nicholas C. Christofilos (1950), E. D. Courant, M. S. Livingston, and H. S. Snyder (1952)
Positively charged particle
Moving into this paper.
Quiz: What is the force (which one is the correct arrow representing the force) on the particle at points A, B and C?
Key word (3) Strong focus

## Slide 29
Analogy with optical thin lens
f1
f2
Net focus
The deflection (u) is always greater at F than at D.
Obtaining a net focus by combining F- and D-
Magnets is called “strong focus”,
as no constraints on “n.”
Entire orbit does not need to be covered by magnets.
Each magnet can be smaller.
Key word (3) Strong focus
Strong focus: Alternating gradient synchrotron

## Slide 30
Basic components
Magnets
Dipole magnets for bending
Quadrupole magnets for focusing
Vacuum pipes
covers the beam passage
RF cavities
Strong focus:
Magnet weight proportional to r
Weak focus:
Magnet weight proportional to r2
The strong-focusing principle revolutionized accelerator design. The principle's practicality was demonstrated in 1954, when Cornell's 1.3-GeV electron accelerator began operation. Then the new technology was applied to larger machines. In 1959, the 25-GeV Proton Synchrotron went into operation at CERN, the European high energy physics laboratory, and in 1960, the 33 -GeV AGS was commissioned. These alternating gradient synchrotrons were constructed using only twice the amount of steel (4,000 tons) needed to construct the weak-focusing, 3.3-GeV Cosmotron.
http://www.bnl.gov/bnlweb/history/focusing.asp
Key word (3) Strong focus
Strong focus: Alternating gradient synchrotron
Some photos
Next slides
Let me take a
Side trip here…

## Slide 31: Basic components: Magnets
Wind a wire on an iron bar.
Flow current through the wire and the bar will be magnetized. Polarity changes when current direction is changed.
Coils on the pole
+ return yoke
→dipole magnet!
Two poles to generate a uniform magnetic field. Charged particles traveling through the field receive a deflecting (bending) force.
Dipole magnet
(Bending magnet)

## Slide 32: Basic components: Magnets
Generates a focusing/defocusing field. The charged particles that travel through the quadrupole magnet receive a focusing/defocusing force. The force is proportional to the distance from the magnet center.
(no force if the beam goes though the center)
Quadrupole magnet
Sextupole magnet
Sextupole fields have a focal length that is inversely proportional to the distance from the centre of the magnet. Used for correcting the effects of focusing dependence on momentum.

## Slide 33: Basic components: Vacuum components
Getter pumps
ion pump
Vacuum duct
~10-8 Pa
Cu, Al, ceramics…
bellows
Gate Valve
Flange & gasket

## Slide 34: Basic components: RF cavities
SAGA-Light Source RF cavity
499.8 MHz
500 kV, 90kW
Load
SR loss 31.8 kW
Wiggler 10.2 kW
Wall loss 35.7 kW
Other 7.8 kW
Total 85.5 kW
R&D Superconducting cavity for ILC
lam29.lebra.nihon-u.ac.jp/WebPublish/4P31.pdf

## Slide 35: Basic components: RF cavities
Pillbox cavity
TM010 mode

## Slide 36: Alternating Gradient Synchrotron (Brookhaven)
28 GeV protons on a beryllium target
Key word (3) Strong focus

## Slide 37
Synchrotron radiation:
Synchrotron radiation (SR) is emitted from a charged particle traveling near the speed of light when its path is bent by a magnetic field. As it was first observed in a synchrotron in 1947,
it was named "synchrotron radiation".
Synchrotron radiation is emitted in a continuous spectrum.
http://www.spring8.or.jp/en/news_publications/publications/sp8_brochure/sr.html/publicdocument_view
Magnetic field
Synchrotron radiation
Charged particle

## Slide 38
Synchrotron radiation: lighter particles suffer more.
SR is an electric dipole radiation from a charged particle in acceleration
Radiation power in the rest frame is given by
Larmor’s formula:
In the laboratory frame, P becomes
Can you derive this?
The radiated energy per turn DE
for a ring of radius r
Practical formula
For relativistic protons and electrons of the same momentum, the energy loss is in the ratio (me/mp)4~1013. It is 1013times smaller for protons than for electrons.
For electrons of energy 10 GeV circulating with r=1 km, the SR energy loss is 0.9 MeV/turn. How much is it for 20 GeV electron?

## Slide 39
Synchrotron radiation:
SR loss is 1013 times smaller for protons than for electrons.
For a high energy electron circular machine, a large ring (radius scaling roughly as the square of the beam energy) is needed.
LEP @ CERN, 100GeV, 27 km in circumference.
Low magnetic “guide” fields
Still loss needs to be compensated by RF power to keep the beam circulating.
A linear accelerator is the natural
solution to the scaling problems of a circular
collider.
SLC (~50 GeV electron-positron beams,
Ecm~91 GeV, lose some at the arcs).
Linear Collider project (following slides)

## Slide 40
Linear Collider:
http://lcdev.kek.jp/LCoffice/OfficeAdmin/
1st stage 500 GeV

## Slide 41
Linear Collider:

## Slide 42: Brief history & major inventions 1960~
    Collider
New era of large circular colliders
Energy frontier
(side trip: storage ring)
Luminosity frontier

## Slide 43: Brief history and inventions before 1960
Cyclotron
Multiple acceleration by RF, orbit changes with energy
Entire orbit covered by magnets
Synchronization becomes difficult as particles become relativistic.
Betatron
Acceleration by magnetic induction
Constant orbit
Entire orbit covered by magnets
(2)Phase stability principle in1945
Synchronization issue is solved.
(1)Orbit stability
Betatron oscillation
Weak focusing
Early Synchrotron
Acceleration by RF
Huge magnets Synchrophasotron 10 GeV, 39000 ton
(3)Strong focusing
1952
Synchrotron
Entire orbit not covered by magnets.
Much higher energy
>10 GeV (10000 MeV)
Circular machine
collider

## Slide 44: Collider

## Slide 45: Collider: the first collider (e-e+):AdA (Anello di Accumulazione) and happened to be Bruno Touschek’s aunt’s name.
The First Electon-Positron Collider
Carlo Bernardini
Phys. Perspect. 6(2004) 156-183
Collision-based computing, Andrew Adamatzky (2002)
ADONE 1969
C=105 m
Ecm < 3 GeV
no J/y …
Orbit radius = 65 cm,
250MeV×250 MeV
Operated 1961-1964.
Many feasibility experiments with this working model.
Followed by a full-size collider ADONE

## Slide 46: Collider: Era of large circular colliders, energy frontier machines
Proton × (anti-)proton, e.t.c.
Lecture by K. Yokoya, “Summer Challenge 2008” @ KEK

## Slide 47: Collider: Era of large circular colliders
Electron × positron
Lecture by K. Yokoya, “Summer Challenge 2008” @ KEK
We are here

## Slide 48: SPS (Super Proton Synchrotron)  SppS(Super Proton Anti-Proton Synchrotron) @CERN
~7km in circumference
1976 commissioning
1981 SppS
1983 Discovery of W± & Z0
Nobel prize for Van der Meer and Rubbia
From a one-beam accelerator into a two-beam collider, SppS. D. Cline, P.McIntyre and C. Rubbia
Collision of a beam of protons with a beam of antiprotons, greatly increasing the available energy in comparison with a single beam colliding against a fixed target.
Rev. Mod. Phys. 57, 689–697 (1985)
Stochastic cooling and the accumulation of antiprotons
Stochastic cooling:
a way of producing and storing dense beams of protons or antiprotons
S. Van der Meer
Collider: Era of large circular colliders, energy frontier machines

## Slide 49: Collider: Era of large circular colliders, energy frontier machines
Tevatron (Fermilab)
1 Tev proton ×1 TeV anti-proton
6.3km circumference
4.2 T superconducting magnets
1983~2011.9.30
Discovery of top quark in 1995.
http://www.fnal.gov/pub/tevatron/

## Slide 50: Collider: Era of large circular colliders, energy frontier machines
http://public.web.cern.ch/public/en/LHC/LHC-en.html
3.5 x 3.5 = 7 TeV
Aug.2009
Celebrating the first beam in the ATLAS
control room, Sep.2008.
http://legacy.kek.jp/newskek/2009/janfeb/LHC_ATLAS.html
LHC (CERN)

## Slide 51
High Energy Machine
Energy frontier
Factory machines
Luminosity frontier
Next-generation B-factories
Mainly e+e- colliders are shown
Two major goals of accelerators for HEP:
energy and luminosity
Collider: Era of large circular colliders

## Slide 52: Storage ring:
A storage ring is a type of synchrotron.
  Conventional synchrotron
    Accelerates particles from low to high energy.
    RF cavities are used to accelerate particles.
  Storage ring
    Keeps particles stored at a constant energy for a long time (storage).
    RF cavities are only used to replace energy lost through synchrotron radiation and other processes.

## Slide 53: Storage ring:
A storage ring
  Collider for HEP
    B-factories (PEP-II, KEKB)
    Tevatron, LHC: energy is ramped up from the injection energy to the target energy at first, but then kept constant for the experiment.
  Synchrotron facilities for applied field
    Keeps particles stored at a constant energy for a long time (storage).
    RF cavities are only used to replace energy lost through synchrotron radiation and other processes.

## Slide 54: Collider: Era of large circular colliders, luminosity frontier machines
Luminosity frontier

## Slide 55: Collider: Luminosity
Event yield
Luminosity
Cross section
Ne-
Ne+
Fixed target
Beam on solid (usually) target
Collision guaranteed
Collider
Bunch against bunch
Some (most) stream through the other
The number of particles per unit area per unit time
More particles in a bunch
Frequent collision
Smaller beam
Higher luminosity

## Slide 56: Collider: realizing small beam for higher luminosity
Beam size
emittance
For non-dispersive place
How can we squeeze down the beam size?
Often we write emittance as e
Some more on emittance for the strong focusing in the next slides.

## Slide 57: Collider: realizing small beam for higher luminosity
y’
y
w
nw/R
emittance
“Weak focus” case
“Strong focus” (n >> 1) case;
b-function describes the amplitude of the motion of the particles:
Constant in “weak focus”
Function of s in “strong focus”
Recall
The area is constant, independent of s
also in strong focusing case.
a,b and g are called
Twiss parameters

## Slide 58: Collider: realizing small beam for higher luminosity
Particles move in an ellipse in phase space.
Ellipse rotates and change in shape in magnets.
The area of the ellipse is often represented as 2pJ
and this is conserved.
Drift space
(between magnets)
Focusing magnets
Defocusing magnets
From lecture by Y. Ohnishi at OHO 2006
Keys for small collision spot size:
Design a machine with small emittance.
Squeeze the beta-function at the collision point.
I would like to introduce you our project SuperKEKB, as an example of a small beam machine.

## Slide 59: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
SuperB
Italy
KEKB &
SuperKEKB
Japan
Global efforts for Next Generation B-factories

## Slide 60
3 km in circumference
11 m below the ground level
~50km
North of Tokyo
Virtual Tour of KEKB: e+e- double ring collider 1999~2010

## Slide 61: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
3.5 GeV positron (LER) ×
8 GeV electron (HER) to produce many
B-mesons at 10.58 GeV.
That is why it is called “B-factory”
Energy is fixed by physics goals.
Look for very rare events.
This is why we need to have high rate collision (high luminosity)
Double ring, because the beam energy is asymmetric.
3 km circumference, reuse of the previous machine called TRISTAN.
Collide at one Interaction Point (IP).
Belle detector collects data at the IP.
Electron (HER)
Positron(LER)

## Slide 62: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
All starts here, the electron gun

## Slide 63: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
e-
electron
positron
Positron production on tungsten target

## Slide 64: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
500 m linear accelerating section
(LINAC).
Bicycle is handy.
Electrons and positrons are accelerated to the target energy and transferred to many beam lines.

## Slide 65: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
Beam Transport Line
From the LINAC to Main Ring,
From 5 m below G.L. to
11m G.L., going down, down, down.

## Slide 66: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
HER e-
LER e+
From Beam Transport Line to the Main Ring.
Electrons are being injected into the electron ring here.

## Slide 67: Virtual Tour of KEKB: e+e- double ring collider 1999~2010

## Slide 68: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
SCC (Single-cell Superconducting cavity) for HER
Highest beam current stored (1.45A) in the world.
TM010 mode
Electric field in the cavity
Timing
important

## Slide 69: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
Positrons (LER)
Electrons (HER)
To the IP

## Slide 70: Virtual Tour of KEKB: e+e- double ring collider 1999~2010

## Slide 71: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
Arc section
(Nominal cell section)
Two rings side by side, LER being inner ring in this section.

## Slide 72: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
ARES (The Accelerator Resonantly coupled with an Energy Storage) Normal conducting Cavity
Storage cavity
Accel. cavity
Coupling cavity
KEKB
Passive stabilization with huge stored energy.
Eliminates unnecessary modes by a coupling of 3 cavities.
Higher Order Mode (HOM) dampers & absorbers.
No need for longitudinal bunch-by-bunch feedback.
No transverse instabilities arise from the cavities.

## Slide 73: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
http://legacy.kek.jp/nobel/photos/photosample/nobel1022.jpg

## Slide 74: Virtual Tour of KEKB: e+e- double ring collider 1999~2010
KEKB control room.
We did not usually have this many people there.

## Slide 75: Challenges: SuperKEKB as an example
Need for even higher luminosity machine
Q: How many years would we need to accumulate 50 ab-1
(the target given by the physics community)
IF we kept running the present KEKB?
A: With the current peak luminosity of 2x1034 cm-2s-1
⇒0.3 ab-1/year (assuming 1.5×107 seconds/year running)
⇒167 years.
Need for much higher luminosity machines:
Next Generation B-factories
Two projects are being pursued: SuperB and SuperKEKB
I will introduce this one today.

## Slide 76: Challenges: SuperKEKB as an example
50 times higher
Next Generation
B-factories
This is our mission
Keys to success:
Production and circulation of the very small emittance beams.
Colliding “nano-spot-size” beams and maintaining a good collision condition.
Increase of the beam currents.

## Slide 77
Low emittance positrons to inject
e- 2.6 A
e+ 3.6 A
Low emittance gun
Nano-Beam
SuperKEKB
Redesign the HER arcs to reduce the emittance.
New IR with S.C.
& P.M. final focusing quads
Colliding bunches
Low emittance electrons to inject
New positron target / capture section
Replace long dipoles with shorter ones (HER).
TiN coated beam pipe with antechambers
Add / modify RF systems
for higher currents.
~40 times gain in luminosity
e+ damping ring
3.016 km

## Slide 78: Challenges: SuperKEKB as an example
Higher beam currents
(a factor of 2 larger than KEKB)
Synchrotron radiation power
Higher photon density
Higher heat & gas load
Higher bunch current
Short bunch length
(though the same as KEKB)
Higher Oder Mode (HOM) heating
Electron cloud instability, heating of components, etc.
Ante-chamber
Ante-chamber with clearing electrodes
Comb-type RF shield
For gate valve
Damaged RF finger
Hardware challenges
Vacuum components as examples.

## Slide 79: Challenges: Recovery from the earthquake
Magnitude 9.0

## Slide 80: Challenges: Recovery from the earthquake

## Slide 81: Challenges: Future Accelerators
ERL: Energy Recovery Linac
LC : Linear Collider
μ-μ Collider and/or μ-Factory
Laser-plasma acceleration

## Slide 82: Challenges: Future Accelerators
While an electron storage ring stores the same electrons for hours in an equilibrium state, an ERL stores the energy of the electrons.
Basic idea: Bring the beam through the accelerating structures timed in a way so that the second-pass beam is decelerated, i.e. delivering its energy to the cavity fields.
Required RF power becomes nearly independent of beam current.
ERL (Energy Recovery Linac)
Superconducting rf cavities
undulators

## Slide 83: Challenges: Future Accelerators
μ-μ Collider and/or μ-Factory
Muon is heavier than electrons
Can accelerate to higher energy with a circular machine than electrons.
How to make a strong muon beam?
Muon life time is only 2.2 ms.
We need to accelerate them quickly.
Use pion decay to generate muons.
But such muons have wide energy spread…
Stochastic cooling is needed.
Neutrino factory?

## Slide 84: Challenges: Future Accelerators

## Slide 85: Final thoughts
The development of accelerators has required developments in many technical fields, such as rf technologies, vacuum technologies, monitoring technologies, surface treatments, beam stabilization, and magnetic field shaping.
Accelerators for high energy physics continue to push new limits.
Accelerators for other uses have also become a very active field, with different metrics for performance than luminosity and energy:
Synchrotron light sources for biological and materials sciences
Medical applications
Heavy ion machines…
The field of accelerator science is still expanding and diversifying.

## Slide 86: Final thoughts
Insulation
laser
Surface treatment
Electronics
Vacuum
Superconductivity
Magnets
Monitors
Controls
Radiation
Pumps
Safety
Civil Engeering
Survey
Geology
Machining
Seismology
RF technology
Orbit
Beam-beam
Instability
Materials
Quality contorl
Computers
Device
New ideas
People
Theory
Intra-beam
intaraction
Power supply
Cable

## Slide 87
Thank you
Merci
謝々
고마웠습니다

## Slide 88: Spare

## Slide 89
Synchrotron radiation: