## Slide 1: R&D for muon g-2 and EDM measurements at J-PARC (new proposal)
TYL-FKPPL WS at Université Blaise Pascal
May 29, 2012
Frédéric Kapusta (LPNHE), Wilfrid da Silva (LPNHE)
Naohito Saito (KEK), Kazuki Ueno (RIKEN), Tsutomu Mibe (KEK)
photo taken from PMCU tower in Paris
Paris trivia (from wikipedia)
0.5ppm
0.1ppm
Population in Paris 2,211,297
Regional population 10,354,675

## Slide 2: Searching for beyond SM with muons
Muon LFV/g-2/EDM aka “muon trio”
  Sensitive probes for BSM (e.g. SUSY, Ext-D, …)
  Clues to fundamental questions : Dark Matter, Baryon Asymmetry…
Hagiwara / Davier et al.
Past - Present
Future
LFV
g-2
EDM
MEG (PSI)
E821 (BNL)
COMET(J-PARC), mu2e (FNAL)
g-2/EDM (J-PARC,FNAL)
μeγ
Renewing upperlimit
Br < 2.4 10E-12
Discovery in horizon
Next stage
EDM
dμ < 2.7 10E-19 e cm (90%CL)
g-2
aμexp = 11 659 208.9 (6.3) x 10-10 (0.5ppm)
aμSM = 11 659 182.8 (4.9) x 10-10
aμexp -aμSM = +3.3 σ

## Slide 3: muon g-2/EDM measurements
In uniform magnetic field, muon spin rotates ahead of momentum due to g-2 = 0
aμ (= (g-2)/2 ) is deduced from this residual rotation (precession).
In general, spin also rotates due to Beff = β×E and EDM.
BNL E821 approach
γ=30 (P=3 GeV/c)
J-PARC approach
E = 0
Proposed at J-PARC with 0.1ppm precision
general form of spin precession vector:
Continuation planned at FNAL with 0.1ppm precision

## Slide 4
Bird’s eye photo in Feb. 2008
J-PARC Facility
(KEK/JAEA)
Material and Life Science
Facility
Neutrino Beam
To Kamioka
Main Ring
(30 GeV)
Hadron Hall
LINAC
3 GeV
Synchrotron

## Slide 5
New Muon g-2/EDM Experiment at
J-PARC with Ultra-Cold Muon Beam
Surface muon
Ultra Cold m+ Source
Muon LINAC (300 MeV/c)
Muon
storage

## Slide 6
Resonant Laser Ionization of Muonium (~106 m+/s)
Graphite target
(20 mm)
3 GeV proton beam
( 333 uA)
Surface muon beam
(28 MeV/c, 4x108/s)
Muonium Production
(300 K ~ 25 meV⇒2.3 keV/c)
New Muon g-2/EDM Experiment at
J-PARC with Ultra-Cold Muon Beam
Surface muon
Ultra Cold m+ Source
Muon LINAC (300 MeV/c)
Muon
storage

## Slide 7
Resonant Laser Ionization of Muonium (~106 m+/s)
Graphite target
(20 mm)
3 GeV proton beam
( 333 uA)
Surface muon beam
(28 MeV/c, 4x108/s)
Muonium Production
(300 K ~ 25 meV⇒2.3 keV/c)
New Muon g-2/EDM Experiment at
J-PARC with Ultra-Cold Muon Beam
Silicon Tracker
66 cm diameter
Surface muon
Ultra Cold m+ Source
Muon LINAC (300 MeV/c)
Muon
storage
Super Precision Magnetic Field
(3T, ~1ppm local precision)

## Slide 8: The muon storage magnet
Super-conducting coils
Cryogenics
e+ tracker
Magnet iron yoke
2900 mm
μ storage orbit

## Slide 9: Positron tracker
Positron tracker consists of silicon-strip vanes.
mm
・ signal e+ (p>200MeV/c)
・ BG e+ (p<200MeV/c)
Silicon-strip vane
GEANT4
In the first 5 ns after muon injection,
  15 signal e+ tracks with p>200 MeV
  30 BG e+ tracks with p<200 MeV
  Hit rate 1-2 MHz/200μm
  Rate reduced by 1/160 after 30 μs (5 x lifetime)

## Slide 10: Expected time spectrum of me+nn decay
Muon spin precesses with time.
 number of high energy e+ changes with time by the frequency :
w
e+ decay time (sec)
p>200 MeV/c
0.1ppm uncertainty

## Slide 11: Expected time spectrum of me+nn decay
dm=2E-20 e・cm
Up-down asymmetry
e+ decay time (sec)
EDM tilts the precession axis.
This yields an up-down decay asymmetry in number of e+
(oscillates with the same frequency ω)
∝EDM
w
p>200 MeV/c

## Slide 12: French-Japan collaboration on the positron tracker development
KEK
  Osamu Sasaki
  Manobu Tanaka
  Masahiro Ikeno
  Tomohisa Uchida
  Takashi Kohriki
  Naohito Saito
  Tsutomu Mibe
RIKEN
  Kazuki Ueno
Univ. of Tokyo
  Takuya Kakurai
Rikkyo Univ.
  Jiro Murata
  Haruna Murakami
LPHNE Paris
  Frédéric Kapusta
  Wilfrid da Silva
  Jean-François Genat
  Jaques David
CC-IN2P3 Lyon
  Yonny Cardenas
French-Japan collaboration on detector development
was initiated with SAKURA program (MAEE-JSPS) (2011-2012).

## Slide 13: 2nd Workshop on muon g-2 and EDM in LHC era
Hosted by LPNHE
Held in May 25 (last Friday) in LPNHE, Paris
30+ participants from France, Germany, Spain and Japan
Round-table discussion on theoretical & experimental issues
Frédéric Kapusta
(LPNHE)

## Slide 14: Proposed research program in FJPPL
The base of research program has been developed under SAKURA program (MAEE-JSPS).
We propose to strengthen the collaboration in following areas :
  Software framework
  Reconstruction software
  Simulation software and Computing resource with CC-IN2P3
  Detector characterization including beam tests of silicon-strip vanes at DESY/J-PARC
Simulated positron track
and reconstruction

## Slide 15: Software framework
Development of software framework become critical as sub-R&D tasks are in advanced stage.
Mokka is a tools developed by French laboratory (Labortoire Leprince-Ringuet (LLR)).
Mokka as example for building the g-2/EDM detector.
Development in FJPPL
  Architecture
  Technology selection and implementation
  Establish link between simulation and hardware design
Plot from Wilfrid da Silva

## Slide 16: Track reconstruction software
Track of e+ will be reconstructed from tracker hits.
Visualization
  Event displays (RIKEN/LPNHE)
Track finding (RIKEN/KEK)
  Hough transformations
  Steering
Track fitting (LPNHE)
  Tools built on GENFIT (made in French)
Performance of track reconstruction has demonstrated for a single track.
Future development in FJPPL
  Multi-tracks reconstruction
  Vertex reconstruction
Plots from Wilfrid da Silva

## Slide 17: Simulation and computing resource
The experiment measures of 10E+13 muon decays.
Thus, 10E+14 decays in MC simulation.
Significant computing resource required
  10E+14 decay/ 1year / 100 cpu = 10E+5/sec
G4 code development (RIKEN/KEK)
Preliminary simulation performed at CC-IN2P3 (Wilfrid da Silva, Yonny Canderas)
Development in FJPPL
  Benchmark tests
  Code optimizations

## Slide 18: Detector characterization
Test detector module (KEK)
  Studies on rate effects
  Impact to precision B-field
Frontend ASICs under development (KEK)
Infrastructure for sensor characterization (LPNHE)
Expertise on silicon detector developments (LPNHE)
Development in FJPPL
  Characterization of Silicon sensor and frontend electronics
  Beam tests at DESY & J-PARC
18

## Slide 19: Summary
In FJPPL, we propose to collaborate in following areas of detector R&D for muon g-2/EDM:
  Software framework
  Reconstruction software
  Simulation software and Computing resource with CC-IN2P3
  Detector characterization including beam tests of silicon-strip vanes at DESY/J-PARC
Other areas, such as detector hardware and muon beam studies, are also being considered for future collaboration.
Exploring possible collaboration with Korean scientists is top list in agenda too.

## Slide 20: Muon g-2 in standard model
D. Nomura (PhiPsi11)

## Slide 21
Breaking news!

## Slide 22: Injection, storage, and positron detection
Muon beam is injected here
Magnet coil (3T)
detector
kicker
mm
Spiral injection
Anti-Helmholtz-type kicker
(Pulse kick to stop spiral)
Positron tracker
ν
ν
e+
Muon storage magnet

## Slide 23: Requirements and core R&D tasks
GEANT4 simulation, toy MC
Track finding studies
DSSD sensor evaluation
E-field calculation model
B-field measurements by NMR
Front-end electronics
Detector should be efficient for
  Positron track with p = 200 - 300 MeV/c in 3T solenoidal B-field
  with a radial vertex resolution of s=1 mm (if very-weak focusing is applied).
Immune to early-to-late effect
  The decay positron rate changes by two orders of magnitude.
  1.6 MHz/strip  10kHz/strip for 200 um pich Silicon strip.
  The positron detector must be stable over the measurements.
Zero E-field (<<10-2 V/cm) at muon storage area
Not spoil the precision B-field ( <10ppm) at muon storage area
Efficient readout in compatible with the J-PARC beam pulse structure
feedback
Software design framework
(Simulation, offline reconstruction, DAQ)
Mechanical design
(thermal, vacuum, EM shield)
Computing environment
(simulation, GRID, finite element analysis)

## Slide 24: Our approach
Compact storage ring
  Suited for precision control of B-field
    Example : MRI magnet , 1ppm local uniformity
Completely different systematics than the BNL E821 or FNAL
70 cm
Hitachi co.
14m
BNL E821 / FNAL g-2
J-PARC g-2
P= 3.1 GeV/c , B=1.45 T
P= 0.3 GeV/c , B=3.0 T

## Slide 25: Design parameters
Item | Specifications
Fiducial volume | 240mm (radial) x 400 mm (axial)
Number of vane | 48 (still subject for optimization)
Sensor technology | Double- or single-sided Silicon strip sensor
Strip | axial-strip : 188mm pitch, 72mm long , 384 ch radial-strip: 255mm pitch, 98mm long, 384 ch
Sensor dimension | 74 mm x 98 mm x 0.32mm
Number of sensor | 576 ( 12 sensors per vane)
Number of channel | 442,368 ch
Time measurement | Period : 33ms, Sampling time : 5ns

## Slide 26: me+nn decay kinematics
The e+ angular distribution is subject to the V-A structure of weak interaction.
High energy positron tends to be emitted into the direction of muon spin.
The optimum e+ momentum threshold is around 200 MeV/c.
200 MeV/c
μ+
spin
V-A favored
V-A suppressed
e+
e+
Positron emission in muon rest frame
p spin
νν
−
νν
−
N(p>p(threshold)) = N (1 + A s・p /(|s||p|)
→ →
Laboratory frame
μ+
W+L
νR
e+R
νL
−

## Slide 27: The Silicon vane
T. Kohriki
Detector modules will be placed in vacuum environment (P<0.1Pa)

## Slide 28: BNL, FNAL, and J-PARC

## Slide 29: Raw occupancy and hit distributions
A GEANT4 simulation has been carried out to evaluate positrons hits as well as background hits.
  BG consists of EM processes: such as bremsstrahlung, annihilation, pair creation etc...
Occupancy is less than 0.5% per 5ns time stamp (5 hits/strip/spill).
Positron tracks at the beginning:
  15 signal e+ tracks with p>200 MeV at first 5ns
  30 BG e+ tracks with p<200 MeV at first 5ns
  Strong hit correlations in fZ plane and XY plane.
z
y
x
f
G4 simulation
1 spill (40000 muon decays)
G4 simulation
first 5ns time stamp
・ signal e+ (p>200MeV/c)
・ BG e+ (p<200MeV/c)
K. Ueno

## Slide 30: Raw occupancy and hit rate
Occupancy is less than 0.5% per 5ns time stamp (5 hits/strip/spill).
Positron tracks at the beginning:
  15 signal e+ tracks with p>200 MeV in first 5ns
  30 BG e+ tracks with p<200 MeV in first 5ns
G4 simulation
1 spill (40000 muon decays)

## Slide 31: Time evolution of track hits
By Kazuki Ueno

## Slide 32: Readout electronics and DAQ
Readout electronics and DAQ are designed to match the time structure of the J-PARC beam.
Signals in Silicon sensors are amplified and digitized at Front end, then transmitted to the backend readout boards.
O. Sasaki
M. Tanaka
T. Uchida
J.F. Genat

## Slide 33: Front-end ASIC
Preamplifier output
Shaper output
Comparator output
Analog and digital part of the ASIC has been designed in JFY2011.
Simulated pulse shape in ASD
M. Tanaka,T. Uchida
M. Ikeno,O. Sasaki

## Slide 34: High precision clock
The system clock utilizes the high precision Rb frequency standard with remote calibration from the national frequency standard NMIJ as well as GPS to realize frequency stability of Df/f <5 x 10-9/s.
GPS antenna at KEK

## Slide 35: R&Ds for early-to-late effects
A silicon-sensor test system with IR laser was built.
The IR laser could be pulsed at repetition rate as high as 80MHz with an asynchronous external trigger.
Systematic studies on early-to-late effects are in progress.
fmax=80MHz
T. Kakurai, T. Mibe,
O. Sasaki, T. Kohriki

## Slide 36: Effect of detector components in the precision B-field
NMR controller
1.6T super-conducting
solenoid
NMR probe
Test material
B-field in the vicinity of material and detector components were measured by NMR probe.
K. Sasaki, T. Kakurai
T. Mibe, O. Sasaki

## Slide 37: Effect of magnetic field due to currents in electronics
A data transfer board with a FPGA and an optical transceiver (prepared for Belle-II exp.) was operated under 1.6 T solenoid.
  Voltage : 3.3 V
  Current : 1 A
  Dummy data transmission
B-field change of 12-25 ppm (2 ppm) was observed at 7.5 mm (150 mm) away from the parts. These changes are due to magnetic susceptibility of materials since no change of B-field beyond the sensitivity was observed when the power is on.
B(blank) = 1600.446 mT
B(off) = 1600.407 mT
B(on, idle) = 1600.407 mT
B(on, data TX) = 1600.407 mT
7.5mm
NMR
Probing point
FPGA
Optical
Transceiver
(3.1Gbps)
Belle-II data transfer board
B(blank) = 1600.446 mT
B(off) = 1600.468 mT
B(on, idle) = 1600.468 mT
B(on, data TX) = 1600.468 mT
Thanks to
Bellle-II group
Nakao-san and Higuchi-san

## Slide 38: Capacitor
Surface mount capacitors were evaluated (1-100pcs).
No strong dependence on capacitance.
More effect in larger-dimension capacitors.
Lines are from OPERA-3D

## Slide 39: Resistor
Surface mount capacitors were evaluated (100pcs).
No strong dependence on resistance, grade.
More effect in larger-dimension registers.
(1 piece)
実線は磁化率をパラメータにしてOPERA計算結果をデータにフィットしたもの

## Slide 40: FPGA/PROM/Optical module
磁場変動の２次元マップ
r [mm]
ΔB/B [ppm]

## Slide 41: Projected schedule
Now
CDR submitted
Stage-1 approved
TDR submmision
Stage-2 request?