## Slide 1
CLAS12
Micromegas Central Tracker
Project
Project launched on November 18 2011
CEBAF the Jlab’s accelerator is upgraded from 6 to 12 GeV
Our Tracker should be ready for October 2014 when Beam is delivered to CLAS12 in Jlab’s Hall B.

## Slide 2
CLAS12
CLAS12 (Large acceptance and high luminosity - L=1035 cm-2s-1 ) to provide a new reach in Hadron Physics
B

## Slide 3
Physics with CLAS12
3D Structure of the Nucleon –
  High precision measurements of exclusive et semi-inclusive processes - Generalized Parton Distributions (GPDs) and Transverse Momentum Dependencies (TMDs).
Precise Measurements of structure functions
Elastic and Transition Form Factors at high moment transfer
Hadronization and Colour Transparency.
Spectroscopy – heavy baryons, hybrid mesons.
5 years of beam already scheduled for JLab PAC approved experiments.

## Slide 4
CLAS12
Forward spectrometer:
- TORUS
HT Čerenkov
Drift chambers
LT Čerenkov
Forward ToF
Preshower Calorimeter
(6 sectors)
E.M Calorimeter. (EC)
Central Detector:
SOLENOID
Tracker Barrel Micromegas/Silicon
Forward Tracker
Central ToF
Central
Detector
Forward
Detector

## Slide 5
Micromegas Tracker
Central Detector
SVT – MVT :
Charged particles Tracking
from 35 to 125° and 5 to 35°( FVT)
Vertexing
CTOF, ΔT < 60psec for particle id
Neutron counter
5T Solénoid,
Active shielding vs Moller electrons
ΔB/B < 10-4 in a 2.5x4 cm2 cylinder
for target polarisation
Barrel: 3 cylindrical double layers (Z,C) bulk Micromegas around 3 SVT double layers
Forward: 3 double disc shaped bulk Micromegas

## Slide 6
Micromegas Tracker
450
225

## Slide 7
CLAS12 Tracking specs
Specification | Forward | Central
Angular Acceptance | 5-35° | 35-125°
σp/p | < 1% | < 5%
σϴ | < 1 mrad | < 5-10 mrad
σφ | < 3 mrad | < 5 mrad

## Slide 8: Resolutions comparison
 | 4 x 2MM | 4 x 2SI | 2 x 2SI + 3 x 2MM | Specs.
pT/pT (%) | 2.9 | 2.1 | 1.6 | 5
 (mrad) | 1.3 | 15.1 | 1.4 | 10
 (mrad) | 10.9 | 2.9 | 2.6 | 5
z (μm) | 212 | 1522 | 267 | tbd.
(for  @ 0.6 GeV/c ,  = 90°)
 Mixed solution benefits from advantages of both MM and Si
 The full Si solution is never the best

## Slide 9: CLAS12 tracking with Barrel MM + Si
 SVT + BMT best solution to reach spec on θ
SVT
SVT+BMT
Very good tracking efficiency thanks to redundancy:

## Slide 10: Geant4 Simulations - Barrel
MM | Layer 1 | Layer 2 | Layer 3 | Layer 4 | Layer 5 | Layer 6
e-/e+ | 1.27 | 2.73 | 1.14 | 2.92 | 1.70 | 3.68
photon | 0.08 | 0.03 | 0.07 | 0.06 | 0.09 | 0.08
hadron | 0.96 | 0.95 | 1.13 | 1.11 | 0.91 | 0.84
total | 2.40 | 3.80 | 2.40 | 4.15 | 2.77 | 4.66
Si | Layer 1 | Layer 2 | Layer 3 | Layer 4
e-/e+ | 3.9 | 3.7 | 4.3 | 4.3
photon | 30.5 | 22.0 | 25.7 | 20.0
hadron | 1.6 | 1.3 | 1.7 | 1.5
total | 36.2 | 27.0 | 31.9 | 26.0
Background noise (MHz)
© S. Procureur

## Slide 11: Simulations Geant4 - Forward
 | Layer 1 | Layer 2 | Layer 3 | Layer 4 | Layer 5 | Layer 6
e-/e+ | 7.6 (7.5) | 4.7 (6.4) | 4.7 (6.6) | 4.0 (7.3) | 4.0 (7.2) | 3.6 (7.5)
photon | 2.0 (13.9) | 0.2 (11.3) | 0.2 (9.5) | 0.1 (8.3) | 0.1 (7.1) | 0.1 (5.7)
hadron | 2.2 (1.6) | 2.1 (1.5) | 2.0 (1.4) | 2.0 (1.4) | 1.9 (1.4) | 1.8 (1.3)
total | 12.0 (23.1) | 7.2 (19.3) | 7.0 (17.7) | 6.2 (17.1) | 6.1 (15.8) | 5.5 (14.6)
Rates in MHz
Very high rates in the central area
© S. Procureur

## Slide 12
The Challenges
Large Cylindrical detectors
5T Magnetic field environment
High flux of particles
Crowded location: deported electronics

## Slide 13: Cylindrical Micromegas
Performance compared to thick flat MM using cosmics
→ similar performance as thick
detectors
Thick detector
Thin detector

## Slide 14: 5 Tesla magnetic field
Z tiles of Barrel Micromegas are sensitive to
the Lorentz angle of drifting electrons
x = h tanθ = h v B / E
x
h
→ minimize h (but less signal)
→ use heavier gas (but more sparks)
→ increase E field (but lower
transparency)
Garfield simulation
→ z ~ 220 µm if  can be lowered
down to 20°

## Slide 15: Spatial resolution in 5 T
Test to validate Garfield simulation with a Micromegas in dvcs magnet (Hall B)
Garfield validated,  can be as low as 20°
→ use of a focused UV laser to extract electrons
from the drift electrode
P. Konczykowski et al., NIM A612 (2010), 274

## Slide 16
Spark Rate studies
→ simulation: try to relate sparks with large
energy deposits with Geant4 (Gemc)
→ spark condition: Nel ~ 107 (Raether)
- Quantitatively reproduces (few) existing data
Explains gas effect & give
predictions (bulk)
S. Procureur et al., NIM A621 (2010), 177

## Slide 17: Tests @ CERN/SPS and PS
Location | CERN/SPS | CERN/PS
Date | 10/2009 | 08/2010
Goals | Spark rate in high E beam Effect of B┴ | Spark rate in low E beam Effect of a GEM foil
Pbeam | 150 GeV/c | 0.2 - 3 GeV/c
Particles | π | π+, π-, p
Beam intensity | ≤ 106 / spill | ≤ 5.105 / spill
Spill | 10 s every 50 s | 0.4 s every 50 s
Gas | Ar+5%iC4H10 | Ar+5%iC4H10

## Slide 18: SPS: results & simulation
- No significant difference between thin and thick mesh
- Reasonable agreement with simulation using Nel = 2.5 107
S. Procureur et al., NIM A659 (2011), 91

## Slide 19: PS: results and simulation
protons @ 280 MeV/c
protons @ 300 MeV/c
→ Understanding of the signals with π+ beam
→ Reasonable agreement with simulation using Nel = 4.107
G. Charles et al., NIM A648 (2011), 174

## Slide 20: Tests @ Jlab/Hall B
Location | JLab/Hall B
Date | 08/2010
Goals | effect of B// effect of a GEM foil
Pbeam | 0 – 5.5 GeV/c
Particles | photons on CH2 target
Beam intensity | ≤ 2.5 109 / s
Spill | continuous beam
Gas | Ar+10%iC4H10

## Slide 21: Tests à Jlab: B//E
Sparks at 0 T
Spark rate vs B(T)
→ reasonable agreement with
the simulation using
Nel = 2.5 107
→ spark rate increased
by a factor of 10
between 0 and 5 T
 Enhancement of charge density in amplification gap
B. Moreno et al., NIM A654 (2011), 135

## Slide 22: MM-GEM: Results and simulation
→ Comparison at ΔVGEM=280 V (intermediate regime):
MM
MM-GEM 1mm
MM-GEM 2mm
dots: data
lines: simulation
(dslim = 2.109 el / mm²)

## Slide 23
Future followed up Projects
Forward Photon Tagger (2.5 to 5°) for CLAS12
MM type Fwd
EIC MM type Barrel

## Slide 24
Summary
The main issues concerning the future working environment CLAS12 Tracker project have been adressed.
Simulation tools have been developed and have enabled to understand more quantitavely the Micromegas detector
To be followed in next talk…

## Slide 26: Working conditions
Parameter | Barrel MVT | Forward MVT
Gain effectif | 5000 | 3000
Mélange gazeux | Ar + 10% iC4H10 | Ne + 10% C2H6
Hauteur de dérive | 3 mm | 5 mm
Feuille de GEM | N/A | 1 GEM à 3 mm
Champ de dérive | 8 kV/cm (Z) et 4 kV/cm (C) | 1 kV/cm
Angle de Lorentz | 20° (Z) et 40° (C) | 0°
Rapport des champs | 5,5 (Z) et 9 (C) | ~ 50
Transparence | 40% (Z) et 50% (C) | 100%
X0 | 0,3% | 0,3%
Segmentation | Longitudinale en 3 parties | Annulaire en 3 parties
Taille maximale PCB (et capa) | 45x43 cm² (16 nF / 3) | Φ 43 cm (12 nF / 3)
Flux de particules / couche | 4 MHz (dont 1 MHz hadrons) | 12 MHz (dont 2 MHz hadrons)
Taux de claquages / mesh | 1 Hz | 1 Hz
Temps mort | < 2 % | < 2%
Efficacité de détection | > 90% | > 95%
Pitch | 540 μm (Z) et 270 μm (C) | 500 μm
Résolution spatiale | 250 μm (Z) et 100 μm (C) | 145 μm
Résolution temporelle | 10 ns | 10 ns