## Slide 1: Using step-like nonlinear magnets for beam uniformization at target in high intensity accelerarors
Zheng Yang, Jing-Yu Tang, IHEP, China
P.A. Phi Nghiem, Nicolas Chauvin, CEA/Saclay/IRFU, France

## Slide 2: Topics
Introduction to CSNS C-ADS IFMIF accelerators
Beam spot uniformization
Introduction of the step-like magnet
Application on the CSNS C-ADS IFMIF

## Slide 3: CSNS high power proton accelerator
Phase | I | II | II’ or III
Beam power on target [kW] | 100 | 200 | 500
Beam energy on target [GeV] | 1.6 | 1.6 | 1.6
Ave. beam current [mA] | 63 | 125 | 315
Pulse repetition rate [Hz] | 25 | 25 | 25
Protons per pulse [1013] | 1.6 | 3.1 | 7.8
Linac energy [MeV] | 80 | 132 | 250
Linac type | DTL | DTL | +SCL
CSNS (China Spallation Neutron Source) is a high-power proton accelerator based multi-disciplinary facility for research, mainly relying on neutron scattering techniques.
Construction: 2011-2017
Site: Dongguan, Guangdong
IHEP and IOP

## Slide 4: China ADS high power proton accelerator
China is pursuing an ADS (Accelerator-Driven Subcritical System) program strongly, under CAS (IHEP, IMP, IPP and USTC)
Accelerator: 10mA, CW proton beam
RFQ+CH
RFQ+Spoke
2013
~5 MeV
2015
25~50 MeV
201X
50/150 MeV
~2022
0.6~1 GeV
~2032
1.2~1.5 GeV
5~10 MWt
100 MWt
≥1 GWt
Verification of two ways
Integration
Integral test
Phase II target
Phase III target
10 MeV
Phase I
R&D Facility
Phase II
Experiment Facility
Phase III
DEMO. Facility

## Slide 5
L
M
H
Test Cells
High (>20 dpa/year, 0.5 L)
Medium (>1 dpa/year, 6 L)
Low (<1 dpa/year, > 8 L)
Lithium Target
25 mm thick, 15 m/s
Typical reactions 7Li(D,2n)7Be 6Li(D,n)7Be 6Li(n,T)4He
2 accelerators, 2x125 mA, 2x5MW
D+
IFMIF: International Fusion Materials Irradiation Facility
The highest average current linac under developing in the world, pose many challenges

## Slide 6
One of the critical issues concerning the interface between a high-power beam and its irradiation target is the spot uniformity to reduce the peak current density at the target and reduce the beam halo
  CSNS
  Beam footprint in rectangular shape: 12 cm (H) x 5cm (V)
  Ratio of the peak current density to the average: <3
  C-ADS
  Beam footprint in rectangular shape: 4.4cm (H) x 4.4cm (V)
  Ratio of the peak current density to the average: <2.5
IFMIF (to be revised)
    Beam footprint in rectangular shape: 20 cm (H) x 5 cm (V)
    Current density across the flat top is uniform (±5%)
    Current density: < 0.5 A/cm2 (for |x|>11 cm)
Beam spot uniformization

## Slide 7
Input beam of C-ADS beam transfer line
Input beam of IFMIF-HEBT

## Slide 8
Nonlinear magnets are needed for the beam spot uniformization at target
  More conventional: single octupole or pair of octupole and dodecapole for each plane (horizontal or vertical)
  New concept-1: step-like field magnets, initially proposed for ESS and CSNS
  New concept-2: simplified multipole magnets including different combinations of anti-symmetric second-order, third-order, fourth-order and fifth-order field magnets, recently proposed at IHEP

## Slide 9: Introduction of the step-like magnet
8 poles -r50 mm
Field on pole 0.30 T
Octupole
2 dipoles-r100 mm
Field on pole 0.040 T
Step-like magnet

## Slide 10: Advantage
Flexibility
uniformization of beam core and beam halo can be done separately by two steps
Cheaper
standard multipoles: 100 thousand dollars
step-like magnets : 20-40 thousand dollars

## Slide 11
Step-like field magnet prototyping

## Slide 12
Optimization principle
1. Change the last four or six quadrupoles and the length of drift to get a larger beam spot on the target and fulfill the request of the flat beams and phase advances (linear optics)
2. Adjust the parameters of the step-like magnets to obtain a good beam spot on the target (nonlinear optics)
3. Repeat 1. and 2. several times to find the best result

## Slide 13
Studies at IHEP:
Using step-like field magnets (SFM) for spot uniformization at CSNS
100000particles

## Slide 14: Tests with beam for spot uniformization
A test beam line using the ADS-RFQ is being set up for studies on both halo development and spot uniformization (plan under modification)
SFM can be step-like field magnets or simplified high-order magnets

## Slide 15
Studies at ADS beam line (dump):
Using step-like field magnets (SFM) for spot uniformization

## Slide 16
Duodecapoles
Octupoles
Adaptation,
9° achromat
Non-linear lenses
Beam homogenisation
Beam expander
Li Target
Dipoles
Quadrupoles
"Classical" HEBT structure
Superconducting Linac
R. Duperrier, J. Payet, D. Uriot, Proc. of EPAC 2004

## Slide 17
Beam distribution at Li Target
Beam losses
scrapers 2.3 kW
(to be optimised)
To be improved
Tuning strategy to be defined

## Slide 18
Duodecapoles
Octupoles
Adaptation,
9° achromat
Li Target
Dipoles
Quadrupoles
Test (temporary) structure with SFM
Superconducting Linac
Step-like Field Magnet
J.Y.Tang, H.H. Li, S.Z. An, R. Maier
NIMA, 2004

## Slide 19
Beam distribution at Li Target
Beam losses
scrapers 2.3 kW
(to be optimised)
To be improved
Larger Footprint
Tuning strategy to be defined

## Slide 20
Adaptation,
11° achromat
Li Target
Dipoles
Quadrupoles
Shorter structure with SFM

## Slide 21
No beam loss

## Slide 22
Density
Start-to-end without errors
Density
Start-to-end with errors

## Slide 23
Thank you