## Slide 1: PANDA EMC BWE Proto18
Mikel Catania Goikoetxea, Javier Navarro Medrano, David Rodríguez Piñeiro, Yue Ma, Frank Maas

## Slide 2: Proto18 Summary
Proto18:
  Motivation
  Configuration
  Sections
Detector:
  Crystal Group
  Preamplifiers Location
  Assembly
Mechanical Structure:
  MP1
  Feet
  MP2
Cooling System:
  Circuits
  Chiller
Insulation System:
  Elements
  Backside
  N2 flow
Wire Evacuation
Sensors
Support System
Proto18 Tests
Proto18: Future Tasks

## Slide 3: Proto18 Motivation
First Prototype for PANDA EMC BWE
  Obtain information for the EMC BWE final design
18 PbWO4 Crystals
Closest working conditions to PANDA BWE EMC
  Temperature of -25°C in Crystals
  All devices held from the backside
  All system circuits get out from the backside
  Minimize insulators
  Avoid cooling in the front due to budget material
Test different cooling configurations
Cooling & Wires: over back side
Cantilever: overhanging structure

## Slide 4: PROTO18 Configuration
18 PbWO4 Crystals divided in two groups: 16 and 2 crystals in each one
20 Crystals available

## Slide 5: Proto18: Sections
Detectors
Crystals
Electronics
Mechanical Structure
Cooling & Insulation

## Slide 6: Detector: Crystal Group

## Slide 7: Detector: Crystal Group
Al Frame
Patch Panel
PVC Capsule
Hole for optic fiber
Dimensions adjusted to crystal (24,4x24,4mm)
Space to apply optical glue
Active part of the APDs centered in the crystal section
Patch Panel wires to connect with Preamplifiers

## Slide 8: Detector: Electronics
4 x PVC Tray
Al Insert
Grooves for trays
Holes for N2 circulation
8 Preamplifiers per tray

## Slide 9: Detector: Electronics
PVC Tray
Al Insert
4 Preamplifiers in a tray

## Slide 10: Detector: Assembly
Crystal located into the alveoli and patch-panels connected to the preamplifiers with small flexible wires
Alveoli glued to the aluminum Insert
Connection wires located into these spaces
CF Stoppers for crystals

## Slide 11: Mechanical Structure: MP1
5x Holes for wires
2 x Holes N2
2x Holes for the supporting feet
Mounting Plate 1
  Aluminum
  15 mm thick
  “Cold Plate”

## Slide 12: Mechanical Structure: Supporting Feet
  Glass Fiber
  From 14 to 23 mm diameter
Max. Stress: 114 MPa
Security Coefficient > 4
Max. Displacement: 0,07 mm
Tensile Yield Point, σradial = 250 MPa
Young´s modulus, Eradial = 25 GPa
Thermal conductivity, λ = 0, 3 W/mK
Thermal linear expansion, 1,2 x 10-5 1/T
  100 mm long
  Conical surfaces to support MP1 and hold in MP2

## Slide 13: Mechanical Structure: Feet
Aluminum caps bolted with 4 screws

## Slide 14: Mechanical Structure
The aluminum Inserts are bolted with 2 screws and positioned by 2 pins each one

## Slide 15: Mechanical Structure: MP2
10 x Cooling holes
2 x Aluminum Lockers
o-ring groove
Mounting Plate 2
  Aluminum
  25 mm thick
  Same drilled holes as in MP2 (N2, feet, wires)
  Groove for o-ring sealing
  “Warm Plate”

## Slide 16: Cooling System: Circuits
4
5
  Aluminum Shell (divided in 3 parts because of the shrinkage) bolted to the MP1 to distribute cooling power
  PU Cooling pipe (internal diameter: 4mm, external diameter: 6mm)
  PVDF 90º elbows
  5 different circuits commanded by an external manifold: ability to study different cooling configurations
1
2
3

## Slide 17: Insulation System: Elements
Al Cover
(2 mm thick)
O-ring
VIP double box
(16 panels 10mm thick )
Vacuum Insulation Panel (λ: 0,008 W/mK)
Styrofoam (λ: 0,03 W/mK)
Insulation tubes around the cooling pipes
Styrofoam blocks (6-7 mm thick)

## Slide 18: Insulation System: Backside
Back Insulation
  Styrofoam 50 mm thick block. Drilled for wire evacuation, Feet, back cooling pipes and N2 pipes (coincident holes with MPs)
  Channels for back cooling pipes

## Slide 19: Wire Evacuation
Current status:
  3 wires going out per preamplifier (signal, high voltage, power supply)
  Working in reducing the quantity of wires
  Study sealing, checking the possible entrance of water-air
Shrinking tubes for wire evacuation. Using black silicone for the sealing
Tight tubes after heat application

## Slide 20: Sensors
2 measurement positions in order to check the crystal gradient
Thermal sensors
  Design from Bochum
  Built by our group at GSI
  Sensors in several positions to monitor temperatures
    Covering most possible number of crystals
    Some also around the prototype, inside
Humidity sensors
  To monitor the relative humidity inside
  4 sensors: 2 in the front, 2 inside Inserts

## Slide 21: Support System
Worm Drive
Bevel Gearbox
Hand Crank
Ball Bearing
Aluminum Profiles Structure
Vertical position for cosmic rays testing

## Slide 22: Support System
Worm Drive
Bevel Gearbox

## Slide 23: Proto18 Tests
Load Test
Mounting Test
VIP Test

## Slide 24: PROTO18: Future Tasks
Mechanical design
  Insert design in two parts due to machining restraints
  Arrange Cover, Mounting Plate designs and o-ring size with Vacuum and Mechanical Workshops
  Check spaces in the front, to test front cooling too
Cooling & Insulation
  Define N2 circuit system
  Chiller Selection
  Define additional cooling circuits
Electronics
  Patch Panels wire selection
  Reduction of preamplifier number
Support & Alignment System
  Design the Support Profile Structure
  Define alignment system
Load Test
  Check crystals deflection using Dial Indicators
VIP Test
  Check VIP efficiency
  Check VIP joints
Mounting test
  Continue the improvement (tools design…)