## Slide 1: Development of Silicon-strip tracker for muon g-2 and EDM measurements at J-PARC
LPNHE, Paris
February 22, 2012
Tsutomu Mibe (KEK)
for the J-PARC muon g-2/EDM collaboration

## Slide 2: Quantum loop
From Lepton Moments (World Scientific, 2010)
The Schwinger term

## Slide 3: Particle dipole moments
Magnetic dipole moment
g = 2 from Dirac equation, in general g≠2 due to quantum-loop effects
＝
＋
＋
＋ …
Hamiltonian of spin 1/2 particle includes
Magnetic dipole moment
Electric dipole moment
a “anomalous magnetic moment”
m
m
m
m
m
m

## Slide 4: More loops
D. Nomura (PhiPsi11)

## Slide 5: Anomalous magnetic moment : g-2
Standard model can predict g-2 with ultra high precision
Useful in searching for new particles and/or interactions
Experiment has reached the sensitivity to see such effects...
0.24ppb
0.54ppm
Dal(SM)/al
4.5 ppb
0.41ppm
Dal(exp)/al
DHMZ, Tau 2010 workshop
a exp – a SM | = | (261 ± 80)  10 –11 (259 ± 81)  10 –11
 3.3 ”standard deviations“ |  | 
HLMNT11

## Slide 6: Hunting for SUSY (or other BSM) signature
~J-PARC
FNAL g-2 proposal
g-2 measurement is complementary to LHC and cLFV
More on physics discussions at Naohito’s seminar at LAL/Orsay tomorrow.

## Slide 7: Muon anomalous spin precession in B and E-field
Muon spin rotates “ahead” of momentum due to g-2 >0.
Precession frequency
BNL E821
  Focusing electric field to confine muons.
  At the magic momentum
  g = 29.3, p = 3.094 GeV/c  (am -1/(g2-1) ) = 0
Safely be neglected with current upper limit on EDM
Continuation of the experiment at FNAL is planned.

## Slide 8
B. L. Roberts, Fermilab , 3 September 2008
- p. 8/68
Inflector
Kicker
Modules
Storage
ring
Central orbit
Injection orbit
Pions
p=3.1GeV/c
BNL E821 Experimental Technique
Muon polarization
R=711.2cm
d=9cm
(1.45T)
Electric Quadrupoles
xc ≈ 77 mm
b ≈ 10 mrad
B·dl ≈ 0.1 Tm
xc
R
R
b
Target
25ns bunch of ≥ 1 X 1012 protons
injection & kicking
Muon storage ring
focus with Electric Quadrupoles
24 electron calorimeters
Slide from Lee Roberts
Notes: 8

## Slide 9: Our approach
Compact storage ring
  Suited for precision control of B-field
    Example : MRI magnet , 1ppm local uniformity
Completely different systematics than the BNL E821 or FNAL
70 cm
Hitachi co.
14m
BNL E821 / FNAL g-2
J-PARC g-2
P= 3.1 GeV/c , B=1.45 T
P= 0.3 GeV/c , B=3.0 T

## Slide 10: Our approach (cont’)
Zero Focusing Electric field (E = 0 )
Ultra-cold muon beam (pT/p < 10-5) by utilizing the laser resonant ionization of muonium makes it possible to realize such experimental condition.
Equations of spin motion is as simple as at the magic momentum

## Slide 11: BNL, FNAL, and J-PARC

## Slide 12: J-PARC (Japan Particle Accelerator Complex)
Mt. Fuji
Tokyo
KEK
J-PARC

## Slide 13
Bird’s eye photo in Feb. 2008
J-PARC Facility
(KEK/JAEA)
Material and Life Science
Facility
Neutrino Beam
To Kamioka
Main Ring
(30 GeV  50 GeV)
Hadron Hall
LINAC
3 GeV
Synchrotron

## Slide 14
New Muon g-2/EDM Experiment at
J-PARC with Ultra-Cold Muon Beam
Surface muon
Ultra Cold m+ Source
Muon LINAC (300 MeV/c)
Muon
storage

## Slide 15
Resonant Laser Ionization of Muonium (~106 m+/s)
Graphite target
(20 mm)
3 GeV proton beam
( 333 uA)
Surface muon beam
(28 MeV/c, 4x108/s)
Muonium Production
(300 K ~ 25 meV⇒2.3 keV/c)
New Muon g-2/EDM Experiment at
J-PARC with Ultra-Cold Muon Beam
Surface muon
Ultra Cold m+ Source
Muon LINAC (300 MeV/c)
Muon
storage

## Slide 16
Resonant Laser Ionization of Muonium (~106 m+/s)
Graphite target
(20 mm)
3 GeV proton beam
( 333 uA)
Surface muon beam
(28 MeV/c, 4x108/s)
Muonium Production
(300 K ~ 25 meV⇒2.3 keV/c)
New Muon g-2/EDM Experiment at
J-PARC with Ultra-Cold Muon Beam
Silicon Tracker
66 cm diameter
Surface muon
Ultra Cold m+ Source
Muon LINAC (300 MeV/c)
Muon
storage
Super Precision Magnetic Field
(3T, ~1ppm local precision)

## Slide 17: Injection, storage, and positron detection
Muon beam is injected here
Magnet coil (3T)
detector
kicker
mm
Spiral injection
Anti-Helmholtz-type kicker
(Pulse kick to stop spiral)
Positron tracker
ν
ν
e+
Muon storage magnet

## Slide 18: The muon storage magnet
Super-conducting coils
Cryogenics
e+ tracker
Magnet iron yoke
3600 mm
• Storage region
– Bz =3T
– Local Uniformity < 1 ppm in storage
Region
• Injection field
– Br × Bz > 0
• Very-weak magnetic focusing field
– Br = −n B0z/Rz
In collaboration with a Japanese private company

## Slide 19: me+nn decay kinematics
The e+ angular distribution is subject to the V-A structure of weak interaction.
High energy positron tends to be emitted into the direction of muon spin.
The optimum e+ momentum threshold is around 200 MeV/c.
200 MeV/c
μ+
spin
V-A favored
V-A suppressed
e+
e+
Positron emission in muon rest frame
p spin
νν
−
νν
−
N(p>p(threshold)) = N (1 + A s・p /(|s||p|)
→ →
Laboratory frame
μ+
W+L
νR
e+R
νL
−

## Slide 20: Expected time spectrum of me+nn decay
Muon spin precesses with time.
 number of high energy e+ changes with time by the frequency :
w
e+ decay time (sec)
p>200 MeV/c

## Slide 21: Expected time spectrum of me+nn decay
dm=2E-20 e・cm
Up-down asymmetry
e+ decay time (sec)
EDM tilts the precession axis.
This yields an up-down decay asymmetry in number of e+
(oscillates with the same frequency ω)
∝EDM
w
p>200 MeV/c

## Slide 22: Requirements to the e+ tracker
Detector should be efficient for
  Positron track with p = 200 - 300 MeV/c in 3T solenoidal B-field
  with a radial vertex resolution of s=1 mm.
Immune to early-to-late effect
  The decay positron rate changes by two orders of magnitude.
  1.6 MHz/strip  10kHz/strip for 200 um pich Silicon strip.
  The positron detector must be stable over the measurements.
Zero E-field (<<10-2 V/cm) at muon storage area
Not spoil the precision B-field ( <10ppm) at muon storage area
Efficient readout in compatible with the J-PARC beam pulse structure

## Slide 23: Detector design concept
Tracking planes consists of silicon-strip vanes.
Silicon sensors :
high granularity
reasonably fast signal
good stability expected

## Slide 24: The Silicon vane
T. Kohriki
Detector modules will be placed in vacuum environment (P<0.1Pa)

## Slide 25: Design parameters
Item | Specifications
Fiducial volume | 240mm (radial) x 400 mm (axial)
Number of vane | 48 (still subject for optimization)
Sensor technology | Double- or single-sided Silicon strip sensor
Strip | axial-strip : 188mm pitch, 72mm long , 384 ch radial-strip: 255mm pitch, 98mm long, 384 ch
Sensor dimension | 74 mm x 98 mm x 0.32mm
Number of sensor | 576 ( 12 sensors per vane)
Number of channel | 442,368 ch
Time measurement | Period : 33ms, Sampling time : 5ns

## Slide 26: Raw occupancy and hit distributions
A GEANT4 simulation has been carried out to evaluate positrons hits as well as background hits.
  BG consists of EM processes: such as bremsstrahlung, annihilation, pair creation etc...
Occupancy is less than 0.5% per 5ns time stamp (5 hits/strip/spill).
Positron tracks at the beginning:
  15 signal e+ tracks with p>200 MeV at first 5ns
  30 BG e+ tracks with p<200 MeV at first 5ns
  Strong hit correlations in fZ plane and XY plane.
z
y
x
f
G4 simulation
1 spill (40000 muon decays)
G4 simulation
first 5ns time stamp
・ signal e+ (p>200MeV/c)
・ BG e+ (p<200MeV/c)
K. Ueno

## Slide 27: Time evolution of track hits
By Kazuki Ueno

## Slide 28: Event gallery
Typical e+ track
A typical event in 5ns time stamp
A 3D MC event display has been developed with ROOT/EVE framework by Wilfrid Da Silva and Frederic Kapusta.
Positron
Electron
Photon

## Slide 29: Track reconstruction
Track finding
  Initial search with Hough transformation algorithm in fz plane
  Track finding efficiency for a single-track is >90%.
Track fitting
  Fitter with GENFIT (track fitting tool kit with Karman filter) is being developed by W. Da Silva and F. Kapusta.
Evaluation of multi-track reconstruction is the next step.
single track finding efficiency
track momentum reconstruction
G4 simulation
Track finder (Hough)
G4 simulation
GENFIT
K. Ueno
W. Da Silva
F. Kapusta

## Slide 30: Readout electronics and DAQ
Readout electronics and DAQ are designed to match the time structure of the J-PARC beam.
Signals in Silicon sensors are amplified and digitized at Front end, then transmitted to the backend readout boards.
O. Sasaki
M. Tanaka
T. Uchida
J.F. Genat

## Slide 31: Front-end ASIC
Preamplifier output
Shaper output
Comparator output
Analog and digital part of the ASIC has been designed in JFY2011.
Simulated pulse shape in ASD
M. Tanaka,T. Uchida
M. Ikeno,O. Sasaki

## Slide 32: High precision clock
The system clock utilizes the high precision Rb frequency standard with remote calibration from the national frequency standard NMIJ as well as GPS to realize frequency stability of Df/f <5 x 10-9/s.
GPS antenna at KEK

## Slide 33: R&Ds for early-to-late effects
A silicon-sensor test system with IR laser was built.
The IR laser could be pulsed at repetition rate as high as 80MHz with an asynchronous external trigger.
Systematic studies on early-to-late effects are in progress.
fmax=80MHz
T. Kakurai, T. Mibe,
O. Sasaki, T. Kohriki

## Slide 34: Timing resolution and rate dependence
Requirement (<10%)
T. Kakurai

## Slide 35: Effect of detector components in the precision B-field
NMR controller
1.6T super-conducting
solenoid
NMR probe
Test material
B-field in the vicinity of material and detector components were measured by NMR probe.
K. Sasaki, T. Kakurai
T. Mibe, O. Sasaki

## Slide 36: Materials and components
PCB board (G10+Cu, 10 layer)
Optical transceiver
Voltage regulator
Registers, capacitors
FPGA/PROM
Solder (with Pb, Pb-free)
10 x 1Gbps optical link
PHENIX trigger board
Belle-II data transmission test board
metals
K. Sasaki, T. Kakurai
T. Mibe, O. Sasaki

## Slide 37: Comparison with calculation (Ti)
 CRC value
Calculated curve (ー) with expected μ/μ0 value agrees with data.
x (mm)

## Slide 38: Comparison with calculation (optical module)
Best estimate μ/μ0 -1 = (9,000 +/- 750 ) E-6.
Calculated curve (ー) with μ/μ0 =1.009 best describes the data.
Not very good agreement with data, maybe due to ambiguity of source volume

## Slide 39: ΔB/B contour
+100ppm
+10ppm
+ 1ppm
+0.1ppm
+0ppm
-0.1ppm
-1ppm
-10ppm
-100ppm

## Slide 40: Core R&D tasks
GEANT4 simulation, toy MC
Track finding studies
DSSD sensor evaluation
E-field calculation model
B-field measurements by NMR
Front-end electronics
Detector should be efficient for
  Positron track with p = 200 - 300 MeV/c in 3T solenoidal B-field
  with a radial vertex resolution of s=1 mm (if very-weak focusing is applied).
Immune to early-to-late effect
  The decay positron rate changes by two orders of magnitude.
  1.6 MHz/strip  10kHz/strip for 200 um pich Silicon strip.
  The positron detector must be stable over the measurements.
Zero E-field (<<10-2 V/cm) at muon storage area
Not spoil the precision B-field ( <<0.1ppm) at muon storage area
Efficient readout in compatible with the J-PARC beam pulse structure
feedback

## Slide 41: Projected schedule
Now
CDR submitted
Stage-1 approved
TDR submmision
Stage-2 request?

## Slide 42: Summary
A new muon g-2/EDM experiment at J-PARC:
  Off magic momentum + compact g-2 ring
  Complementary to FNAL g-2
  Start in 2016
Silicon tracker for g-2
  A tracker for incoming low energy positrons
  Stringent requirements on early-to-late effect, E-field and B-field
  Conceptual design has been developed.
LPNHE group has made significant contribution in the detector design.
Looking forward to continuous (possibly larger) contribution from LPNHE and other French group in the future.