L'expérience de HESS
- Vue générale de l'acquisition
- Camera DAQ
- Event Builder

---
Data Acquisition

---
General Concepts (I)
- Multiplatform, multitasking, evolutive environment
  - Inter-process communication based on CORBA (distributed object programming)
  - Several languages: C++ (time critical parts) and python (control)
- Orchestration based on state machines for each hardware
- Definition of runs (participating elements, ...) entirely configured through databases
- New hardware can be added to the system without any change to the existing DAQ

---
General Concepts (II)
- Data format based on ROOT
  - Introspection capabilities allows to access any member (for display, analysis, ...) without recompilation
  - No distinction between offline and online algorithms

---
General Concepts (II)
- Data format based on ROOT
  - Introspection capabilities allows to access any member (for display, analysis, ...) without recompilation
  - No distinction between offline and online algorithms

---
DAQ Software
DAQ Building blocks
Dash provides all necessary classes and interfaces for the processes in the DAQ
Interprocess communication: CORBA (open source implementation omniORB)
Data processing chain:
Controllers
Receivers
Readers
Managers
Hardware
push
control
Controller
push
Receiver
data
pull
Reader
data
Display
File
data
data
data
Manager

---
Bancs Test
Philosophie générale
Pilotage
Interface graphique
(Python / GTK)
Contrôleur 1
Hardware 1
Contrôleur 2
Hardware 2
Contrôleur n
Hardware n
- Un contrôleur par instrument (petits modules autonomes)
  - Composants développés pour les bancs tests, réutilisables selon les besoins
  - Intégration aisée
Analyse
(ROOT)
DB
dbgui
CORBA
dbtools
CORBA

---
Exemples d'interfaces graphiques

---
Process State Control
Process State Control
StateControllers:
each process is a StateController
generic states for all processes
only certain transitions allowed
Example: Camera
States
Safe: power off
Ready: power on, lid open, send monitoring data
Running: HV and trigger enabled, send event data
Transitions
Configure: read configuration from database, power on, open lid, reactivate PMTs
Start: enable HV, contact Receiver, start trigger
Stop: disable HV and trigger, send event data
GotoSafe: switch power off, close lid
Safe
Ready
Running
Paused
Configure
Start
Pause
Resume
Stop
GotoSafe
Configure

---
Message Passing, Error Handling
Message Passing, Error Handling
Message categories:
Assign shift crew feedback or automatic action to certain message type
Messages are passed through Manager hierarchy
SubArray/Manager
Manager




Error
Stop
Fatal
Stop, GotoSafe
Warning
Caution
Info
Process
Stop
Stop, GotoSafe

---
Configuration
- Paramètres de configuration associés à chaque contrôleur:
  - Valeurs par défaut spécifique de chaque type de run:
  - DAQ_RunParametersList

---
Monitor client: ROOT
- Uses Sash framework (Sash::CameraMonitorEvent,...)
- Handles history
- Configurable through databases

---
Monitor client: python
Access to the SASH objects converted to Python NTuples
by the MonitorServer

---
Run Control
Run Control
Control of data taking:
measurement organized in runs of 30 min duration
assign set of configuration parameters  run types e.g. ObservationRun, FlatfieldingRun, …
Processes read their configuration according to run parameters in database
Managers take over control of processes in contexts
Parallel runs possible by using different contexts
	SubArray/Manager controls all contexts in the run
CT1/Camera
CT1/Manager
CT1/CameraHV
CT1/CameraLid
CT1/Tracking
CT1/Radiometer
CT1/Flatfield
CT1 context
RunManager
SubArray01/Manager
SubArray02/Manager
SubArray02
SubArray01
CT1/Manager
CT2/Manager
CT3/Manager
CT4/Manager
CT1
CT2
CT3
CT4

---
Status of the Online Analysis
Online Analysis
- Running stable in parallel to data taking
- Performs online calibration:
  - online pedestals (running average)
  - Nominal gain and flat field coefficients: - y = 1/80, FF = 1
- Provides pedestal corrected event display
- Generates excess maps using static background model (simplified RegionBgMaker)

---
DAQ Hardware
Linux PC Cluster
~40 commercial i86 machines
2.4 Tbyte disk space
2 LTO-2 tape drives
Partly 1 Gbit network
(optical network to cameras)
OS: Fedora Core 12
UPS!

---
Camera DAQ

---
DAQ Scheme (simplified)
< 20 MBytes/s /Node
Node 1
 Monitoring Server
1Hz
Disk
Plain C
 Events
 CAMERA
Node 2
Disk
 Temperatures
Status
Commands
 Scalers
ROOT/C++
LEDs
Python/Gtk
+CORBA
(StateController)
ROOT/C++
Node 16
Events/Monitor
displays
Disk
ROOT/C++ or
Python
MySQL
Database
Dbgui:
Python implementation
of dbtools
 Camera Controller
Data blocks
Socket
C2corba (CORBA client)
Corba
Pull Mode

---
Partie embarquée - HESS-I
Chassis cPCI
SLCD
Pilotage
Interface graphique
(Python / GTK)
Slow control
TCP-IP
ACQ_Camera
données
Node
- Un démon slow contrôle (slcd)
  - Interpréteur de commande, piloté par une interface graphique au sol
  - Boucle de monitoring (HV, températures,...)
- Un démon d'acquisition
  - « data pooling », envoi vers la ferme
DB
dbgui
CORBA

---
Data Flow – I - Camera
Readout based on ARS
"Ring Analog Memories"
Two gains:
High gain (0 – 200 pe)
Low gain (=> 2000 pe)
4 channels per ARS
4 PMTs, same gain
FARM
NODE
TCP/IP
PMT 1
PMT 2
ARS HG 1
ARS LG 1
PMT 4
PMT 13
PMT 14
ARS HG 8
ARS LG 8
PMT 16
Drawer 60
PMT 1
PMT 2
ARS HG 1
ARS LG 1
PMT 4
PMT 13
PMT 14
ARS HG 8
ARS LG 8
PMT 16
Drawer 2
PMT 1
PMT 2
ARS HG 1
ARS LG 1
PMT 4
PMT 13
PMT 14
ARS HG 8
ARS LG 8
PMT 16
Drawer 1
Box BUS

---
Data flow
Data flow – II – Central Acquisition & Online Merging
Central trigger data
CT2/Camera
Node01
Node01
CT3/Camera
Central Trigger
Controller
Node02
CT4/Camera
Node_n
Connector
- Each node receives data during 4 seconds
- Automatic node switching
- One data file per node, with all telescopes
Node01
running
trigger
confirm/fast clear
event, bunch, node #
data
data

---
CameraReader scheme
 CAMERA 1
 CAMERA 2
 CAMERA 3
 CAMERA 4
Node
Buffer 1
Buffer 2
Buffer 3
Buffer 4
Events
Converter
Data blocs
Merger/Converter
Merge event with same event number and convert them to sash
Monitoring event
Monitoring server
Online analysis
Online calibration
ROOT File
One thread per buffer

---
Online Data Merging
CT2/Camera
- Process running on each farm
  node (camerareader)
- Merge data from all camera
  together an with central
  trigger data
- Relies on bunch/event number
  (sent by central trigger to all
  camera @ trigger confirm)
- Buffers the data during 4 second (receiving time)
- Process the data while the other nodes are receiving data
  (< 1 mn) – Speed issue is critical
- Requires perfect consistency between information coming from each source
data
Node01
Node01
CT3/Camera
Node02
CT4/Camera
data
Node_n
Node01
running

---
DataMerger
Off line data sorting
Intermediate node files
Node01
Final data file(s)
Node02
<2Gb
runxxx_Camera_001.root
runxxx_Camera_002.root
Node03
Node04
time
- Runs offline (during day time) in Nambia
- Relies on the central trigger time to produce a time-ordered sequence of events
runxxx_camera_node01_001.root
runxxx_camera_node02_001.root
runxxx_camera_node03_001.root
runxxx_camera_node04_001.root

---
Problems in event building
- Constant shift in Central GPS:
  - Due to missing antenna or software problemOffset can be large always entire number of seconds (?)
- Freeflying Cameras GPS
- Ghosts events produced by a second trigger generated by noise during the data transfer
  - Not-matching global and local counter
- Incorrect data read from local module
  - Corrupted data, stucked bit
- Need for a complicated software that corrects for these effects based on a probabilistic approach (redonduncy)

---
DAQ for H.E.S.S. II
DAQ for H.E.S.S. II
RunManager
RunManager
Configures runs
Get resources from ResourceHandler
Get status from atmospheric monitoring (to come)
Get OK from SecurityController
Automatic run processing
ResourceHandler
Atmosphere
Monitoring
SubArrayManager
SecurityController
Camera
DataReceiver
[Speaker Notes: Stats?]

---
Partie embarquée - HESS-II
Chassis SLC
Slow control
TCP-IP
BIGD
Pilotage
Interface graphique
(Python / GTK)
Chassis Data
données
ZORA
Node
Chassis Trigger
EMILIE
Chassis Sécurité
Bunny
DB
dbgui
CORBA

---
Extenstions: SAMTEXT
- Interface avec SAM
- Pilotage LeCroy 9210 (Interface GPIB), Alimentations et atténuateur
- Résultats systématiquement sauvés dans la base de données
- Sera installé en Namibie pour une maintenance aisée des tiroirs
Pilotage
Interface graphique
(Python / GTK)
GPIB
Contrôleur
LeCroy 9210
GPIB
Contrôleur
Atténuateur
GPIB
Contrôleur
Alimentations
ALTERA
(accès aux registres)
TCP-IP
Acquisition
(cPCI)
SAM
Box-bus
dbgui
CORBA
DB

---
Conclusion
- Le système d'acquisition de HESS est évolutif et flexible
- Peut accomoder de nombreux systèmes
- Quelques difficultés au démarrage (apprentissage, mais aussi rendre ROOT multitaches)
- L'intégration de HESS-II s'est faite rapidement.
- Volume de données important: 30GB/s sans problèmes avec HESS-II
- Mais certaines améliorations possible, notamment en ce qui concerne la tolérance aux pannes et la réaction à des erreurs
- Les instruments n'ont pas de driver unifiés => Multiplicité de sous systèmes indépendants (tracking, méteo, caméra, ...)