## Slide 1: 12 GeV Hall DVCS DAQ
Alexandre Camsonne
Hall A DVCS collaboration meeting
November 13th 2012

## Slide 2: Outline
Overview
HRS
  Trigger
  Detector stack
  VME crate
DVCS DAQ
  ARS
  Trigger
Timeline

## Slide 3: Detectors
Left arm
S0 (2)
1st FPP chamber(318)
Gas Cerenkov(10)
S2m(32)
Pion rejector 1(34)
Pion rejector 2(34)
Right arm
S0 (2)
1st FPP chamber(318)
Gas Cerenkov(10)
S2m(32)
Preshower(48)
Shower(75)
DVCS
PbF2 calorimeter ( 208 )

## Slide 4: Left HRS possible layout
FPP
FPP
elect
DVCS
elect
LVDS
DVCS
patch
Fastbus
Detector stack

## Slide 5: Left HRS possible layout ?
Trigger
electronics
FPP electronics
2nd level Left HRS platform

## Slide 6: Overview
VDC
Cerenkov
S2m
Pion rejector
HRS
Calorimeter
208 calorimeter channels
S0
FPP

## Slide 7: HRS
VDC
  Switch to MAD amplifier discriminator card going
Trigger
  Main : S2m Cerenkov
  Efficiency : S2m S0, S0 Cerenkov
  Additionnal efficiency triggers : S0 Shower
New :
  Send signals to VME high resolution TDC
  Replacement CAMAC crate by VME, efficiency trigger done with V1495
  Avoid remote delays : go for fixed delays for DVCS and GMp

## Slide 8
Discr
Discr
Or
And
Or
And
And
S0
TS
T3
20
20
Delay 8
8
3
T5=S2.T3.Valid
25 ns
Start trigger
stop
valid
g
Busy
S2
T3
Inhibit calo
Logic module
ROC5
ROC6
ROC18
ROC17
L1A
S2.not busy
RT
880 ns
Analog delay
Calo
TM
330 ns
ROC4
ROC3
ROC19
Fastbus
Fastbus
Fastbus
VME


## Slide 9: Detector stack
Detector | channels | Readout
VDC | 384*4 | Fastbus
S0 | 2 | Fastbus + VME
Gas Cerenkov | 10 | Fastbus+VME
S2m | 16*2 | Fastbus+VME
Pion rejector | 34*2 | Fastbus
FPP |  | Fastbus

## Slide 10: Counting house
Not final setup because of refurbishing will have to test with final network switch configuration
Use switch in Hall A until CH is done

## Slide 11: TEDF space

## Slide 12: TEDF installation
Shelve
Table
Calorimeter
Locker
HV cables
Signal
cables
HV
crate
DAQ
crate

## Slide 13: DVCS DAQ
3 VME64X/VXS crate + trigger = 1 rack
New Intel VME CPU ( 40 MB/s to 100 MB/s )
300 Mb/s max, need check network
208 calorimeters channels : 13 ARS boards
New trigger to be tested

## Slide 14: Man power
Alexandre Camsonne : DVCS DAQ, HRS DAQ / Trigger, Compton
Robert Michaels : HRS DAQ / Trigger , Moller, Raster , BCM , BPM
1 DVCS student ?
1 MIT Postdoc / 1 Graduate student
?

## Slide 15: Rough timeline
Month | Year | Task 1 | Task 2 | Task 3
11 | 2012 | Install VDC AD | Install FPP | Setup / check Lumi
12 | 2013 | Install 1877S | Cable VDC | Cable FPP
1 | 2013 | Install S0 | Run Gas / Cosmics trigger | Cable BCM / BPM / Raster
2 | 2013 | HRS cosmics checkout | Setup EDTM | Timing S2m
3 | 2013 | HRS cosmics / high rate tests | Single arm trigger both HRS | Implement sparsification
4 | 2013 | DVCS electronics install | Install RG213 | (MQT installation ? )
5 | 2013 | DVCS calorimeter install | DVCS cosmics trigger | Setup / check helicity
6 | 2013 | HRS and DVCS calo cosmics | DVCS high rate tests | 
7 | 2013 | DVCS trigger timing |  | 
8 | 2013 | Install Intel CPU | HRS and DVCS calo cosmics | 
9 | 2013 | Install CODA3 TS and TI | Debug | 

## Slide 16: Timeline
Month | Year | Task 1 | Task 2 | Task 3
10 | 2013 | HRS and DVCS calo cosmics | HRS and DVCS calo cosmics | 
11 | 2013 |  | HRS / DVCS high rate tests | 
12 | 2013 |  |  | 
1 | 2014 |  |  | 
2 | 2014 |  |  | 
3 | 2014 | Commissioning beamline | Commissioning HRS | GMp / DVCS
4 | 2014 | GMp / DVCS |  | 
5 | 2014 | GMp / DVCS |  | 
6 | 2014 | Can install DVCS here |  | 
7 | 2014 |  |  | 
8 | 2014 | GMp/DVCS |  | 
9 | 2014 | GMp/DVCS |  | 
10 | 2014 | GMp/DVCS |  | 

## Slide 17: Conclusions
Starting HRS work
Few minor changes to HRS trigger
Mostly same setup as previously
Early testing of calorimeter trigger