## Slide 1: The COMPASS experimental setup
  Stephane Platchkov
  IRFU/SPhN, CEA-Saclay
Requirements, implementation, performances
(with a few physics examples)

## Slide 2: The COMPASS experiment at CERN
LHC
SPS
COMPASS

## Slide 3: CERN accelerators (not to scale)
Compass

## Slide 4: COMPASS – some facts
Located at CERN North Area beam line
  Possible beams: µ+, µ-, p+, p-, e- => Several physics programs
Experiments with muon beam
  Spin structure, Gluon polarization
  Flavor decomposition
  Transversity
  Transverse Momentum-dependent Distributions
  DVCS and HEMP
  Unpolarized SIDIS and TMDs
Experiments with hadron beams
  Pion polarizability
  Diffractive and Central production
  Light meson spectroscopy
  Baryon spectroscopy
  Pion and Kaon polarizabilities
  Drell-Yan studies
COMPASS - I (2002 – 2011)
COMPASS - II (2012 – 2017)

## Slide 5: COMPASS – some facts
Located at CERN North Area beam line
  Possible beams: µ+, µ-, p+, p-, e- => Several physics programs
Experiments with muon beam
  Spin structure
  Polarized target (L & T)
  DVCS
  Long LH2 target
Experiments with hadron beams
  Hadron spectroscopy
  Small LH2 or nuclear targets
  Drell-Yan studies
  Polarized target (T)
COMPASS - I (2002 – 2011)
COMPASS - II (2012 – 2017)
Reconfigurable target region - versatile experimental setup!

## Slide 6: Requirements for a COMPASS detector 1/2
Detect several particles in coincidence:
  Incident and scattered beam particle
  Two or more outgoing charged hadrons
  Neutral particles (photons)
Large angle and momentum acceptance
  Momentum: 1 GeV/c to >50 GeV/c
  Angular acceptance: ± 180 mrad
Exclusivity
  Detect recoil protons : momentum: < 1 GeV/c
Particle identification
  RICH detector: separate p, K, p;
  Hadronic and Electromagnetic calorimeters
  Muon identification

## Slide 7: Requirements for a COMPASS detector 2/2
Tracking
  Good space and/or time resolution
  High counting rate,
  From small to really large size detectors
  Low material budget, cost, etc...
Polarized target
  Large target size for reaching high luminosity
  Oppositely polarized cells
Large data flow capabilities
  Trigger rates: from few to 30 kHz
  More than 250 000 detectors channels

## Slide 8: COMPASS Beams
Muon beam
  Energy: 160 GeV
  Intensity: 2x108/spill
  Polarization: 80%
Hadron beams
  Pions(97%), kaons(2.6%), anti-p(0.6%)
  Energy: 190 GeV
  Intensity: up to 108/spill
Electron beam
  40 GeV, few 103/spill, used for calibration

## Slide 9
COMPASS Beam Line
A very long beam line, to allow for good secondary and tertiary beams
Protons from SPS
Compass
Target

## Slide 10: COMPASS Polarized target
Specifications
  Superconducting solenoid : 2.5 T
    16 trim coils
    Field homogeneity: 10-4
  Dipole filed: 0.5 T
  Temperature: ~50 mK (frozen)
  Materials: NH3, 6LiD
  Dilution factor: ~0.4
Performances
  Polarization: >50%, >90%
  Field reversal: 8h, 24h
Two 60 cm oppositely polarized cells
Largest polarized target in the world

## Slide 11: Polarization build-up
NH3 material
6LiD material
  Build-up time : ~1-2 days
  Relaxation time : 0.05-0.2%/d (2.5T)
1 day
2 days

## Slide 12: The COMPASS setup – Three main parts
50m
Target
region
Large
Angle
Spectrometer
Small
Angle
Spectrometer
SM1
SM2
1 Tm
4 Tm

## Slide 13: The COMPASS setup – Space resolution
10 µ 100µ 200µ 500µ 1 mm
Target
region
Large
Angle
Spectrometer
Small
Angle
Spectrometer
SM1
SM2
  Space resolution is function of the distance to the target

## Slide 14: Large Angle Spectrometer
ECAL1
Drift Tubes
Beam
Opening angle = ±180 mrad
SM1
SDC
Straw chambers
RICH

## Slide 15: Very Small Angle Trackers - Scintillating Fibers
Specifications
  9 stations, 21 coordinates
  0.5, 0.75 and and 1.0 mm fibers
  2668 channels
  8-14 layers per projection
Performances
  Time resolution: 350-400 ps
  Spatial resolution: 130-210 µm
  Efficiency: 97-99%
  High-rate capability
Very good time resolution, high-rate capability

## Slide 16: Very Small Area Trackers - Silicons
Specifications
  5x7 cm2, 1280 and 1024 strips
  5 N-cooled stations
  52 µ and 55 µ pitch
  2 projections per detector
  Designed for high fluencies
  R/O: APV25 chip, 128 ch
Performances
  Time resolution: 1.4 ns
  Spatial resolution: 6 – 11 µm
Very good spatial resolution
preliminary
preliminary

## Slide 17: Very Small Angle Trackers - PixelGEMs
Specifications
  Active size: 100x100 mm2
  Strip: 2 x 512, pitch=400 µ
  Pixel area: 32x32 mm2
  Pixel size: 1 mm2
  APV chip R/O, 128 ch.
Performances
Good space resolution, minimized material along the beam
preliminary
preliminary
preliminary

## Slide 18: Small Area Trackers - GEM detectors
Specifications
  3 GEM stages
  Active area: 31x31 cm2
  Dead area diameter: 5 cm
  Minimal material budget
  11 stations (22 planes)
  Two sets of 768 perpendicular strips
  400 µ pitch X and Y
Specific features
  2-dim read-out
  Very large integration
      APV chip = 128 ch

## Slide 19: Small Angle Trackers - GEM detectors
Performances
  Space resolution: 68 µ
  Time resolution: 12 ns
  Efficiency: > 97%
First GEMs detectors used in a High Energy Experiment

## Slide 20: Small Angle Trackers - Micromegas
Specifications
  Large active area: 40x40 cm2
  3 stations (12 detectors)
  Dead area diameter: 5 cm
  Pitch: 360µ, 420µ
  4 planes per station: X, Y, U, V
Specific features
  High magnetic field (up to 0.2 T)
  High-rate environment
      450 kHz/cm2; 200 kHz/ch
  Large detector
  Custom Front-end chip SFE16
      peaking time: 85 ns
      Leading+Trailing edge
Performances
  Efficiency: > 97%
  Space resolution: ~90 µ
  Time resolution: <10 ns
s = 92 µm

## Slide 21: Micromegas in COMPASS
First Micromegas used in a High Energy Experiment
Detector
40x40 cm2
Electronics

## Slide 22: Large Angle Trackers – Drift Chambers
Specifications
  Sensitive area: 180x127 cm2
  3 stations (8 planes/station)
  Dead area diameter: 30 cm
  Drift cell: 7mm(pitch) x8 mm2
Performances
  Efficiency: > 97%
  Space resolution: 170 µ
Specific features
  Located near high magnetic field
      (up to 0.3 T)
  Operate in a high-rate environment
  Large areas. Very high-rate capability -- up to 700 kHz/ch!
700 kHz

## Slide 23: Electromagnetic calorimeters (x2)
ECAL1
  1500 channels
  Pb0 modules (3 dimensions)
    18-20 X0
  Energy range: 0.2-60 GeV
ECAL2
  2180 Pb0 type modules
  888 “Shashlik” type (Pb/Scint)
    (radiation hardness)
  Energy range: 1-200 GeV
  Detect photons and electrons = maximize RADIATION Length

## Slide 24: ECAL performances
sE = 7.8 MeV
sE = 3.9 MeV
Dt = 1 ns
p0 linearity (±1 MeV)
  Good time resolution, reasonable energy resolution
ECAL1
ECAL2
preliminary
preliminary
preliminary
preliminary

## Slide 25: Hadron calorimeter
Hadron calorimeters (x2)
  HCAL1: 480 channels (20x28)
    Each block: 15x15 cm2
  HCAL2: 216 ch (22x10)
    Each block: 20x20 cm2
.
Fe-Scintillator sandwich (x40)
  Detect hadrons = maximize INTERACTION Length

## Slide 26: COMPASS RICH
Requirements
  Identification range: 5 – 50 GeV/c
  Angular acceptance:
  Photon detectors outside acceptance
Implementation
  C4F10 radiator gas (n=1.0015)
    Needed: controlled purity, constant pressure, temperature.
  Large volume vessel: 80 m3
  Large mirror system: 21 m2, Rc=6.6 m
    Total detection area of 5.6 m2
    VUV domain: 150 – 210 nm
  Two detector technologies
    MWPC/CsI photon detectors
    MAPMTs
5.5 m
3.3 m

## Slide 27: COMPASS RICH
Performances:
  Cherenkov angle: 25 – 54 mrad
  Photons (VUV) per ring (rec): 5 – 60
  Typical efficiency: ~80%
  Typical purity: ≤70%
preliminary

## Slide 28: Dedicated electronics developments
F1-TDC chip – for most detectors
  8ch, 130/65 ps resolution
  22 ns dpr, 160 pins, etc…
ANALOG R/O SFE16 chip for Micromegas
  16 ch, low noise (<1000 e-)
  Peaking time 80 ns, L+T edge
CATCH VME R/O driver module
  9U, 16 inputs, clock dist’on,
  event framing
  Hotlink input, S-link output,
SADC for ECAL and HCAL
  32 ch, 80 kHz sampling rate
  12b, Latency compensation
  0-suppression, hotlink output
Spill buffer
  512 MB SDRAM (S-link to PCI)
Many Front-End cards…etc..

## Slide 29: COMPASS DAQ
Readout requirements
  Total number of channels : 250 000
  Event size : 40 – 45 kB
  Minimal dead time: 3 µs
Rate requirements
  Trigger rates: 5 – 30 kHz
  Data rates: 1 – 10 GB/spill
  Throughput to R/O buffers: 250 MB/s
Online filtering
  Decrease amount of transmitted and stored data
Implementation – main features
  Custom readout-driver modules
  Buffering of bursts
  Pipelined readout
  Network event-building (Gigabit Ethernet)
  Synchronization: TCS (adapted from LHC)
  Dead Time: 15% at 30 kHz
9.6 sec
~42 sec
beam extraction
off spill

## Slide 30: Compass DAQ: Trigger rate vs Event size

## Slide 31
Some specific examples:
DVCS
Hadron spectroscopy
Drell-Yan

## Slide 32: DVCS – COMPASS kinematical coverage
Beams
  100 – 190 GeV
  Polarization: ~80%
  Both m+ and m- beams
x-Q2 region: ≈ 0.01 – 0.1
  Between HERA – Jlab/Hermes
Detect both outgoing photon and recoiling proton

## Slide 34
DVCS : μ p  μ’ p 
New :
2.5m LH2 target
4m TOF CAMERA
ECAL0
ECAL0
CAMERA
μ’

μ
p

## Slide 35: CAMERA (TOF Recoil Proton Detector)
Ring A
Ring B

## Slide 36: DVCS – COMPASS xB regions – SIMULATION
Relative amplitude dramatically changes as a function of x

## Slide 37: DVCS – COMPASS xB regions – REAL DATA
Test runs in 2009 – 40 cm long H2 target
BH
DVCS
Clear signal from DVCS
278 ev.
134 ev.
54 ev.
44 ev.
10 ev.

## Slide 38: Hadron beam: Primakoff and spectroscopy
Si stations
Recoil Proton Detector
Target
LH2/Nuclear
inside

## Slide 39: Primakoff and pion polarizability
Primakoff scattering: on the Coulomb field of the nucleus
Measure exclusivity:
  DE = Ebeam – Eg –Ep
  Beam energy
  Scattered pion energy
  Energy of the recoiling photon

## Slide 40: Some final states (pion beam)
charged
neutrals
charged AND neutrals
p-p  p-p-p+p
p-p  p-p0p0p
p-p  p-p-p+p0p
p-p  p-p-p+hp
h
h’
w
a2

## Slide 41: Hadron beam: Drell-Yan setup
Thick hadron absorber/beam dump
Vertex detector
Beam telescope

## Slide 42: DY test in 2009 : 3 days of data taking
2-cell polyethylene target, hadron absorber
Vertex reconstruction
Mass reconstruction

## Slide 43: A long road ahead
Towards a setup for AFTER – tentative agenda
  Identify the relevant physics processes
  Perform simulations – consider kinematics
  Estimate the magnetic field (Tm)
  Implement the relevant types tracking detectors
  PID detectors (hadrons, neutrals?)
  Consider background processes...
  Go To 2
  Add absorbers, simulations again
  Do not forget about triggers (L1, L2,... ), event rates, throughput, radiation protection, etc...
  Come back here next year....

## Slide 44
Thank you

## Slide 45: Compass acceptances
Production of high-pt hadrons (muon program)
Diffractive dissociation of pions (hadron program)
Negative hadrons
Positive hadrons

## Slide 46: Polarized DY – expected results
2 x 5 months of data taking
6.108 pions/spill
1.1 m NH3 target
Mass: 4<Mmm<9 GeV
Sivers
Boer-Mulders
Pretzelosity
Transversity

## Slide 47: Large Area Trackers – Large Drift Chambers
Specifications
  Large active area: 500x250 cm2
  6 stations (18 double planes)
  Dead area diameter: 50, 100 cm
  Pitch: 4 cm
  Anode-Cathode gap: 1 cm
Performances
  Efficiency: > 93%
  Space resolution: ~500 µ