## Slide 1: Alpine layout simulation
Teddy Todorov
19/11/2012
AUW ITK simulation meeting

## Slide 2
Alpine pixel layout for Letter of Intent comparisons
Letter of Intent baseline pixel layout
4.6 m2 pixel area
8.2 m2 pixel area
Alpine and LoI layouts on equal footing is standalone simulation

## Slide 3: Material assignment on Alpine layout
0.5% X/X0 on barrel stave
0.5% X/X0 on endcap stave
0.5% X/X0 on endcap blocks
1.0% on all modules
All material on staves, staves extend to full eta acceptance
Material on surfaces (planes and cylinders), not in volumes
Track crossing angle amplifies the material

## Slide 4: LoI Pixel detector material assignment
X-Y projection of LoI Pixel barrel + first disk
All modules have 1.0% X/X0
Barrel staves have 0.5% (same as Alpine)
Endcap disks have two parts: front and back
  Both halves have 0.5% X/X0 to account for more complex mechanics and services than on barrel staves
End-Of-Stave cards have 5% X/X0 Over 120 mm length just after the last module
No EOS cards for disks yet
No service material yet

## Slide 5: Material comparison
In the Alpine layout all material is on the stave
In the LoI layout the services material is playing a big role
Alpine
LoI
Current ATLAS
LoI: EOS cards only, no cables, no pipes

## Slide 6: Track fit details
Tracks propagated through all surfaces
On each surface:
  a “SimHit” is recorded
  The track is scattered randomly according to multiple scattering and energy loss Gaussian models
The SimHits are Gaussian smeared according to sensor pitch
  Pitch/4 for pixel and precise strip coordinate
Barrel strip sensors simulated as pixel sensors with very big eta pitch
  To get ~correct resolution
Endcap strip rings make pure R.phi – R measurements
Kalman Filter track fit using all “Hits”
Similar in spirit to a subset of FATRAS

## Slide 7: Very Forward tracking – LoI like

## Slide 8: Very forward tracking – maxi disks
Very complex disk
Modelled with 2% of X/X0 to reflect services/support complexity

## Slide 9: Very-very preliminary resolutions
Non-optimized pixel sizes (bad for Z0)

## Slide 10: Summary
Standalone simulation starts to be useful
  Limited to single track performance
Performance between the Alpine and the LoI layout depends strongly on the service material assumptions in the LoI layout
Very forward tracking looks possible
  Just starting…