## Slide 1: Alpine, very forward, EOS…
Teddy Todorov for the LAPP-ATLAS team,
21/11/2012
AUW ITK modules/ladders meeting

## Slide 2
Alpine pixel layout for Letter of Intent comparisons
Letter of Intent baseline pixel layout
4.6 m2 pixel area
8.2 m2 pixel area
Alpine and LoI layouts on equal footing is standalone simulation

## Slide 3: Material assignment on Alpine layout
0.5% X/X0 on barrel stave
0.5% X/X0 on endcap stave
0.5% X/X0 on endcap blocks
1.0% on all modules
All material on staves, staves extend to full eta acceptance
Material on surfaces (planes and cylinders), not in volumes
Track crossing angle amplifies the material

## Slide 4: LoI Pixel detector material assignment
X-Y projection of LoI Pixel barrel + first disk
All modules have 1.0% X/X0
Barrel staves have 0.5% (same as Alpine)
Endcap disks have two parts: front and back
  Both halves have 0.5% X/X0 to account for more complex mechanics and services than on barrel staves
End-Of-Stave cards have 5% X/X0 Over 120 mm length just after the last module
No EOS cards for disks yet
No service material yet

## Slide 5: Material comparison
In the Alpine layout all material is on the stave
In the LoI layout the services material is playing a big role
Alpine
LoI
Current ATLAS
LoI: EOS cards only, no cables, no pipes

## Slide 6: Single track performance comparisons
Alpine versus LoI
Very similar track parameter resolutions
  As expected from geometry and material
  Even if we look at pixel-only tracks
Don’t have the services material yet
  Except for End-Of-Stave cards
  Will degrade LoI pixel performance a bit, but not Alpine

## Slide 7
All services out of tracking acceptance!
(lines correspond to eta=2.5 from z=-15cm)

## Slide 8: First look at Very Forward tracking – LoI like
Main physics motivation: very forward jet rejection based on primary vertex association

## Slide 9: Very forward tracking – maxi disks
Very complex disk
Modelled with 2% of X/X0 to reflect services/support complexity

## Slide 10: Very-very preliminary resolutions (last Friday)
Non-optimized pixel sizes (bad for Z0)
Looked promising!

## Slide 11: Pt measurement at large eta
Color code:
Black – with EOS
Red – no EOS
Blue – no material at all

## Slide 12: Eta coverage
3.0
2.0
1.0
4.0

## Slide 13: Hit coverage

## Slide 14: Pitch choice
250u pixel eta pitch
50u pixel eta pitch
Go for 50x50 microns on the following plots

## Slide 15: End-Of-Stave problem
EOS material
No EOS
EOS card modelled as 12cm long, stave width, 5% X/X0

## Slide 16
¼ view (half in Z and half in phi

## Slide 17
Pixel package interconnection board
(Name contest still open)
Stave flexes run to board without break at EOS
Board at R>20cm, compatible with opto converters
Strongly reduced number of external connectors

## Slide 18: Transverse impact parameter resolution 5 GeV MIP
Color code:
Black – with EOS
Red – no EOS
Blue – no material at all

## Slide 19: Longitudinal impact parameter resolution 5 GeV MIP
Color code:
Black – with EOS
Red – no EOS
Blue – no material at all

## Slide 20: Pt resolution 5 GeV MIP, constant 2 T field
Color code:
Black – with EOS
Red – no EOS
Blue – no material at all
We must measure Pt to distinguish between low and high momentum for multiple scattering treatment in the track fit

## Slide 21: Very-very preliminary: Very Forward Alpine layout
No track fit yet
Lots of new ideas, need some time to settle down
Main principle: hermetic cylindrical surfaces up to > 3m
Silicon area advantage over disks preserved at large eta

## Slide 22: Summary
Alpine layout up to eta 2.5 engineered in some detail
  Interconnection boards with opto-converters in pixel package
Very forward tracking (up to eta = 4.3 – 4.4) looks promisin on single track level
  Need feedback from physics groups if/how much to pursue this
  Alpine-like layout at large eta in progress