## Slide 1: PP1 developments at LAPP Nicolas Massol, on behalf of the LAPP team ATLAS Upgrade Week CERN, Nov 20th 2012

## Slide 2: PP1 design
Based on a moveable PCB :
patch-panel + cables rerouting + environmental barrier

## Slide 3: PP1 based on a PCB
Type I side
Type II side
AXON hybrid nano-D
Hypertac

## Slide 4
Specifications :
20 Layers
Total thickness : 2,76mm
Top and Bottom layers for LV signals
8 Inner layers for the HV signal
10 Inner layers for DCS differential pairs
Components :
6 Hypertac connectors
40 Axon nano-D connectors
The MAPP (Moveable ATLAS Patch-Panel) Board

## Slide 5
Number of pins :
DCS : 1600
HV : 1920
LV : 320
GND : 228
PCB area : ~1000 cm² (including mechanics)
Electrical part area: ~600 cm²
PCB produced and received, not yet tested
The MAPP Board : routing

## Slide 6
  Electrical tests on the first version:
    HV spark on the 12 channels: around 1.5kV  safety margin not big enough
    Weak point in this design : distance between pins row and metallic shell
    Air gap between male and female inserts is also a weakness
  Modification of the current design:
        Before After
    Wall thickness of the female metallic shell / length of the male metallic shell decreased
    Mechanical tolerance on the insert part removed  tolerance now on the shells
  New order placed for a new harness
The Axon type I harness: new version

## Slide 7: Fake harnesses
Fake type I harnesses manufacturing: 40 per PCB
  Fake cables based on the real prototype harness specs
  Hybrid nanoD connectors made in rapid prototyping
  Real screws + standoffs to study the plug locking and the accessibility

## Slide 8: PP1 region mockup
Transparent box to simulate the tracker volume
  Direct vision on the bundles behaviour during the PP1 closing
  Possibility to pressurize the box to measure the PP1 tightness
All the material available but the full assembly not yet started