## Slide 1: LHC Open Network Project status and site involvement
Ramiro Voicu (Caltech/USLHCNet)
ALICE T1/T2 workshop
Lyon, June 5th, 2013

## Slide 2: Outline
Background
LHCONE Overview
L3VPN service, VRF
Connection recommendations
R&D activities
Summary

## Slide 3: Background: LHCOPN
2004/2005 timeframe the LHC Optical Private Network (LHCOPN) was designed
  Hierarchical MONARC model (late 1990 – early 2000)
    Every T2 associated to a T1[*]
  Evolved from a star to partial mesh
  Dedicated network resources for T0 – T1 and T1 – T1 data movement
  Federated governance (no single administrative body)
  [*] ALICE adopted a different model

## Slide 4: LHCOPN
Edoardo Martelli, CERN

## Slide 5: Background
Transatlantic connectivity workshop in 2010 at CERN
  Moving from hierarchical pre-placement models towards a flatter, peer-to-peer model: greater availability, locality
    Suits ALICE data access model
Tier 0
Tier 1
Tier 2
Tier 2
Tier 2
Tier 1
Tier 2
Tier 2
Tier 2
Tier 0
Tier 1
Tier 2
Tier 2
Tier 2
Tier 1
Tier 2
Tier 2
Tier 2

## Slide 6: LHCONE Introduction
LHCONE was born to address two main issues:
  ensure that the services to the science community maintain their quality and reliability
    “The Network infrastructure is the most reliable service we have”
          Ian Bird – WLCG project leader
  protect existing R&E infrastructures against very large LHC data flows
    accomplished through distinct infrastructure and/or traffic engineering
LHCONE is expected to
  provide some guarantees of performance
    Large data flows across managed bandwidth that would provide better determinism than shared IP networks
    Segregation from competing traffic flows
    Manage capacity as # sites x Max flow/site x # Flows increases
  provide ways for better utilization of resources
    Use all available resources
    Provide Traffic Engineering and flow management capability
    Leverage investments being made in advanced networking

## Slide 7: LHCONE Overview
Open Exchange Points
Distributed exchange point
Single node exchange point

## Slide 8: LHCONE Overview
Current activities split in several areas:
Multipoint connectivity through L3VPN (Production)
Point-to-point dynamic circuits (R&D)
  targeting demonstration this year
Common to both is logical separation of LHC traffic from the General Purpose Network (GPN)
  Avoids interference effects
  Allows trusted connection and firewall bypass
More R&D in SDN/Openflow for LHC traffic
  for tasks which cannot be done with traditional methods

## Slide 9: Routed L3VPN Service, VRF
Based on Virtual Routing and Forwarding (VRF)
BGP peerings between the VRF domains
Currently serving 44 LHC computing sites

## Slide 10: Routed L3VPN Service, VRF, cont.
Current logical connectivity diagram:
Mian Usman, DANTE

## Slide 11: Inter-domain connectivity
Many of the inter-domain peerings are established at Open Lightpath Exchanges
Any R&E Network or End-site can peer with the LHCONE domains at any of the Exchange Points (or directly)

## Slide 12: LHCONE L3VPN for Service Providers
See information on wiki:
  https://twiki.cern.ch/twiki/bin/view/LHCONE/LhcOneVRF
List of BGP communities on the wiki
Implementation recommendations:
  Do not filter by prefix length. Any prefix length must be accepted
  Apply maximum-prefix checks. Ad-hocs for TierXs, 3000 between VRFs
  Do not allow private AS Numbers

## Slide 13: Computing Site Connection HOWTO
Wiki instructions: https://twiki.cern.ch/twiki/bin/view/LHCONE/LhcOneHowToConnect
Any LHC computing site can connect to the LHCONE infrastructure
  Connect to one of the VRF domains
    see Wiki for list of active VRF domains
  directly or at exchange point
A computing site (TierX) needs to have
  public IP addresses
  a public AS Number
  a BGP capable router
LHCONE transports LHC data traffic only
  Announce only LCG IP prefixes
  Traffic must be symmetric, to avoid problems with stateful firewalls

## Slide 14: Connection recommendations
Recommendations to address asymmetric routing:
Define local LAN address ranges that will participate in LHCONE. Advertise these address range prefixes to LHCONE using BGP
Agree to accept all BGP route prefixes advertised by the LHCONE
Ensure that only hosts in your locally defined LHCONE ranges have the ability to forward packets into the LHCONE network
Ensure that the LHCONE paths are preferred over general R&E IP paths
End sites should avoid static configuration of packet filters, BGP prefix lists and policy based routing, where possible.
More details here: https://indico.cern.ch/getFile.py/access?contribId=8&resId=1&materialId=slides&confId=179710
Michael O’Connor, ESnet

## Slide 15: LHCONE Operational Aspects
The Operational Model is broadly based on the LHCOPN experience
Basic principle: A sites experiencing problems contacts its first LHCONE upstream provider
Still in the process of being worked out
Current operational handbook draft: https://twiki.cern.ch/twiki/pub/LHCONE/LhcOneVRF/LHCONE_VRF_Operational_Handbook-v0.5.pptx

## Slide 16: Point-to-point service
PATH TO A DEMONSTRATION SYSTEM

## Slide 17: Dynamic Point-to-Point Service
Point-to-point circuit service complements the L3VPN service and provides predictable performance
  Guaranteed bandwidth between a pair of end-points (VRF domains and/or end-sites)
  No jitter and predictable delay
Several provisioning systems developed by R&E community: OSCARS (ESnet), OpenDRAC (SURFnet), G-Lambda-A (AIST), G-Lambda-K (KDDI), AutoBAHN (GEANT)
Inter-domain: need accepted standard
OGF NSI: The standards Network Services Interface
Connection Service (NSI CS):
  v1 ‘done’ and demonstrated e.g. at GLIF and SC’12
  Currently standardizing v2

## Slide 18: Point-to-Point Service in LHCONE
Intended to support bulk data transfers at high rate
Separation from GPN-style infrastructure to avoid interferences between flows
Conducted 2 workshops:
  1st LHCONE P2P workshop was held in December 2012
    https://indico.cern.ch/conferenceDisplay.py?confId=215393
  2nd workshop held May 2013 in Geneva
    https://indico.cern.ch/conferenceDisplay.py?confId=241490
(Some) Challenges:
  multi-domain system
  edge connectivity – to and within end-sites
  how to use the system from LHC experiments’ perspective
    e.g. ANSE project in the US
  manage expectations

## Slide 19: Point-to-point Demo/Testbed
Demo proposed and led by Inder Monga (ESnet)
  Choose a few interested sites
  Build static mesh of P2P circuits with small but permanent bandwidth
  Use NSI 2.0 mechanisms to
    Dynamically increase and reduce bandwidth
    Based on Job placement or transfer queue
    Based or dynamic allocation of resources
Define adequate metrics!
  for meaningful comparison with GPN or/and VRF
Time scale: TDB (“this year”)
Participation: TDB (“any site/domain interested”)
More discussion at the next LHCONE/LHCOPN meeting in Paris (June 2013)

## Slide 20: SDN/Openflow
OTHER R&D ACTIVITIES

## Slide 21: Meeting on SDN in LHCONE, May 3rd, 2013
Discussed the potential use case: SDN/Openflow could enable solutions to problems where no commercial solution exists
Identify possible issues/problems Openflow could solve, for which no other solution currently exists?
Multitude of transatlantic circuits makes flow management difficult
  Impacts the LHCONE VRF, but also the GPN
  No satisfactory commercial solution has been found at layers 1-3
  Investigate the use of Openflow to address the problem at Layer2
  Caltech has a DoE funded project running, developing multipath switching capability (OLiMPS)
  Will examine this for use in LHCONE
Second use case: ATLAS is experimenting with OpenStack at several sites.
  Openflow/SDN is the natural technology in the network. Could be used to bridge the data centers.

## Slide 22: Summary
The LHCONE is currently operating a L3VPN (aka VRF) service
  44 LHC computing sites connected
The Point-to-point circuit service will be first shown in a demonstration
  Based on NSI
  Interested Networks and Sites are welcome to join
Ideas in the SDN/Openflow space are currently investigated
  Useful to LHCONE participating networks?
  Any direct benefit to the LHC computing model?

## Slide 23: Information exchange
Weekly audio conference, 14.30 UTC, alternating every second week:
  architecture discussion
  operations
mailing lists:
  lhcone-operations@cern.ch
  lhcone-architecture@cern.ch
LHCONE wiki: https://twiki.cern.ch/twiki/bin/view/LHCONE/WebHome
Next LHCONE/LHCOPN meeting: Paris, June 17/18, 2013
  http://indico.cern.ch/conferenceDisplay.py?confId=236955

## Slide 24
More details:
http://lhcone.net