## Slide 1: Network Monitoring and Troubleshooting with perfSONAR MDM
Domenico Vicinanza
DANTE, Cambridge UK
perfSONAR Training event for French Tier2 Sites
Paris, 4 April 2013

## Slide 2: Outline
What is perfSONAR?
perfSONAR outside Europe
What does perfSONAR measure and how?
Interfaces:
  Web UI
  Mobile support (work in progress)
  Weather maps

## Slide 3: perfSONAR in a nutshell
Multi-domain distributed monitoring
International collaboration
  GÉANT, Internet2, ESnet, and RNP
Flexibility, extensibility, open, and decentralization.
Currently
  perfSONAR MDM within GÉANT: http://perfsonar.geant.net
  perfSONAR PS within I2/ESnet: http://psps.perfsonar.net/
Open OGF protocol to exchange data
Web-service based

## Slide 4: How does perfSONAR work?
Measurement points (MPs) across the networks.
Small server (or virtual server) connected to a network interface
MP runs the perfSONAR software to measure the following metrics:
  Available Bandwidth
  One Way Delay / Jitter (One Way Delay variation)
  Route Tracing
PerfSONAR MDM web interface
  Inspect measurements between any two MPs
  Request a variety of ad hoc measurements.

## Slide 5: How does perfSONAR work?
perfSONAR MP
perfSONAR MP
  Available Bandwidth
  One Way Delay
  Jitter
  IP Route Tracing
Web UI

## Slide 6: A new perfSONAR MDM: Compatible, open, interoperable
Actively working with the user community
  direct user feedback
  perfSONAR User Panel
Simplifying installation procedure
  RPMs and DEB packages available
  Virtual Machines images available
    ftp://ftp.uni-ruse.bg/perfsonar-vm/
  Live distribution on a USB stick
Revised documentation (lightweight and modular)
Interoperable with perfSONAR-PS

## Slide 7: interoperability with perfSONAR PS (cont.)
Interoperable core components
perfSONAR user interface is able to interact with either perfSONAR MDM and PS archives
  Retrieving and displaying measurements from any LHCONE MP

## Slide 8: perfSONAR MDM deployment in Asia/Pacific
Active collaboration with TEIN3 NOC
3 Measurement Points:
  Singapore
  Hong Kong
  Beijing
Already available in the current perfSONAR MDM UI

## Slide 9: Interoperability with US deployments (ESnet/I2)
37 measurement points in the GÉANT service area
8 measurement points in ESnet
9 measurement points in Internet2
Measurements between perfSONAR MDM and PS from the same interface
Interoperability with perfSONAR-PS
Interest from perfSONAR-PS community in using our web UI
GEANT
ESnet
Internet2

## Slide 10: What does perfSONAR measure and how?

## Slide 11: Link utilisation, input errors, output drops (RRD-MA)
Purpose:
  Monitor link utilisation, input errors, packet drops
  Provide access to historical measurements
Strategy:
  Query router interfaces statistics using SNMP
  Store data into RRD files
    made accessible through web-service

## Slide 12: Link Utilisation User Interface

## Slide 13: OWD, jitter, packet loss, traceroute (HADES/OWAMP)
Purpose:
  Monitor OWD, jitter, packet loss, traceroute variations
    Regularly scheduled
    On demand (to be implemented)
  Provide access to historical measurements
Strategy:
  Sending 9 packets/minute between MPs (HADES)
  Sending 10 packets/second between MPs (OWAMP)
    Measure OWD, jitter, packet loss and tracking IP route
  Store data into archives
    made accessible through web-service

## Slide 14: Web User Interface – OWD, jitter packet loss

## Slide 15: Example of packet loss: from regularly scheduled measurements
Look at here for packet loss

## Slide 16: 1-way delay on-demand (OWAMP)
Look at here for 1-way delay

## Slide 17: Web User Interface – route comparison
Simple route comparison

## Slide 18: Achievable bandwidth (BWCTL)
Purpose:
  Measure the achievable bandwidth between two MPs
    Regularly scheduled and
    on demand (only for NREN NOC/PERT engineers)
  Provide access to historical measurements
Strategy:
  Run bandwidth test between MPs using a web-service interface to BWCTL
  Display data with graph and store into perfSONAR SQL-MA archive
    made accessible through web-service

## Slide 19: Accessing Historical Bandwidth Measurements
Each dot is a measurement.
Clicking on the dot a window displays the details

## Slide 20: …and getting the results in two clicks from the web interface
Textual output
Graph

## Slide 21: Support for mobile devices

## Slide 22: iPhone App (currently being developed)

## Slide 23: Native smartphone integration

## Slide 24: Example: Query One-Way Delay
Select end points and time
Timeframe selected

## Slide 25: The result

## Slide 26: Zoom in/out

## Slide 27: Detailed inspection

## Slide 28: New developments: Integration of the new weather map

## Slide 29: What’s new about the weathermap
Weather map reading live perfSONAR MDM data
Customisable coloured map
  19 metrics implemented
    The actual availability depends on what it is deployed on each site
  Colour-coded according to the metric chosen
Wide variety of metrics to choose, including
  OWD
  Jitter
  Packet Loss
  Bandwidth
  Link Utilisation / Input errors / Discarded packets

## Slide 30: What’s new about the weathermap (cont.)
Interoperability:
  Able to read OWAMP data
  4 OWAMP metrics available at the moment (more to come)
  Tested within the GÉANT/I2/ESnet collaboration framework DICE

## Slide 31: New weather map integration 19 perfSONAR parameters available

## Slide 32: Weather map examples (Packet loss)

## Slide 33: Weather map examples (One-way delay)

## Slide 34: Another example: access to interface statistics

## Slide 35: Another example: Interface input errors

## Slide 36: Example: Selecting one-way delay metric and clilcking on a link

## Slide 37: It is possible to select an area to magnify for further inspection

## Slide 38: The OWD results after having magnified the area

## Slide 39: Site-specific star display shown when clicking on each site

## Slide 40: Interoperability with perfSONAR-PS

## Slide 41: Four OWAMP metrics implemented up to now

## Slide 42: An example about OWAMP data retrieved by the interface

## Slide 43: Details of the interoperability: perfSONAR MDM and PS connected
GÉANT Node with MDM
I2 Node with PS

## Slide 44: Work in progress: The new weather-map for LHC (based on Open Street Map)

## Slide 45: Several metrics to choose

## Slide 46: Graph
Notes: Clicking on any link a graph is displayed showing the data from the perfSONAR archives

## Slide 47: New developments. A proof of concept: VRF Monitoring with perfSONAR MDM

## Slide 48: VRF Monitoring with perfSONAR MDM
VRF monitoring activity:
  Both passive:
    Monitoring VRF interfaces, link utilisation and errors/drops within the L3 VPN
  And active
    Bandwidth measurements
    One Way Delay
    Jitter
    Packet Loss

## Slide 49: perfSONAR VRF monitoring

## Slide 50: LHCONE VRF monitoring
Three NRENs volunteered to start a first perfSONAR MDM deployment within the LHCONE L3VPN (VRF)
  DFN
  GARR
  RENATER
Each NREN deployed a perfSONAR MDM server within LHCONE VRF
DANTE/GÉANT was running:
  Central monitoring based on NAGIOS
  Service desk (run by the Multi-Domain Service Desk)
  Central archives
  Central scheduling
  perfSONAR web UI server
  perfSONAR weathermap server

## Slide 51: Status of the VRF monitoring
GARR, DFN, RENATER deployed three servers within LHCONE VRF
A perfSONAR dedicated web UI has been deployed for LHCONE
Nagios monitoring is in place
Service desk function is in place
More NRENs to come.
Please feel free to contact us to be added to the infrastructure or for additional info
  Open to MDM and PS sites
  On-demand capabilities only available with perfSONAR MDM
  You can use a pre-installed VM image to be immediately onboard:
    ftp://ftp.uni-ruse.bg/perfsonar-vm/

## Slide 52: NAGIOS monitoring in place for LHCONE VRF MPs

## Slide 53: First screenshot of the LHCONE VRF monitoring

## Slide 54: First results from LHCONE VRF monitoring web UI

## Slide 55: perfSONAR MDM website: http://perfsonar.geant.net
Goals:
Single point of access for perfSONAR
Contact points, FAQs, resources & downloads, and support
Host news and success stories from Users

## Slide 56: perfSONAR Twitter
Weekly tweets
Messages re-tweeted by other sister networks and organisations
Growing community of followers around the world
@perfSONARMDM

## Slide 57: perfSONAR MDM. Be part of it.
Follow perfSONAR at:
http://twitter.com/#!/perfSONARMDM
Website: http://perfsonar.geant.net
Twitter: @perfSONARMDM
Info: domenico.vicinanza@dante.net