## Slide 1: FD relative displacement measurements
A.Jeremie
ATF2 GM System team:
K.Artoos, C.Charrondière, A.Jeremie, J.Pfingstner, D.Schulte, R.Tomas-Garcia
B.Bolzon (past experience)

## Slide 2
FD:Doublet Final
Mesure de taille de faisceau: Shintake

## Slide 3
ATF2 au Japon
Objectifs de ATF2:
Faisceau de 37nm de rayon au point focal de façon stable et reproductible
Trajectoire stable (D<2nm) et feedback intra-train comme à l’ILC
Test grandeur nature

## Slide 6
QD0FF
QF19X
QD18X
QD16X
QF13X
QF4X
QD5X
QF11X
QD12X
QF1X
QD2X
QF3X
QF15X
QD14X
DAQ

## Slide 7: Histoires de câbles…
Trouver le cheminement idéal pour longueur de câble
Il faudrait inventer des câbles qui ne font pas de nœuds!
Combien de mètres? 605 m
Ouf!

## Slide 8: Les joies de l’installation!
Alim capricieuse avec faux contact!
Protection en Pb installée 5 minutes avant démarrage du faisceau et fermeture d’accès!
Petit coin « cosy » pour l’acquisition

## Slide 9: Mouvement relatif au FD

## Slide 10
Sol
Shintake monitor
Derniers aimants de focalisation
Faisceau
Interference
fringes
Aimants situés en amont
Mouvement relatif entre l’interféromètre et les derniers aimants focalisants
4m
Bonne cohérence du mouvement du sol: mesurée sur site
Premier objectif: obtenir un faisceau de 37nm dans l’axe vertical
  Shintake monitor: mesure de la taille du faisceau (interféromètre)
  Mouvement relatif entre Shintake monitor et derniers aimants: 6nm dans l’axe vertical au-dessus de 0,1Hz (gamme de fréquence plus basse et tolérances moins sévères que CLIC)
Supports rigides séparés
Application au projet ATF2 (Accelerator Test Facility 2)
Soutenance B.Bolzon

## Slide 11
Ajouter ici la figure de tauchi sur les tolérances
For QD0 at ATF2: 7 nm tolerance
For QF1 at ATF2: 20 nm tolerance

## Slide 12: Why make new measurements? (already done by Benoit Bolzon in 2008)
Shintake monitor has more components and is in operation
QF1FF has been replaced by a heavier magnet with better field quality and larger radius
2008
2008
2013
2013
QD0
QF1

## Slide 13: Set-up
After installation of 14 Guralp 6T sensors all along ATF2 ext and FF line in May 2013, the last 2 sensors were moved to the FD section (QD0, QF1 and Tabletop of Shintake Monitor) for relative displacement measurements => Comparison with measurements done by Benoit Bolzon in 2008.
Guralp 6T: 0,5Hz-100Hz, two directions connected (vertical and horizontal can be placed parallel or perpendicular to beam direction); sensors similar to the ones used in 2008
FFT parameters:
Window: Hanning
Overlap: 66.67%
Averaging: 51 averages
Measurement : 20 minutes
Relevant information is the relative displacement
Natural Ground motion is high at ATF2 (~200nm, and ~100nm peaks when people inside)
Measurements done simultaneously on two sensors and no one inside ATF2.

## Slide 14
Problématique: Mouvement du sol composé de bruit aléatoire
Traitement des résultats
Optimisation des paramètres temporels pour traiter ce bruit
Capteurs de vibration et instrumentation
Passage dans le domaine fréquentiel
Intégration dans une gamme de fréquence
Puissance moyenne du bruit à une fréquence: Calcul de la Densité Spectrale de Puissance (DSP)
  Niveau de bruit moyen dans une gamme de fréquence: Calcul du Root Mean Square (RMS) intégré
4Hz
50nm
Soutenance B.Bolzon

## Slide 15
Nous cherchons donc à avoir des composants (ici, les aimants de focalisation finale QD0 et QF1) dans la ligne de faisceau avec la première résonnance à une fréquence la plus élevée possible.

## Slide 16: QD0 relative to ground
Transfer Function flat below the resonance
Vertical resonance at 68 Hz
Horizontal resonance at 18 Hz
Vertical Relative displacement at 1Hz is 4 nm
2008
68 Hz
18 Hz
4 nm
28 nm
! Benoit used green for « vertical »

## Slide 17: Shintake Monitor relative to ground
Transfer Function flat below the resonance
Vertical resonance at 50 Hz
Horizontal resonance at 50 Hz
Vertical Relative displacement at 1Hz is 6.8 nm
2008
50 Hz
6.8 nm

## Slide 18: QF1 relative to ground
Coupling between vertical and horiz. vibrations
Vertical resonance at 31 Hz
Horizontal resonance at 8 Hz
Vertical Relative displacement at 1Hz is 21 nm
2008
31 Hz
8 Hz
21 nm
290 nm

## Slide 19: Displacement relative to ground
2013 (2008) | Shintake Monitor | QD0 | QF1
Main resonance (vertical) | 50 Hz (50 Hz) | 68 Hz (66 Hz) | 31 Hz (66 Hz)
Vertical displacement | 6,8 nm (4 nm) | 4 nm (3 nm) | 21 nm (4 nm)
Main resonance (perpendicular) |  |  | 15 Hz (21 Hz)
Displacement perpendicular to the beam | Not done | Not possible (hole on top QD0) | 100 nm (30 nm)
Main resonance (parallel) | 50 Hz (50 Hz) | 18Hz (17 Hz) | 8 Hz (19 Hz)
Displacement Parallel to the beam | 13 nm (11 nm) | 28 nm (25 nm) | 290 nm (21 nm)

## Slide 20: QD0 relative to Shintake Monitor in vertical direction (Transfer Function and Relative displacement)
68 Hz
4.8 nm
Transfer Function flat below the resonance
Vertical resonance at 68 Hz
Horizontal resonance at 20 Hz
Vertical Relative displacement at 1Hz is 4.8 nm

## Slide 21: QF1 relative to Shintake Monitor in vertical direction (Transfer Function and Relative displacement)
Transfer Function not flat below the resonance
Vertical resonance at 31 Hz
Horizontal resonance at 8 Hz
Vertical Relative displacement at 1Hz is 30 nm
31 Hz
30 nm

## Slide 22: With ground motion, relative motion at 1 Hz of Shintake to [QD0; QF1] :
2008 by Benoit BOLZON | Tolerance | Measurement (between QD0) | Measurement (between QF1)
Vertical | 7 nm (for QD0) 20 nm (for QF1) | 4.8 nm | 6.3 nm
Perpendicular to the beam | ~ 500 nm | 30.7 nm | 30.6 nm
Parallel to the beam | ~ 10,000 nm | 36.5 nm | 27.1 nm
2013 by Andrea JEREMIE (same analysis) | Tolerance | Measurement (between QD0) | Measurement (between new QF1)
Vertical | 7 nm (for QD0) 20 nm (for QF1) | 4.8 nm | 30 nm
Parallel to the beam | ~ 10,000 nm | 25 nm | 290 nm
Outside tolerance for 2% effect on beam!

## Slide 23: Conclusion
En attente de résultats de détection du mouvement du sol avec les 14 capteurs
Trouver un meilleur QF1 (mêmes caractéristiques magnétiques, mais moins lourd)
Nouvelle campagne de mesures (?) avec une nouvelle instrumentation installée au IP (collaboration LAL-LAPP/Laurent Journet)