## Slide 1
ESS
Mats Lindroos on behalf of the ESS
Milano, LASA, 12 March 2014

## Slide 2: A European research center

## Slide 3
Cs
Zr
Mn
S
O
C
Li
H
X-rays
neutrons
Light and neutrons

## Slide 4: Engineering materials
Source: PSI, CEMNET workshop 2007
Non-destructive analysis of a steel armed concrete block with neutron imaging and X-ray tomography.

## Slide 5: Neutrons and x-rays are complementary - neutrons…
..see inside materials
..see light atoms
..see isotopes
..see atoms move
..see magnetic atoms
Courtesy of Ian S. Anderson
Notes: Brief description:
Neutron scatter from the nucleus and not the electrons -> penetrating, see light atoms, and magnetic structures.
Top clockwise:
Neutron Radiograph (from Munich) of an operating BMW engine
X-rays reveal the protein crystal structure – neutrons reveal the positions of the H atoms which are key to the catalytic activity
Isotope contrast (H/D in this case) allows specific strands to be picked out in this complex polymer
Neutrons have mass similar to atoms – and can measure dynamics easily. This is a CH4 electrolyte – the H is transferred via a rotation and cross over mechanism – revealed by neutrons
Neutrons have a magnetic moment. Most magnetic structures have been determined with neutrons. Can also be applied to magnetic dynamics e.g. Spin waves – important in studies of high Tc materials.

## Slide 6: ICNS talk: Predicting and preventing failure Prof. Phil Withers, Manchester University

## Slide 7
Berkeley 37-inch cyclotron
350 mCi Ra-Be source
Chadwick
1930
1970
1980
1990
2000
2010
2020
105
1010
1015
1020
1
ISIS
Pulsed Sources
ZINP-P
ZINP-P/
KENS
WNR
IPNS
ILL
X-10
CP-2
Steady State Sources
HFBR
HFIR
NRU
MTR
NRX
CP-1
1940
1950
1960
Effective thermal neutron flux n/cm2-s
(Updated from Neutron Scattering, K. Skold and D. L. Price, eds., Academic Press, 1986)
FRM-II
SINQ
SNS
ESS
ESS - Bridging the neutron gap
J-PARC
Notes: Many of the reactor based neutron sources are being phased out = decline in the availability of neutrons = decline in competence and competitiveness
The vast majority of users will profit from a pulsed structure
A large fraction of users are fully satisfied by a long pulse source
Existing short pulse sources (ISIS, JPARC and SNS) can supply the present and imminent future need of short pulse users
Long pulse for physics flexibility (cold and thermal neutrons available)
++. Keep competency in communities – countries balance in science knowledge

## Slide 8: ESS is a long pulse source

## Slide 9
17 nations committed to build ESS
Cash contributions
from Sweden, Denmark and Norway
50% of construction and 15-20% of operations costs
In-kind contributions
from the other 14 nations
Construction cost: 1843 M€
Operation cost: 140 M€
Decommissioning cost: 177 M€
ESS AB 2014, ca 250 personer, 32 nationaliteter

## Slide 10: Helicopter view of ESS

## Slide 11: Road to realizing the world’s leading facility for research using neutrons
2014
Construction work starts on the site
2009
Decision: ESS will be built in Lund
2025
ESS construction complete
2003
First European design effort of ESS completed
2012
ESS Design Update phase complete
2019
First neutrons on instruments
2023
ESS starts
user program

## Slide 12: Commissioning and operations
Initial User Ops
Criteria for start of Initial Operations: Deliver a measurable number of moderated neutrons to an instrument.
TDR Performance Goals Strategy
Initially keep radioactivity and doses low to allow hands on maintenance.
Ramp up power quickly to find limitations and increase reliability before user operations start.

## Slide 13: Collaborative projects
ESS is an emerging research laboratory with (still) very limited capacity in-house
Two possibilities:
  Limit the scope of the project so that it can be done with in-house resources
  Work in a collaboration where the scope of the project can be set by the total capacity (distributed) of the partners
The accelerator part of the project well suited for this as this community has a strong tradition of open collaboration
To keep cost down and to optimize schedule this requires that investments in required infrastructure is done at the partner with best capacity to deliver
13
Notes: User driven innovation – external actor to be collective ownership

## Slide 14: ESS accelerator
Key parameters:
    -2.86 ms pulses
    -2 GeV
    -62.5 mA
    -14 Hz
    -Protons (H+)
    -Low losses
    -Attention is paid to cryoplant turn down capabilities to minimize use of electrical heaters at low temperatures and proper cryogenic design techniques to minimize static heat leaks
    -Flexible design for
    future upgrades
Design Drivers:
High Average Beam Power
5 MW
High Peak Beam Power
125 MW
High Availability
> 95%

## Slide 15: What is 5 MegaWatts?
At 5 MegaWatts,
  one beam pulse
    has the same energy as a 16 lb (7.2kg) shot traveling at
      1100 km/hour
      Mach 0.93
    Has the same energy as a 1000 kg car traveling at 96 km/hour
    Happens 14 x per second
  You boil 1000 kg of ice in 83 seconds
    A ton of tea!!!

## Slide 16: ESS Linac
 | Energy (MeV) | No. of Modules | No. of Cavities | βg | Temp (K) | Cryo Length (m)
Source | 0.075 | 1 | 0 | – | ~300 | –
LEBT | 0.075 | – | 0 | – | ~300 | –
RFQ | 3.6 | 1 | 1 | – | ~300 | –
MEBT | 3.6 | – | 3 | – | ~300 | –
DTL | 90 | 5 | 5 | – | ~300 | –
Spoke | 220 | 13 | 2 (2S) × 13 | 0.5 βopt | ~2 | 4.14
Medium β | 570 | 9 | 4 (6C) × 9 | 0.67 | ~2 | 8.28
High β | 2000 | 21 | 4 (5C) × 21 | 0.86 | ~2 | 8.28
HEBT | 2000 | – | 0 | – | ~300 | –
Spokes
Medium β
High β
DTL
MEBT
RFQ
LEBT
Source
HEBT & Contingency
Target
2.4 m
4.5 m
3.6 m
40 m
54 m
75 m
174 m
75 keV
3.6 MeV
90 MeV
220 MeV
570 MeV
2000 MeV
352.21 MHz
704.42 MHz

## Slide 17
Sebastien Bousson
Pierre Bosland
Santo Gammino
Søren Pape Møller
Roger Ruber
Ibon Bustinduy
CERN
The National Center for Nuclear Research, Swierk
Anders J Johansson
Prototyping the ESS accelerator
Roger Barlow

## Slide 18: Organization and Work package leaders
Division and project aligned at high level
  “WP as a group” would make for too big fragmentation
  Four WPs have external leaders
Weekly or bi-weekly meetings at ESS Accelerator Division
  Management board of project and division
  WP leaders
  Lead engineers
  Safety
Regular meetings for ACCSYS project
  Technical board (all WP leaders and reps of labs/uni. with contract) as governance and CCB on project level (6 meetings per year)
  Collaboration board with reps of director of of labs/uni. with contracts as oversight committee
  Audits yearly of every WP
  Reviews (Conceptual, design, ready to build) as required mostly co-organized with audits
Lead engineers: Aurelien Ponton, Stephen Molloy, Tom Shea

## Slide 19: Very high level Schedule
2010
14
11
12
13
15
19
16
17
18
20
21
22
23
ESS ADU starts
CM prototypes launched
First SC cavity ordered
Ellip CM productionlaunched
Early access to tunnel
NC linac ready
SC linac 570 MeV ready
First protons to target
Early access cryo and test buildings
1370 MeV protons available
2 GeV protons available
NC and FE IK contracts
Spoke CM prototype available
Redesign approved
Prototype IOT tubes delivered
Injector test at Saclay
Decision IOT or klystrons
Cryoplant ready
Conceptual Design
SC RF
NC linac
RF
Cryogenics
Services, installation and com.
Decision on
Scope
Klystrons and IOTs ordered
RF for medium beta ready
RF for High beta ready
Acc cryoplant ordered
Cryo dist. line ordered

## Slide 20: The target station design is detailed in the Technical Design Report
Helium-cooled rotating tungsten target
Nearly 5 MW of heat carried away by cooling systems
Entombed in 5 m of steel
Critical components become highly activated, requiring remote handling for servicing
ESS Technical Design Report, ESS-2013-001, April 22, 2013, available at http://eval.esss.lu.se/cgi-bin/public/DocDB/ShowDocument?docid=274 .
Source: KIT

## Slide 21: High beam power leads to an innovative design
Rotating tungsten target
  2.5 m diameter
  33 sectors
  Suspended on a 6 m shaft
  Total mass: 17 tonnes
  Rotational speed = 0.42 Hz
  Estimated lifetime = 5 years
Helium coolant
  3 kg/s flow rate
  4 bar inlet, 1 bar ∆P
  20°C inlet, 200°C ∆T
Source: KIT

## Slide 22: Liquid hydrogen moderators deliver cold neutrons to instruments
Liquid para-hydrogen at 20 K carries away 20 kW of deposited heat
Moderators surrounded by beryllium reflector provides peak neutronic performance
Moderator-reflector plug weighs 24 tonnes
Estimated lifetime = 1 year
moderators
inner Be reflector
outer SS reflector
Moderator- Reflector Plug

## Slide 23: ESS Reference suite of instruments

## Slide 24
ESS In-kind contributions potential
Target station
€ 154M
Accelerator
€ 510M
NSS/Instruments
€ 350M
In-kind
Cash
Total construction cost: € 1,84 billion

## Slide 25: Fundamental physics at ESS
The ESS Scientific and Technical Advisory Panel (STAP) on fundamental physics is charged to evaluate the scientific opportunities at the ESS for experiments that address questions in nuclear, particle, and astrophysics, as well as those that probe the character of the fundamental symmetries of nature and search for physics beyond the Standard Model. The STAP reports to the ESS Scientific Advisory Committee (SAC).
Last report “there are extraordinary opportunities for a class of fundamental neutron physics experiments that require the highest possible integrated neutron flux. Particularly notable among these is the proposed search for neutron-antineutron oscillations”
In addition to the neutron measurements relevant for fundamental physics possible at ESS the construction of a proton high intensity frontier accelerator also open possibilities for many other experiments such as neutrino oscillation measurements. The STAP recognized that this is beyond the competence of this committee to give recommendations.
ESS looking forward to relevant bodies in particle physics to study the case for ESSnuSB and make recommendations
25
Notes: User driven innovation – external actor to be collective ownership

## Slide 26: A sustainable research facility
Renewable
Carbondioxide: - 120 000 ton/year
Recyclable
Carbondioxide:
- 15 000 ton/year
Responsible
Carbondioxide:
- 30 000 ton/year
Notes: Högsta temp: 118 GWH
All värme: 215 GWh = 10 000 villor

## Slide 27
1.8 Billion Euros:
Biggest investment in Science ever in Scandinavia?
In modern time, definitely YES!
“With better measurements of the stars positions and movements I can make much better horoscopes for you, your majesty!”
However, Tycho Brahe’s Stjärneborg costed the Danish king 1% of the state budget in 1580.
Notes: 1% would be 1.7 Billion Dollars in 2011

## Slide 28
ESS will be at the proton high intensity frontier!
Welcome!

## Slide 29: Short pulse neutron sources-SNS
SNS, SC LINAC/Storage ring, 2007, 1.4 MW, 1 GeV, 26 mA in linac, 627 ns long pulse, 60 Hz
Examples of challenges: Better understand stripping reaction in linac, accumulation in storage ring

## Slide 30: Short pulse sources-LANCSE
LANCSE, NC LINAC /Storage ring, 1972, 100 kW, 800 MeV, 17 mA in linac, 600 ns, 20 Hz
Examples: Combined H- and H+ acceleration

## Slide 31
Accelerated intensity at 800 MeV:
2.5x1013 ppp - 3.75x1013 ppp
(200 µA) (300 µA)
Neutron scattering facility
Two target stations
Muon facility
Examples of challenges: Ceramic vacuum chambers, high space charge synchrotron