## Slide 1: The Alpha Magnetic Spectrometer on the International Space Station
S.Rosier-Lees
LAPP-CNRS-IN2P3-Université de Savoie
Grands Instruments - IAP 2nd April 2014

## Slide 2
USA
MIT - CAMBRIDGE
NASA GODDARD SPACE FLIGHT CENTER
NASA JOHNSON SPACE CENTER
UNIV. OF HAWAII
UNIV. OF MARYLAND - DEPT OF PHYSICS
YALE UNIVERSITY - NEW HAVEN
MEXICO
UNAM
FINLAND
UNIV. OF TURKU
FRANCE
LUPM MONTPELLIER
LAPP ANNECY
LPSC GRENOBLE
GERMANY
RWTH-I.
KIT - KARLSRUHE
ITALY
ASI
IROE FLORENCE
INFN & UNIV. OF BOLOGNA
INFN & UNIV. OF MILANO-BICOCCA
INFN & UNIV. OF PERUGIA
INFN & UNIV. OF PISA
INFN & UNIV. OF ROMA
INFN & UNIV. OF TRENTO
NETHERLANDS
ESA-ESTEC
NIKHEF
RUSSIA
ITEP
KURCHATOV INST.
SPAIN
CIEMAT - MADRID
I.A.C. CANARIAS.
SWITZERLAND
ETH-ZURICH
UNIV. OF GENEVA
CALT (Beijing)
IEE (Beijing)
IHEP (Beijing)
NLAA (Beijing)
SJTU (Shanghai)
SEU (Nanjing)
SYSU (Guangzhou)
SDU (Jinan)
KOREA
EWHA
KYUNGPOOK NAT.UNIV.
PORTUGAL
LAB. OF INSTRUM. LISBON
ACAD. SINICA (Taipei)
CSIST (Taipei)
NCU (Chung Li)
TAIWAN
TURKEY
METU, ANKARA
AMS : an International Collaboration
15 Countries, 44 Institutes and 600 Physicists
Notes: 2
2

## Slide 3
TRD
TOF
Tracker
TOF
RICH
ECAL
1
2
7-8
3-4
9
5-6
TRD
Identify e+, e-
Silicon Tracker
Z, P
3D imaging ECAL
E of e+, e-, γ
RICH
Z, E
TOF
Z, E
Particles and nuclei are identified by their charge (Z) and energy (E ~ P)
Z, P are measured independently from Tracker, RICH, TOF and ECAL
Magnet
±Z
5m x 4m x 3m 7.5 tons
AMS: A TeV precision, multipurpose spectrometer in space
6
Notes: 3
3
3

## Slide 4: Extensively tested before the launch
For each subdetector : Engineering Model (EM) and the Flight Model(FM)
EM : 2001-2005
  (qualification tests and Test beam 2002-2004)
FM :
  2006->2008 Ecal Standalone (Test beam 2007 => Calor 2008)
  2008-2009 :AMS Assembly
ESA, April, 2010, ESTEC, Noordwijk
Thermal Vacuum Tests,330 hours
Test Beam(e+,e--,Protons@400 GeV, pions)
CERN, 8-20 August 2010,
KSC , cosmic rays
NASA, Cape Canaveral,
30 August 2010 – March 2011

## Slide 5: Outline
Introduction
Nuclei flux measurements (LPSC et al, 2 postdoc: CNRS,Enigmass, 2 Phd Université Grenoble-Alpes)
  Hydrogen, Helium nuclei
  Boron/carbon
Positron fraction, positron and electron fluxes (LAPP et al, 3 postdocs: CNRS, CNES, ANR, 3 PhD Université Grenoble-Alpes)
Summary
References: Phys.Rev.Lett. 110 (2013) 14, ICRC2013, EPS2013
1

## Slide 6: AMS Physics Potential
Searches for primordial antimatter:
  Anti-nuclei: anti He, …
Dark Matter searches:
  e+ , e± , anti p , g…
  simultaneous observation of several signal channels.
Searches for new forms of matter:
  strangelets, …
Measuring CR spectra – refining propagation models;
Study effects of solar modulation on CR spectra over 11 year solar cycle
…
2

## Slide 7: Cosmic Ray Flavors (balloons, PAMELA,..)
Protons : 88 %
Proton ~ 1
Helium ~ 10 --1
Electron ~ 10 --2
Positron ~ 10 --3
Carbon ~ 10 --4
Antiproton ~ 10 --4
Iron ~ 10 --5
Power law E-γ γ [2-3.5]
3

## Slide 8: Cosmic Ray Issues
Production = Primaries (protons, Nuclei, e-, …) from the sources (Super Novae Remnant, Pulsar Nebula, ..)
  E -α α~2
Propagation and diffusion
  E –d d~ [0.3-0.8]
Secondaries
  C, O spallation within the Interstellar Medium
    C + (p,He)IM → B + ... Boron, Be, Li,
  He and H nuclei interacting with the Interstellar Medium
    p + (p,He)IM → e+ + Positrons, Anti protons , …..
Diffusive galactic halo
20 kpc
2-6 kpc
4

## Slide 9: AMS02 – May 2011
Cape Canaveral,STS-134 launch
May 16, 2011
              Endeavour approaches the International Space Station
Cape Canaveral, May 16 2011.
STS 134 Mission, Launch of Endeavour Shuttle
Endeavour approaching the
International Space Station (ISS ~300 km)
7
AMS02 is grappled by the Shuttle
Remote Manipulator System (SRMS)
May 19, 2011
May 19 2011
AMS installation completed on ISS at 5:15 CDT,
start taking data 9:35 CDT Until …. 2020
(CDT Central Daylight Time)

## Slide 10: ISS orbit
ISS velocity: 8km/s, one orbit every 90 mn
Altitude 340-400 km
ISS orbits
Movement direction from wake to ram
8

## Slide 11: Orbital DAQ parameters
DAQ efficiency
Acquisition rate [Hz]
Particle rates vary from
200 to 2000 Hz per orbit
On average:
DAQ efficiency 85%
DAQ rate ~700Hz
9
Longitude (0)
Longitude (0)
Latitude (0)
Latitude (0)

## Slide 12
AMS Data Flow
White Sands Ground Terminal, NM
AMS Computers at MSFC, AL
AMS Payload Operations Control and Science Operations Centers (POCC, SOC) at CERN since June 2011
AMS
TDRS Satellites
Astronaut at ISS AMS Laptop
Ku-Band
High Rate (down):
Events <10Mbit/s>
S-Band
Low Rate (up & down):
Commanding: 1 Kbit/s Monitoring: 30 Kbit/s
10

## Slide 13
C) Solar Array Positions
Visiting Vehicles
Soyuz or Progress
Main Radiator
The thermal environment on the ISS is constantly changing due to:
B)
SUN
AMS
Port
orbit plane
Starboard
13
13
A) The position of the Sun
C
B
A
Ecal – Temperature variation :-100C-280C
11

## Slide 14: Data sample and data taking time
25 billion events are used
in the present analysis
~up to now: 48 billions of data
20 years of operation foreseen
Data take from : 19 May 2011 to : 19 May 2013 (1.5 or 2 years)
Total exposure time : Texp. (Rigidity > 25 GV) = 51.2 ✕ 106 s
12

## Slide 15
ACC
UToF
Horizontal Particle
Rejected
High-Z particle
Accepted
ECAL
TOF + ECAL Trigger
Accepted
Trigger efficiency is estimated with an unbiased trigger sample.
.
MAGNET
LToF
AMS-02 Trigger
13

## Slide 16: AMS-02 Nuclei Properties Measurement
14

## Slide 17: Rigidity measurement
100% relative error for the rigidity
So called Maximum Detectable Rigidity(MDR)
15

## Slide 18: Charge Measurement
16

## Slide 19
TRD
TOF
Tracker
TOF
RICH
ECAL
1
2
7-8
3-4
9
5-6
Tracker Plane 1 (L1)
RICH
Inner Tracker (L2-L8)
Tracker Plane 9 (L9)
TRD
Upper TOF (1 counter)
Lower TOF (1 counter)
Carbon (Z=6)
ΔZ (cu)
0.30
0.12
0.32
0.30
0.33
0.16
0.16
Charge measurement (|Z|)
17

## Slide 20: Nuclei Identification in AMS: ToF and Tracker
18

## Slide 21: ECAL : Description
A 3-D sampling calorimeter made of
lead foils and scintillating fibers
18.5mm
21
y
x
z
particle direction
Lead (58%), Scintillating fibers (33%),
Optical glue (9%), Density ~ 6.8 g/cm3
Dimensions 648x648x167 mm
9 super layers : 4 in The X view and 5 in the Y views
Weight: 661 kg (“pancake” 512 kg)
Acceptance : 0.06 m2sr
One Super Layer
3D Imaging
Calorimeter
17 X0
lI/X0 ~22
Energy range 8 MeV To 1 TeV
19

## Slide 22
30 mm
Light guides
PMT
HV Divider
Front End Board with an ASIC
Shielding
Front End and light collection system
Calorimeter
- Robust (fulfill space constraints)
- Compact (70 mm long)
- Light (67 kg)
- Low Power consumption (12W)

## Slide 23: Front End electronics dependence with temperature
  Variation: Anti-correlated
  with temperature: - 0.36 ‰ per OC
Saturation
Slope = Gain Ratio

## Slide 24: Energy Linearity and Energy resolution
Test beam Data (Aug 2010)
Linearity better than 1%
Energy resolution better than 2 % for Energy>80 GeV
20

## Slide 25
Acceptance
(m2 sr)
Efficiency(trigger, selection)
Exposure Time
Number of counts
Flux is given by:
Kn is the kinetic energy per nucleon, or the momentum for electron, positron is measured from TOF and RICH (beta)
or from Tracker (rigidity) or ECAL(leptons)
Flux and Ratio measurements
Bin Width
21

## Slide 26: Spectrum unfolding
1/R
Entries
True spectrum
1/R
Resolution function :
σ= 1/MDR
=
1/R
Entries
Measured spectrum
×
log(R)
log(F ✕ Rγ)
log(R)
log(F ✕ Rγ)
MDR
Deformation
Unfolding
22

## Slide 27: Protons - Systematic errors
Acceptance εac = 2.8 %
Trigger efficiency εtrg.= 1.0 %
Track reconst. Efficiency εtrk.= 1.0 %
Total systematic errors of normalization :
εnorm. = (εacc2 + εtrg2 + εtrk2 ) ½ = 3.1 %
Systematic error of unfolding εunfold < 1 % at R < 200 GV εunfold = 5.4 % at R = 1 TV
e
γ
P
EEcal = Ee+ Eγ
23

## Slide 28: Proton Flux
From 1 GV to 1.8 TV
Binning chosen according to the resolution
24
Power law behaviour, index > 2.7, > 1000 protons above 1 TV

## Slide 29: Protons Fluxes
25
Total Syst. errors Unfolding errors
Stat. errors

## Slide 30: Ams-02 Helium flux
26
Power law behaviour, index < 2.7

## Slide 31: Helium - Comparison with Pamela measurements
27
He Power law behaviour, index < 2.7
H Power law behaviour, index > 2.7
Helium
Protons

## Slide 32
Layer 1 = 6.1
TRD = 6.0
UTOF = 7.6
Inner = 4.8
LTOF = 5.2
RICH = 5.0
Carbon
Boron
B/C :Identification of Fragmentation Events
R = 10 GV
One of the most systematic uncertainty : The fragmentation inside the detector.
The first layer do play a key role in the selection
28

## Slide 33: Estimation of the fragmentation B/C
Acceptance is convolution of geometry and fragmentation effects.
Carbon selected with L1 and UTOF. Fragmentation distribution evaluated with LTOF.
Data and MC agreement evaluated being at 2% level.
29

## Slide 34: AMS-02 - Boron/Carbon Ratio
30

## Slide 35: e+,e- Identification in AMS
Proton rejection goal > 1/100000 => 3 independent detectors are used
e-
p
MDR=2 TV
31

## Slide 36
Proton rejection
TRD estimator :likelihood based on
the signal amplitude in each layer (20 in total)
ECAL estimator : Boost Decision Tree
based on the 3D shower shape features
ISS 50-100 GeV
32
350-500 GeV
TRD Estimator
Hadrons
Leptons
Ecal Estimator
83.2-100 GeV
Notes: 36
36

## Slide 37
Electron rejection
2 sources
Multiple scattering and finite resolution of the tracker
Secondary tracks produced along the the path of primary e+- (tagged and controlled with the lower TOF)
Good agreement Data/MC
● Data
-- MC
Charge confusion average Tracker patterns
33

## Slide 38: Positron fraction
34
The relative fluctuations of the ratio across the observed sky map show no evident pattern
6.8 millions of leptons
(170 citations)
Anisotropy
r-<r>/<r>
Phys.Rev.Lett. 110 (2013)

## Slide 39: Propagation Model tests
Excluded
---- Positron fraction from secondary
------ “+ Dark Matter
 AMS data
---- Positron fraction from secondary
------ “ + Dark Matter
 AMS data
---- Positron fraction from secondary
------ “ + Dark Matter
 AMS data
Minimal Model
Maximal Model
Maximal Model
Medium Model
Important to constraint the propagation model parameters to draw any interpretations (B/C and δ)
Important also to look at the positron and electron fluxes separately
Independently of the origin of the Source
36

## Slide 40: Impact of the precision of the measurement: shape
If 100% WIMP DM origin
37
I.Colis et al arXiv:1304.1840 [astro-ph.HE]
“Dark Matter models in which the WIMP annihilates 100% into e+e- are no longer of producing positron rise in the positron fraction”
e+ e- from pulsars
Di Mauro et al arXiv 1402.0.0321v1

## Slide 41: AMS-02 Electron and Positron fluxes
Scaled by E3
Index > 3 for electrons
500 electrons expected in 4 years
above 500 GeV
38
Index < 3 for positrons
=> primary sources of positrons

## Slide 42: Positron flux and Pulsar interpretation
Effect of the propagation Models (P.Salati et al)
39

## Slide 43: AMS-02 lepton Flux up to 350 GeV
Scaled by E3
The spectral index and its dependence on energy is clearly different from electrons
Statistical errors only
Scaled by E3
40

## Slide 44: First flux measurements by AMS
41
In the past hundred years, measurements of charged cosmic rays by balloons and satellites have typically contained ~30% uncertainty.
AMS will provide cosmic ray information with ~1-3% stat. uncertainty.
The 30 times improvement in accuracy will provide new insights.
The Space Station has become a unique platform for precision physics research.

## Slide 45
AMS Physics in the next 10 years
42
Positron fraction sensitivity In 10 years
pbar /p sensitivity in 10 years
Positron fraction
Positron, electron, lepton fluxes up to the TeV
B/C and heavy Nuclei up to the TeV ranges : test of the propagation model
Anti proton ratio and fluxes
Anti Matter flux
Nearby Pulsars
DM or 1 pulsar
Secondaries

## Slide 46: Summary
AMS02 is operating on the ISS since the 19th May 2011 and has collected more than 40 billions of events: All AMS subsystems are fully operational and behaves as expected.
Variations of ambient conditions (temperature in first place) are accounted for, with proper calibrations and alignments
For most of the measurements, systematics uncertainties are estimated from the data thanks to the redundancy of AMS-02
Proton flux from 1 GV to 1.8 TV and Helium flux from 2GV to 3.2GV for have been measured by AMS during the first two years of operation on ISS
  In high rigidity region (R > 100 GV) : The spectra are consistent with a single power law and shows no structure nor break
B/C ratio has been measured between 05 to 670 GeV/n. the behaviour at high energy will become more clear with more statistics
Positron fraction has been measured from 0.5 to 350 GeV using the first 6.8 million positron and electrons. Nearby Primary positron sources are needed to explain the measurement.
An electron spectrum in the energy 1-500 GeV and and a positron spectrum in the energy range 1-300 GeV were shown with different spectral indices of electrons and positrons. Systematic errors being under study. The behaviour at high energy will become more clear with more statistics.

## Slide 47: Errors and binning
Total Syst. errors Unfolding errors
Stat. errors
Binning chosen according to the resolution

## Slide 48: Daily flux Stat. Error < ~1% (1 < R < ~20 GV)
Daily flux
Average

## Slide 49: Daily normalized flux
7 Mar. 2012 (X5.4)
17 May 2012 (M5.1)
9 Aug.2011 (X6.9)
27 Jan. 2012 (X1.7)
R < ~30 GV : Variation due to the solar modulation and solar events

## Slide 50: Helium Nuclei Selection

## Slide 51
Isotopic Fraction Evaluation
RICH evaluates the isotopic composition of Boron.
This fraction is used for the Tracker rigidity  kinetic energy conversion.
11B/(11B + 10B) = 0.7 ± 0.1  ~ 1% systematic error on ratio

## Slide 52: Positron fraction AMS
Results of the fit to the data in the energy range 1 to 350 GeV yields:
e- − e+ = −0.63 ± 0.03, i.e., the diffuse positron spectrum is less
energetic than the diffuse electron spectrum;
 e- −  S = 0.66±0.05, i.e., the source spectrum is more energetic than the diffuse electron spectrum;
Ce+ /Ce- = 0.091 ± 0.001, i.e., the weight of the diffuse positron flux amounts to ∼10% of that of the diffuse electron flux;
CS /Ce- = 0.0078 ± 0.0012, i.e., the weight of the common source constitutes only ∼1% of that of the diffuse electron flux;
1/Es = 0.0013 ± 0.0007 GeV−1, corresponding to a cutoff energy of 760+1000 GeV.
=> Primary positrons are needed

## Slide 53: Impact of the precision of the measurement: shape
If 100% WIMP DM origin: different branching ratio scenarios can be tested
I.Colis et al arXiv:1304.1840 [astro-ph.HE]
+ AMS data
+ AMS data

## Slide 54: Pulsar as potential sources of the positron excess

## Slide 55: Pulsar as potential primary positron sources

## Slide 56: SNR acceleration and propagation as potential primary positron sources

## Slide 60: Rigidity measurement (R=pc/Ze)
Span: Inner Tracker(L2->L8)
Span: Inner Tracker+Layers L1 and L9
Challenges:
Alignment feature: Inner and external layers (due to the temperature variations on the ISS)
Track resolution depends on the number of layers included in the reconstruction
19

## Slide 61: Tracker Alignement Occuracy
18

## Slide 62
TRD
24 Heaters
82 Temperature Sensors
Silicon Tracker
32 Heaters
142 Temperature Sensors
ECAL
16 Heaters
80 Temperature Sensors
RICH
16 Heaters
96 Temperature Sensors
TOF & ACC
16 Heaters
64 Temperature Sensors
Magnet
68 Temperature Sensors
TRD
TOF
Tracker
TOF
RICH
ECAL
1
2
7-8
3-4
9
5-6
Thermal Control
MS has no control of ISS orbits and movements of Solar Panels and Radiators.
Temperatures must be kept within limits. There are 1118 temperature sensors and 298 heaters
62
13
Notes: 62
62
62
62

## Slide 63
Representative bins of the positron fraction
44

## Slide 64: Positron mode : features and strategy
×
=
Positron flux
(Signal in data)
Particle Physics
(annihilation modes)
Propagation effect: probed zones for e+,e- within 1-4 kpc
Boost factor: over densities (clumps)
Background
protons : p 10 3-4 *  e+
electrons : e- 10 *  e+
48

## Slide 65: Anisotropy Measurements
Selected events are grouped in 5 cumulative energy bins:
16-350, 25-350, 40-350, 65-350 and 100-350 GeV
Their arrival directions are used to build sky maps in the galactic coordinate(b,l)
55

## Slide 66: Anisotropy Measurements
The coefficients of the multiple expansion are found to be consistent with the expectations from isotropy.
Upper limits on the dipole parameter δ are set.
- After 20 years a sensitivity of the order of 0.014 is expected  could it constraint the pulsar component ?
r-<r>/<r>
56
The relative fluctuations of the ratio across the observed sky map show no evident pattern

## Slide 67: Positron fraction
Positrons:
e+ = Ce+ E−e+ + CsE−s e-E/Es
Secondaries plus source component
Electrons :
e- = Ce- E−e- + CsE−s e-E/Es
Secondaries+ Astrophysics primaries (SNR+..) plus the same source component
Positron source components: pulsars, Dark matter , secondaries near the SNR…
47

## Slide 68: AMS-02 - Boron and Carbon Fluxes
31
BORON
CARBON
AMS-02
HEAO
TRACER

## Slide 69: Pulsars: Possible sources of primary positrons
Mechanism : the spinning B of the pulsar strips electrons that emit gamma => production of e+e- pair that are trapped in the cloud, further accelerated and later released
The pulsar must be young (< 105 years) and nearby (<1 kpc)
Predicted Flux:
16% of the pulsar energy goes into e+e- pairs for all the pulsars
I.Colis et al arXiv:1304.1840 [astro-ph.HE]
Using also the constraint on e+ + e- data
Positron Spectrum
Or
Important to measure the positron and electron spectrum separately
Anisotropy for both electrons and positrons (r:distance, t=age
Di Mauro et al arXiv 1402.0.0321v1

## Slide 70: Cosmic Ray Issues
Ncr(E)
t(E)
Qcr(E)
γ = a + d ≈ 2.7 (Nuclei)
E-α
Source spectrum
Injection rate
a = 2.0 … 2.4
d = 0.3 … 0.7
E-γ
Measured
CR density
Measured spectrum index (γ) results from :
  Production/acceleration mechanism (a)
  Diffusion term (d)
E- Diffusion/
confinement
time
5