## Slide 1: Exemples d'utilisation des outils TCAD pour la technologie HVCMOS
Journées VLSI - FPGA - PCB de l'IN2P3, Marseille
Jian LIU — SDU/CPPM (PhD Student)
12 June 2014
On behalf of the HV CMOS ATLAS Collaboration

## Slide 2: Outline
ATLAS Phase II Upgrade and HV CMOS Introduction
Sentaurus TCAD Introduction and Simulation Procedure
GF BCDlite Technology TCAD Simulation
Conclusion and Perspective

## Slide 3: HL-LHC Environment
Fluence at 5 cm radius:
NIEL: ~1-2•1016 neq cm-2
TID: ~1 GRad
The new Inner Tracker should be rad-hard, cope with high occupancy and lower material budget.
After the Phase II upgrade ~2025,
The HL-LHC will operate at a nominal instantaneous luminosity of 5×1034cm-2s-1 .
Total pixel silicon area of ATLAS Inner Tracker (ITk) is 8.2m2.
More detail of ATLAS Upgrade please see Patrick Pangaud’s talk: La technologie HVCMOS pour les upgrades de LHC

## Slide 4: HV CMOS for Phase II Upgrade
Explore industry standard CMOS processes as sensors:
Basic requirement is Deep N Well(DNW)=>high substrate bias voltage=>drift=>rad-hard
Existing in many processes, especially in HV CMOS technologies, such as AMS 0.18um HV CMOS, GF 0.13um BCDlite and LF 150nm technology…
Main advantages:
Commercial CMOS technology lower price per unit area.
Can be thinned to tens of um  material budget reduced.
Pixel size can be reduced.
1st amplifier in-sensor  capacitive coupling to a specific digital part by gluing (compatible with ATLAS FE-I4).
Questions:
Radiation hardness (sensor / transistors).
Signal to Noise Ratio / Efficiency.
In order to verify the feasibility of specific HV CMOS technologies, we need to understand the DNW electrical behavior carefully  3D TCAD simulations were and are being performed using Sentaurus.
More detail of HV CMOS project please see Patrick Pangaud’s talk: La technologie HVCMOS pour les upgrades de LHC

## Slide 5: Sentaurus Framework and Tools
Green items : we are using at this moment.
Sentaurus is a suite of TCAD tools which simulates the fabrication, operation and reliability of semiconductor devices.

## Slide 6: Device Simulation Flow
Sde
Input: xx_sde.cmd
xx_sde.sat
Output: xx_bnd.tdr
Snmesh
Input: xx_bnd.tdr
Output: xx_msh.tdr
Sdevice
Input: xx_des.tdr xx_des.plt xx_des.log
Svisual
Output: xx_des.tdr
xx_des.plt
xx_des.log …
Input: xx_msh.tdr xx_sdevice_des.cmd
Sentaurus Visual allows you to visualize complex simulation results generated by physical
simulation tools in one, two and three dimensions.
Sentaurus Device simulates numerically the electrical behavior of a single semiconductor
device in isolation or several physical devices combined in a circuit.
Mesh Generation Tools is a suite of tools that produce finite-element meshes for use in
applications such as semiconductor device simulation, process simulation.
Sentaurus Structure Editor can be used as a two-dimensional (2D) or three-dimensional (3D)
structure editor, and a 3D process emulator to create TCAD devices.
Substrate boundary and doping:
(sdegeo:create-cuboid (position 0 0 0) (position 387.47 878.28 250) "Silicon" "bulk" )
(sdedr:define-refinement-size "bulk" 30 80 50 2 2 2 )
(sdedr:define-refinement-placement "bulk" "bulk" (list "material" "Silicon" ) )
(sdedr:define-refinement-function "bulk" "BoronActiveConcentration" "MaxTransDiff" 1e10)
(sdedr:define-constant-profile "bulk" "BoronActiveConcentration" 1.34e15)
(sdedr:define-constant-profile-material "bulk" "bulk" "Silicon")
File {
*input files:
Grid= "n3_ccpd_ams_msh.tdr“
*output files:
Plot= "n1_des.tdr“
Current = "n1_des.plt“
Output = "n1_des.log“
}
Electrode {
{ Name="dnw1" Voltage=1.8 }
{ Name="p+2" Voltage=0 }
}
Physics{
Mobility( PhuMob HighFieldSaturation Enormal )
Recombination( SRH( DopingDependence ) )
}
Plot {eDensity hDensity eCurrent hCurrentPotential SpaceCharge ElectricFieldeMobility hMobility eVelocity hVelocityDoping DonorConcentration AcceptorConcentration}
Math {
Wallclock ParallelLicense (Wait) Number_of_Threads = 4 Extrapolate RelErrControl NotDamped=50 Iterations=20
}
Solve {
PoissonCoupled {Poisson Electron}Coupled {Poisson Hole Electron }
Quasistationary (Goal { Name="p+1" Voltage=-60 }InitialStep=-0.1 Maxstep=-5 MinStep=-0.01){Coupled {Poisson Electron Hole }}
}
3D Structure
Define input and output file
Declare electrodes
Declare physics models
Declare parameters which will be saved to .tdr file
Declare math method and settings
Declare solve method and steps

## Slide 7: Sdevice Physics
Physics | Models
Mobility | Concentration-dependent mobility , High-Field saturation, Mobility degradation at interfaces, Philips Unified mobility(temperature dependence)
Generation recombination | Concentration dependent Shockley-Read-Hall(SRH), Avalanche generation
Traps and Fixed Charges | Bulk traps, interface traps, charges
Tunneling | Band-to-band tunneling, Trap-Assisted tunneling, Fowler-Nordheim tunneling
Radiation | Heavy Ion Model,
Hot carrier | Classical lucky electron injection, Fiegna Hot-Carrier Injection

## Slide 8: Bulk Damage Model
Implement radiation damage effects via traps in the forbidden gap.
V. Eremin, E. Verbitskaya, Z. Li, Nucl. Instr. and Meth. A 476 (3) (2002) 537.
Notice: this model is valid for Non Ionizing Energy Loss (NIEL) and equivalent fluence up to 1e16neq/cm2
Bulk damage is induced by interaction of the incident particles with the nuclei of the silicon lattice atoms.

## Slide 9: TID Effect Simulation (X-ray)
For Total Ionization Dose effects,
Calculate Not and Nit density from analytical models;
Not is simulated as a fixed charge sheet in the oxide;
Nit is simulated with a TCAD interface trap model.
Pre-irradiation TCAD device simulation
Bias conditions
Eox extraction
Nit calculation
Not calculation
Irradiation condition (D)
Post-irradiation TCAD device simulation
Fix charge
Interface trap
Two discrete levels at 0.3 and 0.8 eV from Valence band

## Slide 10: Goals of Simulation
1) Depletion  signal amplitude, charge sharing
2) Electrical Field & Weighting Potential  signal formation, breakdown voltage
3) Leakage Current  SNR
4) Breakdown & Punch Through
5) Capacitance  SNR
6) Noise  SNR
7) MIPs Response and Efficiency  signal formation
8) Spice Parameter Extraction
Above items will be simulated with both NIEL and TID effects.

## Slide 11: GF BCDlite TCAD Simulation Geometry
Layout in Cadence
Transport to Sentaurus Ligament
3-pixel device generated by Procem
Pixel size: 33*125um2
Substrate thickness:
200um
Substrate resistivity: p-type 10 ohm.cm

## Slide 12: GF Doping Profile
P-SUB
DNW (N-epi)
DW
PF1VA
NAT
By checking design rules, mask generation and doping schematic, try to use an uniform p-type doping in regions 1-6 (P-region).
Note: the p-region is the most crucial area, which will determine the breakdown and lateral capacitance.
GF BCDlite doping schematic
Architecture in simulation

## Slide 13: GF Simulation — Depletion
~4.8um depletion depth is obtained @Vsub= -30V  384e (MIPs)
Depletion width is ~1.5um @ Vsub= -30V.
Due to the relative heavy doping in the p-region, large dead region exits between pixels.
@Vsub=-30V: the simulation junction capacitance is ~80fF, which is agree with the calculated value ~60fF(using SPICE model parameters)

## Slide 14: GF Simulation — Breakdown
doping
Hole current density
Breakdown occurs at metallurgy junction and beneath the STI.
If reduce p-region doping, increasing breakdown is obtained.
Breakdown ~-40V
Measured value ~-33V

## Slide 15: GF Simulation — Leakage Current with NIEL Effect
Fluence( )/neq.cm-2 | Current/A @ -30V
0 | 6.5e-13
1e14 | 7.8e-11
1e15 | 7.9e-10
1e16 | 8.2e-9
Measured value is ~9e-13A (matrix ~1nA)
(source meter has a large fluctuation +-1nA)
To simulate non-ionizing energy loss (NIEL) effect, we can implement discrete traps into the forbidden gap.

## Slide 16: Conclusion and Perspective
What we can do using Sentaurus:
  2D/3D Process/Device simulations
    DC/AC parameters extraction
    Transient response(MIPs)
    Irradiation effects
  Multi projects manipulation
    Define parameters and variables for a specific technology in Workbench
By TCAD simulation (GF BCDlite), ~77% p-region between pixels is un-depleted, which will reduce the efficiency!! Alternative approach Normal 130nm LP Process with HR substrate.
Will continue to perform simulations of NIEL, TID effects and transient response.

## Slide 17
Thanks for your attention!!