## Slide 1: La technologie HVCMOS pour les upgrades de LHC
Patrick Pangaud
12 juin 2014
Journées VLSI - FPGA - PCB de l'IN2P3 2014

## Slide 2: Inner Tracking ATLAS detector
Straw tubes
Silicon strip
Silicon pixel
Pixels area ~1.5m²
Strip area ~100m²

## Slide 3: LHC and ATLAS upgrade
∫ L dt
Year
phase-0
phase-1
phase-2
2013/14
2018
~2022
7 TeV
→14 TeV
1027 →
2x1033cm-2s-1
→ 1x1034cm-2s-1
1x1034 →
~2x1034cm-2s-1
Now
~10 fb-1
~50 fb-1
~300 fb-1
3000 fb-1
→ 5x1034cm-2s-1
luminosity leveling
Possible upgrade timeline
T. Kawamoto, TIPP2011, Chicago, USA

## Slide 4
Hybrid Pixels Detector for particles trackers
An early 3-D approach!!
  Sensor for particles detection
  Dedicated electronic chip
  AND
  A fine pitch bump-bonding solder for interconnection
Sensors (Si, CdTe, GaAs, Diamond…) for ionizing particles
Electronic pixel readout
  Monolithic device
  Analog detection (low noise, low power)
  Discriminator
  Digital readout

## Slide 5: From Hybrid to Monolithic pixel sensor
Hybrid Pixel Detectors
Charge collection by drift in depleted bulk -> High signal and radiation hardness
d ~(ρV)1/2
Full CMOS technology
- high material budget
- high cost (chip + sensor + hybridization)
Depleted MAPS
Charge collection by drift in depleted bulk -> High signal and radiation hardness
d ~(ρV)1/2
Usually not full CMOS
AND material budget
AND low cost
for HL-LHC need
Properties

## Slide 6: Smart pixel Project
From the Hybrid Pixel, the outer sensor is placed now into the substrate. The CMOS signal processing electronics are placed inside the deep-n-well. PMOS are placed directly inside n-well, NMOS transistors are situated in their p-wells that are embedded in the Deep-well as well.
The best results are achieved when a standard high voltage CMOS technology is used.
A lowly-doped deep n-well can be then used. Such an n-well can be reversely biased with a high voltage.
We expect a large depleted area thickness
The charge generated by ionizing particles in the depleted area is collected by drift. Due to high electric field and small drift path, charge collection is very fast
Due to drift based charge collection we expect to get an high radiation tolerance
P-substrate
NMOS transistor
in its p-well
PMOS transistor
in its n-well
Particle
E-field
Deep n-well
Pixel electronics in the deep n-well
The sensor is based on the “deep” n-well in a p-substrate

## Slide 7: Charge collection by drift (HV vs HR)
Drift means to get the biggest depleted area -> fast charges collection, more radiation hardness
The depletion (d) is proportional to
The equivalent charge collection is 80e-/µm
  Example
The reality is a mixed of depletion and diffusion charge collected, maybe in-between.
charges sharing Psub
DNWELL
NWELL
PWELL
DNWELL
NWELL
PWELL
reduced charges sharing Psub
DNWELL
NWELL
PWELL
DNWELL
NWELL
PWELL
    200Ω.cm gives d=15µm@100V (1200 e-)
    2kΩ.cm gives d=50µm@10V (3500 e-)

## Slide 8: Using Hybrid or Monolithic Detectors
Hybrid detector characteristics:
  n-in-n or n-in-p silicon sensor with reduced drift distance
  DSM rad-hard IC (-130nm- or reduced feature size 65nm?).
  Valid option: should work (after development).
  Drawback: 1- Price of hybridization / of non-standard sensors (yield?) and for a large area.
  2- Will stay rather thick.
  3- High bias voltage.
  4- Deep charge collection leads to difficult 2-track separation in boosted jets.
Monolithic detectors characteristics :
  -> Next slide

## Slide 9: Monolithic Detectors Main Characteristics
CMOS electronics inside deep n-well.
Negatively biased substrate leads to ~10-15μm depletion zone  charge collection by drift.
Small feature size + relatively low complexity of in-pixel logic  small pixel size.
1st stage signal amplification on-sensor (low capacitance  good SNR).
Featuring: 1- electronics rad-hard (DSM technology).
2- sensor rad-hard (small depletion depth, small ΔNeff).
3- low price (standard CMOS process).
4- low material budget (can be thinned down).
5- low maximum bias voltage (moderate substrate resistivity).
6- fast (electronics on sensor).
7- great granularity (1st prototype 33×125μm , can go down).

## Slide 10: Technologie HVCMOS : Echéances
Période 2014-2015 : Capteur HVCMOS couplé capacitivement au circuit FE-I4-B (pour ATLAS) Objectif : atteindre 99 % d'efficacité (moins de 1 % masqué pixels) avec un « time-walk » de 25ns, un décodage d'adresse des sous-pixel sur toute la surface de 2cm x 2 cm, avec une tolérance de au moins 300 MRads. Doit servir de démonstrateur in-situ. Pour cela, recherche de la meilleur technologie(HT ou HR), avec contact par colle mais aussi par bump-bonding (coûts plus élevés).
Période 2015-2019 : Capteur HVCMOS couplé au nouveau circuit numérique (FE65 ou FEI4-C) (couplé capacitivement ou par liaison 3D avec TSVs) ou bien directement intégré dans le prochain circuit (FE65 ou autre). Tolérance au radiations jusqu'à 1000 MRad. La technologie HVCMOS devra être fiable, de faible coût avec un fondeur acceptant une grosse production pour fournir les expériences ATLAS et CMS.

## Slide 11: ATLAS Readout -with larger pixels-
Combine 3 pixels together to fit one FE-I4 (50×125μm2 pixels), with HVCMOS pixels encoded by pulse height.
The tiny HV2FEI4p2 prototype glued on the large FE-I4

## Slide 12: HV2FEI4 chips
2011
AMS 0.18µ HV
3mm x 4mm
CCPD_AMS V1
ρ : 10 Ω.cm
HV : 60V
Few MRads
2012
AMS 0.18µ HV
3mm x 4mm
CCPD_AMS V2
ρ : 10 Ω.cm
HV : 60V
860 MRads
2013
GF 0.13µ BCDLite
3mm x 3mm
CCPD_GF V1
10 Ω.cm
HV : 30V
1 GRads
2014
LF 0.15µ
3mm x 3mm
CCPD_LF V1
1k-3k Ω.cm
10V
? GRads
RAD-HARD
RAD-HARD
RAD-HARD & EFFICACITE
RAD-HARD & EFFICACITE
2014
GF 0.13µ LP
3mm x 3mm
CCPD_GF V2
1K- 3k Ω.cm
HV : 30V
1 GRads

## Slide 13: AMS 1nd prototype : unglued
Recorded routinely 90Sr and 55Fe spectra.
Degradation at 80MRad proton irradiation (dead at 200MRad!)

## Slide 14: AMS 1nd prototype on FEI4
90Sr-source.
Readout through FE-I4.
kHz rate recorded!
The sub-addresses of the CCPD pixels as reconstructed in units of Time-Over-Threshold (ToT, 25 ns) by the FE-I4 chip.
Figure 1: the sub-addresses of the CCPD pixels as reconstructed in units of Time-Over-Threshold (ToT, 25 ns) by the FE-I4 chip.

## Slide 15: AMS 1nd prototype : Bulk damage
Small depletion depth  bulk enough rad-hard?
Non-ionizing radiation at neutron source (Ljubljana) to 1.1016 neq.cm-2.
leakage current increase
(as expected)
sensor works at room T!
Note: 30 days annealing at room temp
No source
With 90Sr

## Slide 16: AMS 2nd prototype : TID issue
Few pixel flavors with enhanced rad-hardness: guard rings, circular transistors… (different pixel types lead to different gains -expected-).
“rad-hard”
“normal”
55Fe spectra, unirradiated
different gains

## Slide 17: AMS 2nd prototype : TID issue
After 862 MRad (annealing included 2h at 70°C each 100MRad), after parameter retuning, amplifier gain loss recovered to 90% of initial value
Recovery at 862 MRad (NOT 900MRad)
Relative preampli amplitude variation as function of dose

## Slide 18: GF BCDLite technology
Why GlobalFoundries BCDLite
  It’s a new and low cost commercial available solution, with a growth has being driven by the smartphones and tablets, in the last years.
  The 0.13µm BCDlite is based on 0.13µm LP baseline, incorporating Bipolar, CMOS and HV transistors.
  GF 0.13µm BCDLite Characteristics
    8 metals (2 Thick) and 1 poly level
    Psub 10 ohms.cm,
    8 inches wafer,
    Reticle size : 26 x 30 mm.
    Low Voltage devices into Low Voltage DeepNwell.
    High voltage devices into High voltage DeepNwell
  By tweaking the Design Rules, it’s possible to put low voltages devices into low Voltage DeepNwell, and to apply High Voltage into the substrate (30V and more), by increasing the breakdown voltage between the N (DeepNwell ) and P (Pwell into the subtrate) junction.
ATLAS Upgrade Week - P. Pangaud

## Slide 19: The HV2FEI4_GF Chip
The CPPM has submitted (June 2013) a new HV2FEI4 version in GlobalFoundries 0.13µm BCDLite technology. The HV2FEI4 GF version is a 26 columns and 14 rows matrix pixels.
The HV CMOS sensor pixels are smaller than the standard ATLAS pixels, in our case 33μm x 125μm - so that three such pixels cover the area of the original pixel.
2
3
1
2
3
1
Bias A
Bias B
Bias C
FEI4 Pixels
CCPD Pixels
Signal transmitted capacitively
The pixel chain contains charge sensitive amplifier, comparator and tune DAC.
The HV2FEI4_GF chip contains additional test structures
Test Transistors :
3 NMOS ; 3 PMOS
Mini size :150n/130n
Narrow channel size : 200n/15µ
ELT size : 2,639µ/1.302µ
Pixels simple (outside of the matrix)
1 pixel chain without discriminator (Pixel_Alone)
1 pixel without analog Front-End chain (Pixel_DNW)
Additional Test
1 inner Current reference readout
1 DAC for test purpose

## Slide 20: TCAD Simulation- a precious help
~4.8um depletion depth is obtained @Vsub= -30V  384e (MIPs)
    Psub 10 ohms.cm
Depletion width is ~1.5um @ Vsub= -30V.
Due to the relative heavy doping in the p-region, large dead region exits between pixels.
More detail of TCAD Simulation please see Jian Liu’s talk

## Slide 21: HV2FEI4_GF Chip: Test results and General Functioning
The chip works well with a HV of -30V.
BUT it has minor defective functions:
Sr90
The test analog buffer has not been optimized : The observed analog output via this buffer is ten times smaller than expected.
The problem is identified: need to optimize the size of 1 transistor.
The loading of data works only if the power values are changed.
The problem is identified : need to add a digital input buffer.
Chart: 

## Slide 22: GF : High voltage Power consomptions
Annealing period helped to recover few µA leakage current up to 600MRads.
After 600MRads, annealing period at 70°C is a mandatory, to recover few µA leakage current

## Slide 23: GF : Pixels behavior at 1GRads (outside of matrix)
SR90
Pixel DNW
After 2hrs at 70°C
SR90
Pixel Alone
After 2hrs at 70°C
After 200MRads, the both signals were to weak to be check by spectrum analysis.
The preamplifier has a defect cascode transistor ( bad size) from the design. This cascode transistor, is not enough hardness for this High Level dose.
At 1GRads, the chip is still alive.
Amplifier output vs. Dose

## Slide 24: A new 3D approach for HEP community
TSV
Bond Interface
Tier 2
Smart Sensor
Tier 1
(thinned wafer)
BackSide Metal (electrical connected)
M6
M5
M4
M3
M2
M1
M1
M2
M3
M4
M5
M6
M6
M5
M4
M3
M2
M1
M1
M2
M3
M4
M5
M6
particle
Electrical field
Wire-Bond PAD
TSV technologies (Via last or middle or first)
HV process
Bond Interface
Backside Metallization
Can we mix the smart diode and the 3D Integrated technology?

## Slide 25: Smart sensor : Qualification Program
HV and HR CMOS technologies evaluation (ATLAS Phase 1 and 2)
  Contact various vendors, offering HV CMOS and/or HR technology
  Qualification program
    Detection efficiency
    Radiation Hardness
    Cost and production
    Reliability
Fonderies | Node size | Prototypes | Triple Well (shallow NWELL) | HV option | HR option | Rad Hard
A | 180nm | 3 | no | 60V | 2015 | 862MRads
B | 150nm | 1 | Shallow NWELL | no | 3kΩ.cm | 50MRads
C | 130nm | 1 | Triple Well | 30V | 3kΩ.cm | 1GRads
D | 130nm | 1 | Triple Well | no | no | 400MRads

## Slide 26: Technology requirements
Capacitive Coupling and Monolithic Pixels
  To increase the depleted zone , we need HV technology and High Resistivity wafer
  To increase the matrix surface, we need to increase the reticle size, by using stitching solution.
  To increase the detection efficiently (smaller pixel and higher S/N ratio), we need to understand the process generation. (profile, process generation, etc..)
  To enhanced the pixel architecture, by applying if possible an Triple-Well into the DNWELL
  To increase the reliability, we need to design a radiation hardness pixel structure.
  Back-Metallization and TSV approach
Business and sales approach
  Which scheme to do prototyping
  Access to MPW
  Partnership
  Production time frame and large scale production

## Slide 27: Conclusions
  Les technologies pouvant être utilisées dans des applications HVCMOS sont de plus en plus nombreuses. ( IBM 0.13µm, AMS 0.35µm HV, AMS, 0.18µ HV, GF 0.13µm, Lfoundry 0.15µm, TowerJazz 0.18µm, XFAB 0.18µm SOI………………………).
  A fortiori, de plus en plus d’applications sont intéressées par le HVCMOS.
  Par contre, elles demandent une connaissance très pointue du process de fabrication, ainsi que de la technologie (profile de dopage, etc…).
  ATLAS et CMS (trackers) sont très demandeurs de cette nouvelle approche ( faible coût, faible bilan matière, meilleure granularité…), pour les upgrades de LHC, mais….
  Rien n’est encore démontré/validé à ce jour ( quelques proto… très prometteurs)
  Par contre, l’arrivée de Wafers High Res (qques KΩ) devrait grandement aider la validation.