## Slide 1: MAPS for ALICE Upgrade and Beyond Frédéric Morel (on behalf of PICSEL and ALICE teams of IPHC Strasbourg)
Outline
Starting point: STAR-PXL
MISTRAL and ASTRAL: general description
MISTRAL upstream: description and test results
ASTRAL upstream: description and test results
MISTRAL and ASTRAL downstreams (SUZE): description and test results
Conclusions
Perspectives for MAPS

## Slide 2: Starting point: Ultimate chip in STAR
Physics data taking since March 3rd, 2014
MIMOSA28
(ULTIMATE)
Pictures Credit: Berkley Lab and IPHC

## Slide 3: Towards Higher Read-Out Speed and Radiation Tolerance
Next generation of experiments calls for improved sensor performances:
Main improvements required while remaining inside the virtuous circle of spatial resolution, speed, material budget, radiation tolerance  move to 0.18 µm process
  To enhance the radiation tolerance
    High resistivity epitaxial layer
    Smaller feature size process
  To accelerate the readout speed
    More parallelised read-out
    Optimised number of pixels per column
    New pixel array architectures
    Smaller feature size process
Expt-System |  t |  sp | TID | Fluence | T op
STAR-PXL | <~ 200 µs | ~ 5 µm | 150 kRad | 3x1012 neq/cm² | 30 °C
ALICE-ITS | 10-30 µs | ~ 5 µm | 700 kRad | 1013 neq/cm² | 30 °C
CBM-MVD | 10-30 µs | ~ 5 µm | <~10 MRad | <~ 1014 neq/cm² | <<0 °C
ILD-VXD | <~2 µs | <~ 3 µm | O(100) kRad | O(1011 neq/cm²) | <~30 °C
Schematic cross section of MAPS in a CIS process with deep p-well feature

## Slide 4: Sensors R&D for the upgrade of the ITS: Our Strategy
R&D of up- & down-stream of sensors performed in parallel at IPHC in order to match the ITS timescale
for 2 final sensors (~3x1.3 cm²)
  - Mature architecture: MISTRAL = MIMOSA Sensor for the inner TRacker of ALICE
    Relatively moderate readout speed (200 ns/ 2rows)
      ~ 200 mW/cm² , σsp ~ 5 µm for inner layers
      ~ 100 mW/cm² , σsp ~ 10 µm for outer layers
  - Improved architecture: ASTRAL = AROM Sensor for the inner TRacker of ALICE
    Higher speed (100 ns/ 2rows) + Lower power
      ~ 85 mW/cm², σsp ~ 5 µm for inner layers
      ~ 60 mW/cm², σsp ~ 10 µm for outer layers
Modular design + reused parts  optimising R&D time
Several groups involved in the ITS design
Upstream
Downstream

## Slide 5: Upstream of MISTRAL Sensor
Pixel level:
  Sensing node: Nwell-PEPI diode
    Optimisation = f (diode size, shape, No. of diodes/pixel, pixel pitch, EPI)
  In-pixel amplification and cDS:
    Limited dynamic range (supply 1.8 V) compared to the previous process (3.3 V)
    Noise optimisation especially for random telegraph signal (RTS) noise
      Sensing diode: avoid STI around N-well diode
      RO circuit: avoid using minimum dimensions for key MOS & avoid STI interface
      Trade off between diode size, input MOS size w.r.t. S/N before and after irradiation
Column level:
  Discriminator: similar schematic as in MIMOSA26 & 28
    Offset compensated amplifier stage + DS (double sampling)
    200 ns per conversion
  Read out 2 rows simultaneously  2 discriminators per column (22 µm)
Designed by Y. Degerli (Irfu/AIDA)
Layout of 2 discri.
(1 columns)
~300 µm
Pixel level
Column level
MIMOSA-34
Sensing node opt.
MIMOSA-32FEE
Amp opt.
MIMOSA-32N
RTS opt.
MIMOSA-22THRa1&2
Chain opt. => 1 D/col
MIMOSA-22THRb
Chain opt. => 2 D/col
2 x FSBB_M0
Verify full chain and full functionalities
1.6 cm
1.8 cm

## Slide 6: Test Results of the Upstream Part of MISTRAL Sensor
LinxWin = 0.18 µm²
LinxWin = 0.36 µm²
LinxWin = 0.72 µm²
Lab test results @ 30 °C (MIMOSA22-THRa1 & 2, MIMOSA22-THRb) :
  Diode optimisation
    CCE optimisation: surface diode of 8-11 µm² (22x33 µm²)
  In-pixel amplification optimisation
    Reduction of RTS noise by a factor of 10 to 100
  MISTRAL RO Architecture: (single & double raw RO)
    2-row RO increases FPN by ~1 e- ENC  negligible impact on ENCtotal
     Design of the upstream of MISTRAL validated
Beam test results (DESY):
  SNR for MIMOSA-22THRa close to MIMOSA 34 result
    8 μm² diode features nearly 20 % higher SNR (MPV)
  Detection efficiency ≥ 99.8% while Fake hit rate ≤ O(10−5)
  22×33 μm² binary pixel resolution: ~5 µm as expected from former studies
  Final ionisation radiation tolerance assessment under way
Pixel not corrected for RTS noise
ENC ~ 17 e-
ENC ~ 4 e-

## Slide 7: Upstream of ASTRAL sensor
Thanks to the quadruple-well technology, discriminator integrated inside each pixel
  Analogue buffer driving the long distance column line is no longer needed
    Static current consumption reduced from ~120 µA up to ~14 µA per pixel
  Readout time per row can be halved down to 100 ns (still with 2 rows at once) due to small local parasitics
Sensing node & in-pixel pre-amplification as in MISTRAL sensors
In-pixel discrimination
  Topology selected among 3 topologies implemented in the 1st prototype AROM-0
  Several optimisations on the 2 most promising topologies in AROM-1
  One third of final sensor (FSBB_A0 ) coming back this week from dicing/thinning
AROM-0
AROM-1
AROM-1b
2x2 pixels
AROM-1a
2x2 pixels
Horizontal controls shared between 2 rows
Horizontal controls
in each row
FSBB_A0
1/3 of final sensor
1.6 cm
0.9 cm

## Slide 8: Summary of the AROM-1 development
AROM-0 submission Feb. 2013
32 x32 pixels (22x33 µm²) Single row readout
32 x32 pixels (22x33 µm²) Single row readout
16 x16 pixels (22x33 µm²) Double row readout
Version 1
Version 2
64 x64 pixels Double row readout
  e: 22x33 µm²
  f: 27x27 µm²
Noise and power consumption optimized
Slightly different timing configuration
Tests in progress
AROM-1e/f submission Nov. 2013
AROM-1a/b/c submission Aug. 2013
64 x64 pixels Double row readout
  a: 22x33 µm² (similar layout as AROM-0v2)
  b: 22x33 µm² (optimized layout)
  c: 24x33 µm² (study impact of pixel pitch)
RTS noise mitigated
Thermal noise from switches optimized
Optimized layout to minimize cross talk and asymmetry
Performance validated already in laboratory
AROM-1 series
AROM-1_a/b/c
More compact
Less stable  more noise
AROM-1_e/f
More stable
Less compact  more noise

## Slide 9: Test Results of the Upstream Part of ASTRAL Sensor
Preliminary lab test results @ 30 °C and @ 100 MHz (instead of 160 MHz)
  Current acquisition board limitation
AROM-1b/c
  Discri alone: TN ~ 0.75 mV, FPN ~ 0.63mV
  Discri+pixel: TN ~ 1.1 mV, FPN ~ 0.66mV
AROM-1e tests are ongoing
  Discri alone: TN ~ 0.29 mV, FPN ~ 0.19mV
  Discri+pixel: TN ~ 0.94 mV, FPN ~ 0.23mV
AROM-1e optimisation is validated
Some residual coupling effects are investigated

## Slide 10: Downstream of Sensors: Zero Suppression Logic (SUZE02)
Identical for both MISTRAL & ASTRAL sensors
  AD conversion (pixel-level or column-level) outputs are connected to inputs of SUZE
Encoding: more efficient than SUZE01 implemented in MIMOSA28 sensor
  Sizable and suitable to process the binary information generated by a 1 cm long pixel array
    Hit density of ~100 hits/collision/cm² + safety factor of 3-4
    Compression factor: 1 to 4 order of magnitude
  Hit clusters identified in 4x5 pixels windows
  Results stored in 4 SRAM blocks allowing either continuous or triggered readout
  Sparsified data multiplexing onto a serial LVDS output
    Prototype data rate: 320 Mbit/s per channel (1 or 2 channels in SUZE02)
SUZE02 preliminary test results: functional and works well @ full speed
  Full sequence of signal processing steps validated using various types of patterns
  SEU sensitivity still to be evaluated
MISTRAL / ASTRAL: 1 Gbits/s data rate required
  One channel output per sensor
    INFN Torino is working on data transmission up to 2 Gbit/s
Row M-1
Row M+1
Row M
HIT
….….…
…….…
Window of 4x5 pixels
2162 µm
2965 µm

## Slide 11: Conclusions
2 sensors being developed at IPHC for the ALICE ITS upgrade:
  MISTRAL: validation of the upstream and downstream architectures completed
    Spatial resolution (22x33 µm² pixel) ~5 µm for inner layers
    Detection efficiency > 99.8 % for fake hit rate ≤ O(10−5)
    Integration time: >~30 µs
    Power consumption ~200 mW/cm² for inner layers & ~100 mW/cm² for outer layers (large pixels)
  ASTRAL: architecture validation on going
    ASTRAL pixel front-end amplification (same as MISTRAL part) validation completed
    Downstream of ASTRAL (shares the same logic with MISTRAL) validation completed
    In-pixel discrimination validation completed
    ASTRAL exhibits 2 x faster readout and lower power consumption than MISTRAL
      Integration time: <~20 µs
      Power consumption ~85 mW/cm² for inner layers & ~30-60 mW/cm² for outer layers (large pixels)
    Beam tests foreseen in Q4/14 for final validation
Characterisation of first large scale prototype (1 cm² sensitive area = 1/3 final sensor), encompassing full signal sensing and processing chain, have been started
  Slow control, Digital test pattern are working

## Slide 12: Perspectives for MAPS
STAR 2013
Solenoidal Tracker at RHIC
EUDET 2006/2010
Beam Telescope
Initial objective: ILC, with staged performances
  CPS applied to other experiments with intermediate requirements
ILC >2020
International Linear Collider
ALICE 2018
A Large Ion Collider Experiment
CBM >2018
Compressed Baryonic Matter
EUDET (R&D for ILC, EU project)
STAR (Heavy Ion physics)
CBM (Heavy Ion physics)
ILC (Particle physics)
HadronPhysics2 (generic R&D, EU project)
AIDA (generic R&D, EU project)
FIRST (Hadron therapy)
ALICE/LHC (Heavy Ion physics)
EIC (Hadron physics)
CLIC (Particle physics)
BESIII (Particle physics)
…

## Slide 13: Outlook
Q2/2014: Submission of various Mimasa22-THRb prototypes to explore and optimise:
  Large pixel pitch optimised for tracker (σsp ~ 10 µm)
  Small diode with thicker hires epi starting material
  PADs on pixel array for laser soldering (4 metal layers used for pixels)
  MISTRAL upstream validation : a mature backup solution for the outer layers
Q3/2014: Submission of optimised versions of AROM-1
  Pixel optimisation
  Last improvement of pixels and sensors for ASTRAL for the inner layers
Q1/2015: Submission of final versions of the FSBBs
  FSBB-M1 which is 1/3 of MISTRAL for outer layers
  FSBB-A1 which is 1/3 of ASTRAL for inner layers

## Slide 14
Thank You !

## Slide 15: Power density, Integration time and Spatial resolution
Effect of pixel pitches on these 3 factors:
  Assumptions
    MISTRAL for outer layers
    Same sensitive area (1.3x3 cm²)
    1 SUZE per final sensor
    Constant power consumption for digital
    NC=Number of Columns (modulo 32)
    NFSBB= Number of FSBBs per final sensor
    NC/NFSBB = Number of rows
  Row pitch (RP) has an effect on Readout time (RT)
    RP = 30000 µm / NC
    RT = (NC / NFSBB ) / 2 x 200 ns
  Column pitch (CP) has an effect on Power density (PD)
    CP = 13000 µm / (NC / NFSBB)
    PD = (60 mA + 0,117 mA x NC x 2) x 1.8 V
    PDopt = (60 mA + 0,09 mA x NC x 2) x 1.8 V
  Both pitches have an effect on Spatial resolution (SR)
    SR = 7µm (RP x CP / (22 x 66 µm²) )1/2 or 1
    Empirical formula for a specific technology and architecture based on the spatial resolution of tested chip with an area of 22 x 66 µm²